Source	CANADA NEWSWIRE
Date	05/04/2021
Time	06:03:15 AM

Company	 Stuhini Exploration Ltd
Title	Stuhini Identifies Gold Target Areas at Ruby Creek and Samples up to 121
g/t gold





    CDNX Symbol: STU











Press Release




" BC-Stuhini-RubyCreekGold   05-04 2091
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.395873:
^Stuhini Identifies Gold Target Areas at Ruby Creek and Samples up to 121
g/t gold@

VANCOUVER, BC, May 4, 2021 /CNW/ - Stuhini Exploration Ltd. (the
"Company" or Stuhini") (TSXV: STU) is pleased to announce further results of
its 2020 field program and identified gold targets on its Ruby Creek Project
(the "Project" or "Property" or "Ruby Creek") located 20 kilometres (km) east
of Atlin, BC.
Highlights include the following grab samples:
<<

--  121.34 grams/tonne ("g/t") Au and 2093 g/t Ag at Boulder Creek
--  34.08 g/t Au and 494 g/t Ag at Lakeview
--  6.03 g/t Au and 51.6 g/t Ag at Birch Creek
--  10.00 g/t Au and 768 g/t Ag at Ruby Creek Au
<>>
Note that rock grab samples are selective by nature and values reported
may not represent the true grade or style of mineralization across the
Property.
Dave O'Brien, Company President and CEO, commented; "We are excited to
add these new gold targets to our exploration objectives and this futher
exhibits the prospectivity of our Ruby Creek tenures. None of these targets
have seen any exploration work for several decades, thus we are hopeful that
new advances and increased breadth and resolution of modern geophysical and
geochemical methods will lead to further advancements."
Southwest Property Targets: Birch Creek, Boulder Creek, and Lakeview
The southwest portion of the Property includes the Birch, Boulder and
Lakeview targets. Both Birch and Boulder Creek were important placer creeks in
the Atlin area with Boulder Creek being the third largest gold producer in the
area. Mineralization occurs in quartz veins hosted within the Cache Creek
complex.
i) Birch Creek Target
The Birch Creek target includes the historic Little Edna showing.
Previous operators focussed on the more prominent north striking and steeply
dipping gossanous structure hosting polymetallic base metal sulfides and
silver mineralization with no significant gold. During the 2020 field program,
gold mineralization was discovered in separate quartz veins on the periphery
of the main Little Edna structure. The gold mineralization is hosted within
narrow, 5 to 20 cm wide, steeply dipping, northeast striking, en echelon
quartz-carbonate veins that appear to widen towards Birch Creek. Birch Creek
is interpreted to be a major fault and conduit for hydrothermal fluids
responsible for the placer gold in the area. Anomalous gold values were
encountered in 3 of the 4 vein samples. The samples were also anomalous in
bismuth and tellurium and absent in base metal mineralization. The highest
grade samples taken 30 metres south of the Little Edna structure returned
values of 6.03 g/t Au and 51.6 g/t Ag. Table 1 summarizes the Little Edna
samples.
Figure 1 - Map of Project Tenures and Gold Targets
Table 1 - Little Edna Assays (6 of 7 samples collected)


Little Edna Gold Veins

---

Sample ID
Sample Source
Au g/t
Ag g/t  Cu %   Pb %     Zn %

---                                                                             
         ---


1905464
Outcrop         6.03      51.6   0.00     0.08       0.00

---                                                                             
         ---


1905461
Outcrop         0.55      31.0   0.01     0.01       0.00

---                                                                             
         ---


1905463
Subcrop         0.23       1.3   0.02     0.00       0.01

---                                                                             
         ---



Little Edna Polymetalic Silver Structure

---


1905373
Outcrop         0.05       487   0.01     1.06       0.02

---                                                                             
         ---


1905374
Outcrop         0.03      75.7   0.15     0.13       0.37

---                                                                             
         ---


1905462
Subcrop         0.08      35.7   0.02     0.13       0.19

---                                                                             
         ---
ii) Boulder Creek Target
The Boulder Creek target is focused on gold mineralization in the
vicinity of the historic Sunbeam showing on the west side of Boulder Creek.
Mineralization is found within quartz vein material that is most likely hosted
within the Cache Creek Complex. The Sunbeam showing is described in a Minister
of Mines Annual Report in 1904, and the exact location uncertain. To date,
several angular proximal float boulders of gold-bearing quartz have been found
in the area with grades as high as 121.34 g/t Au and 2,093 g/t Ag and the
previously reported 78 g/t Au and 1,282 g/t Ag (see June 29, 2020
press-release). Further work on this compelling target is planned for the
upcoming field season.
Figure 2 - Gold & Silver Rock Sample Results, Southwest Property Area
iii) Lakeview Target
The historic Lakeview showing consists of gold bearing quartz veins
hosted in intermediate to mafic volcanic rocks of the Cache Creek Complex. The
target has not received any significant exploration since 1987. Samples in the
2020 program are from steeply dipping north-northeast trending
quartz-carbonate veins and assayed as high as 34.08 g/t Au and 494 g/t Ag.
Table 2 summarizes the Lakeview assays.
In addition to prospecting and rock sampling, 25 soil samples were
collected along a line perpendicular to a geophysical anomaly identified in
the 2020 SkyTEM survey. Two gold in soil anomalies have been recognized on
this line, including a 100 metre long anomaly and a second single sample
anomaly at the very end of the line (see Figure 3 below). An expanded soil
geochemistry survey will be conducted over the areas of interest 2021 field
season.
Table 2 - Lakeview Assays (19 of 29 samples collected)
Sample ID
Sample Source
Au g/t  Ag g/t  Cu %   Pb %     Zn %

---


1905471
Subcrop        34.08     494   0.00     0.03      0.01

---


1996438
Subcrop        25.95     420   0.00     0.03      0.01

---


1905472
Subcrop         19.8     238   0.00     0.01      0.01

---


1478133
Outcrop        15.44     303   0.00     0.57      0.07

---


1905473
Subcrop        14.61     187   0.00     0.00      0.01

---


1905468
Subcrop        13.27     167   0.00     0.10      0.01

---


1905469
Subcrop        10.06     189   0.00     0.33      0.01

---


1478134
Outcrop         8.92     197   0.00     0.01      0.01

---


1905470
Subcrop         7.14     191   0.00     0.41      0.00

---


1478132
Outcrop         6.15     167   0.00     0.25      0.07

---


1905467
Subcrop         2.54      40   0.00     0.04      0.00

---


1905478
Subcrop         0.76      26   0.00     0.06      0.00

---


1478128
Outcrop         0.36     0.5   0.00     0.00      0.00

---


1905304
Subcrop         0.35     5.3   0.00     0.00      0.00

---


1905480
Subcrop         0.33     2.1   0.00     0.00      0.00

---


1905466
Subcrop         0.27     102   0.00     1.00      0.00

---


1478127
Outcrop         0.22     6.0   0.00     0.02      0.00

---


1905231
Subcrop         0.12     0.2   0.00     0.00      0.01

---


1905465
Subcrop         0.11     1.8   0.00     0.00      0.01

---
Figure 3 - Lakeview Gold in Soil Geochemistry
Ruby Creek Gold Target
The Ruby Creek Gold target area begins approximately half a km east of
the historic Adanac molybdenum resource and extends into upper Ruby Creek.
Ruby Creek was the fourth highest gold producing creek in the Atlin Placer
Camp.
Mineralization consists of gold, silver, lead, copper and tungsten in
quartz veins, quartz vein stockwork, and breccias hosted within the Surprise
Lake Batholith. Assays of up to 10 g/t Au were returned from the 2020 program
(Table 3). The target area also encloses two historic diamond drill holes from
2008. The two holes were part of the condemnation drilling for the proposed
Adanac open-pit molybdenum mine. The holes are more than 950 metres apart and
intersected 76.2 metres averaging 0.15 g/t Au and 73.2 metres averaging 0.21
g/t Au respectively (Table 4), including a 3 metre sample assaying 0.6 g/t Au.
Both holes were drilled within the Surprise Lake Batholith.
Figure 4 - Select Gold & Silver Rock Sample Results, Ruby Creek Au Target
Area
Table 3 - Ruby Creek Au Target Assays (18 of 46 samples)
Sample
ID
Sample Source Ag g/t Au g/t
% Cu
% Pb
% Zn
% Mo
% WO3

---


1869576
Felsenmeer     768    10.0     1.06      0.99      0.04        0.001        1.59

---


1996460
Outcrop      17.4    7.82     0.04      0.10      0.01        0.001        0.04

---


1905043
Felsenmeer     305    3.97     0.06      2.73      0.03        0.008        0.00

---


1905037
Outcrop       290    3.84     0.12      5.17      0.04        0.062        0.00

---


1478184
Outcrop       296    3.19     0.10      1.02      0.04        0.000       17.09

---


1905050
Felsenmeer    28.8    2.73     0.14      0.05      0.00        0.001        0.04

---


1905032
Felsenmeer    39.1    1.74     0.08      0.08      0.00        0.002        0.71

---


1996473
Subcrop       4.8    1.53     0.23      0.01      0.00        0.006        0.44

---


1905036
Subcrop        96    1.19     0.10      1.93      0.24        0.018        0.26

---


1869599
Felsenmeer    31.0    0.86     0.02      0.09      0.01        0.000        0.02

---


1905038
Outcrop       571    0.71     0.04      2.86      0.00        0.004        0.03

---


1905045
Subcrop      18.4    0.56     0.08      0.07      0.01        0.002        0.15

---


1996472
Felsenmeer     225    0.48     0.26      0.44      0.00        0.007        0.32

---


1905049
Outcrop      13.7    0.36     0.12      0.01      0.02        0.001        0.03

---


1905047
Subcrop      25.5    0.30     0.11      0.01      0.00        0.000        0.05

---


1905041
Outcrop       4.6    0.30     0.00      0.02      0.00        0.013        0.01

---


1996451
Outcrop      15.6    0.24     0.02      0.12      0.00        0.001        0.09

---


1905039
Outcrop       4.7    0.11     0.01      0.05      0.01        0.370        0.03

---
Table 4 - Condemnation Drill Holes with Anomalous Gold Values (Adanac
2008)

Drill Hole ID
From (m)
To (m)
Interval (m)
Au (ppm)
Ag (ppm)

---                                                                           
---


AD-390              22.9       99.1                76.2            
0.15               0.42

---


Including            53.3       74.7                21.3            
0.21               0.11

---




AD-393             184.4      257.6                73.2            
0.21               0.28

---
In other Company news, Stuhini wished to announce that despite
challenging weather, it has successfully completed its recently announced 2021
SkyTEM airborne geophysical survey on key remaining portions of its Ruby Creek
Project. Company consulting geophysicist Todd Ballantyne will be reviewing and
compiling results in the coming months, which will help Company geologists
define exploration targets for the upcoming 2021 exploration program. The
Company also wishes to announce that it has received a 5 year drill permit for
the Ruby Creek Project. Lastly, on April 22nd the Company hosted it's first
webinar with a series of live corporate presentations. A video recording of
the webinar has been posted on the home page of our website - we encourage
those of you who were not able to attend the presentations to view the
recording so as to better appreciate and understand the Company and its suite
of assets.
QA/QC Protocol: Rock material was collected in poly bags and then
transported to the Bureau Veritas sample preparation facility located in
Whitehorse, Yukon. Samples were crushed, and then pulps were sent to the
Bureau Veritas lab in Vancouver for assay. Four acid digestion and Ultratrace
ICP-MS analysis for 59 elements and fire assay for gold, platinum and
palladium were performed on all samples. Over-limit copper, lead, zinc and
silver samples were analyzed by multi-acid digestion and ICP-ES (MA370).
Conversion to WO3 % (equal sign) W % x 1.2616. All results have passed the QA/QC
screening by the lab.
Ruby Creek Project: The 27,354-hectare Ruby Creek Project is road
accessible and located 20 km east of Atlin, BC. There are 48 different
documented mineral occurrences on the Property, of which 16 are gold-related,
with 4 active gold placer creeks. The Property also hosts the historic Ruby
Creek Molybdenum resource, which has an intact BC Mines Act permit. Stuhini
has an option to acquire 100% of the Ruby Creek Project subject to a 1% Net
Smelter Royalty.
The geological content of this news release has been reviewed andapproved by 
Andrew Wilkins, P. Geo., a qualified person as defined under the
terms of National Instrument 43-101.
About Stuhini Exploration Ltd.
Stuhini is a mineral exploration company focused on the exploration and
development of precious and base metals properties in western Canada, with its
focus on the Ruby Creek Property located approximately 20 km east of Atlin, BC
and the Que Property located approximately 70 km north of Johnson's Crossing
in the Yukon.
Forward-Looking Statements
This news release contains "forward-looking statements" within the
meaning of Canadian securities legislation. Such forward-looking statements
concern the Company's strategic plans, timing and expectations for the
Company's exploration and drilling programs, estimates of mineralization from
sampling, and geological information projected from sampling results. Such
forward-looking statements or information are based on a number of
assumptions, which may prove to be incorrect. Assumptions have been made
regarding, among other things: conditions in general economic and financial
markets; accuracy of assay results; geological interpretations from sampling
results, timing and amount of capital expenditures; the affect of Covid-19 on
the Company's ability to conduct exploration; performance of available
laboratory and other related services; and future exploration costs. The
actual results could differ materially from those anticipated in these
forward-looking statements as a result of the risk factors including: the
timing and content of work programs; results of exploration activities and
development of mineral properties; the interpretation and uncertainties of
sampling results and other geological data; receipt, maintenance and security
of permits and mineral property titles; environmental and other regulatory
risks; project costs overruns or unanticipated costs and expenses;
availability of funds and general market and industry conditions.
Forward-looking statements are based on the expectations and opinions of the
Company's management on the date the statements are made. The assumptions used
in the preparation of such statements, although considered reasonable at the
time of preparation, may prove to be imprecise and, as such, readers are
cautioned not to place undue reliance on these forward-looking statements,
which speak only as of the date the statements were made. The Company
undertakes no obligation to update or revise any forward-looking statements
included in this news release if these beliefs, estimates and opinions or
other circumstances should change, except as otherwise required by applicable
law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
r

" BC-Stuhini-RubyCreekGold   05-04 2091
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.395873:
^Stuhini Identifies Gold Target Areas at Ruby Creek and Samples up to 121
g/t gold@

VANCOUVER, BC, May 4, 2021 /CNW/ - Stuhini Exploration Ltd. (the
"Company" or Stuhini") (TSXV: STU) is pleased to announce further results of
its 2020 field program and identified gold targets on its Ruby Creek Project
(the "Project" or "Property" or "Ruby Creek") located 20 kilometres (km) east
of Atlin, BC.
Highlights include the following grab samples:
<<

--  121.34 grams/tonne ("g/t") Au and 2093 g/t Ag at Boulder Creek
--  34.08 g/t Au and 494 g/t Ag at Lakeview
--  6.03 g/t Au and 51.6 g/t Ag at Birch Creek
--  10.00 g/t Au and 768 g/t Ag at Ruby Creek Au
<>>
Note that rock grab samples are selective by nature and values reported
may not represent the true grade or style of mineralization across the
Property.
Dave O'Brien, Company President and CEO, commented; "We are excited to
add these new gold targets to our exploration objectives and this futher
exhibits the prospectivity of our Ruby Creek tenures. None of these targets
have seen any exploration work for several decades, thus we are hopeful that
new advances and increased breadth and resolution of modern geophysical and
geochemical methods will lead to further advancements."
Southwest Property Targets: Birch Creek, Boulder Creek, and Lakeview
The southwest portion of the Property includes the Birch, Boulder and
Lakeview targets. Both Birch and Boulder Creek were important placer creeks in
the Atlin area with Boulder Creek being the third largest gold producer in the
area. Mineralization occurs in quartz veins hosted within the Cache Creek
complex.
i) Birch Creek Target
The Birch Creek target includes the historic Little Edna showing.
Previous operators focussed on the more prominent north striking and steeply
dipping gossanous structure hosting polymetallic base metal sulfides and
silver mineralization with no significant gold. During the 2020 field program,
gold mineralization was discovered in separate quartz veins on the periphery
of the main Little Edna structure. The gold mineralization is hosted within
narrow, 5 to 20 cm wide, steeply dipping, northeast striking, en echelon
quartz-carbonate veins that appear to widen towards Birch Creek. Birch Creek
is interpreted to be a major fault and conduit for hydrothermal fluids
responsible for the placer gold in the area. Anomalous gold values were
encountered in 3 of the 4 vein samples. The samples were also anomalous in
bismuth and tellurium and absent in base metal mineralization. The highest
grade samples taken 30 metres south of the Little Edna structure returned
values of 6.03 g/t Au and 51.6 g/t Ag. Table 1 summarizes the Little Edna
samples.
Figure 1 - Map of Project Tenures and Gold Targets
Table 1 - Little Edna Assays (6 of 7 samples collected)


Little Edna Gold Veins

---

Sample ID
Sample Source
Au g/t
Ag g/t  Cu %   Pb %     Zn %

---                                                                             
         ---


1905464
Outcrop         6.03      51.6   0.00     0.08       0.00

---                                                                             
         ---


1905461
Outcrop         0.55      31.0   0.01     0.01       0.00

---                                                                             
         ---


1905463
Subcrop         0.23       1.3   0.02     0.00       0.01

---                                                                             
         ---



Little Edna Polymetalic Silver Structure

---


1905373
Outcrop         0.05       487   0.01     1.06       0.02

---                                                                             
         ---


1905374
Outcrop         0.03      75.7   0.15     0.13       0.37

---                                                                             
         ---


1905462
Subcrop         0.08      35.7   0.02     0.13       0.19

---                                                                             
         ---
ii) Boulder Creek Target
The Boulder Creek target is focused on gold mineralization in the
vicinity of the historic Sunbeam showing on the west side of Boulder Creek.
Mineralization is found within quartz vein material that is most likely hosted
within the Cache Creek Complex. The Sunbeam showing is described in a Minister
of Mines Annual Report in 1904, and the exact location uncertain. To date,
several angular proximal float boulders of gold-bearing quartz have been found
in the area with grades as high as 121.34 g/t Au and 2,093 g/t Ag and the
previously reported 78 g/t Au and 1,282 g/t Ag (see June 29, 2020
press-release). Further work on this compelling target is planned for the
upcoming field season.
Figure 2 - Gold & Silver Rock Sample Results, Southwest Property Area
iii) Lakeview Target
The historic Lakeview showing consists of gold bearing quartz veins
hosted in intermediate to mafic volcanic rocks of the Cache Creek Complex. The
target has not received any significant exploration since 1987. Samples in the
2020 program are from steeply dipping north-northeast trending
quartz-carbonate veins and assayed as high as 34.08 g/t Au and 494 g/t Ag.
Table 2 summarizes the Lakeview assays.
In addition to prospecting and rock sampling, 25 soil samples were
collected along a line perpendicular to a geophysical anomaly identified in
the 2020 SkyTEM survey. Two gold in soil anomalies have been recognized on
this line, including a 100 metre long anomaly and a second single sample
anomaly at the very end of the line (see Figure 3 below). An expanded soil
geochemistry survey will be conducted over the areas of interest 2021 field
season.
Table 2 - Lakeview Assays (19 of 29 samples collected)
Sample ID
Sample Source
Au g/t  Ag g/t  Cu %   Pb %     Zn %

---


1905471
Subcrop        34.08     494   0.00     0.03      0.01

---


1996438
Subcrop        25.95     420   0.00     0.03      0.01

---


1905472
Subcrop         19.8     238   0.00     0.01      0.01

---


1478133
Outcrop        15.44     303   0.00     0.57      0.07

---


1905473
Subcrop        14.61     187   0.00     0.00      0.01

---


1905468
Subcrop        13.27     167   0.00     0.10      0.01

---


1905469
Subcrop        10.06     189   0.00     0.33      0.01

---


1478134
Outcrop         8.92     197   0.00     0.01      0.01

---


1905470
Subcrop         7.14     191   0.00     0.41      0.00

---


1478132
Outcrop         6.15     167   0.00     0.25      0.07

---


1905467
Subcrop         2.54      40   0.00     0.04      0.00

---


1905478
Subcrop         0.76      26   0.00     0.06      0.00

---


1478128
Outcrop         0.36     0.5   0.00     0.00      0.00

---


1905304
Subcrop         0.35     5.3   0.00     0.00      0.00

---


1905480
Subcrop         0.33     2.1   0.00     0.00      0.00

---


1905466
Subcrop         0.27     102   0.00     1.00      0.00

---


1478127
Outcrop         0.22     6.0   0.00     0.02      0.00

---


1905231
Subcrop         0.12     0.2   0.00     0.00      0.01

---


1905465
Subcrop         0.11     1.8   0.00     0.00      0.01

---
Figure 3 - Lakeview Gold in Soil Geochemistry
Ruby Creek Gold Target
The Ruby Creek Gold target area begins approximately half a km east of
the historic Adanac molybdenum resource and extends into upper Ruby Creek.
Ruby Creek was the fourth highest gold producing creek in the Atlin Placer
Camp.
Mineralization consists of gold, silver, lead, copper and tungsten in
quartz veins, quartz vein stockwork, and breccias hosted within the Surprise
Lake Batholith. Assays of up to 10 g/t Au were returned from the 2020 program
(Table 3). The target area also encloses two historic diamond drill holes from
2008. The two holes were part of the condemnation drilling for the proposed
Adanac open-pit molybdenum mine. The holes are more than 950 metres apart and
intersected 76.2 metres averaging 0.15 g/t Au and 73.2 metres averaging 0.21
g/t Au respectively (Table 4), including a 3 metre sample assaying 0.6 g/t Au.
Both holes were drilled within the Surprise Lake Batholith.
Figure 4 - Select Gold & Silver Rock Sample Results, Ruby Creek Au Target
Area
Table 3 - Ruby Creek Au Target Assays (18 of 46 samples)
Sample
ID
Sample Source Ag g/t Au g/t
% Cu
% Pb
% Zn
% Mo
% WO3

---


1869576
Felsenmeer     768    10.0     1.06      0.99      0.04        0.001        1.59

---


1996460
Outcrop      17.4    7.82     0.04      0.10      0.01        0.001        0.04

---


1905043
Felsenmeer     305    3.97     0.06      2.73      0.03        0.008        0.00

---


1905037
Outcrop       290    3.84     0.12      5.17      0.04        0.062        0.00

---


1478184
Outcrop       296    3.19     0.10      1.02      0.04        0.000       17.09

---


1905050
Felsenmeer    28.8    2.73     0.14      0.05      0.00        0.001        0.04

---


1905032
Felsenmeer    39.1    1.74     0.08      0.08      0.00        0.002        0.71

---


1996473
Subcrop       4.8    1.53     0.23      0.01      0.00        0.006        0.44

---


1905036
Subcrop        96    1.19     0.10      1.93      0.24        0.018        0.26

---


1869599
Felsenmeer    31.0    0.86     0.02      0.09      0.01        0.000        0.02

---


1905038
Outcrop       571    0.71     0.04      2.86      0.00        0.004        0.03

---


1905045
Subcrop      18.4    0.56     0.08      0.07      0.01        0.002        0.15

---


1996472
Felsenmeer     225    0.48     0.26      0.44      0.00        0.007        0.32

---


1905049
Outcrop      13.7    0.36     0.12      0.01      0.02        0.001        0.03

---


1905047
Subcrop      25.5    0.30     0.11      0.01      0.00        0.000        0.05

---


1905041
Outcrop       4.6    0.30     0.00      0.02      0.00        0.013        0.01

---


1996451
Outcrop      15.6    0.24     0.02      0.12      0.00        0.001        0.09

---


1905039
Outcrop       4.7    0.11     0.01      0.05      0.01        0.370        0.03

---
Table 4 - Condemnation Drill Holes with Anomalous Gold Values (Adanac
2008)

Drill Hole ID
From (m)
To (m)
Interval (m)
Au (ppm)
Ag (ppm)

---                                                                           
---


AD-390              22.9       99.1                76.2            
0.15               0.42

---


Including            53.3       74.7                21.3            
0.21               0.11

---




AD-393             184.4      257.6                73.2            
0.21               0.28

---
In other Company news, Stuhini wished to announce that despite
challenging weather, it has successfully completed its recently announced 2021
SkyTEM airborne geophysical survey on key remaining portions of its Ruby Creek
Project. Company consulting geophysicist Todd Ballantyne will be reviewing and
compiling results in the coming months, which will help Company geologists
define exploration targets for the upcoming 2021 exploration program. The
Company also wishes to announce that it has received a 5 year drill permit for
the Ruby Creek Project. Lastly, on April 22nd the Company hosted it's first
webinar with a series of live corporate presentations. A video recording of
the webinar has been posted on the home page of our website - we encourage
those of you who were not able to attend the presentations to view the
recording so as to better appreciate and understand the Company and its suite
of assets.
QA/QC Protocol: Rock material was collected in poly bags and then
transported to the Bureau Veritas sample preparation facility located in
Whitehorse, Yukon. Samples were crushed, and then pulps were sent to the
Bureau Veritas lab in Vancouver for assay. Four acid digestion and Ultratrace
ICP-MS analysis for 59 elements and fire assay for gold, platinum and
palladium were performed on all samples. Over-limit copper, lead, zinc and
silver samples were analyzed by multi-acid digestion and ICP-ES (MA370).
Conversion to WO3 % (equal sign) W % x 1.2616. All results have passed the QA/QC
screening by the lab.
Ruby Creek Project: The 27,354-hectare Ruby Creek Project is road
accessible and located 20 km east of Atlin, BC. There are 48 different
documented mineral occurrences on the Property, of which 16 are gold-related,
with 4 active gold placer creeks. The Property also hosts the historic Ruby
Creek Molybdenum resource, which has an intact BC Mines Act permit. Stuhini
has an option to acquire 100% of the Ruby Creek Project subject to a 1% Net
Smelter Royalty.
The geological content of this news release has been reviewed andapproved by 
Andrew Wilkins, P. Geo., a qualified person as defined under the
terms of National Instrument 43-101.
About Stuhini Exploration Ltd.
Stuhini is a mineral exploration company focused on the exploration and
development of precious and base metals properties in western Canada, with its
focus on the Ruby Creek Property located approximately 20 km east of Atlin, BC
and the Que Property located approximately 70 km north of Johnson's Crossing
in the Yukon.
Forward-Looking Statements
This news release contains "forward-looking statements" within the
meaning of Canadian securities legislation. Such forward-looking statements
concern the Company's strategic plans, timing and expectations for the
Company's exploration and drilling programs, estimates of mineralization from
sampling, and geological information projected from sampling results. Such
forward-looking statements or information are based on a number of
assumptions, which may prove to be incorrect. Assumptions have been made
regarding, among other things: conditions in general economic and financial
markets; accuracy of assay results; geological interpretations from sampling
results, timing and amount of capital expenditures; the affect of Covid-19 on
the Company's ability to conduct exploration; performance of available
laboratory and other related services; and future exploration costs. The
actual results could differ materially from those anticipated in these
forward-looking statements as a result of the risk factors including: the
timing and content of work programs; results of exploration activities and
development of mineral properties; the interpretation and uncertainties of
sampling results and other geological data; receipt, maintenance and security
of permits and mineral property titles; environmental and other regulatory
risks; project costs overruns or unanticipated costs and expenses;
availability of funds and general market and industry conditions.
Forward-looking statements are based on the expectations and opinions of the
Company's management on the date the statements are made. The assumptions used
in the preparation of such statements, although considered reasonable at the
time of preparation, may prove to be imprecise and, as such, readers are
cautioned not to place undue reliance on these forward-looking statements,
which speak only as of the date the statements were made. The Company
undertakes no obligation to update or revise any forward-looking statements
included in this news release if these beliefs, estimates and opinions or
other circumstances should change, except as otherwise required by applicable
law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Stuhini Exploration Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/May2021/04/c3622.html

-0-                           05/04/2021
/For further information: David O'Brien, President & Chief Executive
Officer, Stuhini Exploration Ltd., Email: dobrien(at)stuhini.com, Phone: (604)
418-4019, Web: www.stuhini.com/
(STU.)

CO:  Stuhini Exploration Ltd.
ST:  British Columbia
IN:  MNG
SU:

-30-