Source	CANADA NEWSWIRE
Date	04/29/2021
Time	07:17:15 AM

Company	 Nubian Resources Ltd.
Title	Nubian Announces Metallurgical Characterization Results for Yandoit Gold
Project, Victoria Australia





    CDNX Symbol: NBR











Press Release




" BC-Nubian-characterizati   04-29 1091
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.132595:
^Nubian Announces Metallurgical Characterization Results for Yandoit Gold
Project, Victoria Australia@

TORONTO, April 29, 2021 /CNW/ - Nubian Resources Ltd. (TSXV: NBR)
("Nubian" or the "Company") is pleased to release metallurgical
characterization results from rock chip samples gathered from mine dumps
associated with the historic Goldsmith mine at Yandoit, Central Victorian
Goldfields, Australia. The 38 square kilometre Yandoit Gold Project is
situated in the Daylesford gold corridor.
Six samples, consisting of sulphide-bearing quartz were sent to Gekko
Laboratories in Ballarat, Victoria for metallurgical characterization and gold
recovery determination. Visible gold was not present in any sample, and
consequently all rocks were regarded as waste and discarded during historic
production. The metallurgical work was undertaken to assist in the design of a
processing circuit to extract gold from Yandoit in a potential future mining
operation.
The samples are considered typical of sulphide-mineralized quartz, mined
but discarded as barren during historic mining at Yandoit. Similar samples are
found on surface dumps around the four sub-parallel gold reef systems
discovered to date (Sardinia, Graveyard, Golconda and Welcome Line) which are
the focus for the Company's upcoming maiden drill program. All samples
correlate with areas of anomalous arsenic in soil sampling. Mapping of the
Welcome, Graveyard and Sardinia reefs suggests they are lateral extensions or
splays off the Golconda and Goldsmith reefs that were the two dominant
historical gold mines.
The six samples were crushed and processed by gravity separation at Gekko
to produce heavy mineral concentrates. These concentrates were assayed for
gold, silver and arsenic (arsenic being a well-known pathfinder for gold).
High gold grades were identified in all concentrate samples, despite free
gold not being visible, indicating the likely presence of gold within
sulphide. Gold recovery from the six concentrate samples are as follows:
Sample                 Mass Yield

Gold Distribution                                   Other Elements

---

grams      %                           Gold

Cumulative              Cumulative Gold      Arsenic                Silver



Cumulative

Distribution

Distribution

---

%      ppm

%

%

ppm

ppm                       ppm

---

Con 1    27.8                  5.2        5.2                    
67.0                          11.9                         11.9         
67.0                  12,704   163

---

Con 2    26.7                  5.0       10.2                    
39.4                           6.7                         18.6         
53.5                  12,483    70

---

Con 3    18.5                  3.5       13.7                    
37.2                           4.4                         23.0         
49.4                  11,756    38

---

Con 4   123.3                 23.1       36.8                    
25.1                          19.7                         42.8         
34.1                   7,404    17

---

Con 5   120.1                 22.5       59.3                    
18.4                          14.1                         56.8         
28.1                   2,808    14

---

Con 6   217.4                 40.7      100.0                    
31.1                          43.2                        100.0         
29.4                   2,238    23

---

Calculated   5.3                100.0                              
29.4                         
100.0                                                           4,947    30
Feed

---
The weighted average grade from the six concentrate samples produced from
rock chips was 29.36 g/t and 30 g/t Ag. This preliminary testwork suggests a
substantial amount of gold may be present within sulphide, that was not
recoverable within historic mining operations. Gravity combined with flotation
may be very effective for the Yandoit Gold Project in the future to produce a
bulk concentrate for sale or further treatment. Detailed test work from drill
core samples along with bulk sampling is required to confirm these results,
determine the distribution of gold between free and sulphide-hosted, and
determine the quantity of sulphide in quartz veins.
"We are very pleased to see such high gold grades within sulphide
concentrates from Yandoit," commented Martin Walter, President and CEO, who
added, "This is invisible gold that was missed by early miners who only had
the technology to extract free gold from quartz veins. These results while
only performed on a modest scale are important as they show gold can be easily
liberated and that good recoveries can be achieved at the Yandoit Gold Project
through the use of simple conventional gold extraction processes. While more
work remains to be done these results provide an early indication on what the
project's metallurgical future flow sheet might look like."
QUALIFIED PERSON
The technical information contained in this news release relating to the
Yandoit Gold Project has been approved by Mark Saxon, an advisor to Nubian,
who is a "qualified person" within the meaning of National Instrument 43-101,
Standards of Disclosure for Mineral Projects. Mark Saxon is an Honours BSc
graduate in Geology from the University of Melbourne, a Fellow of the
Australasian Institute of Mining and Metallurgy, and a Member of the
Australian Institute of Geoscientists.
ABOUT NUBIAN
Nubian Resources Ltd. is a publicly traded precious and base metals
exploration company listed on the TSX Venture Exchange. The Company is managed
by a team of experienced mining and geological professionals. Nubian's
projects are focused in key mining jurisdictions in central Victoria and
Tasmania, Australia and Peru.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Caution Regarding Forward Looking Statements
Certain statements contained in this press release constitute
forward-looking information. These statements relate to future events or
future performance. The use of any of the words "could", "intend", "expect",
"believe", "will", "projected", "estimated" and similar expressions and
statements relating to matters that are not historical facts are intended to
identify forward-looking information and are based on Nubian's current belief
or assumptions as to the outcome and timing of such future events. Actual
future results may differ materially. Although such statements are based on
reasonable assumptions of Nubian's management, there can be no assurance that
any conclusions or forecasts will prove to be accurate.
Forward looking information involves known and unknown risks,
uncertainties and other factors which may cause the actual results,
performance or achievements to be materially different from any future
results, performance or achievements expressed or implied by the
forward-looking information. Such factors include risks inherent in the
exploration and development of mineral deposits, including risks relating to
changes in parameters of the Projects as plans continue to be redefined, risks
relating to variations in grade or recovery rates, risks relating to changes
in mineral prices and the worldwide demand for and supply of minerals, risks
related to the COVID-19 pandemic and current global financial conditions,
increased competition, access and supply risks, reliance on key personnel,
operational risks, regulatory risks, including risks relating to licenses and
permits, financing, capitalization and liquidity risks and title and
environmental risks.
The forward-looking information contained in this release is made as of
the date hereof, and Nubian is not obligated to update or revise any
forward-looking information, whether as a result of new information, future
events or otherwise, except as required by applicable securities laws.
Because of the risks, uncertainties and assumptions contained herein,
investors should not place undue reliance on forward-looking information. The
foregoing statements expressly qualify any forward-looking information
contained herein.
SOURCE Nubian Resources Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/April2021/29/c2666.html

-0-                           04/29/2021
/For further information: For further information, please contact Martin
Walter, Chief Executive Officer, Nubian Resources Ltd., at +1-416-389-5692 or
martin(at)nubianr.com/
/Web Site: www.nubianr.com /
(NBR.)

CO:  Nubian Resources Ltd.
ST:  British Columbia
IN:  MNG
SU:

-30-