Source	MARKET NEWS
Date	09/07/2011
Time	07:43:11 AM

Company	 Rhyolite Resources Ltd.
Title	Drills 
14.2 G/t Gold Over 2.8 Meters At Low: Sig





    CDNX Symbol: RYE











Press Release	





RHYOLITE RESOURCES LTD ("RYE-V")
- Drills 14.2 G/t Gold Over 2.8 Meters At Low: Significantly
- Increases Land Package At Paxson

Rhyolite Resources Ltd. ("Rhyolite" or the "Company") reports that the
initial drill hole into the Low target on its wholly-owned Paxson gold
project in the Tintina Gold Belt, eastern Alaska has returned significant
gold values.

//st
Drill Hole From (m) To (m) Interval (m)                Weighted Grade
(g/t Gold)

WG11-05     9.5   21.9          2.4                                3.2
And        26.9   54.3         27.4                                1.9
Includes   38.7   52.3         13.6                                3.4
Includes   40.2   43.0          2.8                               14.2
//et

Hole WG11-05 was drilled to the south, angled at -45 degrees and tested
the Low target located approximately 3.2 km east southeast of the Shalosky
zone where the results from the first two diamond drill holes of the 2011
program returned (Press Release August 18, 2011):

//st
Drill Hole From (m) To (m) Interval (m)                Weighted Grade
(g/t Gold)

WG11-01    56.1   77.1         21.0                                1.9
Includes   56.1   59.1          3.0                                7.2
Includes   70.1   71.8          1.7                                6.3
And        97.5   99.0          1.5                                2.7
//et

//st
Drill Hole From (m) To (m) Interval (m)                 Weighted Grade
(g/t Gold)

WG11-02    88.3  111.4         23.1                                3.5
Includes   90.4  103.6         13.2                                5.4
//et

The lengths indicated are drilled intervals and do not necessarily
represent true widths of mineralized sections. Additional drilling is
warranted to assess the geometry of the intercepted structures. The results
from holes WG11-03 and WG11-04 drilled at the Shalosky zone are still
awaited due to pending assays from infill sampling required on the holes.

Based on the initial results of the 2011 diamond drill program,
Rhyolite has staked an additional 106 contiguous mineral claims at its
wholly-owned Paxson gold property.

The Paxson property now comprises 135 mineral claims for a total of
8,670 hectares (86.7 square kilometers). The objective of the property
addition is to cover the projections of multi-kilometer scale structures
that appear to control the gold mineralization on the Paxson property. Of
particular interest to the property expansion is the northeast and
southwest extensions of the Shalosky zone.

To date, the Shalosky zone is defined by a 1,100-metre-by-50- to
500-metre greater-than-100-part-per-billion gold-in-soil geochemical
anomaly. However, compilation work and prospecting in 2011 indicates that
the controlling Shalosky structure may extend for a much greater strike
distance. Prospecting along the southwestern projection of the Shalosky
structure by Rhyolite in 2011 has intermittently identified siliceous
breccia in float and sub-parallel structures for over 1.6 km west of hole
WG11-01. Assay results from the surface sampling program are pending.

Rhyolite also reports that the 2011 Paxson reconnaissance diamond
drill program has now been successfully completed. A total of eight diamond
drill holes comprising 1,388 meters have tested the Shalosky zone over a
600 meter strike length and down to depths of approximately 160 meters
below surface, four diamond drill holes comprising 536 meters have been
completed 3.2-km east southeast at the Low zone where surface sampling in
2010 returned 13.37 grams gold per tonne over 3 meters (Press Release
November 10, 2010), and two holes comprising 323 meters were collared
approximately 2.8-km west of the Low zone at the Hunter showing where
surface sampling returned grab samples of up to 50.8 grams gold per tonne
(Press Release November 10, 2010). All diamond drill holes completed to
date have encountered sulphide bearing structures. Results from remaining
11 diamond drill holes will be released once received and compiled.

Details and results from the 2011 program are being compiled into a
brand new corporate website that is currently nearing completion. Rhyolite
expects that the new website will be launched by the end of September and
will serve as a hub for investors to keep up to date with the company, its
developments and to review the exploration data in more detail.

Quality control/Quality assurance

The 2011, mineralized intervals in the BTW-size drill core were sawn
longitudinally and half the drill core was sampled in intervals not
exceeding 3.0 meters. All samples are transported in security-sealed bags
to the lab for analyses. All samples collected in 2011 were sent for gold
fire assay and 48-element ICP analysis to ALS Chemex Labs. Samples were
prepared in ALS Chemex's Fairbanks prep facility and then sent to Reno
Nevada for analysis. Gold fire assays were on 50 gram pulp splits with an
AA finish. One in every ten samples contains a control (blank or gold
standard).

Qualified Persons

The foregoing disclosure has been reviewed, compiled and is the
responsibility of Richard A. Graham, P. Geol., President of Rhyolite and a
"qualified person" for the purpose of NI 43-101.

//st
ON BEHALF OF THE BOARD OF DIRECTORS OF
RHYOLITE RESOURCES LTD.

Richard Graham, President and CEO
//et

Forward-Looking Statement

Some statements in this report contain forward-looking information.
These statements include, but are not limited to, statements with respect
to future exploration, expenditures, transactions and financings. These
statements address future events and conditions and, as such, involve known
and unknown risks, uncertainties and other factors which may cause the
actual results, performance or achievements of to be materially different
from any future results, performance or achievements expressed or implied
by the statements. Such factors include, among others, risks related to
actual results of exploration activities, the timing and amount of
expenditures and the completion of transactions and financings.

Neither the TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for RYE-V
Date: 2011/08/29
Closing Price: 0.45

TEL:  604-488-8717   Richard Graham, P.Geol.,
Rhyolite Resources Ltd.
____________________________________________________________
(c)2011 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1124900025TS11124901682-07421920110907