Source	MARKET NEWS
Date	09/03/2014
Time	06:06:12 AM

Company	 Colombian Mines Corporation
Title	Drills 
More High Grade Mineralization At El Dovi





    CDNX Symbol: CMJ











Press Release	





COLOMBIAN MINES CORP ("CMJ-V;CMBPF-0")
- Drills More High Grade Mineralization At El Dovio

Colombian Mines Corporation ("Colombian Mines" or the "Company") is
pleased to announce significant high grade zones within larger
mineralized intervals in recently completed core holes 1360-02 and
1360-03. Hole 1360-02 intersected six meters (19.7 feet) grading 7.9
grams gold per metric tonne or 8.3 grams per tonne gold equivalent (g/T
AuEq)within 27.5 meters (90.2 feet) averaging 2.3 g/T Au (2.5 g/T
AuEq), drill hole 1360-03 intersected 5 meters (16.4 feet) of
mineralization averaging 6.8 g/T Au or 7.1 g/T AuEqwithin 20.5 meters
(67.2 feet) averaging 1.5 g/T Au or 1.7 g/T AuEq. Table 1 below,
summarizes salient mineral intercepts in holes 1360-02 and 03.

//st
Table 1.Summary Drill Intercepts

Hole      From    To  Length   Au    Ag             Combined
(m)   (m)     (m)  g/T   g/T  Cu %  Zn %     AuEq
1360-02    0.0  27.5    27.5  2.3   6.2   0.2   0.9      2.5
Including  1.5  11.8    10.3  5.2  12.3   0.5   2.2      5.4
Including  4.3  10.3     6.0  7.9  18.2   0.8   3.7      8.3
1360-03    0.0  20.5    20.5  1.5  12.6   0.1   0.6      1.7
Including  4.4   9.4     5.0  6.8  13.1   0.5   4.1      7.1
//et

//st
* Note: Gold Equivalent values were calculated using the following metal
prices, Gold $41.47 / gram ($1,290/oz), Silver $0.63 / gram ($19.63 / oz),
Copper $3.16 / pound & Zinc $1.06 / pound.
//et

Discussion and Results

Holes 1360-02 and 1360-03 were drilled from the intersection of
the Sabana Blanca Adit and the first cross cut south (XC-1S) at an
Azimuth of 173 and Inclinations of -70 and -50 below horizontal
respectively. Both intersected disseminated, semi-massive and massive
sulfide mineralization comprised of chalcopyrite, sphalerite, pyrite
and pyrrhotite as disseminated to massive sulfide zones in a gangue of
multi-phased crystalline quartz. Mineralization is hosted in
metamorphosed and brecciated mafic volcanic rocks in and near the
contact zone of the large diabase dike and shows ample evidence of
mulitple episodic and repetitive mineralizing events. Core from hole
1360-03 shows striking evidence of multiple phases of brecciation and
mineralization. Such multi-phased mineralization and brecciation is
often considered a key aspect in developing sufficient mineral
endowment to form substantial high grade systems. Photographs of this
mineralization can be viewed on the Company's website by clicking here.


Drilling from the 1360 meter level of the Sabana Blanca Adit
provides access to drill test high grade targets the Company has not
been able to adequately test from the surface. Drill results to date
corroborate the Company's high grade saw cut channel samples in the
Sabana Blanca Adit.

Notes and Comments

Holes reported here test of a portion of the mineralized zone but
do not cross the entire zone due to limitations of underground access.
All drill intercepts reported are drilled intercept length.
Insufficient drilling has been completed in this area to reasonably
determine the geometry and estimate true width.

Gold equivalency calculations are included to more clearly present
the approximate value of the high grade polymetallic mineralization at
El Dovio. Gold equivalent values, (g/T AuEq) were calculated using the
following metal prices, Gold: $1290 per troy ounce ($41.47 / gram),
Silver: $19.63 per troy ounce ($0.63 / gram), Copper: $3.16 / pound and
Zinc: $1.06 / pound. One troy ounce contains approximately 31.104 grams
and one percent equals approximately 22 pounds per metric tonne.

About El Dovio: The Company's 100% owned El Dovio project covers
gold rich, high grade poly metallic mineralization where the Company
owns 100% of both the surface and mineral rights covering the entire
zone of mineralization and surrounding areas. Work to date indicates
the Sabana Blanca zone is a feeder or "stringer zone" that may have a
strike length in excess of of one (1) kilometer that lies beneath a
horizon highly prospective for the development of Volcanogenic Massive
Sulfide (VMS) type deposits in the Brazo 1 zone. Metallurgical studies
on bulk samples from the Sabana Blanca zone show the mineralization is
highly amenable to conventional froth flotation yielding more than 96%
recovery of the gold, coper and zinc values and more than 91% of the
contained silver values.

Sample Collection - Quality Control - Quality Assurance

The Company's samples are collected in accordance with accepted
industry best practices. Core is transported from the site to the
Company's core facility in Medellin, Colombia by Company personnel.
After being logged, photographed, diamond saw cut and sampled, samples
are delivered the SGS's Medellin laboratory for preparation and
analyses, (ISO9001:2000). Gold is analyzed by fire assay with an
ICP/AES finish. Silver and base metal analyses were determined with
ICP/AES techniques. The Company maintains and continuously monitors its
rigid QC-QA through insertion of a series of blank, duplicate,
certified standard samples at a rate of 1:30 or higher into the sample
stream.

Mr. Robert G. Carrington, P.Geo., a Qualified Person as defined by
National Instrument 43-101 and President of the Company, has reviewed
and verified the technical information in this news release.

About Colombian Mines Corporation:Colombian Mines Corporation is
an aggressive explorer with a "first mover" advantage in Colombia.
Focused on developing shareholder value through exploration and
development of key projects, the Company is also one of Colombia's
leading "prospect generators". Further information can be found on our
website at www.colombianmines.com.

Robert G. Carrington, President & CEO

Website: www.colombianmines.com

Neither the TSX Venture Exchange nor the Investment Industry
Regulatory Organization of Canada accepts responsibility for the
adequacy or accuracy of this release.

Forward-Looking Statement:

Some of the statements in this news release contain
forward-looking information that involves inherent risk and uncertainty
affecting the business of Colombian Mines Corporation. Actual results
may differ materially from those currently anticipated in such
statements.

TSX Venture closing price for CMJ-V
Date: 2014/08/27
Closing Price: 0.18

TEL: (604) 649-9195         Sharon Hebgin
shebgin@colombianmines.com  Corporate Communications
www.colombianmines.com      Colombian Mines Corporation
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1424500021TS11424500957-06040220140903