Source	MARKET NEWS
Date	09/03/2014
Time	05:55:36 AM

Company	 Barisan Gold Corporation
Title	Receives Final 
Assays For Holes UTD-007 & UTD-00





    CDNX Symbol: BG











Press Release	





BARISAN GOLD CORP ("BG,BG.S-V;BRSGF-0")
- Receives Final Assays For Holes UTD-007 & UTD-008 And Provides
- Exploration Update For Its Upper Tengkereng Prospect

Barisan Gold Corporation is pleased to provide investors with an
update on exploration activities at its Upper Tengkereng gold-copper
porphyry discovery, located in the Province of Aceh, Indonesia.

Assay Results

Final assay results have been received for holes UTD-007 and
UTD-008. UTD-007 was a vertical hole drilled in the eastern part of the
deposit to test the vertical extensions of the high-grade zone
discovered in that area in holes UTD-002/003/005 whereas UTD-008 was
drilled in the southern portion of the deposit to test the newly
discovered near surface high-grade zone located in that area.

Hole UTD-008 is the best hole drilled so far at Upper Tengkereng,
returning the highest grades intercepted over the entire length of a
hole as well as the longest intercept above 1% copper equivalent of any
hole drilled so far at Upper Tengkereng. As a whole, UTD-008 returned
890 metres of 0.5 g/t gold + 0.5% copper (0.8% copper equivalent at
current market prices) 4 metres from surface to the bottom of the hole
at 894 metres, including 506 meters of 0.7 g/t gold + 0.6% copper (1.1%
copper equivalent at current market prices) from 188 metres to 694
metres.

//st
From       To   Intercept      Gold    Copper  Gold Eq.    Copper
(m)      (m)         (m)     (g/t)       (%)     (g/t)    Eq. (%)
----------------------------------------------------------------------------
4      894         890      0.51      0.47       1.3        0.8
----------------------------------------------------------------------------
Incl.        4      750         746      0.57      0.53       1.5        0.9
----------------------------------------------------------------------------
Incl.      188      694         506      0.71      0.62       1.8        1.1
----------------------------------------------------------------------------
Incl.      188      464         276      0.68      0.74       1.9        1.2
----------------------------------------------------------------------------
Incl.      226      464         238      0.72      0.78       2.0        1.2
----------------------------------------------------------------------------
Incl.      296      464         168      0.85      0.85       2.3        1.4
----------------------------------------------------------------------------
And        464      694         230      0.75      0.49       1.6        1.0
----------------------------------------------------------------------------
Incl.      568      640          72      0.90      0.56       1.9        1.1
----------------------------------------------------------------------------
Copper Eq. & Gold Eq. calculated using current market prices.
No adjustments have been made for metallurgical recovery as these remain
uncertain at this time.
//et



Geological understanding of the near surface high-grade zone is
advancing following receipt of the drill results and assays from holes
UTD-002/006/008. Based on results so far, the zone seems to be
approximately 700-800 metres depth starting from surface and contains
three distinct types of mineralization stacked one on top of the other.
From surface to approximately 100 metres depth, there is the presence
of a top layer of advanced argillic altered hydro breccia
mineralization where grades average approximately 0.4-0.6% copper
equivalent; from 100 to 400 metres depth, there is the presence of
high-grade covellite rich silica-pyrophyllite-alunite mineralization
where grades average 1.0-1.2% copper equivalent; and from 400 to 800
metres depth, there is the presence of high-grade
chalcocite-chalcopyrite mineralization where grades average 0.7-1.0%
copper equivalent (see update presentation on the Barisan Gold website
at www.barisangold.com for cross-section map interpretations).

Similarly, hole UTD-007 was the second best hole drilled so far at
Upper Tengkereng, after hole UTD-008. UTD-007 returned 824 metres of
0.7 g/t gold + 0.3% copper (0.7% copper equivalent at current market
prices) 292 metres from surface to the bottom of the hole at 1,116
metres (UTD-007 was drilled from outside the porphyry back towards it,
hence why the first 292 metres were not meaningful), including 386
meters of 0.8 g/t gold + 0.5% copper (1.0% copper equivalent at current
market prices) from 510 metres to 896 metres.

//st
From       To   Intercept      Gold    Copper  Gold Eq.    Copper
(m)      (m)         (m)     (g/t)       (%)     (g/t)    Eq. (%)
----------------------------------------------------------------------------
292    1,116         824      0.65      0.34       1.2        0.7
----------------------------------------------------------------------------
Incl.      510    1,068         558      0.77      0.39       1.4        0.9
----------------------------------------------------------------------------
Incl.      510      896         386      0.82      0.45       1.6        1.0
----------------------------------------------------------------------------
Incl.      510      598          88      0.93      0.53       1.8        1.1
----------------------------------------------------------------------------
And        644      788         144      0.94      0.48       1.7        1.1
----------------------------------------------------------------------------
Copper Eq. & Gold Eq. calculated using current market prices.
No adjustments have been made for metallurgical recovery as these remain
uncertain at this time.
//et

Ongoing Drilling

Drilling continued throughout the summer at Upper Tengkereng, save
for the Idul Fitri holiday period in late July/early August. Holes
UTD-009 and UTD-011 have since been completed and hole UTD-012 has
recently started. Unfortunately hole UTD-010 was abandoned.

UTD-009 was drilled from a new platform located at the
south-central edge of the porphyry discover and was drilled in a
southeast-northwest direction (302 degree azimuth) with a shallow dip
of 50 degrees. UTD-009 was the first hole drilled on a north-south axis
into the near-surface high-grade zone previously discovered in holes
UTD-002/006/008. Objectives of hole UTD-009 were to extend the
footprint of the high-grade zone along the north-south axis. Assays are
pending.

UTD-011 was drilled in the opposite direction of UTD-009 (120
degree azimuth) also with a shallow dip of 50 degrees to test the same
north-south axis of the near-surface high-grade zone but drilling
towards the south. With the rig sitting in the southern edge of the
deposit, hole UTD-011 was a short hole to identify the boundaries of
the zone. Assays are pending.
UTD-012 began last week and is in the same direction as UTD-011
but with a steeper dip of 85 degrees allowing for a more vertical
definition of the high-grade zone in the southern edge of the deposit.
As of September 1, 2014, UTD-012 had reached 244 metres in length.

Exploration Program for Next 12 Months

Barisan Gold has refocused all its efforts on the near surface
high-grade zone located in the south-central part of the deposit. All
resources (drilling, geology, human and financial) are being directed
towards that area with a 12-month objective of producing a maiden
mineral resource estimate in accordance with NI 43-101.

Initially, the focus will be on delineating the boundaries of the
zone. Approximately 10 holes of various lengths and dips have been
planned to delineate the east-west-north-south boundaries of the
near-surface high-grade zone. At this stage, the zone remains open in
all directions, except towards the southeast corner where hole UTD-011
reached the boundary of the porphyry deposit.

After having delineated the boundaries of the zone, resource
drilling will commence, where at least 8-10 holes will be required (in
addition to holes already drilled or being planned) depending on the
final footprint of the zone.

Barisan Gold retained the independent laboratory services of PT
Intertek Utama Services of Jakarta, Indonesia, which, in the case of
UTD-007/008, employed the fire assay method (FA50) on gold samples and
for other precious and base metal analyses, ICP with multi acid
digestion.

Dibiansyah Hamid, MAIG, the designated QP within the meaning of NI
43-101, has reviewed and approved the content of this release.

Neither TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

To receive or stop receiving BG news via email, please email
info@barisangold.com and state your preference in the subject line.

FOR FURTHER INFORMATION, visit the Company's website at
www.barisangold.com.

About Barisan Gold Corporation

Barisan Gold (TSX VENTURE:BG) is a Canadian-based minerals
exploration company listed on the TSX Venture Exchange under the symbol
"BG". The Company is engaged in the exploration, acquisition and
development of mineral properties in Indonesia. Barisan Gold currently
owns and operates two gold and gold-copper properties in Indonesia's
Aceh Province on the northern tip of Sumatra Island, namely the Barisan
gold-copper porphyry belt and the Abong epithermal gold project.
Barisan Gold currently has 40,721,186 shares outstanding.

Caution Regarding Forward Looking Statements

Certain statements in this News Release, which are not historical
in nature, constitute "forward looking statements" within the meaning
of that phrase under applicable Canadian securities law. These
statements include, but are not limited to, statements or information
concerning future work programs at the Company's Upper Tengkereng
Porphyry prospect, results and timing of any work programs, the
Company's performance or events as of the date hereof. These statements
reflect management's current assumptions and expectations and by their
nature are subject to certain underlying assumptions, known and unknown
risks and uncertainties and other factors which may cause actual
results, performance or events to be materially different from those
expressed or implied by such forward looking statements. Those risks
include the interpretation of drill results; the geology, grade and
continuity of mineral deposits; the possibility that future
exploration, development or mining results will not be consistent with
our expectations; commodity and currency price fluctuation; failure to
obtain adequate financing; regulatory, recovery rates, refinery costs,
and other relevant conversion factors, permitting and licensing risks;
and general market and mining exploration risks. Forward-looking
statements should not be construed as investment advice. Readers should
perform a detailed, independent investigation and analysis of the
Company and are encouraged to seek independent professional advice
before making any investment decision. Accordingly, readers should not
place undue reliance on any forward looking statement. Except as
required by applicable securities laws, the Company disclaims any
obligation to update or revise any forward looking statements to
reflect events or changes in circumstances that occur after the date
hereof.

TSX Venture closing price for BG-V
Date: 2014/09/02
Closing Price: 0.17

TEL:  +1 604 684 8676  Barisan Gold Corporation
Steven Feldman, Manager Investor Relations
info@barisangold.com
www.barisangold.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1424500016TS11424500863-05525520140903