Source	Marketwire
Date	09/03/2014
Time	05:00:32 AM

Company	 BARISAN GOLD CORPORATION
Title	Barisan Gold Receives Final Assays for Holes UTD-007 & UTD-008 and 
Provides Exploration Update for Its Upper Tengkereng Prospect





    CDNX Symbol: BG











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Barisan Gold Corporation

TSX VENTURE SYMBOL: BG

September 3, 2014

Barisan Gold Receives Final Assays for Holes UTD-007 & UTD-008 and Provides 
Exploration Update for Its Upper Tengkereng Prospect

UTD-008 INTERSECTS 506 METRES OF 0.7G/T GOLD + 0.6% COPPER (1.1% COPPER 
EQUIVALENT)

UTD-007 INTERSECTS 386 METRES OF 0.8G/T GOLD + 0.5% COPPER (1.0% COPPER 
EQUIVALENT)

DRILLING CONTINUES, FOCUSED ON THE RECENTLY DISCOVERED NEAR SURFACE HIGH-GRADE 
ZONE WITH THE GOAL OF PRODUCING A MAIDEN RESOURCE ESTIMATE

VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 3, 2014) - Barisan Gold 
Corporation (TSX VENTURE:BG) is pleased to provide investors with an update on 
exploration activities at its Upper Tengkereng gold-copper porphyry discovery, 
located in the Province of Aceh, Indonesia.

Assay Results

Final assay results have been received for holes UTD-007 and UTD-008. UTD-007 
was a vertical hole drilled in the eastern part of the deposit to test the 
vertical extensions of the high-grade zone discovered in that area in holes 
UTD-002/003/005 whereas UTD-008 was drilled in the southern portion of the 
deposit to test the newly discovered near surface high-grade zone located in 
that area.

Hole UTD-008 is the best hole drilled so far at Upper Tengkereng, returning the 
highest grades intercepted over the entire length of a hole as well as the 
longest intercept above 1% copper equivalent of any hole drilled so far at 
Upper Tengkereng. As a whole, UTD-008 returned 890 metres of 0.5 g/t gold + 
0.5% copper (0.8% copper equivalent at current market prices) 4 metres from 
surface to the bottom of the hole at 894 metres, including 506 meters of 0.7 
g/t gold + 0.6% copper (1.1% copper equivalent at current market prices) from 
188 metres to 694 metres.

/T/

----------------------------------------------------------------------------
From       To   Intercept      Gold    Copper  Gold Eq.     Copper
(m)      (m)         (m)     (g/t)       (%)     (g/t)    Eq. (%)
----------------------------------------------------------------------------
4      894         890      0.51      0.47       1.3        0.8
----------------------------------------------------------------------------
Incl.        4      750         746      0.57      0.53       1.5        0.9
----------------------------------------------------------------------------
Incl.      188      694         506      0.71      0.62       1.8        1.1
----------------------------------------------------------------------------
Incl.      188      464         276      0.68      0.74       1.9        1.2
----------------------------------------------------------------------------
Incl.      226      464         238      0.72      0.78       2.0        1.2
----------------------------------------------------------------------------
Incl.      296      464         168      0.85      0.85       2.3        1.4
----------------------------------------------------------------------------
And        464      694         230      0.75      0.49       1.6        1.0
----------------------------------------------------------------------------
Incl.      568      640          72      0.90      0.56       1.9        1.1
----------------------------------------------------------------------------
Copper Eq. & Gold Eq. calculated using current market prices.
No adjustments have been made for metallurgical recovery as these remain
uncertain at this time.

/T/

Geological understanding of the near surface high-grade zone is advancing 
following receipt of the drill results and assays from holes UTD-002/006/008. 
Based on results so far, the zone seems to be approximately 700-800 metres 
depth starting from surface and contains three distinct types of mineralization 
stacked one on top of the other. From surface to approximately 100 metres 
depth, there is the presence of a top layer of advanced argillic altered hydro 
breccia mineralization where grades average approximately 0.4-0.6% copper 
equivalent; from 100 to 400 metres depth, there is the presence of high-grade 
covellite rich silica-pyrophyllite-alunite mineralization where grades average 
1.0-1.2% copper equivalent; and from 400 to 800 metres depth, there is the 
presence of high-grade chalcocite-chalcopyrite mineralization where grades 
average 0.7-1.0% copper equivalent (see update presentation on the Barisan Gold 
website at www.barisangold.com for cross-section map interpretations).

Similarly, hole UTD-007 was the second best hole drilled so far at Upper 
Tengkereng, after hole UTD-008. UTD-007 returned 824 metres of 0.7 g/t gold + 
0.3% copper (0.7% copper equivalent at current market prices) 292 metres from 
surface to the bottom of the hole at 1,116 metres (UTD-007 was drilled from 
outside the porphyry back towards it, hence why the first 292 metres were not 
meaningful), including 386 meters of 0.8 g/t gold + 0.5% copper (1.0% copper 
equivalent at current market prices) from 510 metres to 896 metres.

/T/

----------------------------------------------------------------------------
From       To   Intercept      Gold    Copper  Gold Eq.     Copper
(m)      (m)         (m)     (g/t)       (%)     (g/t)    Eq. (%)
----------------------------------------------------------------------------
292    1,116         824      0.65      0.34       1.2        0.7
----------------------------------------------------------------------------
Incl.      510    1,068         558      0.77      0.39       1.4        0.9
----------------------------------------------------------------------------
Incl.      510      896         386      0.82      0.45       1.6        1.0
----------------------------------------------------------------------------
Incl.      510      598          88      0.93      0.53       1.8        1.1
----------------------------------------------------------------------------
And        644      788         144      0.94      0.48       1.7        1.1
----------------------------------------------------------------------------
Copper Eq. & Gold Eq. calculated using current market prices.
No adjustments have been made for metallurgical recovery as these remain
uncertain at this time.

/T/

Ongoing Drilling

Drilling continued throughout the summer at Upper Tengkereng, save for the Idul 
Fitri holiday period in late July/early August. Holes UTD-009 and UTD-011 have 
since been completed and hole UTD-012 has recently started. Unfortunately hole 
UTD-010 was abandoned.

UTD-009 was drilled from a new platform located at the south-central edge of 
the porphyry discover and was drilled in a southeast-northwest direction (302 
degree azimuth) with a shallow dip of 50 degrees. UTD-009 was the first hole 
drilled on a north-south axis into the near-surface high-grade zone previously 
discovered in holes UTD-002/006/008. Objectives of hole UTD-009 were to extend 
the footprint of the high-grade zone along the north-south axis. Assays are 
pending.

UTD-011 was drilled in the opposite direction of UTD-009 (120 degree azimuth) 
also with a shallow dip of 50 degrees to test the same north-south axis of the 
near-surface high-grade zone but drilling towards the south. With the rig 
sitting in the southern edge of the deposit, hole UTD-011 was a short hole to 
identify the boundaries of the zone. Assays are pending.

UTD-012 began last week and is in the same direction as UTD-011 but with a 
steeper dip of 85 degrees allowing for a more vertical definition of the 
high-grade zone in the southern edge of the deposit. As of September 1, 2014, 
UTD-012 had reached 244 metres in length.

Exploration Program for Next 12 Months

Barisan Gold has refocused all its efforts on the near surface high-grade zone 
located in the south-central part of the deposit. All resources (drilling, 
geology, human and financial) are being directed towards that area with a 
12-month objective of producing a maiden mineral resource estimate in 
accordance with NI 43-101.

Initially, the focus will be on delineating the boundaries of the zone. 
Approximately 10 holes of various lengths and dips have been planned to 
delineate the east-west-north-south boundaries of the near-surface high-grade 
zone. At this stage, the zone remains open in all directions, except towards 
the southeast corner where hole UTD-011 reached the boundary of the porphyry 
deposit.

After having delineated the boundaries of the zone, resource drilling will 
commence, where at least 8-10 holes will be required (in addition to holes 
already drilled or being planned) depending on the final footprint of the zone.

Barisan Gold retained the independent laboratory services of PT Intertek Utama 
Services of Jakarta, Indonesia, which, in the case of UTD-007/008, employed the 
fire assay method (FA50) on gold samples and for other precious and base metal 
analyses, ICP with multi acid digestion.

Dibiansyah Hamid, MAIG, the designated QP within the meaning of NI 43-101, has 
reviewed and approved the content of this release.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

To receive or stop receiving BG news via email, please email 
info@barisangold.com and state your preference in the subject line.

FOR FURTHER INFORMATION, visit the Company's website at www.barisangold.com.

About Barisan Gold Corporation

Barisan Gold (TSX VENTURE:BG) is a Canadian-based minerals exploration company 
listed on the TSX Venture Exchange under the symbol "BG". The Company is 
engaged in the exploration, acquisition and development of mineral properties 
in Indonesia. Barisan Gold currently owns and operates two gold and gold-copper 
properties in Indonesia's Aceh Province on the northern tip of Sumatra Island, 
namely the Barisan gold-copper porphyry belt and the Abong epithermal gold 
project. Barisan Gold currently has 40,721,186 shares outstanding.

Caution Regarding Forward Looking Statements

Certain statements in this News Release, which are not historical in nature, 
constitute "forward looking statements" within the meaning of that phrase under 
applicable Canadian securities law. These statements include, but are not 
limited to, statements or information concerning future work programs at the 
Company's Upper Tengkereng Porphyry prospect, results and timing of any work 
programs, the Company's performance or events as of the date hereof. These 
statements reflect management's current assumptions and expectations and by 
their nature are subject to certain underlying assumptions, known and unknown 
risks and uncertainties and other factors which may cause actual results, 
performance or events to be materially different from those expressed or 
implied by such forward looking statements. Those risks include the 
interpretation of drill results; the geology, grade and continuity of mineral 
deposits; the possibility that future exploration, development or mining 
results will not be consistent with our expectations; commodity and currency 
price fluctuation; failure to obtain adequate financing; regulatory, recovery 
rates, refinery costs, and other relevant conversion factors, permitting and 
licensing risks; and general market and mining exploration risks. 
Forward-looking statements should not be construed as investment advice. 
Readers should perform a detailed, independent investigation and analysis of 
the Company and are encouraged to seek independent professional advice before 
making any investment decision. Accordingly, readers should not place undue 
reliance on any forward looking statement. Except as required by applicable 
securities laws, the Company disclaims any obligation to update or revise any 
forward looking statements to reflect events or changes in circumstances that 
occur after the date hereof.

- 30 -

CONTACT INFO:

Barisan Gold Corporation
Steven Feldman
Manager Investor Relations
+1 604 684 8676
info@barisangold.com
www.barisangold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=496915431