Source	CANADA NEWSWIRE
Date	09/03/2014
Time	06:03:11 AM

Company	 Mirasol Resources Ltd.
Title	Mirasol provides exploration update on Rubi copper- gold porphyry JV
with First Quantum Minerals in Northern Chile





    CDNX Symbol: MRZ











Press Release	




" BC-Mirasol-Exploration   09-03 1135
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Mirasol provides exploration update on Rubi copper- gold porphyry JV
with First Quantum Minerals in Northern Chile@

VANCOUVER, Sept. 3, 2014 /CNW/ - Mirasol Resources Ltd. (TSX-V: MRZ,
Frankfurt: M8R)
<<

--  3D modelling of helicopter air magnetics survey with leading-edge
technology
--  Completed extensive property-wide soil geochemical program
--  Detailed gravity survey being used to model depth of post-mineral gravel
cover
--  Alteration vectoring studies undertaken
--  Completed systematic mapping and sampling of areas of outcrop
--  Integrated targeting and modelling underway
>>
<<

--  8 preliminary targets identified both in outcrop and gravel-covered
areas
--  Electrical geophysical test-lines in progress over key targets
--  Drill permitting process initiated
>>
Mirasol is pleased to provide an exploration update on its Rubi porphyry
copper - gold JV with First Quantum Minerals (First Quantum) in the El
Salvador - Potrerillos copper mining districts of northern Chile. First
Quantum has been conducting an aggressive surface exploration program under
the terms of a binding Letter Agreement, spending approximately US$680,000 in
the September 2013 to June 2014 period. With the signing of the Definitive
Option and Joint Venture Agreement on August 14, 2014 (see news release August
27, 2014), First Quantum can now begin preparations to scout drill-test
priority targets at Rubi. An archeological and environmental management plan,
and drill proposal, was submitted to the Chilean authorities in late July
2014. This may take up to 10 weeks to process.
Some of the exploration completed and results from the Rubi project to
date include:
<<

--  Processing of 2,460 line-km of a detailed helicopter magnetics survey of
the project with leading-edge 3D modelling software to highlight
structure and potential exploration target areas.

--  An extensive property-wide soil survey using both conventional soil
samples in areas of locally derived soils and enzyme partial leach(x)
technique in the gravel-covered areas. The partial leach technique was
applied in the gravel areas, as under some circumstances this approach
can detect mineralization through transported overburden. Soil buffer
capacity(x)(x) (acidity) was also measured as an additional technique to
potentially detect buried areas of oxidizing sulphide mineralization.

--  A gravity survey covering much of the property was completed and
combined with field observations to model the depth of gravel cover over
the majority of the property. These results suggest that much of the
project is covered by zero to less than 100 metres of gravel. This is
considered relatively thin cover for modern Chilean porphyry
exploration. The gravity model will be used to help prioritize targets
in the shallower cover areas for drill testing.
>>
<<

--  Outcropping areas of alteration were surveyed with grid-based hand-held
infrared spectrometer(x)(x)(x) measurements. This information is used to
identify alteration mineral species and changes in chemical composition
and degree of crystallinity of these minerals. A combination of these
factors can be used to vector towards more prospective parts of a
mineralized system. Systematic geological mapping and rock chip sampling
was also completed over the main prospects where outcropping alteration
is evident.
>>
Initial integrated analysis of the new data sets by First Quantum has
highlighted eight preliminary target areas (Figure 1) in the Rubi claims.
These include;
1)             Refining of targets in the
Lithocap, Corner Zone and
Portezuelo areas originally
identified by Mirasol; and


A number of prospective new
target areas identified
within the large gravel-
covered plain at the centre
2)             of the project.
An electrical geophysical survey has been initiated over some target
areas at Rubi. This survey combines high sensitivity Induced Polarization (IP)
and Magneto Telluric (MT) geophysical techniques. Combined, these techniques
can be used to detect buried sulphide or silica accumulations through gravel
cover and at significant depth that can indicate potential areas of
mineralization. This geophysical data will be used as a final layer of
information to filter and prioritize areas for drill testing.
Mirasol's management are pleased with the exploration approach and
outcomes to-date from the First Quantum program at Rubi. This work has
increased the number of potential targets and has built a strong
knowledge-base to leverage final drill target selection.
The Rubi project is located adjacent to two large porphyry copper - gold
mining districts in what Mirasol believes is an underexplored section of one
of the world's more productive porphyry copper belts. Mirasol will continue to
report on progress toward drill testing of the Rubi Project as new information
is received.
Stephen Nano, President and CEO is the Qualified Person under NI 43-101
who has prepared and approves the technical content of this news release.
First Quantum Minerals operates the Rubi Joint Venture and generated the
geological, geophysical and geochemical information reported to Mirasol
Resources. First Quantum uses industry accepted procedures for the collection
and analysis of this information including a formal quality assurance and
quality control (QA/QC) program and ISO 9001:2000-accredited assay
laboratories for geochemical analysis. Mirasol has performed an independent
analysis of the information and reports provided by First Quantum. Stephen
Nano has reviewed the data and prepared this news release, and is a qualified
person as defined by National Instrument 43-101.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Additional explanatory notes:
(x) Enzyme partial leach soil sampling: Actlabs Enzyme Leach SM used at the
Rubi Project is a partial leach technique that selectively extracts elements
from amorphous manganese oxide coatings on soil materials. Under the right
circumstances, these elements potentially derived from underlying concealed
mineralization are transported through the soil profile and concentrate in the
oxide coatings. The Enzyme Leach soil technique has been successfully used to
detect soil or gravel-covered mineralization by other companies in Chile and
at other locations around the world.
(x)(x)Soil buffer capacity: Oxidizing sulphide mineralization generates
hydrogen ions that are acid by nature. These ions migrate vertically above an
oxidizing sulphide body and come in contact with carbonates that naturally
occur in the near-surface soil, dissolving the carbonate and lowering the
buffering capacity of the soil. Systematic measuring the buffering capacity in
the soil can map areas of low buffering capacity that may indicate the
presence of an oxidizing sulphide body at depth.
(x)(x)(x)Hand-held spectrometer: A field portable device (PIMA, ASD, PSM
devices) that measures the absorption of light in specific wavelengths of the
infrared spectrum to identify certain mineral species and changes in their
chemical composition or crystal structure. Some mineral species are known to
occur in altered rock associated with or in the periphery to mineral deposits.
In known metalliferous deposits some of these minerals have been demonstrated
to also show systematic changes in their mineral chemistry or increasingly
ordered crystal structure as a vector towards mineralization. By analogy this
information can be used as an exploration vector in alteration system to help
focus exploration into areas with better potential for mineral discovery.
SOURCE Mirasol Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/September2014/03/c1462.html

-0-                           09/03/2014
/For further information: Stephen Nano, President and CEO, Tel: (604)
602-9989: Fax: (604) 609-9946, Email: contact(at)mirasolresources.com, Website:
www.mirasolresources.com/
/Web Site: http://www.mirasolresources.com /
(MRZ.)

CO:  Mirasol Resources Ltd.
ST:  British Columbia
IN:  MNG
SU:

-30-