Source	Marketwire
Date	09/08/2014
Time	04:01:27 AM

Company	 TERRAX MINERALS INC.
Title	TerraX Assays 878 and 712 g/t Au in Grab Samples From Two New Veins 
Discovered on the Yellowknife City Gold Project





    CDNX Symbol: TXR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
PINKSHEETS SYMBOL: TRXXF

September 8, 2014

TerraX Assays 878 and 712 g/t Au in Grab Samples From Two New Veins Discovered 
on the Yellowknife City Gold Project


YELLOWKNIFE, NORTHWEST TERRITORIES--(Marketwired - Sept. 8, 2014) - TerraX 
Minerals Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(OTC PINK:TRXXF) has now received 
all surface sampling results from the summer prospecting and mapping program on 
its Yellowknife City Gold Project ("YCGP"), immediately north of Yellowknife in 
the Northwest Territories. This release summarizes the assay results from 718 
grab, chip and channel samples taken during this program. Assay results from 
the nine holes drilled at the Crestaurum deposit this summer will be announced 
once received and interpreted.

Combined with 2013 results, this summer's surface work on the YCGP has led to 
the generation of more than 10 additional discoveries which could be quickly 
made 'drill ready' in the short term. Several of the new high grade targets are 
oblique or high angle veins that occur near the main Crestaurum and Barney 
structures and they could be indicative of gold bearing vein sets common to 
large mineralized systems.

At least four new targets were identified in the Crestaurum area:

/T/

1.  Three grab samples were taken from a 20 cm wide, northwest trending
quartz vein 250 m northwest of the Crestaurum structure. The vein
contains visible gold; assay results from grab samples taken from this
vein were 24.7, 157.5 and 878 g/t Au. This vein could intersect the
Crestaurum structure at a high angle.



2.  The newly identified Milner SW structure 250 m northeast of the known
extent of the Crestaurum structure was sampled over a strike length of
75 m. This structure could be an extension of, or a splay off, the main
Crestaurum structure. Nine samples were collected, with seven grab
samples returning results ranging from 1.05 to 712 g/t Au, including 326
and 103 g/t Au. Visible gold is apparent in the higher grade samples.
Two of the samples were chip samples over 1 m intervals; these assayed
11.65 and 33.1 g/t Au.



3.  A grab sample taken from quartz stringers potentially on the southwest
extension of the Crestaurum structure 230 m southwest of the main
trenches ran 40.2 g/t Au.



4.  Four grab samples from a north-northwest trending, 15 cm wide quartz
vein southeast of the Crestaurum structure assayed between 6.69 and 27.1
g/t Au. Minor visible gold was noted in this vein, which outcrops over a
strike length of 30 m. This vein could be a splay off the Crestaurum
structure or a new vein intersecting it at a low angle.


/T/

The map of the Crestaurum surface results on the TerraX website 
(www.terraxminerals.com) under "2014 Field Exploration" has been updated to 
include these results.

In the Barney area a 2 m wide shear zone trending north-northwest was 
discovered halfway between Crestaurum and the Barney Zone in the Milner Lake 
area. A grab sample from this zone assayed 44.3 g/t Au. A quartz vein/shear 
zone on the east edge of Milner Lake was channel sampled in three locations; 
the best result was 1.4 m @ 2.03 g/t Au. This vein is interpreted as the 
possible surface expression of the Barney Zone, where TerraX recently drilled 
22.42 m @ 6.35 g/t Au, inclusive of 5.16 m @ 18.40 g/t Au (news release of 
August 25, 2014).

Geologists provided by Virginia Mines Inc. conducted reconnaissance mapping in 
the extreme southern portion of the YCGP, mapping the extension of the Barney 
Shear over a strike length of 1 km to within 100 m of the southern boundary of 
the property. They also noted a series of north-northeast trending shear zones 
on the Northbelt property which probably represent the northern extension of 
the Giant shear system. A grab sample from one of these shears ran 7.34 g/t Au.

Other areas sampled included:

/T/

--  The AES structure, where a southwest extension of this structure was
sampled. Ten grab samples were collected over a 400 m strike length;
gold results ranged from 0.035 to 21.7 g/t Au, and five samples had
values greater than 1 g/t Au. These results are up to 5 km from
mineralization reported from the same structure last year (grab sample
of 12.85 g/t Au, chip sample of 1 m @ 4.76 g/t Au; news release of Nov.
6, 2013), and indicate another promising long strike length target area
on the YCGP.



--  The Walsh Lake property, where previous chip sampling at the Sam Otto
zone produced 5.0 m @ 1.90 g/t Au, and a historical drill intersection
of 15.85 m @ 2.59 g/t Au was reported (see news release of Oct. 30,
2013). Chip sampling of a previously unsampled trench returned 8.0 m @
0.89 g/t Au, and a grab sample from a quartz vein 100 m northeast of the
main zone assayed 72.6 g/t Au. A newly discovered quartz vein in the
eastern part of the Walsh Lake property ran 11.1 g/t Au.


/T/

Assay values from the samples reported today ranged from below detection to a 
high of 1,205 g/t Au at Crestaurum, with 59 samples greater than 5 g/t Au and 
17 samples greater than 30 g/t Au.  Certified standards and blanks were 
inserted into the stream of samples for chemical analysis. Samples were 
prepared at ALS Chemex's laboratory in Yellowknife and shipped to their 
Vancouver facility for gold analysis by fire assay and other elements by ICP 
analysis. ALS is a certified and accredited laboratory service. It should be 
noted that, due to their selective nature, assay results from grab samples may 
not be indicative of the overall grade and extent of mineralization on the 
subject area. The technical information contained in this news release has been 
approved by Tom Setterfield, Vice President Exploration of TerraX, who is a 
Qualified Person as defined in "National Instrument 43-101, Standards of 
Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold Project encompasses 93.5 sq km of contiguous land 
immediately north of the City of Yellowknife in the Northwest Territories and 
includes TerraX's wholly-owned Northbelt property acquired in February 2013.

The project lies on the prolific Yellowknife greenstone belt and covers 15 km 
of strike length on the northern extension of the shear system that hosts the 
high-grade Con and Giant gold mines. The project area contains multiple shears 
that are the recognized hosts for gold deposits in the Yellowknife gold 
district, with innumerable gold showings and historic high grade drill results. 
Since January 2013, TerraX has consolidated the project area by acquiring and 
optioning numerous properties, including: Northbelt, Goodwin, Ryan Lake, Walsh 
Lake, and U-Breccia, as well as staking additional contiguous lands. Being 
all-season road accessible and within 15 km of the City of Yellowknife, the 
YCPG is close to vital infrastructure, including transportation, service 
providers, hydro-electric power and skilled trades people.

For more information on TerraX and the Yellowknife City Gold Project, please 
visit our web site at www.terraxminerals.com.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

Paradox Public Relations
514-341-0408
Toll Free: 1-866-460-0408
info@paradox-pr.ca

or

Vanguard Shareholder Solutions
604-608-0824
Toll Free: 1-866-801-0779
ir@vanguardsolutions.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=497538265