Source	MARKET NEWS
Date	09/04/2014
Time	06:49:56 AM

Company	 Golden Predator Mining Corp.
Title	Gravity Tests Indicate 87% to 96% Gold Recovery





    CDNX Symbol: GPY











Press Release	





Gravity Tests Indicate 87% to 96% Gold Recovery At Golden Predator's3 Aces 
Project --->@NEWS RELEASE
GOLDEN PREDATOR MINING CORP ("GPY-V;NTGSF-0")
- Gravity Tests Indicate 87% to 96% Gold Recovery
- At Golden Predator's 3 Aces Project

Golden Predator Mining Corp. (the "Company") announces that
results from Gravity Recoverable Gold (GRG) tests done on three samples
from the three Aces project in the Yukon Territory have returned GRG
recoveries of 86.9 to 95.8%.  The GRG testing was completed on three
20-kg sub-samples taken from three larger volume samples collected at
the three Aces Project's Sleeping Giant Zone for metallurgical and
mineralogical characterization test work (news release dated July 15,
2014).  The three samples will now be processed in their entirety in
bulk fashion to measure total gold recovery from each of the 600 to 800
kg samples.



//st
Summary of Gravity Recoverable Gold Tests




Metallurgical  Head Grade  Total   GRG %     GRG %    GRG %
Sample ID      (Au g/t)    GRG %   P80 -20   P80 -75  P80 -200
mesh      mesh     mesh
BS-3A13-01      1.79       86.9    52.1      27.5     7.3
BS-3A13-02      10.5       93.7    51.7      37.2     4.8
BS-3A13-03     212.5       95.8    69.2      22.0     4.6
//et

Prior to the GRG tests, SGS Canada Inc. completed screen metallic
assays on three 2-kg sub-samples split from the larger volume samples.
The screen metallic assays compare very well with the GRG tests and
indicate that routine large pulp (approximately 2-kg at minus 10 mesh)
screen metallic assays should provide reliable assays going forward in
exploration and delineation of the high-grade coarse gold
mineralization at the 3 Aces project.



//st

Summary of Screen Metallic Assay Results
Metallurgical Sample ID  Screen Metallic    +150 fraction  -150 fraction
Total Au g/t       Au g/t         Au g/t
BS-3A13-01               1.6                    6.3           1.3
BS-3A13-02               10.5                 117.9           6.5
BS-3A13-03               215.5               2109.8         105.3
//et



In 2013 GPY collected 3 samples, 842 kg, 800 kg and 620, kg from
the hanging wall portion of the Sleeping Giant vein zone. The samples
were shipped via truck to SGS Canada Inc. Laboratories in Burnaby,
British Columbia and stored in a secure location.  All three samples
were collected in areas that were previously channel sampled, and the
areas were selected in order to obtain samples from areas with low,
medium and high gold values.



The characterization test work is being carried out by SGS Canada
Inc. in Burnaby, British Columbia. The remaining material from each
large sample is now being processed for total gold recovery with
gravity methods and processed in bulk fashion.   A representative split
from the tails of each sample will be subjected to test for
identification of additional gold recovery by traditional mineral
process techniques by grinding the tails to 75 microns and leaching
with cyanide.



Results from the processing of the complete large samples should
be available in the fourth quarter of 2014.



3 Aces Project, Yukon
The 3 Aces property consists of 1,108 contiguous quartz claims
(23,000 hectares) located in southeast Yukon. The property is located
along the Nahanni Range Road which accesses the operational Cantung
Mine located 40 kilometres to the north.



The 3 Aces property contains a number of quartz veins and vein
zones that cut Cambrian aged limestone, shale, quartz grits and pebble
chert conglomerates of the Hyland Group.  Previous sampling and
exploration by Golden Predator (formerly Northern Tiger) has outlined
extensive gold-in-soil anomalies over nine square kilometres, including
numerous high-grade gold showings (see property map  below).
The 3 Aces property is located in the traditional territory of the
Kaska Nation.  In January 2013, Golden Predator signed an Exploration
Agreement with the Kaska Nation, as represented by the Ross River Dena
Council and the Liard First Nation, with respect to activities within
their traditional territories.



Mr. Mike Maslowski, CPG, a Qualified Person as defined by National
Instrument 43-101 and a consultant for the Company, has reviewed,
verified and approved disclosure of the technical information contained
in this news release.




To view the graphic in its original size, please click here

Golden Predator Mining Corp.
Golden Predator's corporate mandate is to advance the Brewery
Creek project towards production through a joint venture arrangement.
The Brewery Creek mine operated from 1996 to 2002, before closing due
to low gold prices. Mining licenses and permits are in place for
continued exploration along with a Socio Economic Accord with the
Tr'ondek Hwech'in. The Company holds additional projects with current
resources and/or new discovery potential, including the high-grade 3
Aces and Grew Creek gold projects and the Marg and Clear Lake
polymetallic massive sulfide deposits.





Neither TSX Venture Exchange nor its Regulation Services Provider (as that
term is defined in policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.




No stock exchange, securities commission or other regulatory authority has
approved or disapproved the information contained herein. This press
release contains projections and forward-looking information that involve
various risks and uncertainties regarding future events. Such
forward-looking information can include without limitation statements based
on current expectations involving a number of risks and uncertainties and
are not guarantees of future performance. There are numerous risks and
uncertainties that could cause actual results and the Company's plans and
objectives to differ materially from those expressed in the forward-looking
information. Actual results and future events could differ materially from
those anticipated in such information. These and all subsequent written and
oral forward-looking information are based on estimates and opinions of
management on the dates they are made and are expressly qualified in their
entirety by this notice. Except as required by law, the Company assumes no
obligation to update forward-looking information should circumstances or












































TEL:  (587) 524 1599  Greg Hayes, Chief Executive Officer
TSX Venture closing price for GPY-V
Date: 2014/09/03
Closing Price: 0.18

TEL:  (208) 635 5415  William M. Sheriff, Co-Chair

info@goldenpredator.com

www.goldenpredator.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1424600027TS11424601037-06482620140904