Source	Marketwire
Date	09/08/2014
Time	06:00:46 AM

Company	 CARLIN GOLD CORPORATION
Title	Carlin Gold Corporation: Cortez Summit Property Geological Update





    CDNX Symbol: CGD











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Carlin Gold Corporation

TSX VENTURE SYMBOL: CGD

September 8, 2014

Carlin Gold Corporation: Cortez Summit Property Geological Update


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 8, 2014) - Carlin Gold 
Corporation (TSX VENTURE:CGD), ("Carlin" or the "Company") is pleased to report 
the geological assessment of its limited core drilling program completed in 
fall 2013 on its Cortez Summit property ("Cortez Summit" or the "Property"), 
Eureka County, Nevada.

In September-October 2013 the Company re-entered vertical reverse circulation 
hole CS12-2 and deepened it by core drilling. Carlin geologists were encouraged 
that the core hole established the presence of favorable 'Lower Plate' rocks 
and retained the services of Dr. Harry Cook, President/CEO of Carbonate Geology 
LLC to review the core. Dr. Cook is a well known geologist specializing in 
carbonate stratigraphy in the major gold districts in Nevada and is very 
familiar with the Cortez area. He has been acknowledged for his role in 
developing an understanding of the gold-hosting Paleozoic stratigraphy, 
including the neighboring Goldrush discovery. Dr. Cook examined the lower 984.5 
feet (300 m) of the core hole CS12-2C and interpreted the bottom 650 feet (198 
m) of the hole to contain Devonian age strata.

Dr. Cook states that "Core CS12-2C strata are comprised of very favorable 
gold-host rocks within both the Wenban Formation and Horse Canyon Formation. 
These strata are coeval (of the same age) with the nearby Wenban Formation and 
Horse Canyon Formation carbonate gold-host strata that comprise the gold hosts 
in Barrick's Goldrush Discovery." Dr. Cook's interpretations of the core are 
based on fossil and sedimentologic observations in context with his extensive 
field, pit and core experience at many locations and mine sites throughout 
Nevada. Additional drilling is recommended by Dr. Cook.

K. Wayne Livingstone, President/CEO of the Company, commented: "The information 
Dr. Cook has provided indicates that Carlin's core hole intersected the 
stratigraphic section containing the main gold-bearing horizons as the 
neighboring Goldrush discovery. This is important as it clearly demonstrates 
the exploration potential of the project and helps to set the stage for 
additional drilling evaluation."

Hole CS12-2C was deepened by core drilling from 1,760 ft. (537 m) to 4,032 ft. 
(1,229 m) and contains short intervals of anomalous gold values to 0.667 grams 
per tonne, along with longer intervals of anomalous arsenic values greater than 
100 ppm in the Devonian Lower Plate section. These core also display 
Carlin-style alteration features such as decalcification, clay alteration, and 
calcite veining.

The 2012 reverse circulation drill program of seven vertical holes, totaling 
11,720 feet (3,573 m.) ranging in depth between 1500 and 1800 feet (450 and 550 
m.), encountered Paleozoic sedimentary rocks which are now considered to be 
structurally and stratigraphically above the calcareous Lower Plate units. 
Short intervals of anomalous gold up to 0.534 grams/tonne with Carlin-type 
pathfinder elements were present in six of the seven holes drilled. Two holes 
with the longest anomalous arsenic intervals were drilled 1,900 feet (580 m) 
apart, and are located in close proximity to the projected Fourmile structural 
zone, a north-northwest trending corridor which trends for 4,500 feet (1,370 m) 
along the west side of the Property. This structural corridor will be targeted 
in future drilling.

In addition to the recent geological studies, the Company has reviewed existing 
ground and airborne geophysical survey data in an effort to enhance future 
drill targeting. This information has been helpful in defining several 
structural zones of interest on the property, including the Fourmile structure.

Cortez Summit Property Setting on Cortez Trend

Cortez Summit is centrally located in Eureka County on the Cortez Trend, in the 
middle of what has become the most active gold exploration area in Nevada. The 
100% owned Property consists of 142 unpatented claims located in the southern 
Cortez Mountains between the historic Buckhorn and Horse Canyon mines. The east 
edge of the Property lies 2/3 mile (1 km) west of the Buckhorn mine, and the 
west edge of the Property lies 1.5 miles (2.5 km) east of the Horse Canyon 
mine. Barrick's Cortez Hills operation (11 million oz gold pre-production 
reserve/resource) lies 4 miles (6.4 km) west of the Property. The Goldrush 
discovery has grown rapidly since the initial announcement on September 7, 
2011, and as of December 31, 2013, the estimated measured and indicated 
resources reported by Barrick stood at 10.0 million ounces, with a grade of 
0.132 oz. per ton gold (4.5 grams/tonne) and the inferred resource was 
estimated to be 5.6 million ounces, with a grade of 0.141 oz. per ton gold (4.8 
grams/tonne). The mineralization is open in several directions and the 
currently defined northern extent lies adjacent to the west side of Cortez 
Summit.

Barrick has announced they are advancing their Goldrush Project through the 
prefeasibility stage, scheduled for completion in mid-2015. Barrick has 
reported encountering deep mineralization along the northern extension of the 
Goldrush, including an intercept of 103 feet (29 m.) containing 0.725 oz. per 
ton gold (24.9 grams/tonne) and have applied for a permit to construct an 
exploration decline in order to better define the existing resource and to test 
for additional mineralization to the north (Barrick Q2 2014 Report). Surface 
infill drilling continues.

CARLIN'S PROPERTIES

Carlin has three properties in northern Nevada including Cortez Summit, all of 
which represent Carlin-type gold targets. The 100% owned JDS property consists 
of 77 unpatented claims located in Eureka County, in the Cortez Trend 
approximately 13 miles southeast of Cortez Summit. The Willow property, 100% 
owned, consists of 89 unpatented claims located in northeast Nevada, northwest 
of the new 2.6 million ounce Long Canyon gold deposit in the Pequop Mountains, 
owned by Newmont Mining Corporation. Newmont has recently staked claims 
adjacent to the Willow property.

Carlin also owns approximately 65,000 hectares (250 square miles) distributed 
over 12 project areas in Yukon, in a 50/50 joint venture with Constantine Metal 
Resources Ltd. (TSX VENTURE:CEM). The properties are early stage, with the 
initial field evaluation program completed in 2011. Several significant gold 
anomalies have been identified to date.

/T/

"K. Wayne Livingstone"
----------------------------------------------------------------------
K. Wayne Livingstone, President and Chief Executive Officer

/T/

Notes:

Robert Thomas CPG, Vice President of Carlin and a qualified person as defined 
by Canadian National Instrument 43-101, has reviewed and approved the technical 
information contained in this news release on behalf of Carlin. Mr. Thomas 
supervised the QA/QC controls. TonaTec Exploration LLC completed the core 
drilling. Core logging was completed on site and core was stored at a secure 
facility prior to being transported to Elko for core sampling. Carlin Trend 
Mining Services in Elko completed the core sampling under the supervision of 
Carlin personnel. Sampling consisted of cutting core with a diamond blade rock 
saw or splitting the material, depending on rock coherence. Core samples ranged 
from 2.7 to 6.5 feet and following cutting half the material was placed in 
polypropylene bags, with the other half placed back in their original core 
boxes for permanent storage. Samples were delivered to American Assay 
Laboratories facility in Sparks, Nevada for preparation and assay/geochemistry. 
Sample delivery was completed by either Carlin or American Assay Laboratories 
personnel. Gold was determined on prepared pulps by fire-assay fusion of a 30 
gram sub-sample by ICP (American Assay Laboratory procedure Au FA30). 0.5 gram 
splits were analyzed for multi-element inductively-coupled plasma (ICP) atomic 
emission spectroscopy (American Assay Laboratory procedure ICP-2BX), following 
multi-acid digestion. The Company's standards and blanks were regularly 
inserted into the sample stream.

Forward looking statements: This news release includes certain "forward-looking 
information" within the meaning of Canadian securities legislation and 
"forward-looking statements" within the meaning of the United States Private 
Securities Litigation Reform Act of 1995 (collectively "forward looking 
statements")." Forward-looking statements include predictions, projections and 
forecasts and are often, but not always, identified by the use of words such as 
"seek", "anticipate", "believe", "plan", "estimate", "forecast", "expect", 
"potential", "project", "target", "schedule", budget" and "intend" and 
statements that an event or result "may", "will", "should", "could" or "might" 
occur or be achieved and other similar expressions and includes the negatives 
thereof. All statements other than statements of historical fact included in 
this news release are forward-looking statements that involve various risks and 
uncertainties. There can be no assurance that such statements will prove to be 
accurate and actual results and future events could differ materially from 
those anticipated in such statements.

Forward-looking statements are based on a number of material factors and 
assumptions. Important factors that could cause actual results to differ 
materially from Carlin's expectations include availability of capital and 
financing in connection with future private placements, regulatory approval, 
actual exploration results, changes in project parameters as plans continue to 
be refined, results of future resource estimates, future metal prices, 
availability of capital and financing on acceptable terms, general economic, 
market or business conditions, uninsured risks, regulatory changes, defects in 
title, availability of personnel, materials and equipment on a timely basis, 
accidents or equipment breakdowns, delays in receiving government approvals, 
unanticipated environmental impacts on operations and costs to remedy same, and 
other exploration or other risks detailed herein and from time to time in the 
filings made by the Company with securities regulators. Although the Company 
has attempted to identify important factors that could cause actual actions, 
events or results to differ from those described in forward-looking statements, 
there may be other factors that cause such actions, events or results to differ 
materially from those anticipated. There can be no assurance that 
forward-looking statements will prove to be accurate and accordingly readers 
are cautioned not to place undue reliance on forward-looking statements.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

Carlin Gold Corporation
K. Wayne Livingstone
President and Chief Executive Officer
(604) 638-1402
www.carlingold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=497524169