Source	CANADA NEWSWIRE
Date	09/11/2014
Time	04:23:56 AM

Company	 Santacruz Silver Mining Ltd.
Title	Santacruz Silver Reports PEA Results and New Resource on San Felipe
Project, Mexico





    CDNX Symbol: SCZ











Press Release	




" BC-Santacruz-PEA   09-11 3653
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Santacruz Silver Reports PEA Results and New Resource on San Felipe
Project, Mexico@

Pre-Tax IRR 61% and 5% NPV of US$104 million; Average Annual Production
of 3.2 M Oz Ag Equivalent(x); All-In Cash Costs of $12.72 oz Ag Equivalent;
Significant Resource Increase
TSX.V: SCZ
VANCOUVER, Sept. 11, 2014 /CNW/ - Santacruz Silver Mining Ltd.
(TSX.V:SCZ) is pleased to announce the results of a Preliminary Economic
Assessment ("PEA") and new resource estimate prepared pursuant to National
Instrument 43-101 ("NI 43-101") on its San Felipe Project located 130 km
northeast of Hermosillo in Sonora State, Mexico. Highlights of the PEA, using
a US$19.91 per ounce silver base case, include:
<<

--  Pre-tax Net Present Value ("NPV") at a 5% discount rate of US $103.5
million and an Internal Rate of Return ("IRR") of 60.6%;
--  After-tax NPV at a 5% discount rate of US $61.2 million and IRR of
37.7%;
--  Production of 24.3 million ounces of silver equivalent (after milling
and smelting recoveries);
--  Average annual production of 3.2 million ounces of silver equivalent
over a 7.5 year mine life;
--  Initial capital cost ("CAPEX") of US $36.3 million, including $6 million
of working capital;
--  Estimated all-in cash costs of US $12.72/oz silver equivalent (including
site operating costs, smelter costs, sustaining capital and NSR payments
); and
--  Pre-tax payback of 1.6 years after start-up, and 2.3 years after-tax
payback.
>>
At a 150 g/t Ag equivalent cut-off, the new resource estimate for all
veins is:
<<

--  Indicated - 1.1Mt at 76.5 g/t Ag, 2.5% Pb and 6.4%Zn (equal sign) 423 g/t 
Ag equiv
or 15.2 Moz Ag equiv
--  Inferred - 3.3Mt at 64.8 g/t Ag, 1.9% Pb and 4.9% Zn (equal sign) 326 g/t 
Aq equiv
or 34.3 Moz Ag equiv
>>
Santacruz President and Chief Executive Officer Arturo Préstamo stated,
"This Preliminary Economic Assessment is excellent news for the Company and
indicates that the San Felipe project has strong economic parameters and is
potentially economically viable in the current market environment. The
estimated CAPEX for the project is relatively low, and the property has
significant exploration upside. The Company will be initiating the priority
studies identified by the study team to de-risk the project immediately. These
include completing more metallurgical work, initiating exploration drifting
and trial mining to evaluate the continuity of higher grade mineralization and
ground conditions for potential future mining."
He continued, "The significant increase in resources in the recent
estimate shows that the efforts of our exploration team are paying off. Some
of the resource areas are still open and surface work over the last year has
identified additional vein targets. The Company believes that, similar to many
vein deposits, if a mine is developed on the current San Felipe resource there
will be opportunities to identify new resources to keep the operation going
for many years to come. With the PEA now complete, the Company will be
initiating the recommended work program to bring the project towards
pre-feasibility and will complete permitting for the proposed infrastructure.
At the same time, the Company will continue to aggressively explore the rest
of the property. In particular, the Company will focus on those areas already
identified with high potential to further increase the resources on the San
Felipe Project."
The PEA is preliminary in nature and includes inferred mineral resources
that are considered too speculative geologically to have the economic
considerations applied to them that would enable them to be categorized as
mineral reserves. There can therefore be no certainty that the PEA will be
realized. It is also important to note that mineral resources that are not
mineral reserves do not have demonstrated economic viability.
(x)For the PEA, Silver Equivalent was calculated using prices of
US$19.91/oz., US$0.99/lb. and US$1.00/lb. for silver, lead and zinc,
respectively.
PEA Summary
The PEA models a combined open pit and underground mine and mill that
produces both a lead and a zinc concentrate with the lead concentrate
containing the payable silver values. Resources on four veins, Ventana, Las
Lamas, San Felipe and Transversales are included in the analysis. In the
model, the upper parts of the Ventana, San Felipe and Tranversales veins are
mined by open-pit methods. Separate underground workings are developed to
access the lower parts of the Ventana and San Felipe veins and the Las Lamas
vein. Proposed mining is by contractor. Underground mining is modeled to be by
long-hole sub-level retreat using diesel mobile equipment. Access to lower
levels is by decline. Just over a year of pre-production construction would be
required. The proposed 1,250 tonnes/day mill contains a crushing circuit, ball
mill and flotation circuits. Concentrates will be sold and delivered to a
smelter or concentrate trader.
The PEA was completed by a group of independent qualified persons (as
such term is defined in NI-43-101), including Gregory Blaylock, P.Eng, P.E. of
JDS Energy & Mining Inc., Deepak Malhotra, Registered SME Member and President
of Resource Development Inc., Fletcher Bourke, P.Geo., of Kuu Exploration Ltd.
and Hans Smit, P.Geo., of Hans Smit, P. Geo. Inc. The PEA incorporates a new
resource estimated by Gary Giroux, P.Eng. of Giroux Consultants Ltd.
A summary of the key parameters and conclusions of the PEA are given in
the table below. The 100-day average as of September 4, 2014 was used as the
base case metal price. The PEA is based on a stand-alone project and evaluates
the potential economics from the start of construction. It does not
incorporate costs before any production decision. The PEA and new resource
estimate will be available on SEDAR within 45 days of this press release.
The reader is advised that the PEA summarized in this press release is
intended to provide only an initial, high-level review of the project
potential and design options. The PEA mine plan and economic model include the
use of inferred mineral resources. Inferred mineral resources are considered
to be too speculative geologically to be used as the basis of an economic
analysis except as permitted under NI 43-101. There is no guarantee that
inferred mineral resources can be converted to indicated or measured mineral
resources, and as such, there can be no certainty the project economics
described herein will be achieved.


San Felipe - September 2014 PEA Results

This PEA is preliminary in nature and there is no certainty that the results of 
the PEA will be realized.

The resources incorporated in this assessment are not mineral reserves and do 
not have demonstrated economic viability.

The first year of this assessment is based almost entirely on inferred 
resources and there is limited metallurgical information
and no geotechnical information to support the first year of the analysis.

The results of this study show that the project has potential to be economic 
and further work to determine economic viability is warranted

This study is too preliminary to demonstrate economic viability.

San Felipe PEA Production Estimate
----------------------------------

Total Tonnes to 
Mill                                                                     3.4 Mt
--------------------                                                            
         ------

Average Milled per 
Day                                                                   1250 t/day
----------------------                                                          
         ----------

Underground Tonnes to 
Mill                                                               2.4 Mt
--------------------------                                                      
         ------

Open Pit Tonnes to 
Mill                                                                  1.0 Mt
-----------------------                                                         
         ------

Open Pit Tonnes 
Waste                                                                    7.1 Mt
---------------------                                                           
         ------

Open Pit Strip 
Ratio                                                                     7:1
--------------------                                                            
         ---

Years 
Production                                                                      
                           7.5
----------------                                                                
                                 ---

Ag                            Pb                   Zn
---                           ---                  ---

Grade                                                                           
                   63.5 g/t                                   1.7%         5.1%
-----                                                                           
                   --------                                    ---           ---

Metal 
Mined                                                                           
             7.0 Moz                      126.5 Mlbs          385.9 Mlbs
-----------                                                                     
                   -------                      ----------          ----------

Recovery - Sulphide   (Oxide 
de-rated)                                                                       
    80%                           86%          87%
-------------------------------------                                           
                                 ---                            ---           
---

Metal Produced in 
Concentrate                                                                     
 5.5 Moz                      107.3 Mlbs          328.7 Mlbs
-----------------------------                                                   
                   -------                      ----------          ----------

Metals Payable after 
Smelting                                                                      
5.2 Moz                      100.9 Mlbs          279.4 Mlbs
-----------------------------                                                   
                   -------                      ----------          ----------

Metal 
Price                                                                           
                     $19.91/oz                      $0.99/lb     $1.00/lb
-----------                                                                     
                           ---------                      --------     --------

Smelter Credit 
($US)                                                                           
             $104.6 M                       $99.9 M     $279.4 M   $483.8 M
-------------------                                                             
                            --------                       -------     
--------   --------


San Felipe PEA Economics - Life of Mine
---------------------------------------

$US '000     $US '000                          Per Tonne

Mined


Smelter Credit                                                              
$483,784                                                  $141.78
--------------                                                           
--------                                                  -------

Smelter Costs                                                
($83,064)                                                 ($24.38)
-------------                                                 
--------                                                   -------

Concentrate Shipping                                         
($12,571)                                                  ($3.68)
--------------------                                          
--------                                                    ------

Total Smelter and Concentrate Charges                                   
($95,605)                                                ($28.02)
-------------------------------------                                    
--------                                                  -------

NSR (1%)                                                                 
($3,540)                                                 ($1.04)
-------                                                                   
-------                                                   ------

Site Operating Costs
--------------------

Mining                                                       
($89,138)                                                 ($26.24)
------                                                        
--------                                                   -------

Milling                                                      
($66,004)                                                 ($19.34)
-------                                                       
--------                                                   -------

G&A                                                          
($23,380)                                                  ($6.85)
---                                                           
--------                                                    ------

Total  Site Operating                                                  
($178,522)                                                ($52.32)
---------------------                                                   
---------                                                  -------

Net Operating Cash Flow                                                  
$206,118                                                   $60.40
-----------------------                                                  
--------                                                   ------

Initial Capital Costs
---------------------

Mining                                                         (2,500)
------                                                          ------
Milling                                                       (15,300)
-------                                                        -------

G&A and Infrastructure                                        (12,460)
----------------------                                         -------

Working Capital                                                (6,000)
---------------                                                 ------

Total Initial Capital                                         
(36,260)                                                 ($10.63)
---------------------                                          
-------                                                   -------

Sustaining Capital Costs
------------------------

Mining                                                       ($26,265)
------                                                        --------

Milling                                                             $0
-------                                                            ---

Infrastructure                                                (5,025)
--------------                                                 ------

Total Sustaining Capital                                     
($31,290)                                                  ($9.17)
------------------------                                      
--------                                                    ------

Closure
-------

Salvage Value                
---                         ---  ---------        
-----   ----        ----              ------ ----------


Ventana                Indicated                        175    764,000        
77.29   3.05        7.18               482.1 11,842,000
-------                ---------                        ---    -------        
-----   ----        ----               ----- ----------

Las Lamas              Indicated                        175     70,000        
81.98   0.27        5.77              311.19    700,000
---------              ---------                        ---     ------        
-----   ----        ----              ------    -------

San Felipe             Indicated                        175    192,000        
95.17    1.7        5.39              355.74  2,196,000
----------             ---------                        ---    -------        
-----    ---        ----              ------  ---------

Total                  Indicated                        175  1,026,000        
80.96   2.61        6.75              446.79 14,738,000
-----                  ---------                        ---  ---------        
-----   ----        ----              ------ ----------

Ventana                Inferred                         175  1,327,000        
62.17    2.7        6.24              416.36 17,764,000
-------                --------                         ---  ---------        
-----    ---        ----              ------ ----------

Las Lamas              Inferred                         175    356,000        
98.63   0.37        5.71              329.13  3,767,000
---------              --------                         ---    -------        
-----   ----        ----              ------  ---------

San Felipe             Inferred                         175    798,000        
73.26   1.63        4.88              312.88  8,027,000
----------             --------                         ---    -------        
-----   ----        ----              ------  ---------

Transversales          Inferred                         175    309,000        
58.37   1.87         2.5                 223  2,215,000
-------------          --------                         ---    -------        
-----   ----         ---                 ---  ---------

Total                  Inferred                         175  2,790,000        
69.57   2.00        5.37              354.22 31,773,000
-----                  --------                         ---  ---------        
-----   ----        ----              ------ ----------


Ventana                Indicated                        200    721,000        
80.53   3.14        7.46              499.88 11,588,000
-------                ---------                        ---    -------        
-----   ----        ----              ------ ----------

Las Lamas              Indicated                        200     59,000        
89.50   0.30        6.17              334.94    635,000
---------              ---------                        ---     ------        
-----   ----        ----              ------    -------

San Felipe             Indicated                        200    175,000       
100.12   1.75        5.65              372.07  2,093,000
----------             ---------                        ---    -------       
------   ----        ----              ------  ---------

Total                  Indicated                        200    955,000        
84.67   2.71        7.05              466.27 14,316,000
-----                  ---------                        ---    -------        
-----   ----        ----              ------ ----------

Ventana                Inferred                         200  1,220,000        
65.34   2.83        6.54              436.41 17,118,000
-------                --------                         ---  ---------        
-----   ----        ----              ------ ----------

Las Lamas              Inferred                         200    322,000       
103.55   0.39        5.96              344.41  3,566,000
---------              --------                         ---    -------       
------   ----        ----              ------  ---------

San Felipe             Inferred                         200    629,000        
83.24   1.69        5.49              347.03  7,018,000
----------             --------                         ---    -------        
-----   ----        ----              ------  ---------

Transversales          Inferred                         200    200,000        
58.74   2.19        2.64              241.34  1,552,000
-------------          --------                         ---    -------        
-----   ----        ----              ------  ---------

Total                  Inferred                         200  2,371,000        
74.72   2.14        5.85              383.75 29,253,000
-----                  --------                         ---  ---------        
-----   ----        ----              ------ ----------
Since the veins contain different metals, a silver equivalent value
cut-off is given in the resource tables to better compare value. The metal
prices used in the silver equivalent estimation are from a 100 day moving
average as of June 3, 2014 and are listed below.
Factor

Ag                     -   US$ 20.06 per ounce   0.64 $/g

Pb                     -   US$ 0.96 per pound              21.16 $/%

Zn                     -   US$ 0.92 per pound              20.28 $/%
The recoveries used in the resource estimation for each metal within each
vein are shown below.
Vein                       Ag Rec.     Pb Rec.     Zn Rec.

Ventana                            70%         86%         87%

Las Lamas                          73%         82%         88%

San Felipe & Transversales         69%         86%         79%
The equation used to establish Ag Equivalent is:
AgEq (equal sign) (Pb% (x) 21.16 (x) Pb Rec%) + (Ag g/t  (x) 0.64 (x) Ag Rec%) 
+ (Zn% (x) 20.28 (x) Zn Rec%)
------------------------------------------------------------------------------

(0.64 (x) Ag Rec%)
Metal prices and recoveries used for the resource are different than
those used in the PEA because the resource was completed earlier than the PEA.
The new San Felipe mineral resource estimate is supported by 55,050 metres of
drilling in 260 drill holes with a total of 11,526 assays. The holes include
those drilled by Santacruz in 2013 and by prior operators in the period 1999
to 2000 and 2006 to 2008. The mineral resources were defined to a maximum
depth of approximately 450 metres below surface with a total of 1,106
down-hole surveys utilized for control.
The resource estimate was completed by Gary Giroux, P.Eng. and utilized a
geological model completed by Hans Smit, P.Geo and Fletcher Bourke, P.Geo. The
geological model has six domains; two at La Ventana (HG, LG), Transverales
(VT), three at San Felipe (SF, HW-1, HW-2) and one at Las Lamas (LL). Assays
for each domain were examined and a top cap was applied to each variable
within each domain. Uniform 2 m composites were formed for the domain
envelopes. Variography was completed for all domains in the La Ventana and Las
Lamas zones. Due to insufficient composites in the VT, SF and HW-2 domains,
variography from the HW-1 domain was used with the orientation changed to fit
the strike and dip of the structures. Grades for all variables were
interpolated into blocks 5 x 2.5 x 5 m using ordinary kriging. For blocks with
multiple domains present, a weighted average was determined for the
mineralized portion. A specific gravity was established for each domain based
on 472 measurements from drill core. Estimated blocks were classified as
Indicated or Inferred based on geologic and grade continuity.
Sampling and Laboratory
The resource is based on holes drilled with HQ-sized core. Core was sawn
in half at site and for all drill campaigns one half sent to ALS Chemex, a
fully accredited and certified laboratory service. Samples were prepared at
the ALS Chemex facility in Hermosillo, Mexico, and were then assayed at ALS
Chemex in Vancouver, Canada. All samples were analysed using a one assay ton
fire assay with an AA finish for Au (Au-AA23) and a 48 element ICP method for
other elements (ME-MS61). Samples with silver results above 100 g/t by
(ME-MS61) were rerun using an aqua regia digestion and ICP-AES or AAS finish
(Ag-OG62). A comprehensive QA/QC procedure was followed using standards,
blanks and duplicates.
Qualified Persons
All scientific and technical information included in this press release
has been reviewed and approved by Gary Giroux, P.Eng., Gregory Blaylock,
P.Eng., P.E., JDS Energy & Mining Inc., Deepak Malhotra, SME Registered
Member, Fletcher Bourke, P.Geo., and Hans Smit, P.Geo who are all independent
of the Company and each of whom is a qualified person, pursuant to the meaning
of such terms in NI 43-101.
Verification
The data in the PEA has been verified by a QP and a full description of
the verified data will be available in the report that will be filed within 45
days.
About Santacruz Silver Mining Ltd.
Santacruz is a Mexican focused silver company with a producing mine
(Rosario); two advanced-stage projects (San Felipe and Gavilanes) and an
early-stage exploration project (El Gachi). The Company is managed by a
technical team of professionals with proven track records in developing,
operating and discovering silver mines in Mexico. Our corporate objective is
to become a mid-tier silver producer.
'signed'
Arturo Préstamo Elizondo,President, Chief Executive Officer and Director
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Forward looking information
Certain statements contained in this news release, such as planned
production levels, exploration programs, mining methods, capital and operating
cost estimates, metal prices, tax rates, permitting, future studies and the
Company's future plans and cash flow position, constitute "forward-looking
information" as such term is used in applicable Canadian securities laws.
Forward-looking information is based on plans, expectations and estimates of
management at the date the information is provided and is subject to certain
factors and assumptions, including, but not limited to, certain assumptions as
to production rate, capital and operating costs, recoveries and metal costs,
that the Company's financial condition and development plans do not change as
a result of unforeseen events, that any additional financing needed will be
available on reasonable terms, that the exchange rates for Canadian, Mexican
and U.S. currencies will be consistent with the Company's expectations, that
requisite regulatory approvals and permits will be obtained in a timely manner
and on acceptable terms, that future metal prices and the demand and market
outlook for metals will be sustained or will improve and that general business
and economic conditions will not change in a materially adverse manner.
Forward-looking information is subject to a variety of risks and uncertainties
and other factors that could cause plans, estimates and actual results to vary
materially from those projected in such forward-looking information. Factors
that could cause the forward-looking information in this news release to
change or to be inaccurate include, but are not limited to, the risk that any
of the assumptions referred to prove not to be valid or reliable, that
occurrences such as those referred to above are realized and result in delays,
or cessation in planned work, that the Company's financial condition and
development plans change, delays in regulatory approval, risks associated with
the interpretation of data, the geology, grade and continuity of mineral
deposits, the possibility that results will not be consistent with the
Company's expectations, as well as the other risks and uncertainties
applicable to mineral exploration and development activities and to the
Company as set forth in the Company's Annual Information Form filed under the
Company's profile at www.sedar.com. There can be no assurance that any
forward-looking information will prove to be accurate, as actual results and
future events could differ materially from those anticipated in such
statements. Accordingly, the reader should not place any undue reliance on
forward-looking information or statements. The Company undertakes no
obligation to update forward-looking information or statements, other than as
required by applicable law.
SOURCE SantaCruz Silver Mining Ltd.



To view this news release in HTML formatting, please use the following 
URL:http://www.newswire.ca/en/releases/archive/September2014/11/c1998.html

-0-                           09/11/2014
/For further information: Neil MacRae, Santacruz Silver Mining Ltd.,
Email: info(at)santacruzsilver.com, Telephone: (604) 569-1609/
(SCZ.)

CO:  SantaCruz Silver Mining Ltd.
ST:  British Columbia
IN:  MIN


" BC-Santacruz-PEA   09-11 3653
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Santacruz Silver Reports PEA Results and New Resource on San Felipe
Project, Mexico@

Pre-Tax IRR 61% and 5% NPV of US$104 million; Average Annual Production
of 3.2 M Oz Ag Equivalent(x); All-In Cash Costs of $12.72 oz Ag Equivalent;
Significant Resource Increase
TSX.V: SCZ
VANCOUVER, Sept. 11, 2014 /CNW/ - Santacruz Silver Mining Ltd.
(TSX.V:SCZ) is pleased to announce the results of a Preliminary Economic
Assessment ("PEA") and new resource estimate prepared pursuant to National
Instrument 43-101 ("NI 43-101") on its San Felipe Project located 130 km
northeast of Hermosillo in Sonora State, Mexico. Highlights of the PEA, using
a US$19.91 per ounce silver base case, include:
<<

--  Pre-tax Net Present Value ("NPV") at a 5% discount rate of US $103.5
million and an Internal Rate of Return ("IRR") of 60.6%;
--  After-tax NPV at a 5% discount rate of US $61.2 million and IRR of
37.7%;
--  Production of 24.3 million ounces of silver equivalent (after milling
and smelting recoveries);
--  Average annual production of 3.2 million ounces of silver equivalent
over a 7.5 year mine life;
--  Initial capital cost ("CAPEX") of US $36.3 million, including $6 million
of working capital;
--  Estimated all-in cash costs of US $12.72/oz silver equivalent (including
site operating costs, smelter costs, sustaining capital and NSR payments
); and
--  Pre-tax payback of 1.6 years after start-up, and 2.3 years after-tax
payback.
>>
At a 150 g/t Ag equivalent cut-off, the new resource estimate for all
veins is:
<<

--  Indicated - 1.1Mt at 76.5 g/t Ag, 2.5% Pb and 6.4%Zn (equal sign) 423 g/t 
Ag equiv
or 15.2 Moz Ag equiv
--  Inferred - 3.3Mt at 64.8 g/t Ag, 1.9% Pb and 4.9% Zn (equal sign) 326 g/t 
Aq equiv
or 34.3 Moz Ag equiv
>>
Santacruz President and Chief Executive Officer Arturo Préstamo stated,
"This Preliminary Economic Assessment is excellent news for the Company and
indicates that the San Felipe project has strong economic parameters and is
potentially economically viable in the current market environment. The
estimated CAPEX for the project is relatively low, and the property has
significant exploration upside. The Company will be initiating the priority
studies identified by the study team to de-risk the project immediately. These
include completing more metallurgical work, initiating exploration drifting
and trial mining to evaluate the continuity of higher grade mineralization and
ground conditions for potential future mining."
He continued, "The significant increase in resources in the recent
estimate shows that the efforts of our exploration team are paying off. Some
of the resource areas are still open and surface work over the last year has
identified additional vein targets. The Company believes that, similar to many
vein deposits, if a mine is developed on the current San Felipe resource there
will be opportunities to identify new resources to keep the operation going
for many years to come. With the PEA now complete, the Company will be
initiating the recommended work program to bring the project towards
pre-feasibility and will complete permitting for the proposed infrastructure.
At the same time, the Company will continue to aggressively explore the rest
of the property. In particular, the Company will focus on those areas already
identified with high potential to further increase the resources on the San
Felipe Project."
The PEA is preliminary in nature and includes inferred mineral resources
that are considered too speculative geologically to have the economic
considerations applied to them that would enable them to be categorized as
mineral reserves. There can therefore be no certainty that the PEA will be
realized. It is also important to note that mineral resources that are not
mineral reserves do not have demonstrated economic viability.
(x)For the PEA, Silver Equivalent was calculated using prices of
US$19.91/oz., US$0.99/lb. and US$1.00/lb. for silver, lead and zinc,
respectively.
PEA Summary
The PEA models a combined open pit and underground mine and mill that
produces both a lead and a zinc concentrate with the lead concentrate
containing the payable silver values. Resources on four veins, Ventana, Las
Lamas, San Felipe and Transversales are included in the analysis. In the
model, the upper parts of the Ventana, San Felipe and Tranversales veins are
mined by open-pit methods. Separate underground workings are developed to
access the lower parts of the Ventana and San Felipe veins and the Las Lamas
vein. Proposed mining is by contractor. Underground mining is modeled to be by
long-hole sub-level retreat using diesel mobile equipment. Access to lower
levels is by decline. Just over a year of pre-production construction would be
required. The proposed 1,250 tonnes/day mill contains a crushing circuit, ball
mill and flotation circuits. Concentrates will be sold and delivered to a
smelter or concentrate trader.
The PEA was completed by a group of independent qualified persons (as
such term is defined in NI-43-101), including Gregory Blaylock, P.Eng, P.E. of
JDS Energy & Mining Inc., Deepak Malhotra, Registered SME Member and President
of Resource Development Inc., Fletcher Bourke, P.Geo., of Kuu Exploration Ltd.
and Hans Smit, P.Geo., of Hans Smit, P. Geo. Inc. The PEA incorporates a new
resource estimated by Gary Giroux, P.Eng. of Giroux Consultants Ltd.
A summary of the key parameters and conclusions of the PEA are given in
the table below. The 100-day average as of September 4, 2014 was used as the
base case metal price. The PEA is based on a stand-alone project and evaluates
the potential economics from the start of construction. It does not
incorporate costs before any production decision. The PEA and new resource
estimate will be available on SEDAR within 45 days of this press release.
The reader is advised that the PEA summarized in this press release is
intended to provide only an initial, high-level review of the project
potential and design options. The PEA mine plan and economic model include the
use of inferred mineral resources. Inferred mineral resources are considered
to be too speculative geologically to be used as the basis of an economic
analysis except as permitted under NI 43-101. There is no guarantee that
inferred mineral resources can be converted to indicated or measured mineral
resources, and as such, there can be no certainty the project economics
described herein will be achieved.


San Felipe - September 2014 PEA Results

This PEA is preliminary in nature and there is no certainty that the results of 
the PEA will be realized.

The resources incorporated in this assessment are not mineral reserves and do 
not have demonstrated economic viability.

The first year of this assessment is based almost entirely on inferred 
resources and there is limited metallurgical information
and no geotechnical information to support the first year of the analysis.

The results of this study show that the project has potential to be economic 
and further work to determine economic viability is warranted

This study is too preliminary to demonstrate economic viability.

San Felipe PEA Production Estimate
----------------------------------

Total Tonnes to 
Mill                                                                     3.4 Mt
--------------------                                                            
         ------

Average Milled per 
Day                                                                   1250 t/day
----------------------                                                          
         ----------

Underground Tonnes to 
Mill                                                               2.4 Mt
--------------------------                                                      
         ------

Open Pit Tonnes to 
Mill                                                                  1.0 Mt
-----------------------                                                         
         ------

Open Pit Tonnes 
Waste                                                                    7.1 Mt
---------------------                                                           
         ------

Open Pit Strip 
Ratio                                                                     7:1
--------------------                                                            
         ---

Years 
Production                                                                      
                           7.5
----------------                                                                
                                 ---

Ag                            Pb                   Zn
---                           ---                  ---

Grade                                                                           
                   63.5 g/t                                   1.7%         5.1%
-----                                                                           
                   --------                                    ---           ---

Metal 
Mined                                                                           
             7.0 Moz                      126.5 Mlbs          385.9 Mlbs
-----------                                                                     
                   -------                      ----------          ----------

Recovery - Sulphide   (Oxide 
de-rated)                                                                       
    80%                           86%          87%
-------------------------------------                                           
                                 ---                            ---           
---

Metal Produced in 
Concentrate                                                                     
 5.5 Moz                      107.3 Mlbs          328.7 Mlbs
-----------------------------                                                   
                   -------                      ----------          ----------

Metals Payable after 
Smelting                                                                      
5.2 Moz                      100.9 Mlbs          279.4 Mlbs
-----------------------------                                                   
                   -------                      ----------          ----------

Metal 
Price                                                                           
                     $19.91/oz                      $0.99/lb     $1.00/lb
-----------                                                                     
                           ---------                      --------     --------

Smelter Credit 
($US)                                                                           
             $104.6 M                       $99.9 M     $279.4 M   $483.8 M
-------------------                                                             
                            --------                       -------     
--------   --------


San Felipe PEA Economics - Life of Mine
---------------------------------------

$US '000     $US '000                          Per Tonne

Mined


Smelter Credit                                                              
$483,784                                                  $141.78
--------------                                                           
--------                                                  -------

Smelter Costs                                                
($83,064)                                                 ($24.38)
-------------                                                 
--------                                                   -------

Concentrate Shipping                                         
($12,571)                                                  ($3.68)
--------------------                                          
--------                                                    ------

Total Smelter and Concentrate Charges                                   
($95,605)                                                ($28.02)
-------------------------------------                                    
--------                                                  -------

NSR (1%)                                                                 
($3,540)                                                 ($1.04)
-------                                                                   
-------                                                   ------

Site Operating Costs
--------------------

Mining                                                       
($89,138)                                                 ($26.24)
------                                                        
--------                                                   -------

Milling                                                      
($66,004)                                                 ($19.34)
-------                                                       
--------                                                   -------

G&A                                                          
($23,380)                                                  ($6.85)
---                                                           
--------                                                    ------

Total  Site Operating                                                  
($178,522)                                                ($52.32)
---------------------                                                   
---------                                                  -------

Net Operating Cash Flow                                                  
$206,118                                                   $60.40
-----------------------                                                  
--------                                                   ------

Initial Capital Costs
---------------------

Mining                                                         (2,500)
------                                                          ------
Milling                                                       (15,300)
-------                                                        -------

G&A and Infrastructure                                        (12,460)
----------------------                                         -------

Working Capital                                                (6,000)
---------------                                                 ------

Total Initial Capital                                         
(36,260)                                                 ($10.63)
---------------------                                          
-------                                                   -------

Sustaining Capital Costs
------------------------

Mining                                                       ($26,265)
------                                                        --------

Milling                                                             $0
-------                                                            ---

Infrastructure                                                (5,025)
--------------                                                 ------

Total Sustaining Capital                                     
($31,290)                                                  ($9.17)
------------------------                                      
--------                                                    ------

Closure
-------

Salvage Value                                                      500
-------------                                                      ---

Recoup of Working Capital                                        6,000
-------------------------                                        -----

Total Closure Capital                                           
$6,500                                                     $1.90
---------------------                                           
------                                                     -----

Total Capital                                                           
($61,050)                                                ($17.89)
-------------                                                            
--------                                                  -------

Reclamation                                                    (3,000)      
(3,000)                                                 ($0.88)
-----------                                                     ------        
------                                                   ------

Net Cash Flow - Pre Tax                                                  
$142,068                                                   $41.63
-----------------------                                                  
--------                                                   ------

Environmental Fee                                               ($533)
-----------------                                                -----

Mining Royalty                                               ($14,143)
--------------                                                --------

Income Tax                                                   ($39,480)    
($53,415)
----------                                                    --------      
--------

Net Cash Flow - After Tax                                                 
$88,653                                                   $25.98
-------------------------                                                 
-------                                                   ------

Total cash cost  (Opex, smelter, NSR and Sustaining 
Capital)                         ($90.54)  per tonne

($12.72)  per oz Ag Eq
-------   ------------
San Felipe NPV and IRR - Base Case   $USM
-----------------------------------------

Pre-Tax NPV         After Tax NPV
-----------         -------------

Discount Rate 0%                                       142.1                 
88.7
---------------                                          -----                 
----

2%              125.0                 76.4
---               -----                 ----

5%              103.5                 61.2
---               -----                 ----

8%               86.1                 48.9
---                ----                 ----

10%               76.3                 42.0
---                ----                 ----

IRR                                                       60.6                 
37.7
---                                                       ----                 
----

Payback (years)                                            1.6                  
2.3
--------------                                             ---                  
---
Note: These tables are in part based on inferred mineral resources which
are considered too speculative geologically to have the economic
considerations applied to them that would enable them to be categorized as
mineral reserves.
(x)The after tax calculation considers the new Mexican tax regime including
a 0.5% environmental fee for gold/silver/platinum, a 7.5% royalty and
depreciation and amortization annually at a 10% rate.
Risks and Opportunities
The San Felipe project is subject to the usual risks that comparable
mining projects face, including decreases in metal prices, increases in costs
and changes in mineral title law and taxation. Mexico is considered a
reasonably stable country and recent changes in taxation are incorporated in
the PEA model. Santacruz has a good relationship with the community of San
Felipe and has an agreement regarding surface land-use with the local Ejido.
As mentioned above, the PEA is based in part on inferred mineral resources
which are too speculative geologically to have the economic considerations
applied to them that would enable them to be categorized as mineral reserves.
Geotechnical analysis of the rock mass indicates potentially difficult ground
conditions. The continuity of higher-grades at a stope scale has not been
confirmed. The first year of open pit production is modeled almost entirely on
inferred resources and there is limited metallurgical information and no
geotechnical information to support this part of the model.
Opportunities include:
<<

--  Higher metal prices - Increases in metal prices from those modeled
results in significant increases in NPV and IRR;
--  Higher grades - The grade of material mined may be higher if
mineralization is continuous at a stope scale, resulting in decreased
dilution and increased mining recovery;
--  Increased resource in mine plan - Any combination of higher metal
prices, lower costs, higher recovery or decreased dilution will result
in more of the current resource being potentially economic;
--  Resource expansion - the San Felipe vein area is open as is the
Transversales vein. Recent exploration has identified new vein targets;
--  Copper extraction - Copper grades average in the range of 0.3 to 0.4%
for the material considered in the PEA. If further testwork can show
that a copper concentrate is possible, it could add to the project
economics.
>>
The effects of changes to various parameters can be seen on the
sensitivity tables below:
San Felipe Project Preliminary Economic Assessment 2014 - Sensitivities:
Metal Prices
------------

-20%    -10%  Base                +10%       +20%
---      ---   ----                 ---         ---

Ag          15.93    17.92            19.91      21.90       23.89

Pb           0.79     0.89             0.99       1.09        1.19

Zn           0.80     0.90             1.00       1.10        1.20

NPV 5% $US M      pre-tax      28.7     66.1            103.5      140.9       
178.3

after-tax    11.8     36.5             61.2       85.8       110.5

IRR %           pre-tax     22.3%   42.1%           60.6%     78.6%      96.4%

after-tax   12.1%   25.5%           37.7%     49.4%      60.8%


Operating Cost
--------------

+20%    +10%  Base                -10%       -20%
---      ---   ----                 ---         ---

NPV 5% $US M      pre-tax      75.8     89.6            103.5      117.3       
131.2

after-tax    42.6     51.9             61.2       70.4        79.7

IRR %           pre-tax     47.2%   54.0%           60.6%     67.3%      73.8%

after-tax   28.6%   33.2%           37.7%     42.2%      46.6%


Capital Cost
------------

+20%    +10%  Base                -10%       -20%
---      ---   ----                 ---         ---

NPV 5% $US M      pre-tax      92.0     97.7            103.5      109.2       
115.0

after-tax    52.5     56.8             61.2       65.5        69.8

IRR %           pre-tax     47.4%   53.5%           60.6%     69.3%      80.0%

after-tax   29.3%   33.2%           37.7%     43.2%      49.8%
---------    ----     ----             ----       ----        ----
Note: This table is in part based on Inferred Mineral Resources which are
considered too speculative geologically to have the economic considerations
applied to them that would enable them to be categorized as Mineral Reserves.
Mineral resources that are not mineral reserves do not have demonstrated
economic viability.Mineral Resources:
Giroux Consultants Ltd. completed the mineral resource estimate on the
San Felipe Project on six separate mineralized structures drilled to date: the
La Ventana, the Las Lamas, the San Felipe, the two San Felipe hangingwall
structures and the Transversales vein. The new mineral resource estimate was
utilized in preparation of the PEA.
A summary of the new resource at various cut-offs is given in the table
below. The San Felipe vein and two hangingwall structures are combined in the
table. In addition to silver, lead and zinc, the veins contain low amounts of
copper and anomalous gold. Since testwork has not been able to produce an
economic copper concentrate and gold values are too low to be significant, the
values for these metals have not been considered at this time.

San Felipe Project Resource July 2014

Vein             Classification   Cut-off            Tonnes > 
Cut-off               Grades > Cut-off

AgEq (g/t)               (tonnes)
---                                             ----------               -------

Ag (g/t)               Pb (%)       Zn (%)    AgEQ (g/t)                    
AgEq Ozs.
--------               -----         -----      ----------                    
---------

Ventana                Indicated                        125    893,000        
69.03   2.79        6.43              434.11 12,464,000
-------                ---------                        ---    -------        
-----   ----        ----              ------ ----------

Las Lamas              Indicated                        125     98,000        
71.14   0.23        4.90              265.66    837,000
---------              ---------                        ---     ------        
-----   ----        ----              ------    -------

San Felipe             Indicated                        125    223,000        
86.55   1.59        4.94              326.66  2,342,000
----------             ---------                        ---    -------        
-----   ----        ----              ------  ---------

Total                  Indicated                        125  1,214,000        
72.42   2.36        6.03              400.77 15,643,000
-----                  ---------                        ---  ---------        
-----   ----        ----              ------ ----------

Ventana                Inferred                         125  1,582,000        
55.48   2.46        5.56              373.14 18,979,000
-------                --------                         ---  ---------        
-----   ----        ----              ------ ----------

Las Lamas              Inferred                         125    402,000        
92.72   0.35        5.36              309.24  3,997,000
---------              --------                         ---    -------        
-----   ----        ----              ------  ---------

San Felipe             Inferred                         125  1,355,000        
55.90   1.43        3.67              244.20 10,638,000
----------             --------                         ---  ---------        
-----   ----        ----              ------ ----------

Transversales          Inferred                         125    662,000        
49.74   1.45        2.09              182.78  3,890,000
-------------          --------                         ---    -------        
-----   ----        ----              ------  ---------

Total                  Inferred                         125  4,001,000        
58.41   1.73        4.33              291.56 37,504,000
-----                  --------                         ---  ---------        
-----   ----        ----              ------ ----------


Ventana                Indicated                        150    826,000        
73.04   2.92        6.81              458.27 12,170,000
-------                ---------                        ---    -------        
-----   ----        ----              ------ ----------

Las Lamas              Indicated                        150     84,000        
76.18   0.25        5.29              286.28    773,000---------              
---------                        ---     ------        
-----   ----        ----              ------    -------

San Felipe             Indicated                        150    208,000         
90.6   1.65        5.15              340.66  2,278,000
----------             ---------                        ---    -------         
----   ----        ----              ------  ---------

Total                  Indicated                        150  1,118,000        
76.54   2.48        6.39              423.47 15,221,000
-----                  ---------                        ---  ---------        
-----   ----        ----              ------ ----------

Ventana                Inferred                         150  1,443,000        
58.97   2.59        5.92              395.94 18,369,000
-------                --------                         ---  ---------        
-----   ----        ----              ------ ----------

Las Lamas              Inferred                         150    383,000        
95.27   0.36         5.5              317.54  3,910,000
---------              --------                         ---    -------        
-----   ----         ---              ------  ---------

San Felipe             Inferred                         150    987,000        
66.15   1.55        4.36              284.01  9,012,000
----------             --------                         ---    -------        
-----   ----        ----              ------  ---------

Transversales          Inferred                         150    460,000        
54.97   1.66        2.27              202.82  3,000,000
-------------          --------                         ---    -------        
-----   ----        ----              ------  ---------

Total                  Inferred                         150  3,273,000        
64.82   1.88        4.89              325.87 34,291,000
-----                  -----
---                         ---  ---------        
-----   ----        ----              ------ ----------


Ventana                Indicated                        175    764,000        
77.29   3.05        7.18               482.1 11,842,000
-------                ---------                        ---    -------        
-----   ----        ----               ----- ----------

Las Lamas              Indicated                        175     70,000        
81.98   0.27        5.77              311.19    700,000
---------              ---------                        ---     ------        
-----   ----        ----              ------    -------

San Felipe             Indicated                        175    192,000        
95.17    1.7        5.39              355.74  2,196,000
----------             ---------                        ---    -------        
-----    ---        ----              ------  ---------

Total                  Indicated                        175  1,026,000        
80.96   2.61        6.75              446.79 14,738,000
-----                  ---------                        ---  ---------        
-----   ----        ----              ------ ----------

Ventana                Inferred                         175  1,327,000        
62.17    2.7        6.24              416.36 17,764,000
-------                --------                         ---  ---------        
-----    ---        ----              ------ ----------

Las Lamas              Inferred                         175    356,000        
98.63   0.37        5.71              329.13  3,767,000
---------              --------                         ---    -------        
-----   ----        ----              ------  ---------

San Felipe             Inferred                         175    798,000        
73.26   1.63        4.88              312.88  8,027,000
----------             --------                         ---    -------        
-----   ----        ----              ------  ---------

Transversales          Inferred                         175    309,000        
58.37   1.87         2.5                 223  2,215,000
-------------          --------                         ---    -------        
-----   ----         ---                 ---  ---------

Total                  Inferred                         175  2,790,000        
69.57   2.00        5.37              354.22 31,773,000
-----                  --------                         ---  ---------        
-----   ----        ----              ------ ----------


Ventana                Indicated                        200    721,000        
80.53   3.14        7.46              499.88 11,588,000
-------                ---------                        ---    -------        
-----   ----        ----              ------ ----------

Las Lamas              Indicated                        200     59,000        
89.50   0.30        6.17              334.94    635,000
---------              ---------                        ---     ------        
-----   ----        ----              ------    -------

San Felipe             Indicated                        200    175,000       
100.12   1.75        5.65              372.07  2,093,000
----------             ---------                        ---    -------       
------   ----        ----              ------  ---------

Total                  Indicated                        200    955,000        
84.67   2.71        7.05              466.27 14,316,000
-----                  ---------                        ---    -------        
-----   ----        ----              ------ ----------

Ventana                Inferred                         200  1,220,000        
65.34   2.83        6.54              436.41 17,118,000
-------                --------                         ---  ---------        
-----   ----        ----              ------ ----------

Las Lamas              Inferred                         200    322,000       
103.55   0.39        5.96              344.41  3,566,000
---------              --------                         ---    -------       
------   ----        ----              ------  ---------

San Felipe             Inferred                         200    629,000        
83.24   1.69        5.49              347.03  7,018,000
----------             --------                         ---    -------        
-----   ----        ----              ------  ---------

Transversales          Inferred                         200    200,000        
58.74   2.19        2.64              241.34  1,552,000
-------------          --------                         ---    -------        
-----   ----        ----              ------  ---------

Total                  Inferred                         200  2,371,000        
74.72   2.14        5.85              383.75 29,253,000
-----                  --------                         ---  ---------        
-----   ----        ----              ------ ----------
Since the veins contain different metals, a silver equivalent value
cut-off is given in the resource tables to better compare value. The metal
prices used in the silver equivalent estimation are from a 100 day moving
average as of June 3, 2014 and are listed below.
Factor

Ag                     -   US$ 20.06 per ounce   0.64 $/g

Pb                     -   US$ 0.96 per pound              21.16 $/%

Zn                     -   US$ 0.92 per pound              20.28 $/%
The recoveries used in the resource estimation for each metal within each
vein are shown below.
Vein                       Ag Rec.     Pb Rec.     Zn Rec.

Ventana                            70%         86%         87%

Las Lamas                          73%         82%         88%

San Felipe & Transversales         69%         86%         79%
The equation used to establish Ag Equivalent is:
AgEq (equal sign) (Pb% (x) 21.16 (x) Pb Rec%) + (Ag g/t  (x) 0.64 (x) Ag Rec%) 
+ (Zn% (x) 20.28 (x) Zn Rec%)
------------------------------------------------------------------------------

(0.64 (x) Ag Rec%)
Metal prices and recoveries used for the resource are different than
those used in the PEA because the resource was completed earlier than the PEA.
The new San Felipe mineral resource estimate is supported by 55,050 metres of
drilling in 260 drill holes with a total of 11,526 assays. The holes include
those drilled by Santacruz in 2013 and by prior operators in the period 1999
to 2000 and 2006 to 2008. The mineral resources were defined to a maximum
depth of approximately 450 metres below surface with a total of 1,106
down-hole surveys utilized for control.
The resource estimate was completed by Gary Giroux, P.Eng. and utilized a
geological model completed by Hans Smit, P.Geo and Fletcher Bourke, P.Geo. The
geological model has six domains; two at La Ventana (HG, LG), Transverales
(VT), three at San Felipe (SF, HW-1, HW-2) and one at Las Lamas (LL). Assays
for each domain were examined and a top cap was applied to each variable
within each domain. Uniform 2 m composites were formed for the domain
envelopes. Variography was completed for all domains in the La Ventana and Las
Lamas zones. Due to insufficient composites in the VT, SF and HW-2 domains,
variography from the HW-1 domain was used with the orientation changed to fit
the strike and dip of the structures. Grades for all variables were
interpolated into blocks 5 x 2.5 x 5 m using ordinary kriging. For blocks with
multiple domains present, a weighted average was determined for the
mineralized portion. A specific gravity was established for each domain based
on 472 measurements from drill core. Estimated blocks were classified as
Indicated or Inferred based on geologic and grade continuity.
Sampling and Laboratory
The resource is based on holes drilled with HQ-sized core. Core was sawn
in half at site and for all drill campaigns one half sent to ALS Chemex, a
fully accredited and certified laboratory service. Samples were prepared at
the ALS Chemex facility in Hermosillo, Mexico, and were then assayed at ALS
Chemex in Vancouver, Canada. All samples were analysed using a one assay ton
fire assay with an AA finish for Au (Au-AA23) and a 48 element ICP method for
other elements (ME-MS61). Samples with silver results above 100 g/t by
(ME-MS61) were rerun using an aqua regia digestion and ICP-AES or AAS finish
(Ag-OG62). A comprehensive QA/QC procedure was followed using standards,
blanks and duplicates.
Qualified Persons
All scientific and technical information included in this press release
has been reviewed and approved by Gary Giroux, P.Eng., Gregory Blaylock,
P.Eng., P.E., JDS Energy & Mining Inc., Deepak Malhotra, SME Registered
Member, Fletcher Bourke, P.Geo., and Hans Smit, P.Geo who are all independent
of the Company and each of whom is a qualified person, pursuant to the meaning
of such terms in NI 43-101.
Verification
The data in the PEA has been verified by a QP and a full description of
the verified data will be available in the report that will be filed within 45
days.
About Santacruz Silver Mining Ltd.
Santacruz is a Mexican focused silver company with a producing mine
(Rosario); two advanced-stage projects (San Felipe and Gavilanes) and an
early-stage exploration project (El Gachi). The Company is managed by a
technical team of professionals with proven track records in developing,
operating and discovering silver mines in Mexico. Our corporate objective is
to become a mid-tier silver producer.
'signed'
Arturo Préstamo Elizondo,President, Chief Executive Officer and Director
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Forward looking information
Certain statements contained in this news release, such as planned
production levels, exploration programs, mining methods, capital and operating
cost estimates, metal prices, tax rates, permitting, future studies and the
Company's future plans and cash flow position, constitute "forward-looking
information" as such term is used in applicable Canadian securities laws.
Forward-looking information is based on plans, expectations and estimates of
management at the date the information is provided and is subject to certain
factors and assumptions, including, but not limited to, certain assumptions as
to production rate, capital and operating costs, recoveries and metal costs,
that the Company's financial condition and development plans do not change as
a result of unforeseen events, that any additional financing needed will be
available on reasonable terms, that the exchange rates for Canadian, Mexican
and U.S. currencies will be consistent with the Company's expectations, that
requisite regulatory approvals and permits will be obtained in a timely manner
and on acceptable terms, that future metal prices and the demand and market
outlook for metals will be sustained or will improve and that general business
and economic conditions will not change in a materially adverse manner.
Forward-looking information is subject to a variety of risks and uncertainties
and other factors that could cause plans, estimates and actual results to vary
materially from those projected in such forward-looking information. Factors
that could cause the forward-looking information in this news release to
change or to be inaccurate include, but are not limited to, the risk that any
of the assumptions referred to prove not to be valid or reliable, that
occurrences such as those referred to above are realized and result in delays,
or cessation in planned work, that the Company's financial condition and
development plans change, delays in regulatory approval, risks associated with
the interpretation of data, the geology, grade and continuity of mineral
deposits, the possibility that results will not be consistent with the
Company's expectations, as well as the other risks and uncertainties
applicable to mineral exploration and development activities and to the
Company as set forth in the Company's Annual Information Form filed under the
Company's profile at www.sedar.com. There can be no assurance that any
forward-looking information will prove to be accurate, as actual results and
future events could differ materially from those anticipated in such
statements. Accordingly, the reader should not place any undue reliance on
forward-looking information or statements. The Company undertakes no
obligation to update forward-looking information or statements, other than as
required by applicable law.
SOURCE SantaCruz Silver Mining Ltd.



To view this news release in HTML formatting, please use the following 
URL:http://www.newswire.ca/en/releases/archive/September2014/11/c1998.html

-0-                           09/11/2014
/For further information: Neil MacRae, Santacruz Silver Mining Ltd.,
Email: info(at)santacruzsilver.com, Telephone: (604) 569-1609/
(SCZ.)

CO:  SantaCruz Silver Mining Ltd.
ST:  British Columbia
IN:  MIN