Source	Marketwire
Date	09/15/2014
Time	04:30:57 AM

Company	 TERRAX MINERALS INC.
Title	TerraX Drills 2.85 m @ 33.60 g/t Au, 3.07 m @ 13.84 g/t Au and 5.10 m @ 
7.01 g/t Au Near Surface at Crestaurum, Yellowknife City Gold Project





    CDNX Symbol: TXR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
PINKSHEETS SYMBOL: TRXXF

September 15, 2014

TerraX Drills 2.85 m @ 33.60 g/t Au, 3.07 m @ 13.84 g/t Au and 5.10 m @ 7.01 
g/t Au Near Surface at Crestaurum, Yellowknife City Gold Project


YELLOWKNIFE, NORTHWEST TERRITORIES--(Marketwired - Sept. 15, 2014) - TerraX 
Minerals Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(OTC PINK:TRXXF) has received 
assay results from nine holes (810.5 m) drilled during the recently completed 
summer drill program on the Crestaurum deposit, one of numerous gold 
occurrences on the Northbelt Property, Yellowknife City Gold Project. 
High-grade gold was intercepted near surface in several holes, with mineralized 
intersections encountered from as little as 5 metres to no more than 70 metres 
vertically below surface. Highlights include:

/T/

--  2.85 m @ 33.60 g/t Au in hole TNB14-019,
--  3.07 m @ 13.84 g/t Au in hole TNB14-015; and
--  5.10 m @ 7.01 g/t Au in hole TNB14-022

/T/

Of the nine holes reported today, four holes (TNB14-0015 to 018) were drilled 
into the South Shoot; two holes (TNB14-019 and 020) were drilled 1 km north 
along strike in the North Shoot; one hole (TNB14-021) was drilled 125 m further 
north along strike in the North Extension Shoot; and two holes (TNB14-022 and 
023) were step-out holes drilled a further 65 m north, intercepting high-grade 
gold mineralization and extending the strike length of the North Extension 
Shoot. During surface exploration in 2013 and 2014, sampling by TerraX has 
indicated that the Crestaurum shear extends up to 650 m to the southwest and up 
to 2 km to the northeast of the area of the historic Crestaurum deposit for an 
overall potential strike length of over 4 km. In addition, many new oblique and 
high angle gold veins were identified and sampled this summer near the main 
Crestaurum zone as well as the nearby (less than 1.5 km) Barney structure that 
could be indicative of gold bearing vein sets common to large mineralized 
systems. A map showing the locations of the drill results reported today will 
soon be available on our web site at www.terraxminerals.com.

/T/

Crestaurum Summer 2014 Drill Results
----------------------------------------------------------------------------
UTM Location (NAD                 From     To Interval     Au
Drill Hole            83)         Azimuth  Dip    (m)    (m)      (m)    g/t
------------------
Easting  Northing
----------------------------------------------------------------------------
TNB14-015       635641   6941546      302  -45  70.40  73.47     3.07  13.84
----------------------------------------------------------------------------
TNB14-016       635641   6941546      302  -68  73.00  76.60     3.60   4.48
----------------------------------------------------------------------------
TNB14-017       635604   6941576      306  -45  29.50  33.44     3.94   0.91
----------------------------------------------------------------------------
TNB14-018       635582   6941529      314  -60  36.00  38.33     2.33   3.21
----------------------------------------------------------------------------
TNB14-019       636008   6942149      310  -45  49.00  51.85     2.85  33.60
----------------------------------------------------------------------------
TNB14-020       635939   6942093      296  -45  31.00  32.78     1.78   1.38
----------------------------------------------------------------------------
TNB14-021       636051   6942266      311  -45   8.50  10.50     2.00   3.66
----                                ------------------------------
and                                  50.98  57.20     6.22   4.34
----                                ------------------------------
incl                                  50.98  53.74     2.76   7.52
----------------------------------------------------------------------------
TNB14-022       636079   6942322      299  -49  27.22  28.10     0.88   1.65
----                                ------------------------------
and                                  49.28  58.28     9.00   4.69
----                                ------------------------------
incl                                  49.28  54.38     5.10   7.01
----------------------------------------------------------------------------
TNB14-023       636079   6942322      298  -65  33.50  34.32     0.82   1.65
----                                ------------------------------
and                                  53.00  57.40     4.40   2.18
----                                ------------------------------
and                                  68.50  70.00     1.50   3.79
----------------------------------------------------------------------------

/T/

Drill holes were all drilled approximately normal to the interpreted strike and 
dip of the mineralized zone, and the mineralized intersections reported today 
represent approximately 93-100% of true thicknesses of the zone.

In 2013, TerraX recovered core from 74 drill holes drilled by Giant Mines Ltd. 
in 1985 to assist them in open-pit and underground planning on the Crestaurum 
deposit. TerraX was able to re-sample and re-assay this core, with assay 
results that included 5.00 m @ 62.90 g/t Au (news release Oct 2, 2013). A 
further 117 holes were drilled into the Crestaurum Zone between 1945 and 1980 
over a strike length of 1.4 km for which drill collar locations were found in 
the field but for which no drill core has been recovered by TerraX. Based on 
this information, TerraX drilled a total of 12 holes this year (three in winter 
and nine this summer) to verify historical information from drill logs and 
possibly allow these 117 drill holes to be incorporated into a future NI 43-101 
resource estimate.

TerraX previously released assay results for the three Crestaurum holes (see 
news release June 2, 2014) that were drilled in the 2014 winter program, 
including 10.02 m @ 4.17 g/t Au inclusive of 2.89 m @ 10.88 g/t Au in hole 
TNB14-011 and 1.47 m @ 8.73 g/t Au in TNB14-006.

TerraX collected 370 samples for assay from the summer Crestaurum drilling 
program. Results for gold ranged from below detection to highs of 100.0 g/t Au.

Drill hole collar locations were surveyed to sub-meter accuracy. Down hole 
surveying (Easy Shot) was completed on all holes. Core sampling included 
insertion of certified standards and blanks. Drill core samples are cut by 
diamond saw at TerraX's core facilities in Yellowknife. A halved core sample is 
left in the core box. The other half core is sampled and transported by TerraX 
personnel in securely sealed bags to ALS Chemex's preparation laboratory in 
Yellowknife. After sample preparation, samples are shipped to ALS Chemex's 
Vancouver facility for gold and ICP analysis. Gold assays of greater than 3 g/t 
are re-assayed on a 30 gm split by fire assay with a gravimetric finish. ALS is 
a certified and accredited laboratory service. ALS routinely inserts certified 
gold standards, blanks and pulp duplicates, and results of all QC samples are 
reported.

The technical information contained in this news release has been approved by 
Joseph Campbell, the President of TerraX, who is a Qualified Person as defined 
in "National Instrument 43-101, Standards of Disclosure for Mineral Projects".

About the Yellowknife City Gold Project

The Yellowknife City Gold Project encompasses 93.5 sq km of contiguous land 
immediately north of the City of Yellowknife in the Northwest Territories and 
includes TerraX's wholly-owned Northbelt property acquired in February 2013.

The project lies on the prolific Yellowknife greenstone belt and covers 15 km 
of strike length on the northern extension of the shear system that hosts the 
high-grade Con and Giant gold mines. The project area contains multiple shears 
that are the recognized hosts for gold deposits in the Yellowknife gold 
district, with innumerable gold showings and historic high grade drill results. 
Since January 2013, TerraX has consolidated the project area by acquiring and 
optioning numerous properties, including: Northbelt, Goodwin, Ryan Lake, Walsh 
Lake, and U-Breccia, as well as staking additional contiguous lands. Being 
all-season road accessible and within 15 km of the City of Yellowknife, the 
YCPG is close to vital infrastructure, including transportation, service 
providers, hydro-electric power and skilled trades people.

For more information on the Yellowknife City Gold Project, please visit our web 
site at www.terraxminerals.com.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

Paradox Public Relations
514-341-0408
Toll Free: 1-866-460-0408
info@paradox-pr.ca

or

Vanguard Shareholder Solutions
604-608-0824
Toll Free: 1-866-801-0779
ir@vanguardsolutions.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=498756501