Source	Marketwire
Date	09/15/2014
Time	04:00:59 AM

Company	 NEWSTRIKE CAPITAL INC.
Title	Newstrike Capital Reports Robust PEA on Ana Paula Project





    CDNX Symbol: NES











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Newstrike Capital Inc.

TSX VENTURE SYMBOL: NES

September 15, 2014

Newstrike Capital Reports Robust PEA on Ana Paula Project

Pre-tax NPV@5% of U.S.$405.3 Million and IRR of 47.5%

Average Annual Gold Production of 116,000 Ounces; All-In Sustaining Costs of US 
$567/Au oz

VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 15, 2014) -

NOT FOR DISTRIBUTION TO U.S. NEWS WIRE SERVICES OR DISSEMINATION IN THE UNITED 
STATES

Newstrike Capital Inc. ("NES" or the "Company) (TSX VENTURE:NES) reports the 
results of an independent technical report developed in accordance with CIM 
guidelines for a National Instrument 43-101 Preliminary Economic Assessment 
("PEA") on its Ana Paula Project ("Ana Paula" or the "Project") located in the 
prolific Guerrero Gold Belt, Mexico.

This study indicates that Ana Paula is a robust, high margin, rapid payback, 
8.2-year open pit mining project that benefits from high gold grades with a low 
strip ratio. The Ana Paula project has excellent access to infrastructure and 
is located in an established mining jurisdiction.

The PEA study was prepared by JDS Energy & Mining Inc., under the direction of 
Thomas H. Bagan, Vice President, Project Development (Newstrike).

The reader is advised that the preliminary economic assessment summarized in 
this press release is only intended to provide an initial, high-level review of 
the project. The PEA mine plan and economic model include the use of inferred 
mineral resources which are considered too speculative geologically to have the 
economic considerations applied to them that would enable them to be 
categorized as mineral reserves and there is no certainty that the preliminary 
economic assessment will be realized.

All dollar amounts in this release are stated in US currency.

PEA HIGHLIGHTS

Base Case at $1,300 Au & $20 Ag per ounce

/T/

--  Pre-tax NPV@5% of $405.3 million, IRR of 47.5% with a 2.0 year payback

--  After-tax NPV@5% of $232.1million, IRR of 32.8% with a 2.4 year payback

--  Initial capital costs of $163.9 million (Total life-of mine ("LOM") -
$219.7 includes sustaining/closure costs of $55.8 million and
contingency costs of $36.2 million)

--  Open pit mine with 6,000 tonne per day ("tpd") gravity/flotation/CIL
process plant

--  Cash costs of $527/ oz gold, $486/oz gold Net of By-Product credits

--  All-in sustaining costs ("AISC") of $567/oz gold, $526/oz gold Net of
By-Product credits

--  Average annual production of 116,000 gold ounces and 239,000 silver
ounces over a 8.2 year mine life

--  LOM average head grades of 2.24 g/t gold and 6.89 g/t silver

--  LOM gold and silver recoveries of 75% and 50%, respectively

--  LOM strip ratio of 2.60 to 1 of waste to mineralized material

/T/

"This PEA supports our view Ana Paula is one of the best development-stage gold 
projects in Mexico. It is a straightforward open pit mine, utilizing 
conventional milling and flotation concentration with robust economics. The 
combination of high gold grades, low capital requirements with low operating 
costs makes this a compelling development project," commented Richard Whittall, 
President and CEO of Newstrike. "With a positive PEA in hand, our next step is 
to evaluate the significant underground potential at Ana Paula and to support 
high priority exploration targets in this prolific gold belt."

In management's view, the economics concluded by the PEA provide a strong 
incentive for continued geotechnical, metallurgical and engineering studies. 
Newstrike believes there are excellent opportunities to refine various project 
elements and improve the economics through gold recovery optimization.

PEA SUMMARY OF RESULTS

/T/


---------------------------------------------------------
Mine Life                           Years             8.2
Total Resource                   M tonnes            17.8
Total Waste                      M tonnes            33.6
Total Capitalized Waste          M tonnes            12.5
---------------------------------------------------------
Total Mined                      M tonnes            63.9
---------------------------------------------------------

---------------------------------------------------------
Strip Ratio                          w:mr            2.60
Mining Rate                           tpd          23,385
Plant Throughput                      tpd           6,000
---------------------------------------------------------

Average Head Grades
---------------------------------------------------------
Au                                    g/t            2.24
Ag                                    g/t            6.89
---------------------------------------------------------
Payable Metal
---------------------------------------------------------
Au                               LOM k oz             957

k oz/yr             116
---------------------------------------------------------
Ag                               LOM k oz           1,961

k oz/yr             239
---------------------------------------------------------

/T/

SUMMARY OF ECONOMICS AT BASE CASE US$1,300/Oz GOLD

/T/


----------------------------------------------------------------------------
LOM Pre-Tax Cash Flow                                      US $M      $742.6
Avg Pre-Tax Cash Flow per Year                             US $M       $90.4
----------------------------------------------------------------------------
Taxes                                                      US $M      $223.6
----------------------------------------------------------------------------
LOM After-Tax Cash Flow                                    US $M      $519.0
Avg After-Tax Cash Flow per Year                           US $M       $63.2
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Discount Rate                                                             5%
----------------------------------------------------------------------------
Pre-Tax NPV (US$M)                                                    $405.3
Pre-Tax IRR                                                            47.5%
Pre-Tax Payback (Yrs)                                                    2.0
----------------------------------------------------------------------------
After-Tax NPV (US$M)                                                   232.1
After-Tax IRR                                                          32.8%
After-Tax Payback (Yrs)                                                  2.4
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Au Cash Cost (US $/oz)                                               $527.26
Au Cash Cost Net of By-Products (US $/oz)                            $486.29
----------------------------------------------------------------------------
Au Cash Cost incl. Sustaining Capital (US $/oz)                      $566.93
Au Cash Cost Net of By-Products incl. Sustaining Capital (US         $525.97
$/oz)
----------------------------------------------------------------------------

/T/

The PEA mine plan and economic model include the use of inferred resources 
which are considered to be too speculative to be used in an economic analysis 
except as permitted by NI 43-101 for use in PEA's. There is no guarantee that 
inferred resources can be converted to indicated or measured resources and, as 
such, there is no guarantee that the project economics described herein will be 
achieved.

CAPITAL AND OPERATING COSTS SUMMARY

/T/


----------------------------------------------------------------------------
Pre-Production  Sustaining/Closure       LOM
Capital Costs                             ($M)                ($M)      ($M)
----------------------------------------------------------------------------
Capitalized Stripping                     16.7                13.4      30.2
Contractor Mob/Demob                       0.4                 0.4       0.8
Process Plant                             45.7                 2.8      48.5
General Site & Utilities                   5.1                   0       5.1
Laboratory                                 1.5                   0       1.5
Construction Camp                          0.6                   0       0.6
Camp Site (Operations)                     1.5                 0.3       1.8
Administration Facilities                  1.1                 0.2       1.3
Tailings Facility                           13                14.8      27.8
Electrical Supply &
Distribution                              4.6                 0.2       4.8
Water Supply &
Distribution                              1.8                   0       1.8
Royalty Purchase                           2.8                   0       2.8
----------------------------------------------------------------------------
Reclamation/Closure                          0                14.4      14.4
Indirects                                 22.4                   0      22.4
EPCM                                      15.4                   0      15.4
Owners Costs                               4.4                   0       4.4
----------------------------------------------------------------------------
Subtotal                                 137.1                46.5     183.6
----------------------------------------------------------------------------
Contingency (20%)                         26.9                 9.3      36.2
----------------------------------------------------------------------------
Total Capital Costs                      163.9                55.8     219.7
----------------------------------------------------------------------------


---------------------------------------------------------------------
Operating Costs                                             LOM Total
---------------------------------------------------------------------
Resource & Waste Mined for OPEX                  tonnes         51.4M
Pre-Stripping and Capitalized Waste              tonnes         12.5M
Resource Processed                               tonnes         17.8M
Mining+                       US$/t processed     $6.58       $116.7M
Resource Rehandle(i)          US$/t processed     $0.12         $2.1M
Processing                    US$/t processed    $17.75       $315.0M
G&A                           US$/t processed     $2.49        $44.2M
---------------------------------------------------------------------
Total Operating Costs         US$/t processed    $26.93       $478.1M
---------------------------------------------------------------------

+Mining Cost is based on $2.30/t mined
(i)Rehandle Cost is based on $0.50/t rehandled

/T/

SENSITIVITIES

/T/


-------------------------------------------------------------------------
Gold Price US$/oz          $1,000  $1,100  $1,200  $1,300  $1,400  $1,500
-------------------------------------------------------------------------
Pre-Tax NPV5%US$            186.7   259.6   332.4   405.3   478.2   551.1
-------------------------------------------------------------------------
After-Tax NPV5%US$           91.5   138.4   185.2   232.1   278.9   325.8
-------------------------------------------------------------------------
Pre-Tax IRR                 27.8%   34.8%   41.4%   47.5%   53.3%   58.8%
-------------------------------------------------------------------------
After-Tax IRR               17.6%   23.1%   28.1%   32.8%   37.2%   41.4%
-------------------------------------------------------------------------
Pre-Tax Payback Yrs           2.6     2.4     2.1     2.0     1.8     1.6
-------------------------------------------------------------------------
After-Tax Payback Yrs         3.3     2.9     2.6     2.4     2.2     2.1
-------------------------------------------------------------------------

/T/

As shown above, the Project has the potential to provide investors with 
commodity resilience as well as significant leverage to movements in the gold 
price.

PROJECT DESCRIPTION

The Ana Paula Project is located in the Guerrero Gold Belt in the State of 
Guerrero, Mexico, roughly half way between the cities of Mexico City and 
Acapulco. Mexico is a favourable jurisdiction for mining investment with 
clearly established mining law and regulatory due process as demonstrated by 
the existence of operating gold mines such as Goldcorp's Los Filos, located in 
close proximity to Ana Paula. Furthermore, Torex Gold's El Limon/Guajes Mine is 
currently under construction in close proximity to the Project. Ana Paula is 
close to all necessary infrastructure including water, road, power, and people.

Mining is via conventional open pit mining methods. Mining will be contracted 
so no capital is included for mining equipment, instead contractor mining rates 
used as the basis for mining costs.

Open pit mining costs were calculated from first principles based on equipment 
required and include pit and dump operations, road maintenance, mine 
supervision and technical services cost.

PREPARATION OF PEA

The PEA was independently prepared by JDS Energy & Mining Inc. ("JDS") of 
Tucson, Arizona. A technical report following the guidelines of the Canadian 
Securities Administrators' National Instrument 43-101 will be filed on SEDAR 
and on the Newstrike Capital's Inc. website within 45 days.
The PEA is based on a mineral resource estimate prepared by Independent Mining 
Consultants, Inc., Tucson Arizona, USA. This mineral resource estimate has been 
developed under the direction of Mr. H. E. Welhener. The resource is based on 
223 diamond core drillholes aggregating 108,832 metres and containing 77,183 
assay intervals, of which effectively all are assayed for gold and silver. The 
mineral resource estimate has an effective date of August 8th, 2014.

The tonnage and grades of the Ana Paula mineral resource(i) at a 0.46 g/t AuEq 
cutoff are shown in the table below:

/T/

----------------------------------------------------------------------------
Category                                                Contained Ounces
----------------------------------------------------------------------------
AuEq,       Au,       Ag,
k tonnes       g/t       g/t       g/t        Gold      Silver
----------------------------------------------------------------------------
Measured        27,767     1.661     1.608      4.90   1,176,748   3,587,101
----------------------------------------------------------------------------
Indicated       18,243     1.229     1.163      5.95     682,243   3,488,565
----------------------------------------------------------------------------
Sum M&I         41,010     1.469     1.410      5.37   1,858,991   7,075,666
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Inferred         1,904     1.233     1.113     10.85      68,145     664,484
----------------------------------------------------------------------------

(i)The resources are classified according to their proximity to sample
locations and are reported, as required by NI 43-101, according to the CIM
Definition Standards for Mineral Resources and Mineral Reserves.
Notes and assumptions:
1. Mineral Resources are not Mineral Reserves until they have demonstrated
economic viability
2. Mineral Resources are reported as undiluted
3. Mineral Resources were developed in accordance with CIM (2010) guidelines
4. Mineral Resources are reported using a long-term gold price of $1,450/oz
and silver price of $23/oz
5. Mining costs used are estimated at $1.85/ton plus $0.02/bench below 900m
elevation
6. Processing costs +general and administrative expenses are estimated at
$17.25 per tonne
7. Gold recoveries are estimated at 80%
8. Silver recoveries are estimated at 55%. A silver divisor of 91.7 was used
to calculate equivalent gold. (Silver is assumed to be recovered along with
gold during processing.)
10. Pit slope angles are 55 degrees east-facing, 45 degrees west-facing
11. Resource QP is H. E. Welhener of IMC
12. M&I = measured and indicated, Mt = million tonnes, g/t = grams per
tonne, Moz = million ounces, Au = gold, Ag = silver, AuEq = gold equivalent
13. There can be no assurance that all or any part of this resource will be
converted into a mineral reserve

/T/

PROJECT DEVELOPMENT PLAN

The proposed project concept is to develop a green-fields gold-silver deposit 
with open pit mining and gravity/flotation/CIL process plant with a production 
rate assumed of 6,000 tonnes per day.

The PEA forecasts an 8.2 year mine life and a LOM strip ratio (the ratio of 
waste rock to economic mineralized rock) of 2.60 to 1. A total of 17.8 million 
tonnes of mineralized resource could be mined and processed with 33.6 million 
tons of waste and 12.5 million tonnes of capitalized waste. Some of the waste 
rock would be stockpiled and an undetermined portion may be reclassified as a 
resource at a later date should metallurgical testwork support economic 
viability. Throughout the life-of-mine, an estimated 957,000 ounces of payable 
gold and 2.0 million ounces of payable silver would be produced at an average 
head grade of 2.24 g/t gold and 6.89g/t silver.

METALLURGY AND PROCESSING

A metallurgical testwork program for the PEA was carried out on samples of 
composited drill core selected to represent the first four years of feed to the 
process plant. The composites were made from six rock types and subjected to 
direct cyanidation testing, flotation and gravity concentration followed by 
cyanidation, coarse particle leaching, and mineralogical deportment. The 
composite responded positively to both direct cyanidation and flotation 
concentration followed by cyanidation. Testwork was conducted by ALS Metallurgy 
in Kamloops BC and reported January 31st, 2014.

The flowsheet selected for Ana Paula consists of a tertiary crushing system, 
followed by ball mill grinding and gravity recovery, flotation, disposal of 
flotation tails, leaching of a combined gravity and flotation concentrate, and 
recovery of precious metals by the carbon-in-leach method. This flowsheet is 
commonly used throughout the world.

ENVIRONMENT, PERMITTING AND CORPORATE SOCIAL RESPONSIBILITY

The project area is not within a known environmental protection area. Formal 
environmental baseline studies have not been initiated but will be required to 
obtain the environmental permits for future mining operations. Communication 
with the local community, private land owners and the "Ejido" (cooperative land 
tenure system) was initiated as part of the exploration program.

PEA CONTRIBUTORS

Qualified Persons and QA/QC

The technical information in this news release has been prepared in accordance 
with Canadian regulatory requirements set out in National Instrument 43-101 
("NI 43-101) and reviewed by Mr. Thomas H. Bagan, a Qualified Person. The field 
programs and selection of the metallurgical samples from Ana Paula were carried 
out under the supervision of Dr. Craig Gibson, PhD, CPG, and a Qualified Person 
under NI 43-101.

The PEA was conducted under the overall direction of Mr. Michel Creek, of JDS 
Energy and Mining, Inc. of Tucson Arizona. Mr Creek is a JDS Project Manager 
and an independent "Qualified Person" under NI 43-101 who has verified the 
technical and scientific information and prepared the economic analysis 
included in this news release. There are no known legal, political, 
environmental, or other risks that could materially affect the potential 
development of the Project.

Under Mr. Creek's review, the following Qualified Persons contributed to their 
respective sections:

Kelly McLeod P.Eng, JDS - Mineral Processing and Recovery Methods

Tony Loschiavo P. Eng, Associate, JDS - Mine Design

Dawn Garcia CPG, JDS - Environmental Studies, Permitting, & Social

Robert Matter P.E., JDS - Infrastructure and Tailings

About Newstrike Capital (TSX VENTURE:NES)

Newstrike Capital Inc., www.newstrikecapital.com, is a precious metal focused 
explorer, targeting known and historic mining districts in Mexico. Newstrike's 
flagship property, 'Ana Paula', is an advanced-stage, high grade, near surface 
gold/silver resource with robust economics in the Guerrero Gold Belt ("GGB"). 
Key senior members of the Company's current management and directors have 
participated in Guerrero Gold Belt discoveries, including Goldcorp Inc.'s 
producing Los Filos Mine and Torex Gold Resources advanced stage Morelos 
Project in Guerrero State.

Newstrike holds a 100% interest in certain exploration properties in Mexico 
located within two established mining districts; the Au (Ag-Cu) skarn-porphyry 
camp of the Guerrero Gold Belt, and the polymetallic Pb-Zn-Ag (Au-Cu) rich 
epithermal camp of the mining districts of Oaxaca State.

Mr. Thomas H. Bagan, a qualified person under NI43-101, has reviewed the 
contents of this press release. The exploration program is conducted under the 
direction and supervision of Dr. Craig Gibson, PhD, CPG and qualified person 
under NI43-101.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Certain of the statements made in this news release contain forward-looking 
information within he meaning of applicable Canadian securities law. Material 
forward-looking information includes, but is not limited to statements or 
information with respect to the resource estimate and potential future 
exploration and development results and results of studies in respect of the 
Company's Ana Paula Project. We have made numerous assumptions about the 
material forward-looking information contained herein, including among other 
things, that prices of gold and silver will remain relatively stable, that 
applicable permits will be obtainable and that any required financing will be 
available on reasonable terms. Even though our management believes that the 
assumptions made and the expectations represented by such statements or 
information are reasonable, there can be no assurance that the forward-looking 
statement or information will prove to be accurate.

Forward-looking information by its nature involves known and unknown risks, 
uncertainties and other factors which may cause the actual results to be 
materially different from any future results expressed or implied by such 
forward-looking information. Such risks, uncertainties and other factors 
include, among others, the following: the inherent risks and uncertainty 
involved in the exploration and development of mineral properties; the 
uncertainties involved in interpreting drill results and other exploration 
data; the potential for delays in exploration or development activities; the 
geology, grade and continuity of mineral deposits; the possibility that future 
exploration, development or mining results will not be consistent with the 
Company's expectations; accidents, equipment breakdowns, labor disputes or 
other unanticipated difficulties with or interruptions in production and 
operations; fluctuating prices of metals and other commodities; currency 
fluctuations; the possibility of project cost overruns or unanticipated costs 
and expenses; uncertainties relating to the availability and costs of financing 
needed in the future; the inherent uncertainty of production and cost estimates 
and the potential for unexpected costs and expenses; regulatory restrictions, 
including environmental regulatory restrictions and liability; competition and 
loss of key employees; political instability in Mexico; the availability of key 
equipment; the risk of disruption from non-governmental organizations; risks 
relating to our common shares and the public markets. Should one or more of 
these risks, uncertainties or other factors materialize, or should underlying 
assumptions prove incorrect, actual results may vary materially from those 
described in forward-looking information. Although we have attempted to 
identify factors that would cause actual results to differ materially from 
those described in forward-looking information, there may be other factors that 
cause actual results, performances, achievements or events to not be as 
anticipated, estimated or intended. Also, many of the factors are beyond our 
control. There can be no assurance that forward-looking information will prove 
to be accurate, as actual results and future events could differ materially 
from those anticipated in such statements. Accordingly you should not place 
undue reliance on forward-looking information. Except as required by law, we do 
not expect to update forward-looking information as conditions change and you 
are referred to the full discussion of the Company's business contained in the 
Company's reports filed with the securities regulatory authorities in Canada.

- 30 -

CONTACT INFO:

Newstrike Capital Inc.
Richard Whittall
Director, President & CEO
604-605-4654
www.newstrikecapital.com
Blog: http://newstrikecapital.com/blog

or

Newstrike Capital Inc.
Patrick Piette
Investor Relations
416-526-9911
ppiette@minera.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Newstrike Capital Inc.

TSX VENTURE SYMBOL: NES

September 15, 2014

Newstrike Capital Reports Robust PEA on Ana Paula Project

Pre-tax NPV@5% of U.S.$405.3 Million and IRR of 47.5%

Average Annual Gold Production of 116,000 Ounces; All-In Sustaining Costs of US 
$567/Au oz

VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 15, 2014) -

NOT FOR DISTRIBUTION TO U.S. NEWS WIRE SERVICES OR DISSEMINATION IN THE UNITED 
STATES

Newstrike Capital Inc. ("NES" or the "Company) (TSX VENTURE:NES) reports the 
results of an independent technical report developed in accordance with CIM 
guidelines for a National Instrument 43-101 Preliminary Economic Assessment 
("PEA") on its Ana Paula Project ("Ana Paula" or the "Project") located in the 
prolific Guerrero Gold Belt, Mexico.

This study indicates that Ana Paula is a robust, high margin, rapid payback, 
8.2-year open pit mining project that benefits from high gold grades with a low 
strip ratio. The Ana Paula project has excellent access to infrastructure and 
is located in an established mining jurisdiction.

The PEA study was prepared by JDS Energy & Mining Inc., under the direction of 
Thomas H. Bagan, Vice President, Project Development (Newstrike).

The reader is advised that the preliminary economic assessment summarized in 
this press release is only intended to provide an initial, high-level review of 
the project. The PEA mine plan and economic model include the use of inferred 
mineral resources which are considered too speculative geologically to have the 
economic considerations applied to them that would enable them to be 
categorized as mineral reserves and there is no certainty that the preliminary 
economic assessment will be realized.

All dollar amounts in this release are stated in US currency.

PEA HIGHLIGHTS

Base Case at $1,300 Au & $20 Ag per ounce

/T/

--  Pre-tax NPV@5% of $405.3 million, IRR of 47.5% with a 2.0 year payback

--  After-tax NPV@5% of $232.1million, IRR of 32.8% with a 2.4 year payback

--  Initial capital costs of $163.9 million (Total life-of mine ("LOM") -
$219.7 includes sustaining/closure costs of $55.8 million and
contingency costs of $36.2 million)

--  Open pit mine with 6,000 tonne per day ("tpd") gravity/flotation/CIL
process plant

--  Cash costs of $527/ oz gold, $486/oz gold Net of By-Product credits

--  All-in sustaining costs ("AISC") of $567/oz gold, $526/oz gold Net of
By-Product credits

--  Average annual production of 116,000 gold ounces and 239,000 silver
ounces over a 8.2 year mine life

--  LOM average head grades of 2.24 g/t gold and 6.89 g/t silver

--  LOM gold and silver recoveries of 75% and 50%, respectively

--  LOM strip ratio of 2.60 to 1 of waste to mineralized material

/T/

"This PEA supports our view Ana Paula is one of the best development-stage gold 
projects in Mexico. It is a straightforward open pit mine, utilizing 
conventional milling and flotation concentration with robust economics. The 
combination of high gold grades, low capital requirements with low operating 
costs makes this a compelling development project," commented Richard Whittall, 
President and CEO of Newstrike. "With a positive PEA in hand, our next step is 
to evaluate the significant underground potential at Ana Paula and to support 
high priority exploration targets in this prolific gold belt."

In management's view, the economics concluded by the PEA provide a strong 
incentive for continued geotechnical, metallurgical and engineering studies. 
Newstrike believes there are excellent opportunities to refine various project 
elements and improve the economics through gold recovery optimization.

PEA SUMMARY OF RESULTS

/T/


---------------------------------------------------------
Mine Life                           Years             8.2
Total Resource                   M tonnes            17.8
Total Waste                      M tonnes            33.6
Total Capitalized Waste          M tonnes            12.5
---------------------------------------------------------
Total Mined                      M tonnes            63.9
---------------------------------------------------------

---------------------------------------------------------
Strip Ratio                          w:mr            2.60
Mining Rate                           tpd          23,385
Plant Throughput                      tpd           6,000
---------------------------------------------------------

Average Head Grades
---------------------------------------------------------
Au                                    g/t            2.24
Ag                                    g/t            6.89
---------------------------------------------------------
Payable Metal
---------------------------------------------------------
Au                               LOM k oz             957

k oz/yr             116
---------------------------------------------------------
Ag                               LOM k oz           1,961

k oz/yr             239
---------------------------------------------------------

/T/

SUMMARY OF ECONOMICS AT BASE CASE US$1,300/Oz GOLD

/T/


----------------------------------------------------------------------------
LOM Pre-Tax Cash Flow                                      US $M      $742.6
Avg Pre-Tax Cash Flow per Year                             US $M       $90.4
----------------------------------------------------------------------------
Taxes                                                      US $M      $223.6
----------------------------------------------------------------------------
LOM After-Tax Cash Flow                                    US $M      $519.0
Avg After-Tax Cash Flow per Year                           US $M       $63.2
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Discount Rate                                                             5%
----------------------------------------------------------------------------
Pre-Tax NPV (US$M)                                                    $405.3
Pre-Tax IRR                                                            47.5%
Pre-Tax Payback (Yrs)                                                    2.0
----------------------------------------------------------------------------
After-Tax NPV (US$M)                                                   232.1
After-Tax IRR                                                          32.8%
After-Tax Payback (Yrs)                                                  2.4
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Au Cash Cost (US $/oz)                                               $527.26
Au Cash Cost Net of By-Products (US $/oz)                            $486.29
----------------------------------------------------------------------------
Au Cash Cost incl. Sustaining Capital (US $/oz)                      $566.93
Au Cash Cost Net of By-Products incl. Sustaining Capital (US         $525.97
$/oz)
----------------------------------------------------------------------------

/T/

The PEA mine plan and economic model include the use of inferred resources 
which are considered to be too speculative to be used in an economic analysis 
except as permitted by NI 43-101 for use in PEA's. There is no guarantee that 
inferred resources can be converted to indicated or measured resources and, as 
such, there is no guarantee that the project economics described herein will be 
achieved.

CAPITAL AND OPERATING COSTS SUMMARY

/T/


----------------------------------------------------------------------------
Pre-Production  Sustaining/Closure       LOM
Capital Costs                             ($M)                ($M)      ($M)
----------------------------------------------------------------------------
Capitalized Stripping                     16.7                13.4      30.2
Contractor Mob/Demob                       0.4                 0.4       0.8
Process Plant                             45.7                 2.8      48.5
General Site & Utilities                   5.1                   0       5.1
Laboratory                                 1.5                   0       1.5
Construction Camp                          0.6                   0       0.6
Camp Site (Operations)                     1.5                 0.3       1.8
Administration Facilities                  1.1                 0.2       1.3
Tailings Facility                           13                14.8      27.8
Electrical Supply &
Distribution                              4.6                 0.2       4.8
Water Supply &
Distribution                              1.8                   0       1.8
Royalty Purchase                           2.8                   0       2.8
----------------------------------------------------------------------------
Reclamation/Closure                          0                14.4      14.4
Indirects                                 22.4                   0      22.4
EPCM                                      15.4                   0      15.4
Owners Costs                               4.4                   0       4.4
----------------------------------------------------------------------------
Subtotal                                 137.1                46.5     183.6
----------------------------------------------------------------------------
Contingency (20%)                         26.9                 9.3      36.2
----------------------------------------------------------------------------
Total Capital Costs                      163.9                55.8     219.7
----------------------------------------------------------------------------


---------------------------------------------------------------------
Operating Costs                                             LOM Total
---------------------------------------------------------------------
Resource & Waste Mined for OPEX                  tonnes         51.4M
Pre-Stripping and Capitalized Waste              tonnes         12.5M
Resource Processed                               tonnes         17.8M
Mining+                       US$/t processed     $6.58       $116.7M
Resource Rehandle(i)          US$/t processed     $0.12         $2.1M
Processing                    US$/t processed    $17.75       $315.0M
G&A                           US$/t processed     $2.49        $44.2M
---------------------------------------------------------------------
Total Operating Costs         US$/t processed    $26.93       $478.1M
---------------------------------------------------------------------

+Mining Cost is based on $2.30/t mined
(i)Rehandle Cost is based on $0.50/t rehandled

/T/

SENSITIVITIES

/T/


-------------------------------------------------------------------------
Gold Price US$/oz          $1,000  $1,100  $1,200  $1,300  $1,400  $1,500
-------------------------------------------------------------------------
Pre-Tax NPV5%US$            186.7   259.6   332.4   405.3   478.2   551.1
-------------------------------------------------------------------------
After-Tax NPV5%US$           91.5   138.4   185.2   232.1   278.9   325.8
-------------------------------------------------------------------------
Pre-Tax IRR                 27.8%   34.8%   41.4%   47.5%   53.3%   58.8%
-------------------------------------------------------------------------
After-Tax IRR               17.6%   23.1%   28.1%   32.8%   37.2%   41.4%
-------------------------------------------------------------------------
Pre-Tax Payback Yrs           2.6     2.4     2.1     2.0     1.8     1.6
-------------------------------------------------------------------------
After-Tax Payback Yrs         3.3     2.9     2.6     2.4     2.2     2.1
-------------------------------------------------------------------------

/T/

As shown above, the Project has the potential to provide investors with 
commodity resilience as well as significant leverage to movements in the gold 
price.

PROJECT DESCRIPTION

The Ana Paula Project is located in the Guerrero Gold Belt in the State of 
Guerrero, Mexico, roughly half way between the cities of Mexico City and 
Acapulco. Mexico is a favourable jurisdiction for mining investment with 
clearly established mining law and regulatory due process as demonstrated by 
the existence of operating gold mines such as Goldcorp's Los Filos, located in 
close proximity to Ana Paula. Furthermore, Torex Gold's El Limon/Guajes Mine is 
currently under construction in close proximity to the Project. Ana Paula is 
close to all necessary infrastructure including water, road, power, and people.

Mining is via conventional open pit mining methods. Mining will be contracted 
so no capital is included for mining equipment, instead contractor mining rates 
used as the basis for mining costs.

Open pit mining costs were calculated from first principles based on equipment 
required and include pit and dump operations, road maintenance, mine 
supervision and technical services cost.

PREPARATION OF PEA

The PEA was independently prepared by JDS Energy & Mining Inc. ("JDS") of 
Tucson, Arizona. A technical report following the guidelines of the Canadian 
Securities Administrators' National Instrument 43-101 will be filed on SEDAR 
and on the Newstrike Capital's Inc. website within 45 days.
The PEA is based on a mineral resource estimate prepared by Independent Mining 
Consultants, Inc., Tucson Arizona, USA. This mineral resource estimate has been 
developed under the direction of Mr. H. E. Welhener. The resource is based on 
223 diamond core drillholes aggregating 108,832 metres and containing 77,183 
assay intervals, of which effectively all are assayed for gold and silver. The 
mineral resource estimate has an effective date of August 8th, 2014.

The tonnage and grades of the Ana Paula mineral resource(i) at a 0.46 g/t AuEq 
cutoff are shown in the table below:

/T/

----------------------------------------------------------------------------
Category                                                Contained Ounces
----------------------------------------------------------------------------
AuEq,       Au,       Ag,
k tonnes       g/t       g/t       g/t        Gold      Silver
----------------------------------------------------------------------------
Measured        27,767     1.661     1.608      4.90   1,176,748   3,587,101
----------------------------------------------------------------------------
Indicated       18,243     1.229     1.163      5.95     682,243   3,488,565
----------------------------------------------------------------------------
Sum M&I         41,010     1.469     1.410      5.37   1,858,991   7,075,666
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Inferred         1,904     1.233     1.113     10.85      68,145     664,484
----------------------------------------------------------------------------

(i)The resources are classified according to their proximity to sample
locations and are reported, as required by NI 43-101, according to the CIM
Definition Standards for Mineral Resources and Mineral Reserves.
Notes and assumptions:
1. Mineral Resources are not Mineral Reserves until they have demonstrated
economic viability
2. Mineral Resources are reported as undiluted
3. Mineral Resources were developed in accordance with CIM (2010) guidelines
4. Mineral Resources are reported using a long-term gold price of $1,450/oz
and silver price of $23/oz
5. Mining costs used are estimated at $1.85/ton plus $0.02/bench below 900m
elevation
6. Processing costs +general and administrative expenses are estimated at
$17.25 per tonne
7. Gold recoveries are estimated at 80%
8. Silver recoveries are estimated at 55%. A silver divisor of 91.7 was used
to calculate equivalent gold. (Silver is assumed to be recovered along with
gold during processing.)
10. Pit slope angles are 55 degrees east-facing, 45 degrees west-facing
11. Resource QP is H. E. Welhener of IMC
12. M&I = measured and indicated, Mt = million tonnes, g/t = grams per
tonne, Moz = million ounces, Au = gold, Ag = silver, AuEq = gold equivalent
13. There can be no assurance that all or any part of this resource will be
converted into a mineral reserve

/T/

PROJECT DEVELOPMENT PLAN

The proposed project concept is to develop a green-fields gold-silver deposit 
with open pit mining and gravity/flotation/CIL process plant with a production 
rate assumed of 6,000 tonnes per day.

The PEA forecasts an 8.2 year mine life and a LOM strip ratio (the ratio of 
waste rock to economic mineralized rock) of 2.60 to 1. A total of 17.8 million 
tonnes of mineralized resource could be mined and processed with 33.6 million 
tons of waste and 12.5 million tonnes of capitalized waste. Some of the waste 
rock would be stockpiled and an undetermined portion may be reclassified as a 
resource at a later date should metallurgical testwork support economic 
viability. Throughout the life-of-mine, an estimated 957,000 ounces of payable 
gold and 2.0 million ounces of payable silver would be produced at an average 
head grade of 2.24 g/t gold and 6.89g/t silver.

METALLURGY AND PROCESSING

A metallurgical testwork program for the PEA was carried out on samples of 
composited drill core selected to represent the first four years of feed to the 
process plant. The composites were made from six rock types and subjected to 
direct cyanidation testing, flotation and gravity concentration followed by 
cyanidation, coarse particle leaching, and mineralogical deportment. The 
composite responded positively to both direct cyanidation and flotation 
concentration followed by cyanidation. Testwork was conducted by ALS Metallurgy 
in Kamloops BC and reported January 31st, 2014.

The flowsheet selected for Ana Paula consists of a tertiary crushing system, 
followed by ball mill grinding and gravity recovery, flotation, disposal of 
flotation tails, leaching of a combined gravity and flotation concentrate, and 
recovery of precious metals by the carbon-in-leach method. This flowsheet is 
commonly used throughout the world.

ENVIRONMENT, PERMITTING AND CORPORATE SOCIAL RESPONSIBILITY

The project area is not within a known environmental protection area. Formal 
environmental baseline studies have not been initiated but will be required to 
obtain the environmental permits for future mining operations. Communication 
with the local community, private land owners and the "Ejido" (cooperative land 
tenure system) was initiated as part of the exploration program.

PEA CONTRIBUTORS

Qualified Persons and QA/QC

The technical information in this news release has been prepared in accordance 
with Canadian regulatory requirements set out in National Instrument 43-101 
("NI 43-101) and reviewed by Mr. Thomas H. Bagan, a Qualified Person. The field 
programs and selection of the metallurgical samples from Ana Paula were carried 
out under the supervision of Dr. Craig Gibson, PhD, CPG, and a Qualified Person 
under NI 43-101.

The PEA was conducted under the overall direction of Mr. Michel Creek, of JDS 
Energy and Mining, Inc. of Tucson Arizona. Mr Creek is a JDS Project Manager 
and an independent "Qualified Person" under NI 43-101 who has verified the 
technical and scientific information and prepared the economic analysis 
included in this news release. There are no known legal, political, 
environmental, or other risks that could materially affect the potential 
development of the Project.

Under Mr. Creek's review, the following Qualified Persons contributed to their 
respective sections:

Kelly McLeod P.Eng, JDS - Mineral Processing and Recovery Methods

Tony Loschiavo P. Eng, Associate, JDS - Mine Design

Dawn Garcia CPG, JDS - Environmental Studies, Permitting, & Social

Robert Matter P.E., JDS - Infrastructure and Tailings

About Newstrike Capital (TSX VENTURE:NES)

Newstrike Capital Inc., www.newstrikecapital.com, is a precious metal focused 
explorer, targeting known and historic mining districts in Mexico. Newstrike's 
flagship property, 'Ana Paula', is an advanced-stage, high grade, near surface 
gold/silver resource with robust economics in the Guerrero Gold Belt ("GGB"). 
Key senior members of the Company's current management and directors have 
participated in Guerrero Gold Belt discoveries, including Goldcorp Inc.'s 
producing Los Filos Mine and Torex Gold Resources advanced stage Morelos 
Project in Guerrero State.

Newstrike holds a 100% interest in certain exploration properties in Mexico 
located within two established mining districts; the Au (Ag-Cu) skarn-porphyry 
camp of the Guerrero Gold Belt, and the polymetallic Pb-Zn-Ag (Au-Cu) rich 
epithermal camp of the mining districts of Oaxaca State.

Mr. Thomas H. Bagan, a qualified person under NI43-101, has reviewed the 
contents of this press release. The exploration program is conducted under the 
direction and supervision of Dr. Craig Gibson, PhD, CPG and qualified person 
under NI43-101.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Certain of the statements made in this news release contain forward-looking 
information within he meaning of applicable Canadian securities law. Material 
forward-looking information includes, but is not limited to statements or 
information with respect to the resource estimate and potential future 
exploration and development results and results of studies in respect of the 
Company's Ana Paula Project. We have made numerous assumptions about the 
material forward-looking information contained herein, including among other 
things, that prices of gold and silver will remain relatively stable, that 
applicable permits will be obtainable and that any required financing will be 
available on reasonable terms. Even though our management believes that the 
assumptions made and the expectations represented by such statements or 
information are reasonable, there can be no assurance that the forward-looking 
statement or information will prove to be accurate.

Forward-looking information by its nature involves known and unknown risks, 
uncertainties and other factors which may cause the actual results to be 
materially different from any future results expressed or implied by such 
forward-looking information. Such risks, uncertainties and other factors 
include, among others, the following: the inherent risks and uncertainty 
involved in the exploration and development of mineral properties; the 
uncertainties involved in interpreting drill results and other exploration 
data; the potential for delays in exploration or development activities; the 
geology, grade and continuity of mineral deposits; the possibility that future 
exploration, development or mining results will not be consistent with the 
Company's expectations; accidents, equipment breakdowns, labor disputes or 
other unanticipated difficulties with or interruptions in production and 
operations; fluctuating prices of metals and other commodities; currency 
fluctuations; the possibility of project cost overruns or unanticipated costs 
and expenses; uncertainties relating to the availability and costs of financing 
needed in the future; the inherent uncertainty of production and cost estimates 
and the potential for unexpected costs and expenses; regulatory restrictions, 
including environmental regulatory restrictions and liability; competition and 
loss of key employees; political instability in Mexico; the availability of key 
equipment; the risk of disruption from non-governmental organizations; risks 
relating to our common shares and the public markets. Should one or more of 
these risks, uncertainties or other factors materialize, or should underlying 
assumptions prove incorrect, actual results may vary materially from those 
described in forward-looking information. Although we have attempted to 
identify factors that would cause actual results to differ materially from 
those described in forward-looking information, there may be other factors that 
cause actual results, performances, achievements or events to not be as 
anticipated, estimated or intended. Also, many of the factors are beyond our 
control. There can be no assurance that forward-looking information will prove 
to be accurate, as actual results and future events could differ materially 
from those anticipated in such statements. Accordingly you should not place 
undue reliance on forward-looking information. Except as required by law, we do 
not expect to update forward-looking information as conditions change and you 
are referred to the full discussion of the Company's business contained in the 
Company's reports filed with the securities regulatory authorities in Canada.

- 30 -

CONTACT INFO:

Newstrike Capital Inc.
Richard Whittall
Director, President & CEO
604-605-4654
www.newstrikecapital.com
Blog: http://newstrikecapital.com/blog

or

Newstrike Capital Inc.
Patrick Piette
Investor Relations
416-526-9911
ppiette@minera.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=498612229