Source	CANADA NEWSWIRE
Date	09/16/2014
Time	07:00:36 AM

Company	 Mundoro Capital Inc.
Title	Mundoro Identifies New Porphyry and Epithermal Targets at Bulgaria
Projects





    CDNX Symbol: MUN











Press Release	




" BC-MundoroBulgariaProjct   09-16 1800
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business  Editors:
^Mundoro Identifies New Porphyry and Epithermal Targets at Bulgaria
Projects@

VANCOUVER, Sept. 16, 2014 /CNW/ - Mundoro Capital Inc. (TSXV: MUN,
www.mundoro.com) ("Mundoro" or the "Company") is pleased to provide an update
on its exploration activities at its 100% owned Bulgarian properties - Zvezda,
Byalo and Chuprene. Recent exploration results have delineated a new porphyry
copper-gold target at the Ramadanska Chuka ("RC") project area within the
southwest corner of the Byalo exploration license, a new epithermal gold
target at the Angel Voyvoda ("AV") project area within the Zvezda exploration
license and confirmed anomalous copper-gold grades in quartz veins at the
Chuprene exploration license.
Teo Dechev, CEO and President of Mundoro commented, "The exploration work
completed to date by our exploration team to identify these new targets on our
three licenses underscores the effectiveness of our exploration programs and
ability to generate new discovery opportunities to our shareholders. At RC,
the delineation of a new porphyry copper-gold-molybdenum system is being
followed up by an Induced Polarization/Resistivity survey in September to
refine the drill targets. At AV, rock sampling of the breccia returned grades
from 1.1 g/t gold to 3.33 g/t gold. A ground magnetic survey is currently
underway to delineate the structures."
Byalo
The Company started a systematic exploration program comprising stream
sediment sampling, rock grab sampling, mapping, soil geochemistry and ground
geophysics. The infill soil sampling program at the RC project area has
delineated a new porphyry copper-gold-molybdenum system approximately 650m x
600m in size which is related to a larger advanced argillic alteration
lithocap.
Rock sampling results returned anomalous copper-gold-molybdenum up to
0.39% copper, 0.55 g/t gold and 587 ppm molybdenum related to quartz stockwork
veining and hydrothermal breccia. Soil geochemical sampling results identified
a well-defined molybdenum anomaly that haloes a copper-gold central core
anomaly and is rimmed by Bi, Te, Pb and Zn. The Company carried out the ground
magnetic survey in Q2 2014 over the RC hydrothermal system approximately 5km²
in size (2.3 x2.2 km). The survey identified several anomalies including a
well-defined magnetic bull's-eye anomaly that overlaps with the porphyry
related copper-gold-molybdenum soil and rock anomalies (see Figure 1).
The Company has mobilised a geophysics team to carry out an Induced
Polarization/Resistivity survey over the RC porphyry target. The survey
includes four lines totalling 10 line km designed to penetrate to 500m in
depth. Current exploration at the Byalo license also includes regional soil
sampling over an area 8km x 8km (64km²) north and east of RC project area and
which was highlighted as anomalous and prospective by the Company's stream
sediment screening program.
The RC project area is located 3km west of Chala, a producing epithermal
quartz vein gold mine which is hosted in the andesite volcanic rocks part of
the Tertiary Volcanic Belt extending from West Turkey through to Northern
Greece, Macedonia and western Serbia. The Tertiary Belt is host to numerous
producing and developing gold and copper-gold mines and projects.
Zvezda
The systematic exploration program carried out by the Company covering
stream sediment screening, mapping, soil and rock sampling at the Zvezda
license resulted in identifying the new Angel Voyvoda ("AV") project area as
prospective for sediment hosted epithermal gold mineralisation. Exploration at
the AV project area initially focused on following up anomalous rock-chip
samples (up to 2.6 g/t Au) that were reported by prior explorer, Newmont.
Follow up reconnaissance mapping established the presence of mineralised
quartz fault breccia which was followed discontinuously for 1.3 km in tertiary
marine sediments. Rock sampling of the breccia along three parallel structures
returned grades from 1.1 g/t gold to 3.33 g/t gold.
Recently completed soil sampling along a focused grid has established
continuity along strike of the fault breccias, which identified several
WNW-ESE trending zones coincident with mapped orientations of the sampled
quartz breccia structures (see Figure 2). The Company will conduct trenching
which will target areas with anomalous gold values in soils that coincide with
anomalous gold values reported from mapped quartz breccias as well as
targeting linear soil anomalies that are interpreted to be breccia structures
which are not exposed at surface. This gold-in-soil anomaly is 2.6km x 2km and
is open to the west and southwest. A ground magnetic survey is taking place at
the AV project area in September to identify fault structures that are
interpreted to be conduits for gold mineralisation in quartz breccias.
Another target area in the Zvezda license is the Eplika project area
where soil sampling identified a north-west trending gold-in-soil anomaly
3.5km long with reported grades up to 1.55 g/t gold. Reconnaissance mapping
identified quartz veins related to the soil anomaly which are immediately
south of the Chala gold mine (see Figure 3). Mapping and rock samples returned
gold values up to 13.6 g/t gold along a quartz vein zone discontinuously
followed for 750 meters. Further mapping has established that faulting across
these vein systems may have offset these structures. Prior explorers had
reported values up to 8 g/t gold. The Company will sample historical trenches
in the vicinity of the reported high grade gold samples in order to establish
the continuity and correct dip of the vein system in order to better define
drill targets.
Chuprene
Mundoro acquired the Chuprene exploration license in July 2014. The
Chuprene license is located approximately 175km NW of Sofia and includes
numerous copper-gold and gold occurrences and mines hosted in the Palaeozoic
Mineral Belt of Bulgaria. The Company has started reconnaissance field work
and assessment of the available historical data.
Initial work includes surveying, mapping and channel sampling of the
known Chuprene copper-gold occurrence which has been exploited since ancient
times. Several mineralised quartz vein zones occupying an area 4,000m x 700m
have been followed up by initial prospecting in the field. The vein zones are
hosted by an NW-SE trending regional thrust fault system mapped in the
northern part of the license for 25km. Initial rock channel sampling included
42 samples collected across the central zone starting from the main adit.
Results returned encouraging copper-gold values up to 2.54% Cu and 2.9 g/t Au.
Distribution of copper and gold values suggests at least two mineralised
pulses: one bearing copper and a second bearing gold following the same
fault-vein structures. Work continues with mapping and sampling parallel and
sub-parallel vein zones along the fault system hosting the Chuprene occurrence
as well as other project areas within the Chuprene license.
Sampling and Analysis Procedure
All channel and rock intercepts were obtained from continuous channel
sampling intervals. All samples are assayed using 50 gram fire assay with
atomic absorption finish by ALS Bor, Serbia. Quality Assurance and quality
control procedures include the systematic insertion of standards and
duplicates into the sample streams. Field duplicate samples are taken every 25
samples and standards and blanks are inserted after every 20th sample. All
data collected in the field and assay results from the laboratories are
routinely verified and entered in an access data base.
Soil samples were collected from the "B" horizon of the soil media by
hand digging a hole from 0.1 to 0.5m. Material of ~500 grams was collected,
sealed and send directly to the ALS laboratory in Bor. Samples were dried at
<60°C/140F, sieve sample to -180 micron (80 mesh) and assayed using 30 gram
fire assay with atomic absorption finish.
The technical information contained in this Press Release has been
reviewed and approved by Mr. G. Magaranov, P. Geo., the Qualified Person as
defined by National Instrument 43-101.
On behalf of the Company, Teo Dechev, Chief Executive Officer, President
and Director
About Mundoro Capital Inc.
Mundoro is a well-funded, Canadian based company focused on mineral
acquisition, exploration and development. Our primary focus is advancing our
properties on the Tethyan Belt in Southeastern Europe. Mundoro has
methodically acquired a district-scale land position on this prolific minerals
belt which hosts significant Gold-Copper porphyry and related epithermal
deposits. Our strong project pipeline which also includes assets in Mexico and
China, is positioned to drive long-term, sustainable growth in order to attain
production and shareholder return.
Caution Concerning Forward-Looking Statements Information included,
attached to or incorporated by reference into this News Release may contain
forward-looking statements. All statements, other than statements of
historical fact, included or incorporated by reference in this News Release
are forward-looking statements, including, without limitation, statements
regarding activities, events or developments that the Board expects or
anticipates may occur in the future. These forward-looking statements can be
identified by the use of forward-looking words such as "will", "expect",
"intend", "plan", "estimate", "anticipate", "believe" or "continue" or similar
words or the negative thereof. The material assumptions that were applied in
making the forward looking statements in this News Release include
expectations as to the Company's future strategy and business plan and
execution of the Company's existing plans. There can be no assurance that the
plans, intentions or expectations upon which these forward-looking statements
are based will occur. We caution readers of this News Release not to place
undue reliance on forward looking statements contained in this News Release,
which are not a guarantee of performance and are subject to a number of
uncertainties and other factors that could cause actual results to differ
materially from those expressed or implied by such forward-looking statements.
These factors include general economic and market conditions, changes in law,
regulatory processes, the status of Mundoro's assets and financial condition,
actions of competitors and the ability to implement business strategies and
pursue business opportunities. The forward-looking statements contained in
this News Release are expressly qualified in their entirety by this cautionary
statement. The forward-looking statements included in this News Release are
made as of the date of this News Release and the Board undertakes no
obligation to publicly update such forward-looking statements to reflect new
information, subsequent events or otherwise, except as required by law.
Shareholders are cautioned that all forward-looking statements involve risks
and uncertainties and for a more detailed discussion of such risks and other
factors that could cause actual results to differ materially from those
expressed or implied by such forward-looking statements, refer to the
Company's filings with the Canadian securities regulators available on
www.sedar.com. Neither TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.
SOURCE Mundoro Capital Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/September2014/16/c9138.html

-0-                           09/16/2014
/For further information:
Teo Dechev, CEO, President and Director of Mundoro Capital Inc. at
+1-604-669-8055 or Michelle Roth, Roth Investor Relations at +1-732-792-2200.
/
(MUN.)

CO:  Mundoro Capital Inc.
ST:  British Columbia
IN:  MNG
SU:  BUZ

-30-