Source	MARKET NEWS
Date	09/16/2014
Time	07:08:01 AM

Company	 Mundoro Capital Inc.
Title	Identifies 
New Porphyry and Epithermal Targets a





    CDNX Symbol: MUN











Press Release	





MUNDORO CAPITAL INC ("MUN-V;MUNMF-0")
- Identifies New Porphyry and Epithermal Targets at Bulgaria
- Projects

Mundoro Capital Inc. (www.mundoro.com) ("Mundoro" or the
"Company") is pleased to provide an update on its exploration
activities at its 100% owned Bulgarian properties - Zvezda, Byalo and
Chuprene. Recent exploration results have delineated a new porphyry
copper-gold target at the Ramadanska Chuka ("RC") project area within
the southwest corner of the Byalo exploration license, a new epithermal
gold target at the Angel Voyvoda ("AV") project area within the Zvezda
exploration license and confirmed anomalous copper-gold grades in
quartz veins at the Chuprene exploration license.

Teo Dechev, CEO and President of Mundoro commented, "The
exploration work completed to date by our exploration team to identify
these new targets on our three licenses underscores the effectiveness
of our exploration programs and ability to generate new discovery
opportunities to our shareholders. At RC, the delineation of a new
porphyry copper-gold-molybdenum system is being followed up by an
Induced Polarization/Resistivity survey in September to refine the
drill targets. At AV, rock sampling of the breccia returned grades from
1.1 g/t gold to 3.33 g/t gold.  A ground magnetic survey is currently
underway to delineate the structures."

Byalo

The Company started a systematic exploration program comprising
stream sediment sampling, rock grab sampling, mapping, soil
geochemistry and ground geophysics.  The infill soil sampling program
at the RC project area has delineated a new porphyry
copper-gold-molybdenum system approximately 650m x 600m in size which
is related to a larger advanced argillic alteration lithocap.

Rock sampling results returned anomalous copper-gold-molybdenum up
to 0.39% copper, 0.55 g/t gold and 587 ppm molybdenum related to quartz
stockwork veining and hydrothermal breccia. Soil geochemical sampling
results identified a well-defined molybdenum anomaly that haloes a
copper-gold central core anomaly and is rimmed by Bi, Te, Pb and Zn.
The Company carried out the ground magnetic survey in Q2 2014 over the
RC hydrothermal system approximately 5km in size (2.3 x2.2 km). The
survey identified several anomalies including a well-defined magnetic
bull's-eye anomaly that overlaps with the porphyry related
copper-gold-molybdenum soil and rock anomalies (see Figure 1).

The Company has mobilised a geophysics team to carry out an
Induced Polarization/Resistivity survey over the RC porphyry target.
The survey includes four lines totalling 10 line km designed to
penetrate to 500m in depth. Current exploration at the Byalo license
also includes regional soil sampling over an area 8km x 8km (64km)
north and east of RC project area and which was highlighted as
anomalous and prospective by the Company's stream sediment screening
program.

The RC project area is located 3km west of Chala, a producing
epithermal quartz vein gold mine which is hosted in the andesite
volcanic rocks part of the Tertiary Volcanic Belt extending from West
Turkey through to Northern Greece, Macedonia and western Serbia. The
Tertiary Belt is host to numerous producing and developing gold and
copper-gold mines and projects.

Zvezda

The systematic exploration program carried out by the Company
covering stream sediment screening, mapping, soil and rock sampling at
the Zvezda license resulted in identifying the new Angel Voyvoda ("AV")
project area as prospective for sediment hosted epithermal gold
mineralisation. Exploration at the AV project area initially focused on
following up anomalous rock-chip samples (up to 2.6 g/t Au) that were
reported by prior explorer, Newmont.  Follow up reconnaissance mapping
established the presence of mineralised quartz fault breccia which was
followed discontinuously for 1.3 km in tertiary marine sediments. Rock
sampling of the breccia along three parallel structures returned grades
from 1.1 g/t gold to 3.33 g/t gold.

Recently completed soil sampling along a focused grid has
established continuity along strike of the fault breccias, which
identified several WNW-ESE trending zones coincident with mapped
orientations of the sampled quartz breccia structures (see Figure 2).
The Company will conduct trenching which will target areas with
anomalous gold values in soils that coincide with anomalous gold values
reported from mapped quartz breccias as well as targeting linear soil
anomalies that are interpreted to be breccia structures which are not
exposed at surface. This gold-in-soil anomaly is 2.6km x 2km and is
open to the west and southwest. A ground magnetic survey is taking
place at the AV project area in September to identify fault structures
that are interpreted to be conduits for gold mineralisation in quartz
breccias.

Another target area in the Zvezda license is the Eplika project
area where soil sampling identified a north-west trending gold-in-soil
anomaly 3.5km long with reported grades up to 1.55 g/t gold.
Reconnaissance mapping identified quartz veins related to the soil
anomaly which are immediately south of the Chala gold mine (see Figure
3).  Mapping and rock samples returned gold values up to 13.6 g/t gold
along a quartz vein zone discontinuously followed for 750 meters.
Further mapping has established that faulting across these vein systems
may have offset these structures. Prior explorers had reported values
up to 8 g/t gold. The Company will sample historical trenches in the
vicinity of the reported high grade gold samples in order to establish
the continuity and correct dip of the vein system in order to better
define drill targets.

Chuprene

Mundoro acquired the Chuprene exploration license in July 2014.
The Chuprene license is located approximately 175km NW of Sofia and
includes numerous copper-gold and gold occurrences and mines hosted in
the Palaeozoic Mineral Belt of Bulgaria. The Company has started
reconnaissance field work and assessment of the available historical
data.

Initial work includes surveying, mapping and channel sampling of
the known Chuprene copper-gold occurrence which has been exploited
since ancient times. Several mineralised quartz vein zones occupying an
area 4,000m x 700m have been followed up by initial prospecting in the
field. The vein zones are hosted by an NW-SE trending regional thrust
fault system mapped in the northern part of the license for 25km.
Initial rock channel sampling included 42 samples collected across the
central zone starting from the main adit. Results returned encouraging
copper-gold values up to 2.54% Cu and 2.9 g/t Au. Distribution of
copper and gold values suggests at least two mineralised pulses: one
bearing copper and a second bearing gold following the same fault-vein
structures. Work continues with mapping and sampling parallel and
sub-parallel vein zones along the fault system hosting the Chuprene
occurrence as well as other project areas within the Chuprene license.

Sampling and Analysis Procedure

All channel and rock intercepts were obtained from continuous
channel sampling intervals. All samples are assayed using 50 gram fire
assay with atomic absorption finish by ALS Bor, Serbia. Quality
Assurance and quality control procedures include the systematic
insertion of standards and duplicates into the sample streams. Field
duplicate samples are taken every 25 samples and standards and blanks
are inserted after every 20th sample. All data collected in the field
and assay results from the laboratories are routinely verified and
entered in an access data base.

Soil samples were collected from the "B" horizon of the soil media
by hand digging a hole from 0.1 to 0.5m. Material of ~500 grams was
collected, sealed and send directly to the ALS laboratory in Bor.
Samples were dried at (60C/140F, sieve sample to -180 micron (80 mesh)
and assayed using 30 gram fire assay with atomic absorption finish.

The technical information contained in this Press Release has been
reviewed and approved by Mr. G. Magaranov, P. Geo., the Qualified
Person as defined by National Instrument 43-101.

On behalf of the Company,
Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a well-funded, Canadian based company focused on
mineral acquisition, exploration and development.  Our primary focus is
advancing our properties on the Tethyan Belt in Southeastern Europe.
Mundoro has methodically acquired a district-scale land position on
this prolific minerals belt which hosts significant Gold-Copper
porphyry and related epithermal deposits.  Our strong project pipeline
which also includes assets in Mexico and China, is positioned to drive
long-term, sustainable growth in order to attain production and
shareholder return.

Caution Concerning Forward-Looking Statements
Information included, attached to or incorporated by reference
into this News Release may contain forward-looking statements. All
statements, other than statements of historical fact, included or
incorporated by reference in this News Release are forward-looking
statements, including, without limitation, statements regarding
activities, events or developments that the Board expects or
anticipates may occur in the future. These forward-looking statements
can be identified by the use of forward-looking words such as "will",
"expect", "intend", "plan", "estimate", "anticipate", "believe" or
"continue" or similar words or the negative thereof. The material
assumptions that were applied in making the forward looking statements
in this News Release include expectations as to the Company's future
strategy and business plan and execution of the Company's existing
plans. There can be no assurance that the plans, intentions or
expectations upon which these forward-looking statements are based will
occur. We caution readers of this News Release not to place undue
reliance on forward looking statements contained in this News Release,
which are not a guarantee of performance and are subject to a number of
uncertainties and other factors that could cause actual results to
differ materially from those expressed or implied by such
forward-looking statements. These factors include general economic and
market conditions, changes in law, regulatory processes, the status of
Mundoro's assets and financial condition, actions of competitors and
the ability to implement business strategies and pursue business
opportunities. The forward-looking statements contained in this News
Release are expressly qualified in their entirety by this cautionary
statement. The forward-looking statements included in this News Release
are made as of the date of this News Release and the Board undertakes
no obligation to publicly update such forward-looking statements to
reflect new information, subsequent events or otherwise, except as
required by law. Shareholders are cautioned that all forward-looking
statements involve risks and uncertainties and for a more detailed
discussion of such risks and other factors that could cause actual
results to differ materially from those expressed or implied by such
forward-looking statements, refer to the Company's filings with the
Canadian securities regulators available on


TEL:  +1-604-669-8055   Teo Dechev, CEO, President and Director
of Mundoro Capital Inc.
TSX Venture closing price for MUN-V
Date: 2014/09/15
Closing Price: 0.23

TEL:  +1-732-792-2200   Michelle Roth, Roth Investor Relations
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1425800018TS11425801390-07063920140916