Source	Marketwire
Date	09/17/2014
Time	04:00:58 AM

Company	 ABEN RESOURCES LTD.
Title	Aben Resources Exploration Update at Justin Gold-Silver-Tungsten Project, 
Southeast Yukon





    CDNX Symbol: ABN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Aben Resources Ltd.

TSX VENTURE SYMBOL: ABN
PINKSHEETS SYMBOL: ABNAF
FRANKFURT SYMBOL: E2L

September 17, 2014

Aben Resources Exploration Update at Justin Gold-Silver-Tungsten Project, 
Southeast Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 17, 2014) - Aben Resources 
Ltd. (TSX VENTURE:ABN)(PINKSHEETS:ABNAF)(FRANKFURT:E2L) is pleased to announce 
an update to its 2014 exploration program at its 100% owned 18,314 acre Justin 
gold-silver-tungsten project. The project area is located in southeast Yukon 
within the Tintina Gold Belt approximately 35 kilometers southwest of the 
Cantung Mine and is accessed by an all-season road.

Justin gold-silver-tungsten project location map:

http://www.abenresources.com/i/maps/ABN-Justin.jpg

Aben's Justin property is host to numerous styles of intrusion-related 
mineralization (IRGS), most notably the newly-discovered auriferous 
gold-silver-tungsten skarn and sheeted vein system which comprise the POW zone. 
The Justin property area includes the POW, Confluence, Main and Kangas zones 
which form part of a 12 kilometer-long mineralized corridor. The property area 
is 35 kilometers from North American Tungsten Corp.'s Cantung 
tungsten-copper-gold mine, with other significant projects in the area 
including Golden Predator's Sprogge and 3-Aces properties. With excellent 
infrastructure and an active mine with similar geology nearby, Aben's Justin 
project boasts highly-prospective near-surface exploration targets for both 
gold and tungsten.

The goals of the 2014 exploration program at the Justin project were as follows:

/T/

--  To assess the potential for Au (gold) mineralization at surface within
the POW Zone skarn through surface trenching;
--  To assess the potential for Au mineralization within the Justin Stock
200 meters south of the POW Zone;
--  To expand geochemical survey coverage in proximity to known mineral
showings;
--  To make a preliminary assessment of the property for economic W
(tungsten) mineralization and re-sample core, previously drilled, for W
specific analysis.

/T/

Summary of Exploration Activities:

Work completed during the 2014 exploration program included the collection of 
60 channel samples from 4 trenches, 24 rock samples, re-analysis of 230 drill 
core samples, 4 silt samples and 151 soil samples with coverage totaling 7.2 
line kilometers. The program was focused on two areas, the POW Zone and the Big 
Swifty Zone, where previous exploration by the Company has shown the potential 
for intrusion related gold mineralization at surface.

Assays from the 2014 trenching program returned encouraging results defining 
gold-bismuth-tellurium bearing sheeted vein systems at surface within the 
Justin Granodiorite stock and adjacent POW Zone skarn.

Trenches TR14-001 and TR14-002 were designed to follow up on a grab sample 
collected in 2012 which returned 22.2 g/t Au from sheeted veins within the 
Justin Stock Granodiorite. Both TR14-001 and TR14-002 successfully delineated 
gold-tellurium-bismuth bearing sheeted vein arrays at surface within the Justin 
Stock extending the prospect 225 meters south along strike from the original 
POW Zone discovery outcrop. TR14-003 was designed to evaluate sheeted vein 
arrays hosted within calcareous chert, a rock unit which defines the upper 
contact of the POW Zone skarn. Well-developed sheeted vein arrays were sampled; 
however TR14-003 returned no significant results. TR14-004 was designed to 
evaluate sheeted vein arrays hosted within the POW Zone skarn, the main 
exploration target on the Justin property. TR14-004 successfully delineated 
gold-tellurium-bismuth bearing sheeted vein arrays within the skarn extending 
gold mineralization at surface 50 meters north from that defined in diamond 
drill holes JN12013 and JN12014 (see news release September 25th, 2012).

Justin Project 2014 trench location map:

http://www.abenresources.com/i/maps/ABN-Justin-2014-Trench-Locations-map.jpg

The intrusion related gold system is comprised of a series of sheeted vein 
arrays emanating from the Justin Stock into the contact aureole skarn. Gold 
mineralization is currently defined within the sheeted vein arrays and the 
skarn over an area measuring 400 meters by 500 meters, and extends from surface 
to depths in excess of 200 meters.

In addition several high-priority exploration targets within 1 kilometer of the 
POW Zone, as defined by geophysics and geochemistry, remain untested and 
represent significant potential for expanding the current extent of the 
intrusion related gold system.

/T/


Table 1 - Trench Summary Results

----------------------------------------------------------------------------
Composite Channel Sample
Zone            Trench       Easting     Northing  Results
----------------------------------------------------------------------------
POW           TR14-001        546710      6839235  0.33 g/t Au over 6.70m,
including
----------------------------------------------------------------------------
POW           TR14-001        546710      6839235  0.59 g/t Au over 3.10m,
including
----------------------------------------------------------------------------
POW           TR14-001        546710      6839235  0.96 g/t Au over 0.50m
----------------------------------------------------------------------------
POW           TR14-002        546737      6839240  0.23 g/t Au over 4.00m,
including
----------------------------------------------------------------------------
POW           TR14-002        546737      6839240  0.95 g/t Au over 0.50m
----------------------------------------------------------------------------
POW           TR14-003        546650      6839490  No Significant Results
----------------------------------------------------------------------------
POW           TR14-004        546650      6839475  0.92 g/t Au over 13.15m,
including
----------------------------------------------------------------------------
POW           TR14-004        546650      6839475  1.15 g/t Au over 7.90m,
also including
----------------------------------------------------------------------------
POW           TR14-004        546650      6839475  2.76 g/t Au over 1.90m
----------------------------------------------------------------------------

(i) g/t = grams per metric tonne


/T/

Examination of drill core using short wave ultraviolet lights in 2012 revealed 
visible scheelite (calcium tungstate) mineralization disseminated within the 
POW Zone Skarn and sheeted vein arrays. Review of the 2011 - 2012 drill hole 
geochemical dataset indicated that anomalous concentrations of tungsten were 
reported in the multi-element ICP analysis from several intervals within the 
POW zone skarn.

With the Justin project being 30 kilometers south of North American Tungsten 
Corporations world-class Cantung tungsten deposit, the Company felt it prudent 
to re-sample select intervals of drill core identified as "anomalous tungsten 
concentrations (greater than 200 ppm W)" within the ICP dataset. A total of 230 
samples from 7 drill holes were selected for analysis using pressed pellet XRF 
and fusion XRF analytical techniques and will provide a preliminary assessment 
of the potential for economic tungsten mineralization within the POW Zone. 
Assay results are currently pending.

Qualified Person and Quality Assurance:

Mike McCuaig, P.Geo., Justin Project geologist and a Qualified Person as 
defined by National Instrument 43-101, has reviewed and approved the technical 
information in this release.

All samples were submitted to ALS Minerals in Whitehorse for preparation. 
Geochemical analysis was completed at ALS Minerals Laboratory in Vancouver. The 
following analytical techniques were used for all rock samples: ME-MS41, 
Au-AA23 30 g Fire Assay, Au-GRA21 30 g Fire Assay for all samples greater than 
10 ppm Au, ME-OG46 for all samples greater than 10,000 ppm Zn, Zn-VOL50 for all 
samples greater than 300,000 ppm Zn, W-XRF05 for all samples greater than 200 
ppm W in the ME-MS41 analysis and W-XRF10 for all samples greater than 5000 ppm 
W in the W-XRF05 analysis. The following analytical techniques were used for 
all soil and silt samples: ME-MS41, Au-ST43 and Au-AROR43 for all samples 
greater than 1 ppm Au. The Company's QAQC measures included insertion of 
external blanks and standards into the sample stream for all rock chip/channel 
samples. A minimum of one standard sample and one blank sample were inserted 
for each trench.

About Aben Resources:

Aben Resources Ltd. is a Canadian gold-silver-tungsten and uranium exploration 
company with projects in the Yukon, NWT and Saskatchewan's Athabasca Basin.

For further information on Aben Resources Ltd. (TSX VENTURE:ABN), visit our 
Company's web site at www.abenresources.com.

ON BEHALF OF THE BOARD OF DIRECTORS

JAMES G. PETTIT, President

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This release includes certain statements that may be deemed to be 
"forward-looking statements". All statements in this release, other than 
statements of historical facts, that address events or developments that 
management of the Company expects, are forward-looking statements. Although 
management believes the expectations expressed in such forward-looking 
statements are based on reasonable assumptions, such statements are not 
guarantees of future performance, and actual results or developments may differ 
materially from those in the forward-looking statements. The Company undertakes 
no obligation to update these forward-looking statements if management's 
beliefs, estimates or opinions, or other factors, should change. Factors that 
could cause actual results to differ materially from those in forward-looking 
statements, include market prices, exploration and development successes, 
continued availability of capital and financing, and general economic, market 
or business conditions. Please see the public filings of the Company at 
www.sedar.com for further information.

- 30 -

CONTACT INFO:

Aben Resources Ltd.
Don Myers
Corporate Communications
604-687-3376 or Toll Free: 800-567-8181
Fax: 604-687-3119
info@abenresources.com
www.abenresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=499007825