Source	MARKET NEWS
Date	09/17/2014
Time	08:18:17 AM

Company	 Oceanus Resources Corporation
Title	Drills 
10.5 Meters of 7.4 gpt Gold at Santo Nino





    CDNX Symbol: OCN











Press Release	





OCEANUS RESOURCES CORPORATION ("OCN-V")
- Drills 10.5 Meters of 7.4 gpt Gold at Santo Nino in Mexico

Oceanus Resources Corporation ("Oceanus" or the "Company") is
pleased to announce assay results from the recently completed drilling
program at the La Lajita property in Durango, Mexico. The program
consisted of twenty-one (21) holes totaling 3,002.5 meters of PQ triple
tube core (PQ3) diamond drill core at the Santo Nino and Dos Hermanos
Prospects.

Santo Nino Prospect Returns More High Grade Results

Six holes totaling 1,143.9 meters were drilled at Santo Nino to
test the down dip extension of the high-grade ore shoot intersected by
the discovery hole OCN-13-005 which returned 7.1 g/t gold and 48.8 g/t
silver over a core length of 20.0 meters, including 18.9 g/t gold and
71.3 g/t silver over a core length of 6.5 meters in greenish quartz
breccia with visible gold. Highlighted assay results from Santo Nino
include the following:



-3.13 g/t gold and 22.3 g/t silver over a core length of 26.0
meters, including




7.42 g/t gold and 34.5 g/t silver over a core length of 10.5
meters in ddh OCN-14-026



-2.08 g/t gold and 25.3 g/t silver over a core length of 28.0
meters, including




5.92 g/t gold and 46.1 g/t silver over a core length of 8.9 meters
in ddh OCN-14-008

-1.50 g/t gold and 17.4 g/t silver over a core length of 25.3
meters, including




11.80 g/t gold and 63.0 g/t silver over a core length of 2.5
meters in ddh OCN-14-027

Dos Hermanos Strike Length Extended

Seven holes totaling 882.1 meters were drilled at the Dos Hermanos
Prospect, four holes totaling 470.6 meters were also drilled at the
northern strike extension of Dos Hermanos and four holes totaling 505.9
meters were also drilled at the southern strike extension at Dos
Hermanos. The drilling completed has effectively doubled the strike
length of the mineralized zone at Dos Hermanos to 225 meters.

Highlighted assay results from the Dos Hermanos north extension
include the following:

-0.81 g/t gold and 18.5 g/t silver over a core length of 24.5
meters, including



2.57 g/t gold and 27.8 g/t silver over a core length of 5.5 meters
in ddh OCN-14-022



-0.82 g/t gold and 21.6 g/t silver over a core length of 29.5
meters, including




5.13 g/t gold and 42.8 g/t silver over a core length of 2.0 meter
in ddh OCN-14-024

Historically drilling at the Dos Hermanos Propect was impacted by
low sample recovery in the breccia zones. In an attempt to improve core
recovery, Oceanus switched from NQ to HQ to PQ3 core size, but 100%
core recovery was not achieved. Oceanus will continue to seek measures
to improve core recovery by controlled drilling with specialty muds and
face discharge bits when drilling resumes. Drill results from the
recently completed drill program are attached in a table as Appendix A.


Mr. Glenn Jessome, President and CEO of Oceanus, commented:

"We are beginning to define the down dip extension of the high
grade ore shoot at the Santo Nino prospect.  The new holes confirm the
high grade mineralization cut in the 2013 discovery hole OCN-13-005
continues down dip towards the contact with the Lower Volcanic Complex.
The strike extension at Dos Hermanos is significant. The widths and
grades at Dos Hermanos have resulted in us beginning modelling to
determine if the upper portion of the zone could be a starter pit. Our
plans are to resume drilling at the exciting new Santo Nino gold
prospect mid-October of this year."

Fall 2014 Program

Following on the success of the summer 2014 drill campaign Oceanus
will begin drilling again mid-October, 2014, with the first six to
eight holes to test the down-dip extension of the Santo Nino high-grade
ore shoot and in particular follow up the high-grade intercepts
encountered in drill holes 5, 8, 26 and 27. A detailed structural
mapping project will be carried out in the area of the Santo Nino ore
shoot.

In October, 2014 a program consisting of geological mapping,
prospecting and channel sampling will be undertaken along the 6
kilometer north-west trending fault to identify additional prospects.
Oceanus will also be testing the other know gold prospects on the
property including a trenching program at the Zanjas Prospect, where
the Company's geologists observed visible gold in outcrop (i.e. quartz
breccia) last year.

La Lajita Property

The La Lajita Property comprises 12 mining concessions held under
option located in the south-west corner of Durango State, Mexico, along
the western flanks of the Sierra Madre Occidental. This area is
recognized as an extremely prospective mineral belt for gold and silver
deposits. Furthermore, this area is a virgin district having never been
discovered or worked by the Spanish and there are no historic mining
records. There are numerous pits, adits and small shafts that have been
developed by local gambusinos during the 1900's and artisanal mining in
the area continues to this day.

Detailed geological mapping and channel sampling program completed
by Oceanus has confirmed the presence of seven (7) gold-silver
prospects along the La Lajita fault system which has been traced along
surface for over three kilometers. These prospects from north to south
are; La Fortuna, Esperanza, Santo Nino, Dos Hermanos, Mina la
Guadalupe, Las Ratones and the Cerro del Sol. At Mina la Guadalupe,
gold mineralization has been exposed for 200 meters on surface in
numerous small scale workings, and in one significant underground
working, where the miners drifted in the high-grade gold mineralization
120 meters along strike.

Gold and silver mineralization at the Santo Nino prospect is
associated with a 20 to 30 meter thick siliceous breccia occurring
along a west dipping fault. The fault dislocates a largely felsic to
andesitic sequence of tuffaceous rocks of the Upper Volcanic Complex.
The gold bearing system at Santo Nino is hosted by a brecciated, maroon
andesite that has two generations of gold-bearing quartz, a green
siliceous breccia variety and a white quartz vein variety.  The green
siliceous breccia is typically auriferous with visible gold and is
enveloped by a broader mineralized white quartz zone.

Lab Preparation and Assay

Oceanus samples are prepared and assayed by Activation
Laboratories Ltd. ("Actlabs"). Actlabs is a CAN-P-1579, CAN-P-4E
(ISO/IEC 17025:2005) accredited laboratory and independent of Oceanus.
The sealed and tagged sample bags are turned over to ActLabs personnel
at the site who transport them to the ActLabs facility in Zacatecas,
Mexico. ActLabs crushes the samples and prepares 200-300 gram pulp
samples with ninety percent of the pulp passing Tyler 150 mesh (106?m).


The pulps are assayed for gold using a 50 gram charge by fire
assay (Code 1A2-50) and over limits greater than 3 grams per tonne are
re-assayed using a gravimetric finish (Code 1A3-50).  Silver is
completed using total digestion Code ME-4 acid procedure and over
limits greater than 100 ppm are fire assayed using a gravimetric finish
(Code 1A3-50). Copper analysis is completed using the total digestion
Code ME-4 acid procedure. Gold screen metallic assays are completed
using the Code 1A4-1000 procedure.

Quality Assurance/Quality Control and Data Verification

Quality assurance and quality control procedures include the
systematic insertion of blanks, standards and duplicates into the
sample strings. The results of the assaying of the QA/QC material
included in each batch are tracked to ensure the integrity of the assay
data. All results stated in this announcement have passed Oceanus's
quality assurance and quality control ("QA/QC") protocols.

David R. Duncan, P. Geo., a director of the Company, is the
Qualified Person for Oceanus as defined under National Instrument
43-101. Mr. Duncan has reviewed the scientific and technical
information in this press release.

About Oceanus Resources Corporation

Oceanus Resources Corporation is a gold exploration company run by
a team of experienced mine finders that have successfully raised $6.4
million over the past 18 months. Oceanus is advancing the La Lajita
Property located in the Sierra Madre Gold and Silver Belt near Durango,
Mexico.

For further information, please contact:

Glenn Jessome

President and CEO

(902) 482-4494

jessome@oceanusresources.ca

CAUTIONARY STATEMENT:

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This News Release includes certain "forward-looking statements".
All statements other than statements of historical fact, included in
this release, including, without limitation, statements regarding
potential mineralization and reserves, exploration results, and future
plans and objectives of Oceanus, are forward-looking statements that
involve various risks and uncertainties. There can be no assurance that
such statements will prove to be accurate and actual results and future
events could differ materially from those anticipated in such
statements. Important factors that could cause actual results to differ
materially from Oceanus's expectations are exploration risks detailed
herein and from time to time in the filings made by Oceanus with
securities regulators.

(Not for distribution to US wire services or for dissemination in
the United States of America)

Appendix A

http://www.thenewswire.ca/archives?tnwarchive2=release_id%3D13286

*  The announced gold intersections are along the hole. Additional
drilling will have to be done to determine the true

thickness of the mineralized zones.

** EqAu60** = Ag grade/60 + Au grade



__________________________________________________
_______________________________________________
TSX Venture closing price for OCN-V
Date: 2014/09/16
Closing Price: 0.50
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1425900032TS11425901474-08165320140917