Source	Marketwire
Date	09/17/2014
Time	07:55:11 AM

Company	 DESERT GOLD VENTURES INC.
Title	Desert Gold Ventures Inc. Announces Results of Preliminary Economic 
Assesment on Its Farabantourou Gold Mining Permit in Western Mali





    CDNX Symbol: DAU











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Desert Gold Ventures Inc.

TSX VENTURE SYMBOL: DAU

September 17, 2014

Desert Gold Ventures Inc. Announces Results of Preliminary Economic Assesment 
on Its Farabantourou Gold Mining Permit in Western Mali


TORONTO, ONTARIO--(Marketwired - Sept. 17, 2014) - Desert Gold Ventures 
Incorporated ("Desert Gold" or "the Company") (TSX VENTURE:DAU) is pleased to 
announce the results of a preliminary economic assessment ("PEA") of its 
proposed Barani East Gold Mine situated in Western Mali.

Desert Gold is developing the Farabantourou permit in Western Mali. The company 
has identified 6 mineralised zones and intends to develop its first mine at the 
Barani East prospect area ("Barani East Project"). Extensive drilling, 
metallurgical analysis, plant and mine design has been undertaken. The Barani 
East Project is situated some 100km south of the town of Kayes. The producing 
Sadiola Hill Gold Mine is located 40km to the north of Barani and Randgold's 
Loulo Gold Mine is located 52km to the south.

On the basis of the capital and operating cost estimates, together with plant 
delivered grades and recoveries, a Discounted Cash Flow ("DCF") analysis has 
indicated that the planned 40ktpm ore production operation is financially 
attractive. Current Net Present Value ("NPV") calculations at a 5.34% per annum 
real discount rate, shows that the proposed mine can generate a pre-tax and 
after tax NPV of some US$15.0 million, net of the initial US$8.7 million 
capital expenditure. These amounts are expressed in mid 2014 money terms. This 
estimate is based on initial 65% total gold recovery in the processing plant. 
The DCF Analysis indicates that until revenues are generated from saleable 
gold, the peak funding requirement is around US$9.8 million. This amount caters 
for the initial capital of US$ 8.69 million and a further US$1.1 million for 
operating costs, principally spent on overburden removal and initial pit 
establishment, during plant construction.

At the Farabantourou Permit Area the Senegal Mali Fault Zone ("SMFZ") cuts 
across the tenement and the mineralisation styles within the permit boundary 
are consistent with the regional geological setting. Six separate zones of 
mineralisation (1 mining target and 5 exploration targets) have been identified 
within the permit boundary. While shallow exploration drilling was conducted on 
all six prospects, the company focused on delimiting an exploitable Mineral 
Resource at Barani East.

The Barani East Project has been comprehensively explored and geologically 
modelled during the drilling programme. The ore body is tabular in shape with a 
northeast strike and steeply dipping between 45 and 60 degrees to the 
south-east. The gold mineralization is associated with quartz haematite rocks 
and kaolinite veins hosted in carbonate-rich siltstone and shale. The thickness 
of the mineralised zone varies between 4.5 m and 15 m in width. Gold 
mineralization extends from surface and is open at depth. Gold mineralisation 
has been tested to a depth of 120 m.

Drilling data on the Project area was analysed by Minxcon and compiled a 
mineral resource prepared in compliance with NI 43-101. The Mineral Resource 
Estimate is made up of an Indicated Mineral Resource of 40 620 ounces at a 
grade of 2.46g/t Au to a depth of 120m, while the inferred resource accounts 
for 67 450 ounces at a grade of 2.53g/t Au to a depth 250m. A total of 
approximately 7600m of sampling boreholes were drilled consisting of 79 
drillholes.

The Mineral Resource for the Project area, was calculated in compliance with 
the specifications and recommendations as embodied in the Standards of 
Disclosure for Mineral Projects as set out by the Canadian Code for reporting 
of Resources and Reserves - National Instrument 43-101 (Standards of Disclosure 
for Mineral Projects) and the resultant Mineral Resource Statement has been 
approved by the Qualified Person for public disclosure.

Following the successful geological drilling programme of the Project area, a 
very successful gold deportment study was carried out at SGS South Africa 
("SGS"). This metallurgical study showed the ore to have excellent gold 
recovery potential which can be achieved under basic processing conditions. 
Following the SGS work, further bulk metallurgical test work was undertaken on 
a large bulk sample by Peacocke, Simpson & Associates (Pty) Ltd ("Peacocke& 
Simpson"). This work resulted in the design of a staged approach to the 
development of the processing facility. The first phase will include a scrubber 
with crushing facilities to allow for the treatment of any harder rock 
fractions and gravity concentration for the recovery of smeltable gold. Gold 
associated with heavy minerals will also be recovered to a secondary 
concentrate, by means of a continuous gravity concentrator and possibly a 
spiral concentrator module. Total gold recovery will be approximately 65%, with 
approximately 40% as free gold, and the remaining 25% as eluted gold. The 
erection of the plant will be of a short duration to build (estimated 18 to 24 
weeks), and fast to commission (estimated 10 to 15 working days). An isometric 
drawing of the proposed plant is shown below.

http://media3.marketwire.com/docs/MAP-2.pdf

The geological study found the mineralized material and waste to be deeply 
weathered. For this reason, it has been assumed that mining will require no 
blasting and will be undertaken by "free digging" with a standard excavator, 
and conventional trucking to the nearby processing plant. The mining function 
is planned to be undertaken through a contractor with a local presence and 
capacity to operate and maintain his own machinery. It is also proposed that 
the mining contractor will be used to construct the tailings impoundment 
facility as well as the roads on and around the mine and to all other 
potentially mineralised zones.

Minxcon Projects ("Minxcon") based in Gauteng South Africa, were tasked with 
designing, scheduling and costing the proposed pit layout. Ore and waste will 
be extracted by means of a large open pit mining operation. The final pit 
geometry on surface will measure some 900m on strike and around 450m in width. 
Final pit depth will be around 215m below surface. Both ore and waste to the 
final pit depth will consist of gravels and soils. As such, no drilling and 
blasting is envisaged to this depth. Therefore a "free dig" mining operation is 
expected and to be confirmed with further studies. If necessary, low grade 
stockpiles can be established and treated at a later stage where mineralization 
is encountered outside the defined ore body.

Mining will commence simultaneously with plant erection. Total refined ounces 
over the 45 month mining duration is estimated at 63 433 oz of gold.

The initial Capital Estimate to establish the mine, supply and erect 40 000 
tonnes per month ("tpm") processing facility, as well as the limited 
infrastructure to operate the mine will cost US$7.5 million in mid 2014 money 
terms. This is inclusive of a 15% contingency allowance for mining and 10% for 
the plant. These Capital Estimates were made by Minxcon.

Operational Costs have been estimated from first principles by Minxcon and 
compare very favourably with other operating open pit mines of similar size in 
Africa. The table below shows a breakdown of typical steady state monthly 
Operating Cost Estimates for the mining operations and processing facility. 
Operating Cost Estimates are expressed in mid 2014 money terms.

/T/

Summary of Unit Operating Costs
(Costs expressed in US$/tonne treated)
----------------------------------------------------------------------
Parameter                                  Barani East
----------------------------------------------------------------------
Net Turnover (Revenue)                                              48
----------------------------------------------------------------------
Mining Costs                                                        19
----------------------------------------------------------------------
Plant Costs                                                          8
----------------------------------------------------------------------
Other Costs (Overheads etc.)                                         2
----------------------------------------------------------------------
Direct Cash Costs (C1)                                              28
----------------------------------------------------------------------
Capex (Amortization)                                                 5
----------------------------------------------------------------------
Production Costs (C2)                                               34
----------------------------------------------------------------------
Royalties                                                            3
----------------------------------------------------------------------
Fully Allocated Costs (C3)                                          37
----------------------------------------------------------------------
Operating Profit                                                    11
----------------------------------------------------------------------

/T/

The Pit Optimisation Study was confined to a mineralized zone of 400m on strike 
to a depth of 250m. There is every reason to believe that gold mineralisation 
continues at depth and may possibly extend further on strike. Upside potential 
exists in the lateral extension of the strike of the current pit.

This lateral extension will be targeted for further exploration once the mine 
is established.

The adjacent Barani Prospect is located approximately 1km due west from the 
Project area. This prospect area contains a mineralised zone, but no Mineral 
Resource has been defined. Early drilling has revealed mineralization in this 
target area. Should the mineralization prove to be economical the material can 
be very easily be loaded and hauled to the Barani East Plant.

Further investigation and analysis shows that with further capital expenditure, 
additional value could be generated by the re-treatment of the tailings stream 
from the primary concentrator facility. The tailings are estimated to contain 
some 34 000 oz of gold. A substantial amount of these gold tailings losses can 
be recovered by plant upgrades and by installing both milling circuit and 
further bulk, low cost, high intensity leach methods. Test work and analysis is 
continuing in this regard.

On obtaining the necessary approvals and increased confidence in the study 
work, site establishment can commence within a relatively short timeframe. 
Current scheduling indicates that work on mine establishment can commence in 
mid 2015.

Minxcon have reviewed the technical content of this document and deem it to be 
fair and accurate. This announcement has been reviewed by Mr. Daniel van 
Heerden, Managing Director of Minxcon, who has more than 25 years of relevant 
experience in the field of Mining Engineering. He is a fellow (No. 37309) of 
the South African Institute of Mining and Metallurgy ('SAIMM') and is 
registered with the Engineering Council of South Africa (No. 20050318) and he 
has consented to the inclusion of the material in the form and context in which 
it appears. In addition, Mr Uwe Engelmann, Director of Minxcon, who has more 
than 16 years of relevant experience in the field of Exploration Geology. He is 
a registered member (No. 400058/08) of the Natural Scientist Institute of South 
Africa ('SACNASP') and is also a member of the Geological Society of South 
Africa ('GSSA'), (No. 966310) and he has also consented to the inclusion of the 
material in the form and context in which it appears.

For further information Please visit our website www.desertgold.ca or refer to 
the technical report which will be available on www.SEDAR.com under the 
company's profile.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

Statements in this presentation, other than historical facts, that address 
exploration activities and mining potential are forward-looking statements. 
Although Desert Gold Ventures Inc. believes that the expectations expressed in 
such forward-looking statements are based on reasonable assumptions, such 
statements should not in any way be construed as guarantees of future 
performance. Factors that could cause developments to differ materially from 
those expressed include: exploration results; technical analysis; and lack of 
availability to the company of necessary capital to progress its projects 
further. The company is subject to specific risks inherent in the exploration 
and mining business and general economic and business conditions.

- 30 -

CONTACT INFO:

Desert Gold Ventures Inc.
Roeland van Kerckhoven
President and CEO
+27 83 455-7847
Fax: +27 86 635-5438
roelandvk@desertgold.ca

or

Desert Gold Ventures Inc.
Jared Scharf
CFO
1 (416) 662-3971
Fax: 1 (604) 408-9301
jared.scharf@desertgold.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=499137924