Source	MARKET NEWS
Date	09/22/2014
Time	06:29:37 AM

Company	 Manson Creek Resources Ltd.
Title	Outlines Large Anomalous Silver Zinc Intersectio





    CDNX Symbol: MCK











Press Release	





Outlines Large Anomalous Silver Zinc Intersections At GuamanProject, Yukon 
--->@NEWS RELEASE
MANSON CREEK RESOURCES LTD ("MCK-V;MCKRF-0")
- Outlines Large Anomalous Silver-Zinc Intersections At
- Guaman Project, Yukon

Manson Creek Resources Ltd. (the "Company") and partner Guatavita
Gold Corporation are pleased to report assay results from the first
Phase of drilling at the Guaman Project, Yukon Territory.

All drill holes intersected anomalous values of silver and zinc
throughout the sulphide bearing shale units and in the contact zone
above the underlying volcanic units. The table below highlights the
intervals with anomalous grades outlined during the maiden phase of
drilling at Guaman, which consisted of 4 drill holes testing some 60
meters of strike length of the 800+ meter geophysical and geochemical
anomaly that underlays the project's numerous mineralized surface
gossan zones.
//st
From              To   Interval     Silver      Zinc    Zinc
Drill hole      (m)             (m)     (m)*        (ppm)     (ppm)     (%)

1                47    49 (eoh)**            2          3      1530    0.15

2                 6   226 (eoh)**          220       3.16      1193    0.12

including      56              68         12       5.95      2237    0.22

and     130             160         30       1.97      2361    0.24

3                92             160         68       3.54      2354    0.24

including      92             114         22       3.42      3035    0.30

and     136             138          2       1.60      7000    0.7

4               140             148          8        2.6      1306    0.13

including     146             148          2        4.2      3320    0.33

*   Intervals are indicative of core sampled, and may not represent true
width of mineralization as insufficient drill data at this time has not
allowed for modeling or estimation of true widths.
**   (eoh) denotes the end of the drill hole.
//et

Jean-Pierre Jutras, P. Geol and President, reports: "The
determination that significant amounts of zinc and silver throughout
the rocks underlying numerous gossans on site is another element that
supports the continued search for potentially economic mineralization
at our Guaman project. While zinc was present and elevated throughout
important intervals, no nickel was found in the core analyzed,
indicating that one of the sources or units responsible for the large
coincident zinc and associated nickel soil anomaly found at surface has
remained elusive through this phase of work. It can be typical of the
zonation in syngenetic systems for zinc, silver and barium to occur on
the fringes or distally to zones of more massive mineralization. Our
team will be going through the data to identify any other vectors that
may assist in finding higher grade zones or feeder structures in the
system."

An updated presentation, with representative pictures of the core
as well as location maps and sections can be found on the Manson Creek
website at manson.ca.

A total of 307 samples, including 5 standards for quality control
purposes were sent to AGAT labs, representing systematic sampling of
the three drill holes completed to depth, in 2 meter intervals.

Quality Control

All drill core was logged, photographed, and cut in half with a
diamond saw on site. One quarter of the core was bagged and sent to
AGAT Laboratories for analysis (which is an ISO 9001 and ISO/IEC 17025
certified lab), while the remaining core was archived and stored on
site for verification and reference purposes. Gold is assayed by
standard fire assay methods with 45 additional elements analyzed by
Induced Coupled Plasma (ICP) utilizing a 4-acid digestion. Quality
assurance and quality control is ensured through the use of certified
standards as well as checks and assay of duplicate samples. Mr.
Jean-Pierre Jutras, P.Geol., President of the Company, is the Qualified
Person for the Guaman project as defined by National Instrument 43-101
and has approved the technical disclosure contained in this news
release.

On Behalf of the Board of Directors,

Jean-Pierre Jutras, President/Director

The TSX Venture Exchange has neither approved nor disapproved of
the contents of this press release.

Except for the historical and present factual information
contained herein, the matters set forth in this news release, including
words such as "expects", "projects", "plans", "anticipates" and similar
expressions, are forward-looking information that represents management
of Manson Creek's internal projections, expectations or beliefs
concerning, among other things, future operating results and various
components thereof or the economic performance of Manson Creek. The
projections, estimates and beliefs contained in such forward-looking
statements necessarily involve known and unknown risks and
uncertainties, which may cause Manson Creek's actual performance and
financial results in future periods to differ materially from any
projections of future performance or results expressed or implied by
such forward-looking statements. These risks and uncertainties include,
among other things, those described in Manson Creek's filings with the
Canadian securities authorities. Accordingly, holders of Manson Creek
shares and potential investors are cautioned that events or
circumstances could cause results to differ materially from those
predicted. Manson Creek disclaims any responsibility to update these
forward-looking statements.

TSX Venture closing price for MCK-V
Date: 2014/09/19
Closing Price: 0.07

TEL:  1.403.233.0464  Manson Creek Resources Ltd.
FAX:  403.266.2606    Jean-Pierre Jutras, President/Director
www.manson.ca
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1426400012TS11426400885-06280920140922