Source	Marketwire
Date	09/22/2014
Time	05:00:36 AM

Company	 NIOCORP DEVELOPMENTS LTD.
Title	NioCorp Updates Elk Creek Niobium Resource-Increases Achieved in Grade and 
Contained Niobium





    CDNX Symbol: NB











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: NioCorp Developments Ltd.

TSX VENTURE SYMBOL: NB
OTCQX SYMBOL: NIOBF
FRANKFURT SYMBOL: BR3

September 22, 2014

NioCorp Updates Elk Creek Niobium Resource-Increases Achieved in Grade and 
Contained Niobium


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 22, 2014) - NioCorp 
Developments Ltd. ("NioCorp" or the "Company") (TSX 
VENTURE:NB)(OTCQX:NIOBF)(FRANKFURT:BR3) is pleased to announce an updated 
NI43-101 resource estimate for the Elk Creek niobium deposit.

Commencing in May, the Company initiated a three phase technical infill 
drilling program, with multiple goals of enhancing the classification of the 
resource; producing geotechnical and geochemical analysis of the deposit; 
provide material for the use in metallurgical studies including pilot plant; 
and to provide all other necessary information required to create and design a 
mine plan. Additional drilling to enhance the overall size of the deposit, 
where it remains open to the northwest, southeast, and at depth, will be 
carried out in the future.

The Company has completed the phase 1, five-hole drill program for a total of 
5,011 m, with the phase 2, six-hole drill program now currently underway. Phase 
3 will follow, if necessary. Utilizing historic and phase 1 drilling results, 
SRK Consulting ("SRK") of Lakewood, Colorado and Cardiff, UK have completed an 
updated mineral resource estimate.

SRK's Mineral Resource is based on a robust 3D model of grade trends within the 
carbonatite complex and is based on good QAQC results. Higher grades are 
associated with pyrochlore contained in magnetite bearing dolomitic 
carbonatite. The Indicated Mineral Resource is confined to a single coherent 
well drilled area containing continuous high grade features.

The estimate has been reported according to CIM Standards and will be supported 
by a NI43-101 independent report which will be published in due course.

The resource estimate for the Elk Creek deposit is summarized in Table 1 below:

/T/

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Table 1 - SRK Mineral Resource Statement Effective Date 9th September 2014
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Cut-off         Tonnage       Grade Contained Nb2O5
Classification        (Nb2O5%)   ('000 Tonnes)    (Nb2O5%)         ('000 kg)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
INDICATED                 0.30          28,200        0.63           177,000
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
INFERRED                  0.30         132,800        0.55           733,700
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
(1) Mineral Resources are not Mineral Reserves and do not have demonstrated
economic viability. All figures are rounded to reflect the relative
accuracy of the estimate and have been used to derive sub-totals, totals
and weighted averages. Such calculations inherently involve a degree of
rounding and consequently introduce a margin of error. Where these occur,
SRK does not consider them to be material. All composites have been capped
where appropriate. The Concession is wholly owned by and exploration is
operated by Niocorp Developments Ltd.
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
(2) The reporting standard adopted for the reporting of the MRE uses the
terminology, definitions and guidelines given in the Canadian Institute of
Mining, Metallurgy and Petroleum (CIM) Standards on Mineral Resources and
Mineral Reserves (December 2005) as required by NI 43-101.
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
(3) SRK assumes the Elk Creek deposit to be amenable to a variety of
Underground Mining methods. In the absence of definitive pricing for Nb and
established rates of metallurgical recovery, SRK has reported the Mineral
Resource at a cut-off of 0.3% Nb2O5. The Company's previous Mineral
Resource dated April 2012 was calculated at a cut-off of 0.4% Nb2O5.
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
(4) SRK Completed a site inspection to the deposit by Mr Martin Pittuck,
MSc., C.Eng, MIMMM, an appropriate "independent qualified person" as this
term is defined in National Instrument 43-101.
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Given the current early stage in the other technical disciplines and on-going 
metallurgical testwork the sensitivity in the Mineral Resource at a range of 
preliminary cut-off grades is presented in Table 2 from 0.3% Nb2O5 to 0.5% 
Nb2O5.

/T/

---------------------------------------------------------------------------
---------------------------------------------------------------------------
Table 2 - SRK Mineral Resource Sensitivity
---------------------------------------------------------------------------
---------------------------------------------------------------------------
Cut-off        Tonnage       Grade  Contained Nb2O5
Classification         (Nb2O5%)  ('000 Tonnes)    (Nb2O5%)        ('000 kg)
---------------------------------------------------------------------------
---------------------------------------------------------------------------
INDICATED                  0.50         19,100        0.74          142,000
---------------------------------------------------------------------------
---------------------------------------------------------------------------
INDICATED                  0.40         22,600        0.70          157,600
---------------------------------------------------------------------------
---------------------------------------------------------------------------
INDICATED                  0.30         28,200        0.63          177,000
---------------------------------------------------------------------------
---------------------------------------------------------------------------

---------------------------------------------------------------------------
---------------------------------------------------------------------------
INFERRED                   0.50         63,700        0.74          469,600
---------------------------------------------------------------------------
---------------------------------------------------------------------------
INFERRED                   0.40         87,000        0.66          573,300
---------------------------------------------------------------------------
---------------------------------------------------------------------------
INFERRED                   0.30        132,800        0.55          733,700
---------------------------------------------------------------------------
---------------------------------------------------------------------------

/T/

Readers should note that this update only includes the results of phase 1 
drilling operations. Work is currently on-going to improve the confidence in 
the current geological model through additional drilling and further validation 
of historical databases. Validation work is aimed to be completed with the 
completion of phase 2 drilling operations in the 4th quarter, at which point 
the company intends to deliver a follow up resource estimate which will include 
that data.

"Drill results have far exceeded our expectations on this deposit, and we are a 
very pleased to be able to deliver this resource update to shareholders," 
stated Mark A. Smith, CEO of NioCorp. "We are also very impressed with the 
significant progress being achieved on the metallurgy program as we rapidly 
approach the pilot plant test stage. The information we now know, combined with 
the upcoming pilot plant results and the updated resource estimate before year 
end, will dovetail into the extensive engineering design work that SRK are 
diligently completing, in order to fully meet our overall objectives for this 
world-class project."

The Company will file the complete NI43-101 compliant report on SEDAR and it 
will be available on the Company's website within the prescribed timeline.

Qualified Persons:

Martin Pittuck, MSc., C.Eng, MIMMM of SRK Consulting (UK) Ltd., a Qualified 
Person as defined by National Instrument 43-101, is responsible for the Elk 
Creek resource estimation and has read and approved the technical information 
contained in this news release.

About the Company: NioCorp are developing the only primary niobium deposit 
known to be under development in the U.S., and the highest grade undeveloped 
niobium deposit in North America, located near Elk Creek, Nebraska. The Company 
has filed an NI43-101 compliant resource report, available on SEDAR, and is in 
the process of filing the updated NI43-101 compliant resource estimate reported 
in this press release. Niobium is mainly used in the form of Ferro-Niobium to 
produce HSLA (High Strength, Low Alloy) steel, to produce lighter, stronger 
steel for use in automotive, structural and pipeline industries. The U.S. 
imports 100% of its niobium needs.

ON BEHALF OF THE BOARD

Peter Dickie, Director, President and Corporate Secretary

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

Certain statements contained in this press release may constitute 
forward-looking statements. Such forward-looking statements are based upon 
NioCorp's reasonable expectations and business plan at the date hereof, which 
are subject to change depending on economic, political and competitive 
circumstances and contingencies. Readers are cautioned that such 
forward-looking statements involve known and unknown risks, uncertainties and 
other factors that may cause a change in such assumptions and the actual 
outcomes and estimates to be materially different from those estimated or 
anticipated future results, achievements or position expressed or implied by 
those forward-looking statements. Risks, uncertainties and other factors that 
could cause NioCorp's plans or prospects to change include changes in demand 
for and price of commodities (such as fuel and electricity) and currencies; 
changes or disruptions in the securities markets; legislative, political or 
economic developments; the need to obtain permits and comply with laws and 
regulations and other regulatory requirements; the possibility that actual 
results of work may differ from projections/expectations or may not realize the 
perceived potential of NioCorp's projects; risks of accidents, equipment 
breakdowns and labour disputes or other unanticipated difficulties or 
interruptions; the possibility of cost overruns or unanticipated expenses in 
development programs; operating or technical difficulties in connection with 
exploration, mining or development activities; the speculative nature of 
mineral exploration and development, including the risks of diminishing 
quantities of grades of reserves and resources; and the risks involved in the 
exploration, development and mining business. NioCorp disclaims any intention 
or obligation to update or revise any forward-looking statements whether as a 
result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

NioCorp Developments Ltd.
(604) 568-7365
www.NioCorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=499573988