Source	Marketwire
Date	09/09/2014
Time	05:32:15 AM

Company	 WEST KIRKLAND MINING INC.
Title	West Kirkland Cuts 50.29 Meters of 0.73 Grams Per Tonne Gold at Three 
Hills, Discovers Additional Near Surface Gold on Hasbrouck





    CDNX Symbol: WKM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: West Kirkland Mining Inc.

TSX VENTURE SYMBOL: WKM

September 9, 2014

West Kirkland Cuts 50.29 Meters of 0.73 Grams Per Tonne Gold at Three Hills, 
Discovers Additional Near Surface Gold on Hasbrouck


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 9, 2014) - West Kirkland 
Mining Inc. (TSX VENTURE:WKM) today announces that in its first phase of 
exploration drilling, the Company intersected 50.29 meters of 0.73 grams per 
tonne (g/t) gold (Au) on the Three Hills deposit and discovered additional near 
surface mineralization on the Hasbrouck deposit, both located near Tonopah, 
Nevada. On the Hasbrouck deposit, drilling followed up on rock chip samples 
with assays including 24.6 g/t Au.

Three Hills

The Company drilled four exploration holes on the eastern flank of the Three 
Hills deposit, testing a newly developed structural interpretation of the 
deposit. West Kirkland tested for zones of structural preparation near the 
contact between the Siebert formation and the Fraction Tuff.

Hole TH14R-004 returned 50.29 meters grading 0.73 g/t Au and 3.22 g/t Ag within 
a zone of intersecting structures. Mineralization started 26 meters above the 
contact between the Siebert and Fraction Tuff and continued 24.4 meters below 
the contact. This intercept is approximately 70 meters northwest of hole 
TH12R-15, drilled by a previous owner, which returned 66 meters of 3.3 g/t Au 
in a similar setting at the same elevation.

A table of West Kirkland's 2014 Exploration drilling at Three Hills is 
presented below.

/T/

-------------------------------------------------------------
Hole ID    From (m)    To (m)  Length (m)  Au (g/t)  Ag (g/t)
-------------------------------------------------------------
TH14R-002    161.54    174.26       12.72      0.61      4.04
-------------------------------------------------------------
TH14R-003    128.02    134.11        6.09      0.48      3.16
-------------------------------------------------------------
and          153.92    158.50        4.58      0.97      7.16
-------------------------------------------------------------
TH14R-004    172.21    222.50       50.29      0.73      3.22
-------------------------------------------------------------
including    172.21    181.36        9.15      2.27      2.03
-------------------------------------------------------------
TH14R-005    179.83    185.93        6.10      1.03      4.98
-------------------------------------------------------------

/T/

(i)true thickness has been estimated by Company geologists to be approximately 
70% of length

"Drilling at Three Hills confirmed the deposit remains open to the east, and 
provided a high grade structural corridor of mineralization that will be tested 
with follow up work," said Michael G. Allen, Vice President of Exploration for 
West Kirkland. "The high grade intercepts in hole TH12R-015 and TH14R-004 have 
the potential to expand the resource further to the east."

West Kirkland's TH14R-002 returned 12.72 meters grading 0.61 g/t Au and 4.04 
g/t Ag starting from 161.54 meters at the Siebert-Fraction contact. This 
intercept was 50 meters south of the previously drilled TH12R-015.

Hole TH14R-003 returned 6.09 meters grading 0.48 g/t Au and 3.16 g/t Ag 
starting at 128.02 m down the hole, at the Siebert Fraction contact, plus an 
additional 4.58 meters grading 0.97 g/t Au and 7.16 g/t Ag starting at 153.92 
meters within the Fraction Tuff, suggesting a further mineralized structure 
exists.

TH14R-005 tested further to the east where the Company projected the 
Siebert/Fraction contact to be nearing surface. Mineralization in this hole was 
entirely in the Fraction Tuff and returned 6.10 meters grading 1.03 g/t Au and 
4.98 g/t Ag. It is thought that this hole intercepted the northwest structure 
which hosts mineralization in holes TH12R-15 and TH14R-004.

Holes TH14R-001 and TH14R-006 were respectively drilled to test a potential 
leach pad and waste rock pile location for mineralization ahead of dedicating 
these areas for this purpose in the ongoing prefeasibility study. These areas 
have been deemed to be appropriate for this purpose as they are near the 
current deposit for short haulage distances and no new mineralization was found 
in these holes.

Hasbrouck

Drilling at the Hasbrouck deposit followed-up on rock chip samples collected by 
West Kirkland. This sampling focused on an underexplored area on the northeast 
flank of Hasbrouck Peak. This sampling returned high grades, including 24.6 g/t 
Au, 6.65 g/t Au and 4.13 g/t Au in select rock chips, and indicated the 
potential to develop significant tonnage in close proximity to existing 
resources. Although over 600 holes have been completed at Hasbrouck and Three 
Hills in previous drilling, there is no documented drill testing in this area. 
The area is within 100 meters of the conceptual pit outline in the ongoing 
prefeasibility study.

Drilling by West Kirkland returned 6.09 meters of 0.38 g/t Au with 6.48 g/t Ag 
starting at depth of 6.10 meters in hole HSB14R-009 and HB14R-010 returned 4.57 
meters of 0.66 g/t Au with 12.2 g/t Ag starting at a depth of 7.62 meters. Each 
mineralized intercept terminated at the contact between the Siebert formation 
and the underlying Fraction Tuff. A second phase of mapping, sampling, and 
trenching will be completed in areas of thicker Siebert formation towards the 
potential pit area, with the goal of establishing refined drill targets with 
potential for thicker mineralized intercepts. The Siebert formation, which 
hosts the main deposit, thickens toward the known resources of the Hasbrouck 
deposit.

Holes HSB14R-001 and HSB-002 were drilled to test for a root zone and a 
projected strike extension of the Hasbrouck Deposit respectively and did not 
return significant results. HSB14R-003 to HSB14R-006 were drilled to confirm 
the appropriateness of potential infrastructure sites on the property. These 
sites did not have significant new mineralization and can be fixed for the 
prefeasibility study.

Maps of recent work at Hasbrouck and Three Hills can be viewed by visiting the 
company's website at www.wkmining.com or from the following link: 
http://wkmining.com/projects/hasbrouck_overview/maps/

About the WKM Hasbrouck Project

The Hasbrouck Project consists of two oxidized deposits, Hasbrouck and Three 
Hills, both with at-surface and near-surface mineralization, potential for 
minimal pre-strip and low overall stripping ratios as a result of the deposit 
geometry, as outlined in the 43-101 Resource Report dated February 21, 2014 and 
filed on SEDAR February 24, 2014. West Kirkland has initiated a prefeasibility 
study on the Hasbrouck Project and has commenced its exploration program as 
outlined in its news release dated June 3, 2014.

Qualified Persons

Michael G. Allen, Vice President of Exploration for West Kirkland, and a 
non-independent Qualified Person as defined by NI 43-101, has reviewed the 
information contained in this news release and has verified the data.

Quality Assurance/Quality Control

West Kirkland Mining utilizes a well-documented system of inserting blanks and 
standards into the assay stream and has a strict chain of custody. Assays are 
completed at independent labs, which also have internal quality assurance and 
quality control mechanisms. Assays were performed by ALS Chemex Labs Ltd., by 
fire assay and ICP methods.

About West Kirkland Mining Inc.

West Kirkland was formed in 2010 to focus on gold exploration along major 
geological trends in North America. The Company has consolidated significant 
mineral rights positions within the known gold trends of Nevada and Utah, 
including the recently acquired the Hasbrouck and Three Hills properties in 
southwestern Nevada. The founders and Board members of West Kirkland have 
successful experience in gold discovery, mine development and mine operations 
in Nevada and other gold producing jurisdictions in North America.

Disclaimer for Forward-Looking Information

This press release contains forward-looking information or forward-looking 
statements (collectively "forward-looking information") within the meaning of 
applicable securities laws. Forward-looking information is typically identified 
by words such as: "believe", "expect", "anticipate", "intend", "estimate", 
"postulate" and similar expressions, or are those, which, by their nature, 
refer to future events. Forward-looking information in this news release 
includes, without limitation, the completion of the Prefeasibility Study, the 
project approach of the Prefeasibility Study and exploration and all 
information under the heading "Prefeasibility Study Detail", including the 
Prefeasibility Study budget. Although West Kirkland believes that such timing 
and expenses as set out in this press release are reasonable, it can give no 
assurance that such expectations and estimates will prove to be correct. The 
Company cautions investors that any forward-looking information provided by the 
Company is not a guarantee of future results or performance, and that actual 
results may differ materially from those in forward-looking information as a 
result of various factors, including, but not limited to, the state of the 
financial markets for the Company's equity securities, the state of the market 
for gold or other minerals that may be produced generally, variations in the 
nature, quality and quantity of any mineral deposits that may be located, the 
Company's ability to obtain any necessary permits, consents or authorizations 
required for its activities, to raise the necessary capital or to be fully able 
to implement its business strategies and other risks associated with the 
exploration and development of mineral properties. The reader is referred to 
the Company's public filings for a more complete discussion of such risk 
factors and their potential effects which may be accessed through the Company's 
profile on SEDAR at www.sedar.com.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

West Kirkland Mining Inc.
R. Michael Jones or Knox Henderson
(604) 685-8311

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=497801764