Source	MARKET NEWS
Date	09/09/2014
Time	05:57:45 AM

Company	 West Kirkland Mining Inc.
Title	Cuts 
50.29 Meters Of 0.73 Grams Per Tonne Gold A





    CDNX Symbol: WKM











Press Release	





WEST KIRKLAND MINING INC ("WKM-V")
- Cuts 50.29 Meters Of 0.73 Grams Per Tonne Gold At Three Hills,
- Discovers Additional Near Surface Gold On Hasbrouck

West Kirkland Mining Inc. announces that in its first phase of
exploration drilling, the Company intersected 50.29 meters of 0.73
grams per tonne (g/t) gold (Au) on the Three Hills deposit and
discovered additional near surface mineralization on the Hasbrouck
deposit, both located near Tonopah, Nevada. On the Hasbrouck deposit,
drilling followed up on rock chip samples with assays including 24.6
g/t Au.

Three Hills

The Company drilled four exploration holes on the eastern flank of
the Three Hills deposit, testing a newly developed structural
interpretation of the deposit. West Kirkland tested for zones of
structural preparation near the contact between the Siebert formation
and the Fraction Tuff.

Hole TH14R-004 returned 50.29 meters grading 0.73 g/t Au and 3.22
g/t Ag within a zone of intersecting structures. Mineralization started
26 meters above the contact between the Siebert and Fraction Tuff and
continued 24.4 meters below the contact. This intercept is
approximately 70 meters northwest of hole TH12R-15, drilled by a
previous owner, which returned 66 meters of 3.3 g/t Au in a similar
setting at the same elevation.

A table of West Kirkland's 2014 Exploration drilling at Three
Hills is presented below.

//st
Hole ID         From (m)    To (m)    Length (m)    Au (g/t)    Ag (g/t)
TH14R-002         161.54    174.26         12.72        0.61        4.04
TH14R-003         128.02    134.11          6.09        0.48        3.16
&                 153.92    158.50          4.58        0.97        7.16
TH14R-004         172.21    222.50         50.29        0.73        3.22
including         172.21    181.36          9.15        2.27        2.03
TH14R-005         179.83    185.93          6.10        1.03        4.98

//et

*true thickness has been estimated by Company geologists to be
approximately 70% of length

"Drilling at Three Hills confirmed the deposit remains open to the
east, and provided a high grade structural corridor of mineralization
that will be tested with follow up work," said Michael G. Allen, Vice
President of Exploration for West Kirkland. "The high grade intercepts
in hole TH12R-015 and TH14R-004 have the potential to expand the
resource further to the east."

West Kirkland's TH14R-002 returned 12.72 meters grading 0.61 g/t
Au and 4.04 g/t Ag starting from 161.54 meters at the Siebert-Fraction
contact. This intercept was 50 meters south of the previously drilled
TH12R-015.

Hole TH14R-003 returned 6.09 meters grading 0.48 g/t Au and 3.16
g/t Ag starting at 128.02 m down the hole, at the Siebert Fraction
contact, plus an additional 4.58 meters grading 0.97 g/t Au and 7.16
g/t Ag starting at 153.92 meters within the Fraction Tuff, suggesting a
further mineralized structure exists.

TH14R-005 tested further to the east where the Company projected
the Siebert/Fraction contact to be nearing surface. Mineralization in
this hole was entirely in the Fraction Tuff and returned 6.10 meters
grading 1.03 g/t Au and 4.98 g/t Ag. It is thought that this hole
intercepted the northwest structure which hosts mineralization in holes
TH12R-15 and TH14R-004.

Holes TH14R-001 and TH14R-006 were respectively drilled to test a
potential leach pad and waste rock pile location for mineralization
ahead of dedicating these areas for this purpose in the ongoing
prefeasibility study. These areas have been deemed to be appropriate
for this purpose as they are near the current deposit for short haulage
distances and no new mineralization was found in these holes.

Hasbrouck

Drilling at the Hasbrouck deposit followed-up on rock chip samples
collected by West Kirkland. This sampling focused on an underexplored
area on the northeast flank of Hasbrouck Peak. This sampling returned
high grades, including 24.6 g/t Au, 6.65 g/t Au and 4.13 g/t Au in
select rock chips, and indicated the potential to develop significant
tonnage in close proximity to existing resources. Although over 600
holes have been completed at Hasbrouck and Three Hills in previous
drilling, there is no documented drill testing in this area. The area
is within 100 meters of the conceptual pit outline in the ongoing
prefeasibility study.

Drilling by West Kirkland returned 6.09 meters of 0.38 g/t Au with
6.48 g/t Ag starting at depth of 6.10 meters in hole HSB14R-009 and
HB14R-010 returned 4.57 meters of 0.66 g/t Au with 12.2 g/t Ag starting
at a depth of 7.62 meters. Each mineralized intercept terminated at the
contact between the Siebert formation and the underlying Fraction Tuff.
A second phase of mapping, sampling, and trenching will be completed in
areas of thicker Siebert formation towards the potential pit area, with
the goal of establishing refined drill targets with potential for
thicker mineralized intercepts. The Siebert formation, which hosts the
main deposit, thickens toward the known resources of the Hasbrouck
deposit.

Holes HSB14R-001 and HSB-002 were drilled to test for a root zone
and a projected strike extension of the Hasbrouck Deposit respectively
and did not return significant results. HSB14R-003 to HSB14R-006 were
drilled to confirm the appropriateness of potential infrastructure
sites on the property. These sites did not have significant new
mineralization and can be fixed for the prefeasibility study.

Maps of recent work at Hasbrouck and Three Hills can be viewed by
visiting the company's website at www.wkmining.com or from the
following link: http://wkmining.com/projects/hasbrouck_overview/maps/

About the WKM Hasbrouck Project

The Hasbrouck Project consists of two oxidized deposits, Hasbrouck
and Three Hills, both with at-surface and near-surface mineralization,
potential for minimal pre-strip and low overall stripping ratios as a
result of the deposit geometry, as outlined in the 43-101 Resource
Report dated February 21, 2014 and filed on SEDAR February 24, 2014.
West Kirkland has initiated a prefeasibility study on the Hasbrouck
Project and has commenced its exploration program as outlined in its
news release dated June 3, 2014.

Qualified Persons

Michael G. Allen, Vice President of Exploration for West Kirkland,
and a non-independent Qualified Person as defined by NI 43-101, has
reviewed the information contained in this news release and has
verified the data.

Quality Assurance/Quality Control

West Kirkland Mining utilizes a well-documented system of
inserting blanks and standards into the assay stream and has a strict
chain of custody. Assays are completed at independent labs, which also
have internal quality assurance and quality control mechanisms. Assays
were performed by ALS Chemex Labs Ltd., by fire assay and ICP methods.

About West Kirkland Mining Inc.

West Kirkland was formed in 2010 to focus on gold exploration
along major geological trends in North America. The Company has
consolidated significant mineral rights positions within the known gold
trends of Nevada and Utah, including the recently acquired the
Hasbrouck and Three Hills properties in southwestern Nevada. The
founders and Board members of West Kirkland have successful experience
in gold discovery, mine development and mine operations in Nevada and
other gold producing jurisdictions in North America.

Disclaimer for Forward-Looking Information

This press release contains forward-looking information or
forward-looking statements (collectively "forward-looking information")
within the meaning of applicable securities laws. Forward-looking
information is typically identified by words such as: "believe",
"expect", "anticipate", "intend", "estimate", "postulate" and similar
expressions, or are those, which, by their nature, refer to future
events. Forward-looking information in this news release includes,
without limitation, the completion of the Prefeasibility Study, the
project approach of the Prefeasibility Study and exploration and all
information under the heading "Prefeasibility Study Detail", including
the Prefeasibility Study budget. Although West Kirkland believes that
such timing and expenses as set out in this press release are
reasonable, it can give no assurance that such expectations and
estimates will prove to be correct. The Company cautions investors that
any forward-looking information provided by the Company is not a
guarantee of future results or performance, and that actual results may
differ materially from those in forward-looking information as a result
of various factors, including, but not limited to, the state of the
financial markets for the Company's equity securities, the state of the
market for gold or other minerals that may be produced generally,
variations in the nature, quality and quantity of any mineral deposits
that may be located, the Company's ability to obtain any necessary
permits, consents or authorizations required for its activities, to
raise the necessary capital or to be fully able to implement its
business strategies and other risks associated with the exploration and
development of mineral properties. The reader is referred to the
Company's public filings for a more complete discussion of such risk
factors and their potential effects which may be accessed through the
Company's profile on SEDAR at www.sedar.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TSX Venture closing price for WKM-V
Date: 2014/09/08
Closing Price: 0.11

TEL:  (604) 685-8311  R. Michael Jones or Knox Henderson
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1425100016TS11425100872-05552720140909