Source	Marketwire
Date	09/09/2014
Time	04:45:36 AM

Company	 GOLDSTRIKE RESOURCES LTD.
Title	Goldstrike Confirms Large Drill Target at Plateau Gold Dome





    CDNX Symbol: GSR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Goldstrike Resources Ltd.

TSX VENTURE SYMBOL: GSR
PINKSHEETS SYMBOL: APRAF
FRANKFURT SYMBOL: KCG1

September 9, 2014

Goldstrike Confirms Large Drill Target at Plateau Gold Dome


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 9, 2014) - Goldstrike 
Resources Ltd. (TSX VENTURE:GSR)(PINKSHEETS:APRAF)(FRANKFURT:KCG1) is pleased 
to report that a three- dimensional induced polarization (IP) survey has 
outlined a large, well defined chargeability anomaly with strong gold potential 
near discovery hole PSVG13-03, which intersected 7.60 grams per tonne gold over 
9.03 metres (News Release September 9, 2013). This anomaly underlying Gold Dome 
is interpreted to represent disseminated mineralization similar to that 
associated with bonanza grade gold found in surface grab samples and drill 
core. The core of the anomaly measures approximately 200 metres by 100 metres, 
and extends from about 100 metres below surface to 200 metres depth (the survey 
limit). It is indicated to be open to the southeast and to depth and remains to 
be drill tested.

The shallowest part of the IP anomaly on Gold Dome is located immediately east 
of the VG zone, which means that the 2013 drilling, which intersected high 
grade gold mineralization, did not test the anomaly. An initial projection of 
IP data to surface suggests the inferred mineralized body strikes northwest- 
southeast and may have a northwest or southeast plunge, consistent with major 
folds that are now believed to be a major control on the distribution of gold 
across the entire property, including the Goldstack zone, where hole PSGS13-04 
intersected 2.28 grams per tonne gold over 53.0 metres, including 10.91 grams 
per tonne gold over 10.0 metres (News Release September 9, 2013). Given the 
success of this high resolution IP survey in outlining disseminated 
mineralization in the highly silicified felsic volcanic host rocks on Gold 
Dome, Goldstrike is planning additional high resolution ground IP surveys to 
outline similar drill targets in numerous other areas on the property where 
bonanza-grade gold mineralization up to 308.49 grams per tonne (News Release 
June 23, 2014) has been found, including the Goldstack zone, the 11-kilometre 
long Goldbank trend, the two kilometre long Ron Stack trend, and the two 
kilometre long Gold Rush zone.

Geochemical and textural evidence indicates that high grade gold mineralization 
on Gold Dome is the upper part of a single, district-scale gold system that is 
exposed on the property over a strike length of 25 kilometres, and a vertical 
extent of 1,000 metres that remains open. The Gold Dome mineralization is 
associated with extensive silicification, alunite and sericite spectral 
signatures, significant strong correlations of gold with mercury, selenium, 
thallium, and vanadium, and typically epithermal textures including silica 
flooding, comb-textured quartz, and numerous crystal-lined vugs. Arsenic, 
tellurium, and sodium are dominant gold pathfinders along the main Yellow Giant 
Trend. In addition, base metals are associated with gold along the Ron Stack 
trend, where coarse pyroclastics indicate proximity to a volcanic source, 
indicating a deeper, more mesothermal environment. The Goldstack zone also 
appears to represent a deeper part of the system, where gold correlates 
strongly with silver and antimony, moderately with arsenic, tungsten, bismuth, 
and lead, and negatively with thallium. Mapping and petrography show that the 
Goldstack mineralization is hosted in hydrothermal breccia zones, within a 
subvolcanic porphyry that forms part of the same volcanic system that is 
believed to be the ultimate source of the gold mineralization in the area. The 
Gold Rush zone north of the Hess River has a different suite of geochemical 
pathfinders that reflect a distal, low-temperature environment and sedimentary 
host rocks. Gold in all the zones appears to have been re-concentrated in the 
axial regions of large folds that formed during the same phase of regional 
deformation.

"We are very pleased to have identified such a compelling target in the Gold 
Dome area," said Goldstrike's Chief Geologist, Trevor Bremner. "The 
geophysicists have stated that the quality of the data is excellent due to the 
high resistivity of the rock, which made for very clean readings. We look 
forward to drill-testing this anomaly at the earliest opportunity. Goldstrike's 
technical team believes that IP is an excellent tool to outline similar drill 
targets in the Goldstack, Goldbank, Ron Stack, and Gold Rush zones."

Results from Goldstrike's 2014 exploration program on the Lucky Strike property 
in the White River gold district are expected in the near future.

Sample analysis and assaying for all of Goldstrike's projects have been 
conducted by Acme Analytical Laboratories Ltd in Vancouver, BC, which is ISO 
9001 accredited. Soil samples are dried at 60C, and 100 grams is sieved to -80 
mesh. A 15 gram sample split is then leached in aqua regia at 95 degrees C, and 
analyzed by a 36-element ICP package that includes semi-quantitative gold. Rock 
samples are crushed to 80% -10 mesh, and a 250 gram sample split is pulverized 
to 85% -200 mesh. 30 gram charges are then assayed for gold using fire assay 
fusion and ICP-ES finish with a lower detection limit of 2 ppb, and an upper 
detection limit of 10 ppm Au. In addition, 0.5 mg charges are digested by 
modified 1:1:1 aqua regia (HCl-HNO3-H20) and analyzed by 36-element ICP-MS that 
also includes semi-quantitative gold with a lower detection limit of 0.5 ppb Au 
and an upper detection limit of 100 ppm Au. All samples containing visible gold 
or returning assays of more than 10 ppm gold are subjected to metallic fire 
assays, for which the plus fraction is finished gravimetrically and the minus 
fraction is finished with AA. Rigorous procedures are in place regarding sample 
collection, chain of custody and data entry. Certified assay standards, 
duplicate samples and blanks are routinely inserted into the sample stream to 
ensure integrity of the assay process.

Note: Grab samples are selective by nature, and are unlikely to represent 
average grades on the property.

Trevor J. Bremner, P. Geo., Chief Geologist and Goldstrike Board Member, is a 
qualified person, as defined by National Instrument 43-101, for Goldstrike's 
Yukon exploration projects and supervised the preparation of, and has reviewed 
and approved, the technical information in this release.

/T/

ON BEHALF OF THE BOARD

Terrence E. King

President and Chief Executive Officer

/T/

For new sections and maps on the Plateau property, please visit Goldstrike's 
website at GoldstrikeResources.com. For further information follow the 
Company's tweets at Twitter.com/GoldstrikeRes.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This news release may contain forward-looking statements including but not 
limited to comments regarding the timing and content of upcoming work programs, 
geological interpretations, receipt of property titles, potential mineral 
recovery processes, etc. Forward-looking statements address future events and 
conditions, and therefore involve inherent risks and uncertainties. Actual 
results may differ materially from those currently anticipated in such 
statements. The reader is cautioned not to place undue reliance on 
forward-looking statements.

To view the figures accompanying this press release, please visit the following 
link:

http://media3.marketwire.com/docs/966932.pdf

- 30 -

CONTACT INFO:

Jeff Stuart
King James Capital Corporation
Investor Relations
(604) 210-2150
jstuart@kingjamescapital.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=497757757