Source	MARKET NEWS
Date	09/09/2014
Time	05:05:36 AM

Company	 Goldstrike Resources Ltd.
Title	Confirms Large Drill Target At Plateau Gold Dome





    CDNX Symbol: GSR











Press Release	





Confirms Large Drill Target At Plateau Gold Dome --->@NEWS RELEASE
GOLDSTRIKE RESOURCES LTD ("GSR-V;APRAF-0")
- Confirms Large Drill Target At Plateau Gold Dome

Goldstrike Resources Ltd. is pleased to report that a three-
dimensional induced polarization (IP) survey has outlined a large, well
defined chargeability anomaly with strong gold potential near discovery
hole PSVG13-03, which intersected 7.60 grams per tonne gold over 9.03
metres (News Release September 9, 2013). This anomaly underlying Gold
Dome is interpreted to represent disseminated mineralization similar to
that associated with bonanza grade gold found in surface grab samples
and drill core. The core of the anomaly measures approximately 200
metres by 100 metres, and extends from about 100 metres below surface
to 200 metres depth (the survey limit). It is indicated to be open to
the southeast and to depth and remains to be drill tested.

The shallowest part of the IP anomaly on Gold Dome is located
immediately east of the VG zone, which means that the 2013 drilling,
which intersected high grade gold mineralization, did not test the
anomaly. An initial projection of IP data to surface suggests the
inferred mineralized body strikes northwest- southeast and may have a
northwest or southeast plunge, consistent with major folds that are now
believed to be a major control on the distribution of gold across the
entire property, including the Goldstack zone, where hole PSGS13-04
intersected 2.28 grams per tonne gold over 53.0 metres, including 10.91
grams per tonne gold over 10.0 metres (News Release September 9, 2013).
Given the success of this high resolution IP survey in outlining
disseminated mineralization in the highly silicified felsic volcanic
host rocks on Gold Dome, Goldstrike is planning additional high
resolution ground IP surveys to outline similar drill targets in
numerous other areas on the property where bonanza-grade gold
mineralization up to 308.49 grams per tonne (News Release June 23,
2014) has been found, including the Goldstack zone, the 11-kilometre
long Goldbank trend, the two kilometre long Ron Stack trend, and the
two kilometre long Gold Rush zone.

Geochemical and textural evidence indicates that high grade
gold mineralization on Gold Dome is the upper part of a single,
district-scale gold system that is exposed on the property over a
strike length of 25 kilometres, and a vertical extent of 1,000 metres
that remains open. The Gold Dome mineralization is associated with
extensive silicification, alunite and sericite spectral signatures,
significant strong correlations of gold with mercury, selenium,
thallium, and vanadium, and typically epithermal textures including
silica flooding, comb-textured quartz, and numerous crystal-lined vugs.
Arsenic, tellurium, and sodium are dominant gold pathfinders along the
main Yellow Giant Trend. In addition, base metals are associated with
gold along the Ron Stack trend, where coarse pyroclastics indicate
proximity to a volcanic source, indicating a deeper, more mesothermal
environment. The Goldstack zone also appears to represent a deeper part
of the system, where gold correlates strongly with silver and antimony,
moderately with arsenic, tungsten, bismuth, and lead, and negatively
with thallium. Mapping and petrography show that the Goldstack
mineralization is hosted in hydrothermal breccia zones, within a
subvolcanic porphyry that forms part of the same volcanic system that
is believed to be the ultimate source of the gold mineralization in the
area. The Gold Rush zone north of the Hess River has a different suite
of geochemical pathfinders that reflect a distal, low-temperature
environment and sedimentary host rocks. Gold in all the zones appears
to have been re-concentrated in the axial regions of large folds that
formed during the same phase of regional deformation.

"We are very pleased to have identified such a compelling
target in the Gold Dome area," said Goldstrike's Chief Geologist,
Trevor Bremner. "The geophysicists have stated that the quality of the
data is excellent due to the high resistivity of the rock, which made
for very clean readings. We look forward to drill-testing this anomaly
at the earliest opportunity. Goldstrike's technical team believes that
IP is an excellent tool to outline similar drill targets in the
Goldstack, Goldbank, Ron Stack, and Gold Rush zones."

Results from Goldstrike's 2014 exploration program on the Lucky
Strike property in the White River gold district are expected in the
near future.

Sample analysis and assaying for all of Goldstrike's projects
have been conducted by Acme Analytical Laboratories Ltd in Vancouver,
BC, which is ISO 9001 accredited. Soil samples are dried at 60C, and
100 grams is sieved to -80 mesh. A 15 gram sample split is then leached
in aqua regia at 95 degrees C, and analyzed by a 36-element ICP package
that includes semi-quantitative gold. Rock samples are crushed to 80%
-10 mesh, and a 250 gram sample split is pulverized to 85% -200 mesh.
30 gram charges are then assayed for gold using fire assay fusion and
ICP-ES finish with a lower detection limit of 2 ppb, and an upper
detection limit of 10 ppm Au. In addition, 0.5 mg charges are digested
by modified 1:1:1 aqua regia (HCl-HNO3-H20) and analyzed by 36-element
ICP-MS that also includes semi-quantitative gold with a lower detection
limit of 0.5 ppb Au and an upper detection limit of 100 ppm Au. All
samples containing visible gold or returning assays of more than 10 ppm
gold are subjected to metallic fire assays, for which the plus fraction
is finished gravimetrically and the minus fraction is finished with AA.
Rigorous procedures are in place regarding sample collection, chain of
custody and data entry. Certified assay standards, duplicate samples
and blanks are routinely inserted into the sample stream to ensure
integrity of the assay process.

Note: Grab samples are selective by nature, and are unlikely to
represent average grades on the property.

Trevor J. Bremner, P. Geo., Chief Geologist and Goldstrike
Board Member, is a qualified person, as defined by National Instrument
43-101, for Goldstrike's Yukon exploration projects and supervised the
preparation of, and has reviewed and approved, the technical
information in this release.

//st
ON BEHALF OF THE BOARD

Terrence E. King

President & Chief Executive Officer
//et

For new sections and maps on the Plateau property, please visit
Goldstrike's website at GoldstrikeResources.com. For further
information follow the Company's tweets at Twitter.com/GoldstrikeRes.

Neither TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release may contain forward-looking statements
including but not limited to comments regarding the timing and content
of upcoming work programs, geological interpretations, receipt of
property titles, potential mineral recovery processes, etc.
Forward-looking statements address future events and conditions, and
therefore involve inherent risks and uncertainties. Actual results may
differ materially from those currently anticipated in such statements.
The reader is cautioned not to place undue reliance on forward-looking
statements.

To view the figures accompanying this press release, please
visit the following link:

http://media3.marketwire.com/docs/966932.pdf
TSX Venture closing price for GSR-V
Date: 2014/09/08
Closing Price: 0.17

TEL: (604) 210-2150           Jeff Stuart, Investor Relations
jstuart@kingjamescapital.com  King James Capital Corporation
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1425100003TS11425100471-05024320140909