Source	MARKET NEWS
Date	09/09/2014
Time	03:35:19 AM

Company	 Red Eagle Mining Corporation
Title	Completes 
Feasibility Study With 52% Irr





    CDNX Symbol: RD











Press Release	





RED EAGLE MINING CORP ("RD-V;RDEMF-0")
- Completes Feasibility Study With 52% Irr

Red Eagle Mining Corporation is pleased to announce the results
from the positive Feasibility Study for the San Ramon deposit on its
100% owned Santa Rosa Gold Project located in Antioquia, Colombia.
Highlights include (all amounts in US$):

Based on a long-term forecast price of $1,300/ounce gold
("Base Case") post-tax Internal Rate of Return is 52% with a payback
period of just 1.5 years;

Initial capital costs for the project are $63 million plus
$7 million contingency and $4 million of recoverable VAT;

Average cash costs of $600/ounce and all-in sustaining
costs of $758/ounce; and

Production in the first two years will average 71,000
ounces of gold per year at an average grade of 6.48 grams gold per
tonne.

Table 1 - Summary of San Ramon Pre-Tax Economic Results by Gold Price

//st
Pre-Tax                 Alternative      Base Case    Alternative
Case                          Case
Gold Price (ounce)     $      1,100  $       1,300  $       1,500
Net Cash Flow          $ 98 million  $ 171 million  $ 243 million
Net Present Value (5%) $ 74 million  $ 135 million  $ 195 million
Internal Rate of Return         39%            62%            82%
Payback                   1.7 years      1.3 years      1.1 years
//et

Table 2 - Summary of San Ramon Post-Tax Economic Results by Gold Price

//st
Post-Tax                Alternative     Base Case     Alternative
Case                          Case
Gold Price (ounce)     $      1,100 $       1,300   $       1,500
Net Cash Flow          $ 77 million $ 138 million   $ 211 million
Net Present Value (5%) $ 56 million $ 108 million   $ 168 million
Internal Rate of Return         32%           52%             74%
Payback                   1.9 years     1.5 years       1.1 years
//et

The Feasibility Study ("FS") was prepared by Lycopodium Minerals
Canada Ltd. ("Lycopodium") in accordance with the definitions in
Canadian National Instrument 43-101 ("NI 43-101"). Lycopodium is an
international engineering and project management consultancy
headquartered in Australia, which has completed feasibility studies and
provided Engineering, Procurement and Construction Management ("EPCM")
services to a large number of successful gold projects globally.

Project Mineral Reserves

The reserves outlined in the Feasibility Study are shown in Table
3 below and use an average cut-off of 2.00 grams gold per tonne and a
minimum mining width of 2.5 metres. Proven and Probable reserves
include dilution by Measured and Indicated resources below the mining
cutoff grade inside of mineable areas with an average grade of 1.60
grams gold per tonne.

Table 3 - San Ramon Reserves Estimate

//st
Tonnes      Gold (g/t)      Gold (ounces)
Proven                 429,000            5.95             82,000
Probable             1,995,000            5.04            323,000
Proven & Probable    2,424,000            5.20            405,000
//et

Mining and Processing

The Feasibility Study is based on San Ramon being an underground
mining operation using conventional shrinkage stoping mining methods
with delayed backfill using dry filtercake process tailings and
development waste. Colombian mining contractors will be utilised and
mining costs are based on contractor proposals.

The ore will be processed incorporating single-stage crushing, SAG
milling and floatation with concentrate re-grinding followed by
conventional carbon-in-leach ("CIL") processing the combined float
tails and reground concentrate to produce gold dore on site. The
leached tailings will be detoxified and filtered for use as mine
backfill and dry stacking on surface. Expected metallurgical gold
recovery is 96% with a total estimated 388,000 ounces of recoverable
gold to be produced.

The total ore mined includes 2.42 million tonnes of Proven and
Probable reserves and an additional 334,000 tonnes of internal dilution
of material that is included at zero grade. Total volume/tonnage
dilution of 23% is included in the mineable material. The plant is
designed to operate at a processing rate of 1,000 tonnes per day and a
total of 2.75 million tonnes of ore will be mined over eight years at
an average run of mine ("ROM") diluted mill feed grade of 4.57 grams
gold per tonne. San Ramon's projected annual gold production is
summarised below:

Table 4 - San Ramon Projected Eight Year Annual Gold Production

//st
Year         Tonnes     ROM Gold    Recoverable
Milled  Grade (g/t)      Gold (oz)
1           352,000         6.21         68,000
2           360,000         6.74         75,000
3           360,000         4.49         50,000
4           360,000         4.11         45,000
5           360,000         4.67         52,000
6           360,000         3.24         36,000
7           360,000         2.77         30,000
8           246,000         4.25         32,000
Years 1-8 2,758,000         4.57        388,000
//et

Capital and Operating Costs

The estimated capital and operating costs for San Ramon are
summarised below. Indirect costs include EPCM and owner's costs.
Sustaining capital for ongoing underground development has been
budgeted at $33 million throughout the eight year mine life.

Table 5 - San Ramon Initial Capital Costs

//st
Mine Underground                $               9,432,000
Processing                      $              31,458,000
Total Direct Costs              $              40,890,000
Indirect Costs                  $              17,584,000
Working Capital                 $               4,048,000
Contingency                     $               7,005,000
Total Capital Costs             $              69,527,000
Recoverable VAT                 $               4,219,000
Import Duties                   $                 399,000
Total                           $              74,145,000
//et

Table 6 - San Ramon Operating Costs

//st
$/Tonne      $/Ounce
Mining                                 37          265
Processing                             25          180
Other                                  11           75
Royalties                              11           80
Cash Costs                 $           84$         600
Sustaining Capital                     11           74
Taxes                                  12           84
All-In Sustaining Costs    $          107$         758
//et

Opportunities for enhanced economics

Dore produced will contain silver which has not been included in
reserves or the Feasibility Study economic analysis. Based on
metallurgical tests and studies, silver grades are approximately 1.85
times gold grades with recoveries of approximately 69%.

High-grade, relatively narrow, veins are known to exist across a
number of areas on the Santa Rosa Gold Project outside of the current
reserves. Over 1,700 historic adits have been mapped. These veins could
potentially be mined as separate small-scale operations to provide
high-grade feedstock to supplement mill feed grade and production.

The San Ramon Gold Deposit is open at depth (with the bulk of the
current reserves within 200 metres of the surface) and on strike,
plunging to the east on to concessions recently acquired from AngloGold
Ashanti (news release dated June 3, 2014). Delineation drilling at
depth and to the east is planned for 2015.

A number of separate exploration targets have been identified on
the 350 km Santa Rosa Gold Project and are ready for drill testing.
These targets have similar characteristics to the San Ramon Gold
Deposit with anomalous gold geochemistry, potassic alteration and
extensive historic underground and surface workings. In providing for
potential exploration success in delineating additional reserves,
current major equipment and layout has been designed with built-in
capacity to accommodate an expansion to double the throughput rates
without disrupting production. Such an expansion would include an
additional ball mill, tower mill, filter press and three leach tanks at
an estimated total cost of under $15 million.

Comparison to September 2013 Preliminary Economic Assessment

The Feasibility Study results are compared in Table 7, below, with
the figures reported in the September 2013 Preliminary Economic
Assessment ("PEA"). While there has been a modest $5 million reduction
in the Net Present Value (5%), the Internal Rate of Return has
escalated from 38% to 52%. This has predominately been driven by a 19%
reduction in initial capital costs and a 35% reduction in sustaining
capital. As expected, life of mine recoverable ounces has declined
reflecting the fact that inferred resources, while included in the PEA,
are excluded from the Feasibility Study mine plan. As average annual
production is broadly unchanged the exclusion of the inferred ounces
has expectedly reduced mine life from ten to eight years. Metallurgical
recoveries have improved from 93% to 96%. Cash costs and all-in
sustaining costs have decreased by $20/ounce and $60/ounce
respectively.

Table 7 - San Ramon PEA/FS Comparison

//st
2013 PEA              2014 FS
Gold Price (oz)              $         1,300      $         1,300
Net Present Value (5%)       $   113 million      $   108 million
Internal Rate of Return                  38%                  52%
Payback                            1.7 years            1.5 years
Mine Life                           10 years              8 years
Min. Mining Width                 2.0 metres           2.5 metres
ROM Gold Grade (g/t)                    4.76                 4.57
Metallurgical Recovery                   93%                  96%
Recoverable Gold (oz)                514,000              388,000
Initial Capital Costs        $    91 million      $    74 million
Sustaining Capital           $    51 million      $    33 million
Cash Costs                   $           620      $           600
All-In Sustaining Costs      $           818      $           758
//et

The complete NI 43-101 Technical Report pertaining to the
Feasibility Study will be filed within 45 days and will be available on
Red Eagle Mining's website and www.sedar.com. The technical information
contained in this news release has been reviewed and approved by Red
Eagle Mining's Vice President of Exploration, Jeff Toohey P.Eng., who
is a Qualified Person as defined under NI 43-101.

The following Qualified Persons as defined under NI 43-101 are
independent of Red Eagle Mining and responsible for the Technical
Report and Feasibility Study for the San Ramon project development:

//st
Qualified Person            Firm                 Scope of
Responsibility
Stefan Gueorguiev - P. Eng. Lycopodium Minerals  Process Design
Canada Ltd.          & Financial Analysis

Michael Lindholm - C.P.G.   Mine Development     Geology &
Associates           Mineral Resources

Thomas Dyer - P. E.         Mine Development     Mining, Mine
Associates           Planning &
Mineral Reserves

Terry Eldridge - P. Eng.    Golder Associates    Management &
Colombia S.A.S.      Design & Hydrology
Geotechnical, Tailings

W. Joseph Schlitt           Hydrometal Inc.      Metallurgy
- Ph.D. P. Eng.                                 & Processing
//et

About Red Eagle Mining

Red Eagle Mining is a well-financed gold exploration and
development company with an experienced mine-development team.
Management is focused on building shareholder value through discovering
and developing gold projects with low costs and low technical risks in
Colombia, a jurisdiction with prolific historic production but until
recently limited modern exploration. Red Eagle Mining is developing the
350 km historic Santa Rosa Gold Project located in the Antioquia
Batholith. Development will initially commence with the San Ramon Gold
Deposit where the positive Feasibility Study supports project
development. Project finance and permitting are well advanced.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release. This news release includes forward-looking statements that are
subject to risks and uncertainties. All statements within, other than
statements of historical fact, are to be considered forward looking.
Although the Company believes the expectations expressed in such
forward-looking statements are based on reasonable assumptions, such
statements are not guarantees of future performance and actual results
or developments may differ materially from those in forward-looking
statements. Factors that could cause actual results to differ
materially from those in forward-looking statements include market
prices, exploitation and exploration successes, continued availability
of capital and financing, and general economic, market or business
conditions. There can be no assurances that such statements will prove
accurate and, therefore, readers are advised to rely on their own
evaluation of such uncertainties. We do not assume any obligation to
update any forward-looking statements. This news release does not
constitute an offer to sell or a solicitation of an offer to sell any
securities in the United States. The securities have not been and will
not be registered under the United States Securities Act of 1933, as
amended (the "U.S. Securities Act") or any state securities laws and
may not be offered or sold within the United States or to U.S. Persons
unless registered under the U.S. Securities Act and applicable state
securities laws or an exemption from such registration is available.

TSX Venture closing price for RD-V
Date: 2014/09/08
Closing Price: 0.29

TEL: +1 604 638 2545     Ian Slater
info@redeaglemining.com  Chief Executive Officer
www.redeaglemining.com   Red Eagle Mining Corporation
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1425100001TS11425100225-03332220140909