Source	Marketwire
Date	09/29/2014
Time	06:36:56 AM

Company	 SAN MARCO RESOURCES INC.
Title	San Marco Resources Inc.: Gold-Bearing Oxidized Shear Zone Discovered at 
Cuatro de Mayo Project 






    CDNX Symbol: SMN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: San Marco Resources Inc.

TSX VENTURE SYMBOL: SMN

September 29, 2014

San Marco Resources Inc.: Gold-Bearing Oxidized Shear Zone Discovered at Cuatro 
de Mayo Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 29, 2014) - San Marco 
Resources Inc. (TSX VENTURE:SMN) ("San Marco" or "the Company") herein provides 
an interim report on its initial phase of confirmatory and early stage 
exploration work on the Cuatro de Mayo Project in eastern Sonora State, Mexico 
and concludes, based on its field observations to date, that additional 
reconnaissance level and follow-up prospecting and sampling are warranted.

San Marco geologists made numerous field visits to the Cuatro de Mayo property 
over the past several months to confirm the location of certain previously 
identified mineral showings. The purpose of this reconnaissance level 
evaluation was to determine which showings warrant additional sampling and 
prospecting aimed at delineating their dimension, continuity and mineralized 
grade. Significant areas of the Cuatro de Mayo property remain to be evaluated. 
However, based on promising early observations as well as ease of 
accessibility, the El Valle zone received additional follow up work in the past 
several months consisting of more detailed prospecting and sampling. Details 
are as follows:

The El Valle target is located in the CdM Central concession block (map 
available at www.sanmarcocorp.com). The goal of the Company's initial 
investigation at El Valle was to confirm the presence of a 
previously-identified gold-bearing shear zone, collect samples across the shear 
zone, and trace its strike extent. The El Valle shear zone was located and 
traced for several hundred meters. It remains open in both directions. This 
shear zone strikes northwest and occurs at the contact between two volcanic 
units (an andesite agglomerate on the footwall and a volcanoclastic unit on the 
hanging wall). While the true width of the El Valle shear zone is yet unknown 
and is expected to vary along strike, its width on surface has been estimated 
to be up to 80 metres and it appears to dip to the northeast. Most importantly, 
where it has been sampled, the El Valle shear zone is highly oxidized and no 
sulphides have been observed.

San Marco initially collected semi-continuous rock channel samples from outcrop 
exposed in two creeks, 400 metres apart, that cross cut the shear zone. Results 
are as follows:

Creek 1: 18.1 metres averaging 0.43 g/t gold including 12.0 metres averaging 
0.57 g/t gold near the western contact, and 14.2 metres averaging 0.90 g/t gold 
near the eastern contact. Approximately 10 metres of lower grade gold exists in 
the center section of the shear.

Creek 2: 9.1 metres averaging 1.0 g/t gold near the western contact. Additional 
sampling to the east was curtailed due to alluvium covering the sides of the 
creek.

These initial results as well as the apparent strike and width of the El Valle 
target prompted San Marco to undertake more systematic trenching across the 
shear zone. Four trenches were dug by hand and backhoe into highly altered and 
oxidized volcanic and volcano-sedimentary rocks, to a depth of up to 3 metres 
below surface. In some minor areas the overburden was too deep for the backhoe 
to reach the shear structure. The trenches range in length from 40 to 120 
metres and cross the shear zone approximately perpendicular to its strike and 
well into its footwall/hanging wall contact zones. Rock channel samples were 
collected continuously along the length of each trench (except where the 
overburden depth prevented sampling), which will provide a more accurate 
evaluation of the mineral potential of the El Valle shear zone. Results from 
the El Valle trench sampling are pending and will be released promptly when 
available.

Robert Willis, CEO of San Marco states "While we are only at the very early 
stages of exploration at Cuatro de Mayo, we are excited by what we see on the 
property so far. We were initially attracted to this project by its 
proliferation of known mineral showings coupled with little to no previous 
exploration. We have been able to confirm the presence of many of these 
showings, and have yet to visit many others. We continue to see potential at 
Cuatro de Mayo and are excited to explore this property further."

Cuatro de Mayo Background

The Cuatro de Mayo property comprises 18,564 hectares in three claim areas 
located approximately 160 km east of Hermosillo, Mexico; CdM Central (seven 
concessions), CdM East, and CdM South (one concession each). Numerous gold, 
silver and base metal showings and historic workings are known to occur in the 
Cuatro de Mayo property and surrounding area. These showings represent a 
variety of deposit types including epithermal gold and silver, structurally 
controlled stratabound gold, CRD-type (mantos, skarns) silver-lead-zinc 
showings, and mesothermal silver showings. Additional details, including the 
Cuatro de Mayo option terms, are provided in San Marco's news release dated May 
14, 2014.

About San Marco

San Marco Resources Inc. is a Canadian mineral exploration company with a 
current portfolio of four promising properties in mining-friendly Mexico and an 
aggressive project generation program focused on high-calibre, low-opportunity 
cost projects. San Marco has a committed management team with extensive 
experience in Mexico and a proven track record of building shareholder value.

National Instrument 43-101 Disclosure

The technical information contained in this document has been verified, and 
this news release has been approved, by San Marco's CEO, Robert D. Willis, P. 
Eng. a "Qualified Person" as defined in National Instrument 43-101, Standards 
of Disclosure for Mineral Projects of the Canadian Securities Administrators.

Samples discussed in this document were prepared for assay at ALS Chemex Lab in 
Mexico and assayed at their facility in Vancouver, BC. Assay methodology is as 
follows. A 30 gram split is analyzed for gold, using the Au-AA23 method. Sample 
results greater than 10 ppm are re-assayed, using AA23 fire assay and 
gravimetric finish. For silver, copper, lead and zinc, a multi-element, four 
acid digestion (ME -- ICP 61) method is used. For initial assays of silver 
greater than 100 ppm, copper, lead and zinc greater than 10,000 ppm (over 
limits), the OG62 method is used for re-analysis. Blanks and certified 
standards are inserted into the sample stream as part of San Marco's quality 
assurance and control program, which complies with National Instrument 43-101 
requirements.

Forward Looking Information

Information set forth in this document includes forward-looking statements, 
such as: potential exploration plans and programs for the Cuatro de Mayo 
project; and, the possibility of acquiring additional exploration projects. 
While these statements reflect management's current plans, projections and 
intents, by their nature, forward-looking statements are subject to numerous 
risks and uncertainties, some of which are beyond the control of San Marco 
Resources Inc. For instance, the execution of any exploration programs planned 
by the Company will be dependent upon the availability of both human and 
financial resources, both of which are presently limited. Readers are cautioned 
that the assumptions used in the preparation of such information, although 
considered reasonable at the time of preparation, may prove to be imprecise 
and, as such, undue reliance should not be placed on these forward-looking 
statements. San Marco's actual results, programs and financial position could 
differ materially from those expressed in or implied by these forward-looking 
statements.

Neither the TSX Venture Exchange nor the Investment Industry Regulatory 
Organization of Canada accepts responsibility for the adequacy or accuracy of 
this release.

- 30 -

CONTACT INFO:

San Marco Resources Inc.
Robert D. Willis
CEO
604-568-5951
Fax: 604-813-2606
rwillis@sanmarcocorp.com

or

San Marco Resources Inc.
Barbara Henderson
Investor Relations Officer
604-568-5951
Fax: 604-789-7689
bhenderson@sanmarcocorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=500530084