Source	Filing Services Canada
Date	09/29/2014
Time	06:37:09 AM

Company	 ENDURANCE GOLD CORPORATION
Title	Endurance Reports 25 metres of 3.4 Grams per Tonne Gold from the Godzilla 
Zone, Pardo Joint Venture, Ontario





    CDNX Symbol: EDG











Press Release	




SOURCE: Filing Services Canada
Date: 09/29/2014
Time: 09:35:00

Company: ENDURANCE GOLD CORPORATION
Title:Endurance Reports 25 metres of 3.4 Grams per Tonne Gold from the Godzilla 
Zone, Pardo Joint Venture, Ontario (EDG - TSXV) 
TSXV SYMBOL: EDG


NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: Endurance Gold Corporation
TSXV SYMBOL: EDG
Monday, September 29, 2014 - 9:35 AM

Original Source Location: 
http://www.fscwire.com/newsrelease/endurance-reports-25-metres-34-grams-tonne-go
ld-godzilla-zone-pardo-joint-venture

Endurance Reports 25 metres of 3.4 Grams per Tonne Gold from the Godzilla Zone, 
Pardo Joint Venture, Ontario


Vancouver, British Columbia (FSCwire) - Endurance Gold Corporation (EDG  TSX.V, 
Endurance) announces new encouraging results from the Godzilla Zone on the 
Pardo Joint Venture Property (Pardo JV Property). The Pardo JV Property is 
comprised of 16 claims located approximately 65 km northeast of Sudbury, 
Ontario. Ginguro Exploration Inc. (Ginguro) is the operator of the Pardo JV 
Property and holds a 64.5% ownership interest and Endurance owns a 35.5% 
ownership interest. Both parties are funding the 2014 program on a pro rata 
basis, based on ownership.



Assays have now been received for six additional channel samples taken at the 
recently discovered Godzilla Zone which previously returned an average of 5.2 
grams per tonne (g/t) gold over 140 metres from Channel 14-34 (see press 
release dated September 2, 2014). Channel 14-37, which was cut perpendicular to 
Channel 14-34, averaged 3.4 g/t gold over 25 metres. Channels 14-38, 14-40 and 
14-41, which were shorter channels cut approximately 35 metres east of Channel 
14-35 in an overlying conglomerate, averaged 0.1g/t gold over 4 metres, 0.7 g/t 
gold over 4 metres, and 0.7 g/t gold over 3 metres, respectively. Channel 14-39 
was cut perpendicular to Channel 14-34 and averaged 0.7 g/t over 13.5 metres 
and Channel 14-42, which was cut sub parallel to Channel 14-34, averaged 0.7 
g/t gold over 8 metres. There are different conglomerate horizons exposed at 
Godzilla however, the significantly gold-bearing conglomerate at the Godzilla 
Zone appears to have an average true thickness of approximately 4 metres.



Maps illustrating the geology and channel sample locations can be found on the 
Companys website at www.endurancegold.com (http://www.endurancegold.com).



The operator reports that a total of 527 metres of channel sample were cut 
across the Godzilla Zone. Assay results for 236.5 metres of channel samples at 
the Godzilla zone remain outstanding and are expected in the next few weeks. 
The exposed outcrop area that contains the Godzilla Zone mineralization 
measures 175 metres north-south by up to 125 metres east-west.



Due to the near flat lying nature of the sedimentary strata, it is not always 
possible to cut samples across the gold-bearing strata. The operator reports 
that samples are collected either parallel or perpendicular to the interpreted 
paleochannel direction. Therefore,the channel lengths reported in this release 
represent the gold distribution over the surface area sampled and do not 
represent true thicknesses of the mineralized unit. The known gold 
mineralization within the nearly flat-lying near-surface basal conglomerate on 
the Pardo JV Property now extends approximately 3 kilometres north-south by 
approximately 1.1 kilometres east-west.







The operator reports that field crews are continuing the work of exploring new 
target areas of the Pardo JV. The prospecting and geological work will continue 
throughout the fall as long as weather permits



In the preparation of this news release, Endurance has relied on data collected 
and compiled by the Operator of exploration programs, and summarized to the 
Company for this release. Robert T. Boyd, P.Geo. is a qualified person as 
defined in National Instrument 43-101 and supervised the compilation of the 
technical information provided by the operator and forming the basis for this 
release. Potential quantity and grade is conceptual in nature. There has been 
insufficient exploration to define a mineral resource on the Pardo JV Property 
to date, and it is uncertain if further exploration will result in the target 
being delineated as a mineral resource. The Operator reports that Pardo JV 
samples are transported in security sealed bags for preparation at AGAT Prep 
Lab located in Sudbury, Ontario. Prepped samples are shipped for analysis to 
the AGAT Assay Laboratory in Mississauga, Ontario. AGAT Laboratories Ltd. is an 
ISO 17025 registered laboratory. The six channel samples summarized in this 
release and channel 14-34 north reported earlier, were assayed using a modified 
pulp metallic assay procedure. The entire sample was crushed and pulverized to 
85% passing 100 mesh. The +100 mesh material was fluxed and assayed in its 
entirety, while two 50 g aliquots of the -100 mesh undersize pulp were cut out 
and fire assayed. Results were reported as a weighted average of gold in the 
three fractions. Earlier reported samples for channels 14-34 south, 14-35 and 
14-36 were crushed in their entirety, with a 1kg split then pulverized. Two 50 
g aliquots of the pulp were cut out and fire assayed. Results were reported as 
a weighted average of gold in the fractions. In instances where the averages 
exceed 10 g/t, the sample is re-run with a gravimetric finish and the 
gravimetric result is reported. For both techniques, the operator inserts a 
certified reference standard or an analytical blank in every batch of 20 
samples. The operator reports that validation parameters are established in the 
database to ensure quality control.



About Endurance

Endurance Gold Corporation is a company focused on the acquisition, exploration 
and development of highly prospective North American mineral properties with 
the potential to develop world-class deposits. The Company's exploration focus, 
for projects operated by Endurance, is intrusive-related mineral systems with 
potential for discovery of major new precious or rare metals deposits, and its 
business plan offers shareholders exposure to several majority-owned 
exploration projects with significant discovery potential such as the Elephant 
Gold Property in Alaska, the Rattlesnake Hills Gold Property in Wyoming, and 
the Bandito Rare Earth-Niobium Property in the Yukon. Please visit 
www.endurancegold.com (http://www.endurancegold.com).



ENDURANCE GOLD CORPORATION



Robert T. Boyd

Per: 

President & CEO



FOR FURTHER INFORMATION, PLEASE CONTACT

Endurance Gold Corporation

(604) 682-2707, info@endurancegold.com (mailto:info@endurancegold.com)

www.endurancegold.com (http://www.endurancegold.com/)



Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release. This news 
release may contain forward looking statements based on assumptions and 
judgments of management regarding future events or results that may prove to be 
inaccurate as a result of factors beyond its control, and actual results may 
differ materially from the expected results.


To view this press release as a PDF file, click onto the following link:
http://www.fscwire.com/sites/default/files/news_release_pdf/EnduranceGoldSept292
014.pdf
Source: Endurance Gold Corporation (TSX Venture:EDG) 
http://www.endurancegold.com



Maximum News Dissemination by FSCwire. http://www.fscwire.com



Copyright(C)2014 Filing Services Canada Inc.