Source	MARKET NEWS
Date	09/30/2014
Time	06:03:05 AM

Company	 Niocorp Developments Ltd.
Title	Metallurgical Flowsheet





    CDNX Symbol: NB











Press Release	





Metallurgical Flowsheet --->@NEWS RELEASE
NIOCORP DEVELOPMENTS LTD ("NB-V")
- Metallurgical Flowsheet

NioCorp Developments Ltd.("NioCorp" or the "Company") is pleased to
announce updates regarding the ongoing metallurgical testing program of
the ore from the Elk Creek deposit, along with a preliminary
metallurgical flowsheet.

Commencing in April, the Company initiated a metallurgical
testwork program to demonstrate the production of a ferroniobium
product from the Elk Creek Ore. The program has been designed around a
series of bench-scale tests that will be used to design a pilot-scale
testing program, which in turn will be used in process plant design and
in a feasibility study for the project.

Highlights of the results from the bench scale tests at SGS in
Lakefield, Ontario include:

//st

Flotation test F55, which demonstrated a niobium recovery of
61% to the flotation concentrate;

Hydrometallurgical tests (PL13, PL15, PL16, AB13, AB15) of pre-leaching and
acid baking on the flotation concentrate, demonstrating a combined
extraction of 98% of the niobium contained in the flotation concentrate;

Additional hydrometallurigcal tests (Test NbP25) demonstrating the recovery
of 98% of the niobium contained in the pre-leach / acid bake products into
a precipitate containing 21% Nb by weight.

//et

The company is currently working with SGS to complete testing on
the balance of the flowsheet, including precipitate dissolution,
solvent extraction and aluminothermic reduction, which should result in
the production of a ferroniobium final product. The company is also
pleased to report the completion of initial pilot scale grinding tests
on a 1.2 tonne sample of the Elk Creek resource, which will be followed
in the coming weeks by a pilot scale flotation testing. Finally, the
company has committed to drilling three dedicated metallurgical holes
at the Elk Creek property, in order to obtain 25-35 tonnes of the
resource. This quantity of material will be used to supply a larger
scale pilot plant that is expected to commence operations later this
fall.

"The metallurgical program has advanced quickly since April, and
has delivered high metallurgical recoveries across the process steps
that have been tested to date," stated Mark A. Smith, CEO of NioCorp.
"We look forward to moving quickly through the balance of the
metallurgical test program as we continue to de-risk the project
through increased technical knowledge of this world-class deposit."

Qualified Persons:

Alain Dorval, B.Sc, Roche Consulting Group Limited, a Qualified
Person as defined by National Instrument 43-101, is responsible for the
Elk Creek mineral processing program and has read and approved the
technical information contained in this news release.

Eric Larochelle, B.Eng, Roche Engineering Inc, a Qualified Person
as defined by National Instrument 43-101, is responsible for the Elk
Creek hydrometallurgical program and has read and approved the
technical information contained in this news release.

About the Company: NioCorp are developing the only primary niobium
deposit known to be under development in the U.S., and the highest
grade undeveloped niobium deposit in North America, located near Elk
Creek, Nebraska. The Company has filed an NI43-101 compliant resource
report, available on SEDAR, and is in the process of filing an updated
NI43-101 compliant resource estimate reporting an Indicated resource of
28.2 Million Tonnes grading 0.63% Nb(sub)2(/sub)O(sub)5(/sub),
containing 177 Million Kg's of Nb(sub)2(/sub)O(sub)5(/sub), and an
Inferred resource of 132,800 Million Tonnes grading 0.55%
Nb(sub)2(/sub)O(sub)5(/sub), containing 733.7 Million Kg's of
Nb(sub)2(/sub)O(sub)5(/sub), (at a 0.3% Nb(sub)2(/sub)O(sub)5(/sub)
cutoff grade). Niobium is mainly used in the form of Ferro-Niobium to
produce HSLA (High Strength, Low Alloy) steel, to produce lighter,
stronger steel for use in automotive, structural and pipeline
industries. The U.S. imports 100% of its niobium needs.

ON BEHALF OF THE BOARD

"Peter Dickie"

Peter Dickie, Director, President and Corporate Secretary

Neither TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Certain statements contained in this press release may
constitute forward-looking statements. Such forward-looking statements
are based upon NioCorp's reasonable expectations and business plan at
the date hereof, which are subject to change depending on economic,
political and competitive circumstances and contingencies. Readers are
cautioned that such forward-looking statements involve known and
unknown risks, uncertainties and other factors that may cause a change
in such assumptions and the actual outcomes and estimates to be
materially different from those estimated or anticipated future
results, achievements or position expressed or implied by those
forward-looking statements. Risks, uncertainties and other factors that
could cause NioCorp's plans or prospects to change include changes in
demand for and price of commodities (such as fuel and electricity) and
currencies; changes or disruptions in the securities markets;
legislative, political or economic developments; the need to obtain
permits and comply with laws and regulations and other regulatory
requirements; the possibility that actual results of work may differ
from projections/expectations or may not realize the perceived
potential of NioCorp's projects; risks of accidents, equipment
breakdowns and labour disputes or other unanticipated difficulties or
interruptions; the possibility of cost overruns or unanticipated
expenses in development programs; operating or technical difficulties
in connection with exploration, mining or development activities; the
speculative nature of mineral exploration and development, including
the risks of diminishing quantities of grades of reserves and
resources; and the risks involved in the exploration, development and
mining business. NioCorp disclaims any intention or obligation to
update or revise any forward-looking statements whether as a result of
new information, future events or otherwise.

TSX Venture closing price for NB-V
Date: 2014/09/29
Closing Price: 0.65

TEL:  (604) 568-7365 NioCorp Developments Ltd.
INTERNET:  www.NioCorp.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1427200013TS11427200945-06001320140930