Source	MARKET NEWS
Date	09/15/2015
Time	06:01:55 AM

Company	 Strategic Metals Ltd.
Title	Intersects 
43.6 g/t Gold In A Metre Wide Skarn H





    CDNX Symbol: SMD











Press Release	





STRATEGIC METALS LTD ("SMD-V;SMDZF-0")
- Intersects 43.6 g/t Gold In A Metre Wide Skarn Horizon
- At Hopper Project, Yukon Territory

Strategic Metals Ltd. ("Strategic") is pleased to announce
additional results from a nine hole, 3,227 m diamond drill program that
was recently completed at its wholly-owned road-accessible Hopper
Project, located in southwestern Yukon Territory. Results from the
first two holes were announced on August 6, 2015 and included 12.15 g/t
gold and 0.95% copper over 2.65 m. Highlights from the other seven
holes include:

//st

43.6 g/t gold over 1.00 m,

0.17% copper over 162.5 m and,

2.4 g/t gold and 1.03% copper over 4.48 m.

//et

"Results from the 2015 program have significantly expanded the area
of known skarn mineralization and provide evidence of a porphyry centre
coring this very large hydrothermal system," states Doug Eaton, CEO of
Strategic. "A sizeable area of mineralization southwest of the main
pluton is now ready for systematic grid drilling and many soil
geochemical and geophysical anomalies elsewhere on the property offer
excellent potential for additional discoveries."
Details concerning the highlight intervals and other significant
intercepts are shown on Table 1, while the drill hole locations are
illustrated on attached Figure 1. Historical work at the property is
described in Technical Report on the Hopper Project by J. Pautler,
P.Geo. which is filed at www.sedar.com. The following paragraphs
summarize the historical work and describe the significance of the 2015
drill holes.

Prior to 2015, all diamond drilling on the property was done near
a copper-rich skarn zone that outcrops in a creek bed, about 1,000 m
southwest of the Hopper pluton. Most of the historical holes were short
and many of them were not analyzed for gold. Recent geochemical surveys
outlined very strong copper, gold and molybdenum soil anomalies that
cover a 3,600 by 2,500 m area. Only a small fraction of these anomalies
have been tested by diamond drilling.

Collectively, the historical drill holes identified three
laterally extensive skarn horizons (now named JG, AM and LV). These
horizons are about 50 m apart stratigraphically and typically range
from 2 to 20 m in thickness. The horizons strike northerly and dip
shallowly (approximately 15) to the east. They are locally cut by
various types of steep intrusive dykes, some of which are weakly
mineralized with copper or molybdenum. Many of the historical skarn
intercepts are moderately to strongly mineralized with copper and gold.
The best historical interval graded 1.94% copper and 0.87 g/t gold
across 18.59 m (true thickness approximately 12 m).

A few of the historical drill holes extended somewhat deeper into
the stratigraphic section and cut other copper-gold bearing skarn
horizons. Most of these intercepts have not yet been assigned to
specific horizons because they are too widely spaced for reliable
correlations. Significantly, one of the deeper holes cut a skarn with a
much higher gold content than has been reported from any of the upper
horizons. This intercept returned 9.44 g/t gold with only 0.01% copper
over 2 m within a broader interval that averaged 3.35 g/t gold and
0.43% copper across 7.5 m.

Seven of the 2015 holes (15-01 through 15-07) tested north and
west of the historical holes, while the other two holes (15-08 and
15-09) re-entered and deepened historical holes (Figure l). Mineralized
skarn horizons have now been discovered in scattered outcrops and
widely-spaced drill holes over a 3,000 m strike length.

Table 1: Significant intercepts in 2015 drill holes, Hopper
Project

//st
Hole         From (m) To (m) Interval (m)+ Au (g/t) Cu (%) Ag (g/t) Mo (ppm)
15-01           90.59  92.26         1.67#    0.119   0.57     4.44    0.31
284.29 286.94         2.65#    12.15   0.95     5.45    3.24
15-02           82.07  91.09         9.02#    0.120   0.24     1.55   32.15
113.13 128.14        15.01#    0.500   0.50     1.64    3.59
incl.           121.7 128.14         6.44#    1.013   1.00     3.86    3.99
136.6  138.6         2.00#    0.142   0.70     4.44    2.11
150.85 151.85         1.00#    1.000   0.45     2.08    5.54
204.9  205.9         1.00#    0.723   0.79     4.24    3.78
15-03           26.92  28.91          1.99    0.109   0.31     1.37   80.70
125.3 128.29          2.99    0.344   0.28     1.65  135.00
266.61 276.15          9.54    1.010   0.35     1.79   45.43
15-04           39.09   52.1         13.01    0.334   0.41     1.70    6.53
196.97  211.4         14.43    1.109   0.60     2.86  183.88
incl.          202.52 207.00          4.48     2.40   1.03     3.98  253.12
325.24 498.91        173.67    0.002   0.01     0.09  157.57
15-05          113.88 276.73        162.85    0.017   0.17     2.08   34.26
incl.          149.74 150.74          1.00    0.257   5.00    17.10    2730
& incl.        275.73 276.73          1.00    0.062   2.40    17.45   61.30
15-06           79.14  84.25          5.11    0.001   0.32     4.35    8.41
110.73 112.15          1.42    0.021   0.36     4.08    3.44
186.23 188.98          2.75    0.031   0.78     3.68   63.96
15-07           48.07  58.64         10.57    0.197   0.49     3.32    6.91
incl.           54.07  55.64          1.57    0.649   1.39     9.28   23.80
60.96  70.42          9.46    0.013   0.12     2.21    3172
349.17 351.98          2.81    0.075   1.25     0.23    1.76
369.35 370.71          1.36    0.294   0.46     1.56    2.57
11-05/15-08*   126.93 128.05         1.12#    1.830   0.46     1.74    7.69
336.66 337.66          1.00     43.6   0.06     1.07   53.30
341.49 342.63          1.14    0.204   0.31     1.91   45.40
11-04/15-09*    57.39  62.53         5.14#    0.740   0.95     5.64    1.54
174.86 182.87         8.01#    0.840   1.58    14.82   43.56
339.33 340.33          1.00    0.171   0.67     3.93   83.70

//et

* holes 15-08 and 15-09 re-entered and deepened holes 11-05 and
11-04, respectively.

# previously announced

+ intersected lengths are believed to represent 95 to 100% of the
true widths, except for the long intervals of fracture- filling
mineralization intersected in holes 15-04 and 15-05.

Hole 15-01 lies 342 m north-northwest of the closest historical
hole and was collared stratigraphically below the main copper horizons
to search for underlying, more gold-rich skarn horizons. This hole
extended deeper than any of the historical holes and discovered a new
well-mineralized skarn horizon (JP). This horizon graded 12.15 g/t gold
and 0.95% copper over a true width of 2.65 m. The JP horizon projects
to surface in an area covered by glacial overburden, about 280 m up dip
of the drill intercept. The up dip projection of the JP horizon has not
been explored.

Hole 15-02 is located 435 m north-northeast of hole 15-01. It was
a shorter hole that was designed to evaluate only the JG, AM and LV
horizons and did not extend deep enough to reach the JP horizon. The
best intercept in the hole is believed to be the JG horizon, which
contains a 6.44 m thick band of skarn grading 1.00% copper and 1.01 g/t
gold within a 15 m section of weak to moderate mineralization. Hole
15-02 also contained other, narrower mineralized skarn intervals, some
of which may have been shortened by cross-cutting, post-mineralization
dykes.

Holes 15-03 and 15-04 are spaced 136 m apart on a section line
located 172 m north of hole 15-02 on the southern flank of the Hopper
pluton. Both holes cut a thick gold and copper enriched skarn horizon
that is believed to be the extension of the JG horizon intersected in
hole 15-02. The deeper part of hole 15-04 tested a small chargeability
anomaly, and it encountered a long interval composed of altered
wallrocks and closely-spaced dykes, which host fractures and veins
containing strongly elevated molybdenum (173.67 m averaging 157.57
ppm).

Hole 15-05 explored beneath a larger chargeability anomaly which
straddles the northern contact of the Hopper pluton 1,750 m north of
holes 15-03 and 15-04. This hole yielded an interval that averaged
0.17% copper over 162.85 m. Molybdenum values are slightly elevated
within this interval but gold values are low. There are many other
untested chargeability anomalies within and adjacent to the Hopper
pluton.
Hole 15-06 was drilled in a large roof pendant of metasediments,
300 m west of hole 15-05. It cut a few skarn horizons that are
moderately enriched for copper.

Hole 15-07, which is located 203 m east of hole 15-01, intersected
three shallow intervals that project stratigraphically above the collar
of 15-01 and two narrower intervals near the bottom of the hole that
may be extensions of the JP horizon.

Hole 15-08 re-entered and extended beneath hole 11-05. It yielded
an intercept of 43.6 g/t gold over a width of one metre. This intercept
is at approximately the same stratigraphical level as the JP horizon
cut in hole 15-01, 367 m to the northwest.

Hole 15-09 deepened hole 11-04, which lies 320 m east of hole
15-08 in the heart of the historical drill area. The top of this hole
contained two thick, well mineralized skarn horizons, but the extension
cut only narrow, weakly to moderately mineralized intervals. It is
possible that this hole did not explore deep enough to reach the
projection of the JP horizon.

All of the sulphide mineralization at the Hopper Project is
relatively coarse grained. Arsenic and antimony contents are low
throughout, but bismuth and tellurium are notably enriched in
gold-bearing intervals.

In summary, results from the 2015 drill program at the Hopper
Project successfully demonstrated that:

//st

the area of mineralized bedrock is much more extensive than was
indicated by historical drilling;

there are areas where gold grades are much higher than were
reported by historical drilling or surface sampling;

the drill-tested chargeability highs are underlain by broad
zones of disseminated and fracture-filling mineralization that could flank
a significant porphyry deposit; and,

the best skarn mineralization is hosted in stacked horizons
with consistent, shallow dips.

//et

Analytical work was done by ALS Minerals, with sample preparation
in Whitehorse, Yukon and assays and geochemical analyses in North
Vancouver, British Columbia. All rock samples were analyzed for gold by
fire assay fusion and inductively coupled plasma-atomic emission
spectrometry (Au-ICP21) and 48 other elements by four acid digestion
and inductively coupled plasma-atomic emission spectroscopy (ME-MS61).
Overlimit values were determined for gold by fire assay fusion and
gravimetric finish (Au-GRA21) and for copper by four acid digestion and
inductively coupled plasma-atomic emission spectroscopy (Cu-OG62).

The 2015 Hopper drill program was managed by Archer, Cathro &
Associates (1981) Limited (Archer Cathro). Technical information in
this news release has been approved by Heather Burrell, P. Geo., a
senior geologist with Archer Cathro and a qualified person for the
purpose of National Instrument 43-101.

About Strategic Metals Ltd.

Strategic is the largest claim holder in Yukon, which the Fraser
Institute recently rated as the best jurisdiction in the world for
mineral potential. Strategic's portfolio of more than 100 projects is
the result of 50 years of focussed exploration and research by a team
with a track record of major discoveries. Current projects available
for option, joint venture or sale include drill-confirmed prospects and
drill-ready targets defined by high-grade surface showings, geochemical
anomalies and/or geophysical features.

Strategic has a current cash position of over $23 million and
significant shareholdings in a number of active mineral exploration
companies including 46.6% of Rockhaven Resources Ltd., 8.6% of ATAC
Resources Ltd., 19.9% of Silver Range Resources Ltd. and 12.9% of
Precipitate Gold Corp.

ON BEHALF OF THE BOARD

W. Douglas Eaton, President and Chief Executive Officer

For further information concerning Strategic or its various
exploration projects please visit our website at
www.strategicmetalsLtd.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release may contain forward looking statements based on
assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of exploration and
other risk factors beyond its control, and actual results may differ
materially from the expected results.

To view the figure associated with this release, please visit the
following link:
http://www.strategicmetalsLtd.com/i/maps/HopperGeochemNews2015PlanViewAll.p
ng



Strategic Metals Ltd. - Corporate Information
W. Douglas Eaton
President and C.E.O.
TEL: (604) 688-2568
Strategic Metals Ltd. - Investor Inquiries
Richard Drechsler




















TSX Venture closing price for SMD-V
Date: 2015/09/14
Closing Price: 0.27

TEL: (604) 687-2522 or NA Toll-Free: (888) 688-2522
E-mail:   rdrechsler@strategicmetalsLtd.com
Internet: www.strategicmetalsLtd.com
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1525700014TS11525700896-05590720150915