Source	Marketwire
Date	09/08/2015
Time	04:01:13 AM

Company	 TERRAX MINERALS INC.
Title	TerraX Discovers New High Grade Gold Zones at Yellowknife City Gold; 
Channel Samples 6.0 m @ 10.26 g/t Au Across Strike on Hebert-Brent Shear





    CDNX Symbol: TXR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
OTC PINK SYMBOL: TRXXF

September 8, 2015

TerraX Discovers New High Grade Gold Zones at Yellowknife City Gold; Channel 
Samples 6.0 m @ 10.26 g/t Au Across Strike on Hebert-Brent Shear


YELLOWKNIFE, NORTHWEST TERRITORIES--(Marketwired - Sept. 8, 2015) - TerraX 
Minerals Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(OTC PINK:TRXXF) has received 
results from channel sampling of additional new zones of mineralization on the 
Hebert-Brent Shear (11.0 m @ 7.55 g/t Au reported August 11, 2015) at 
Yellowknife City Gold ("YCG"), immediately north of Yellowknife in the 
Northwest Territories. Assays from cut channel sampling across the strike of 
two zones returned:

/T/

--  6.0 m @ 10.26 g/t Au ("Hebert-Brent South") and
--  15.3 m @ 2.23 g/t Au, including 6.00m @ 4.05 g/t Au ("Hebert-Brent
East").

/T/

These result are highly significant, indicating high grade zones of 
mineralization across a sheared area approximately 80 metres wide in the 
Hebert-Brent Shear area which is 1 km south and on strike with the Barney Zone 
drilled in 2014 (22.42 m @ 6.35 g/t Au in hole NB95-16W1 - see our news release 
of August 25, 2014), all within the newly mapped deformation zone called the 
Barney Deformation Corridor ("BDC").

Joe Campbell, P. Geo, President of TerraX, states "These high grade sampling 
results give added confirmation of the gold endowment in the recently 
discovered Hebert-Brent Shear area. Despite 75 years of exploration on the YCG 
property this outstanding area of gold mineralization went undiscovered, with 
no previous surface workings or drilling prior to TerraX's work in 2014 and 
2015. This exploration success is a strong endorsement of our corporate 
strategy to acquire property and explore within an established major Canadian 
Gold camp."

The trench on the Hebert-Brent South zone is located approximately 75 metres 
south of the original channel samples reported on August 11, 2015 (11.0 m @ 
7.55 g/t Au) and returned 6.0 m @ 10.26 g/t Au. The Hebert-Brent South Zone is 
potentially the strike extension of the original Hebert-Brent Zone, or is a 
closely parallel zone.

The Hebert-Brent East trench is 45 metres east and across strike from the 
original Hebert-Brent zone and returned 15.3 m @ 2.23 g/t Au, including 6.00 m 
@ 4.05 g/t Au. The Hebert-Brent East Zone is interpreted as a new mineralized 
structure parallel to the Hebert-Brent Zone. Cursory examination of the area 
between the Hebert-Brent and Hebert-Brent East Zones suggests significant 
additional mineralization, including the original Brent showing (44 g/t Au in a 
grab sample), and outcrops of altered and sheared mafic volcanics and felsic 
intrusions. This area will be subjected to further detailed exploration work.

Channel results were from contiguous one (1) metre channel samples, except for 
the most westerly sample in the Hebert-Brent East zone which was 1.30 metres 
long. Maps and pictures of the sampled areas described in this news release are 
available under "Barney Deformation Corridor" on our web site at 
www.terraxminerals.com.

Hebert-Brent South

/T/


Sample ID              From (m)         To (m)   Interval (m)         Au g/t
----------------------------------------------------------------------------
Q635117                    0.00           1.00           1.00          16.35
----------------------------------------------------------------------------
Q635118                    1.00           2.00           1.00           1.38
----------------------------------------------------------------------------
Q635119                    2.00           3.00           1.00           1.72
----------------------------------------------------------------------------
Q635121                    3.00           4.00           1.00          18.80
----------------------------------------------------------------------------
Q635122                    4.00           5.00           1.00          16.45
----------------------------------------------------------------------------
Q635123                    5.00           6.00           1.00           6.87
----------------------------------------------------------------------------

/T/

Hebert-Brent East

/T/


Sample ID              From (m)         To (m)   Interval (m)         Au g/t
----------------------------------------------------------------------------
Q635101                    0.00           1.00           1.00           1.97
----------------------------------------------------------------------------
Q635102                    1.00           2.00           1.00          10.80
----------------------------------------------------------------------------
Q635103                    2.00           3.00           1.00           4.23
----------------------------------------------------------------------------
Q635104                    3.00           4.00           1.00           2.86
----------------------------------------------------------------------------
Q635105                    4.00           5.00           1.00           1.89
----------------------------------------------------------------------------
Q635106                    5.00           6.00           1.00           2.53
----------------------------------------------------------------------------
Q635107                    6.00           7.00           1.00           0.75
----------------------------------------------------------------------------
Q635108                    7.00           8.00           1.00           1.13
----------------------------------------------------------------------------
Q635109                    8.00           9.00           1.00           0.76
----------------------------------------------------------------------------
Q635111                    9.00          10.00           1.00           1.29
----------------------------------------------------------------------------
Q635112                   10.00          11.00           1.00           1.04
----------------------------------------------------------------------------
Q635113                   11.00          12.00           1.00           1.50
----------------------------------------------------------------------------
Q635114                   12.00          13.00           1.00           1.35
----------------------------------------------------------------------------
Q635115                   13.00          14.00           1.00           1.13
----------------------------------------------------------------------------
Q635116                   14.00          15.30           1.30           0.68
----------------------------------------------------------------------------

/T/

Additional zones of mineralization have been sampled and assay results are 
pending. A program of more extensive stripping and channel sampling at 
Hebert-Brent has also been initiated to further expose the across strike 
dimensions of the reported channel sampled areas, as none of the three zones 
have been delimited across or along strike yet. All this surface work is being 
conducted to assist in the successful planning of a first phase drilling 
program in the Hebert-Brent Shear area.

Sampling included insertion of certified standards and blanks into the stream 
of samples for chemical analysis. Samples were prepared at ALS Chemex's 
laboratory in Yellowknife and shipped to their Vancouver facility for gold 
analysis by fire assay and other elements by ICP analysis. ALS is a certified 
and accredited laboratory service.

The channel samples reported here are considered representative of the overall 
grade and extent of mineralization on the subject areas. For grab samples also 
mentioned in this news release, and illustrated on maps, it should be noted 
that due to their selective nature assay results from grab samples may not be 
indicative of the overall grade and extent of mineralization on the subject 
area. The technical information contained in this news release has been 
approved by Joseph Campbell, President of TerraX, who is a Qualified Person as 
defined in "National Instrument 43-101, Standards of Disclosure for Mineral 
Projects."

About the Hebert-Brent Shear

Geological mapping in June and July identified areas of extensive sericite 
alteration which occurs in a recognizable structural zone called the Barney 
Deformation Corridor (see August 11, 2015 news release for more detail). The 
altered areas in the Hebert-Brent Shear area are approximately 1 km south and 
on strike with the Barney Zone drilled by TerraX in 2014 and winter 2015. 
Mineralization appears to be related to east-southeast trending felsic dykes 
crossing north and north-east shear zones with dextral deformation/rotation 
into the shears. Higher grade areas of mineralization are also recognized at 
the contacts of the felsic dykes with mafic volcanics and gabbros. Channel 
sampling was carried out in one area of visible sulphide mineralization in July 
2015, and this new zone was coined the "Hebert-Brent Zone". Subsequent 
exploration and mapping in the area of the Hebert-Brent Zone revealed several 
other similarly mineralized zones within a definable area of intense shearing 
and sericite alteration. This broader area has been termed the Hebert-Brent 
Shear. The results presented today are from the first two of these additional 
mineralized zones that are being channel sampled.

About the Yellowknife City Gold Project

The Yellowknife City Gold Project encompasses approximately 99.3 sq km of 
contiguous land immediately north of the City of Yellowknife in the Northwest 
Territories. Through a series of acquisitions, TerraX now controls one of the 
six major high-grade gold camps in Canada - and the least explored.

The project lies on the prolific Yellowknife greenstone belt and covers 15 km 
of strike length on the northern extension of the shear system that hosts the 
high-grade Con and Giant gold mines. The project area contains multiple shears 
that are the recognized hosts for gold deposits in the Yellowknife gold 
district, with innumerable gold showings and high grade drill results this past 
year that serve to indicate the project's potential as a world-class gold 
district. Since February 2013, TerraX has consolidated the project area by 
acquiring, optioning and staking numerous properties, including: Northbelt, 
Goodwin, Ryan Lake, Walsh Lake, and U-Breccia, as well as staking additional 
contiguous lands. Being all-season road accessible and within 15 km of the City 
of Yellowknife, the YCG is close to vital infrastructure, including 
transportation, service providers, hydro-electric power and skilled trades 
people.

For more information on the Yellowknife City Gold Project, please visit our web 
site at www.terraxminerals.com.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

Paradox Public Relations
514-341-0408
1-866-460-0408
info@paradox-pr.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=541405067