Source	MARKET NEWS
Date	09/08/2015
Time	04:29:12 AM

Company	 Terrax Minerals Inc.
Title	Discovers 
New High Grade Gold Zones At Yellowkni





    CDNX Symbol: TXR











Press Release	





TERRAX MINERALS INC ("TXR-V")
- Discovers New High Grade Gold Zones At Yellowknife City
- Gold; Channel Samples 6.0 M @ 10.26 G/t Au Across Strike On
- Hebert-brent Shear

TerraX Minerals Inc. has received results from channel sampling of
additional new zones of mineralization on the Hebert-Brent Shear (11.0
m @ 7.55 g/t Au reported August 11, 2015) at Yellowknife City Gold
("YCG"), immediately north of Yellowknife in the Northwest Territories.
Assays from cut channel sampling across the strike of two zones
returned:

//st

6.0 m @ 10.26 g/t Au ("Hebert-Brent South") and

15.3 m @ 2.23 g/t Au, including 6.00m @ 4.05 g/t Au ("Hebert-Brent East").

//et

These result are highly significant, indicating high grade zones of
mineralization across a sheared area approximately 80 metres wide in
the Hebert-Brent Shear area which is 1 km south and on strike with the
Barney Zone drilled in 2014 (22.42 m @ 6.35 g/t Au in hole NB95-16W1 -
see our news release of August 25, 2014), all within the newly mapped
deformation zone called the Barney Deformation Corridor ("BDC").

Joe Campbell, P. Geo, President of TerraX, states "These high
grade sampling results give added confirmation of the gold endowment in
the recently discovered Hebert-Brent Shear area. Despite 75 years of
exploration on the YCG property this outstanding area of gold
mineralization went undiscovered, with no previous surface workings or
drilling prior to TerraX's work in 2014 and 2015. This exploration
success is a strong endorsement of our corporate strategy to acquire
property and explore within an established major Canadian Gold camp."

The trench on the Hebert-Brent South zone is located approximately
75 metres south of the original channel samples reported on August 11,
2015 (11.0 m @ 7.55 g/t Au) and returned 6.0 m @ 10.26 g/t Au. The
Hebert-Brent South Zone is potentially the strike extension of the
original Hebert-Brent Zone, or is a closely parallel zone.

The Hebert-Brent East trench is 45 metres east and across strike
from the original Hebert-Brent zone and returned 15.3 m @ 2.23 g/t Au,
including 6.00 m @ 4.05 g/t Au.The Hebert-Brent East Zone is
interpreted as a new mineralized structure parallel to the Hebert-Brent
Zone. Cursory examination of the area between the Hebert-Brent and
Hebert-Brent East Zones suggests significant additional mineralization,
including the original Brent showing (44 g/t Au in a grab sample), and
outcrops of altered and sheared mafic volcanics and felsic intrusions.
This area will be subjected to further detailed exploration work.

Channel results were from contiguous one (1) metre channel
samples, except for the most westerly sample in the Hebert-Brent East
zone which was 1.30 metres long. Maps and pictures of the sampled areas
described in this news release are available under "Barney Deformation
Corridor" on our web site at www.terraxminerals.com.

Hebert-Brent South

//st
Sample ID      From (m)      To (m)      Interval (m)      Au g/t
Q635117            0.00        1.00              1.00       16.35
Q635118            1.00        2.00              1.00        1.38
Q635119            2.00        3.00              1.00        1.72
Q635121            3.00        4.00              1.00       18.80
Q635122            4.00        5.00              1.00       16.45
Q635123            5.00        6.00              1.00        6.87
//et

Hebert-Brent East

//st
Sample ID      From (m)      To (m)      Interval (m)      Au g/t
Q635101            0.00        1.00              1.00        1.97
Q635102            1.00        2.00              1.00       10.80
Q635103            2.00        3.00              1.00        4.23
Q635104            3.00        4.00              1.00        2.86
Q635105            4.00        5.00              1.00        1.89
Q635106            5.00        6.00              1.00        2.53
Q635107            6.00        7.00              1.00        0.75
Q635108            7.00        8.00              1.00        1.13
Q635109            8.00        9.00              1.00        0.76
Q635111            9.00       10.00              1.00        1.29
Q635112           10.00       11.00              1.00        1.04
Q635113           11.00       12.00              1.00        1.50
Q635114           12.00       13.00              1.00        1.35
Q635115           13.00       14.00              1.00        1.13
Q635116           14.00       15.30              1.30        0.68
//et

Additional zones of mineralization have been sampled and assay
results are pending. A program of more extensive stripping and channel
sampling at Hebert-Brent has also been initiated to further expose the
across strike dimensions of the reported channel sampled areas, as none
of the three zones have been delimited across or along strike yet. All
this surface work is being conducted to assist in the successful
planning of a first phase drilling program in the Hebert-Brent Shear
area.

Sampling included insertion of certified standards and blanks into
the stream of samples for chemical analysis. Samples were prepared at
ALS Chemex's laboratory in Yellowknife and shipped to their Vancouver
facility for gold analysis by fire assay and other elements by ICP
analysis. ALS is a certified and accredited laboratory service.

The channel samples reported here are considered representative of
the overall grade and extent of mineralization on the subject areas.
For grab samples also mentioned in this news release, and illustrated
on maps, it should be noted that due to their selective nature assay
results from grab samples may not be indicative of the overall grade
and extent of mineralization on the subject area. The technical
information contained in this news release has been approved by Joseph
Campbell, President of TerraX, who is a Qualified Person as defined in
"National Instrument 43-101, Standards of Disclosure for Mineral
Projects."

About the Hebert-Brent Shear

Geological mapping in June and July identified areas of extensive
sericite alteration which occurs in a recognizable structural zone
called the Barney Deformation Corridor (see August 11, 2015 news
release for more detail). The altered areas in the Hebert-Brent Shear
area are approximately 1 km south and on strike with the Barney Zone
drilled by TerraX in 2014 and winter 2015. Mineralization appears to be
related to east-southeast trending felsic dykes crossing north and
north-east shear zones with dextral deformation/rotation into the
shears. Higher grade areas of mineralization are also recognized at the
contacts of the felsic dykes with mafic volcanics and gabbros. Channel
sampling was carried out in one area of visible sulphide mineralization
in July 2015, and this new zone was coined the "Hebert-Brent Zone".
Subsequent exploration and mapping in the area of the Hebert-Brent Zone
revealed several other similarly mineralized zones within a definable
area of intense shearing and sericite alteration. This broader area has
been termed the Hebert-Brent Shear. The results presented are from the
first two of these additional mineralized zones that are being channel
sampled.

About the Yellowknife City Gold Project

The Yellowknife City Gold Project encompasses approximately 99.3
sq km of contiguous land immediately north of the City of Yellowknife
in the Northwest Territories. Through a series of acquisitions, TerraX
now controls one of the six major high-grade gold camps in Canada - and
the least explored.

The project lies on the prolific Yellowknife greenstone belt and
covers 15 km of strike length on the northern extension of the shear
system that hosts the high-grade Con and Giant gold mines. The project
area contains multiple shears that are the recognized hosts for gold
deposits in the Yellowknife gold district, with innumerable gold
showings and high grade drill results this past year that serve to
indicate the project's potential as a world-class gold district. Since
February 2013, TerraX has consolidated the project area by acquiring,
optioning and staking numerous properties, including: Northbelt,
Goodwin, Ryan Lake, Walsh Lake, and U-Breccia, as well as staking
additional contiguous lands. Being all-season road accessible and
within 15 km of the City of Yellowknife, the YCG is close to vital
infrastructure, including transportation, service providers,
hydro-electric power and skilled trades people.

For more information on the Yellowknife City Gold Project, please
visit our web site at www.terraxminerals.com.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains forward-looking information, which
involves known and unknown risks, uncertainties and other factors that
may cause actual events to differ materially from current expectation.
Important factors - including the availability of funds, the results of
financing efforts, the completion of due diligence and the results of
exploration activities - that could cause actual results to differ
materially from the Company's expectations are disclosed in the
Company's documents filed from time to time on SEDAR (see
www.sedar.com). Readers are cautioned not to place undue reliance on
these forward-looking statements, which speak only as of the date of
this press release. The company disclaims any intention or obligation,
except to the extent required by law, to update or revise any
forward-looking statements, whether as a result of new information,
future events or otherwise.


TEL:   514-341-0408
TSX Venture closing price for TXR-V
Date: 2015/09/04
Closing Price: 0.30

TEL: 1-866-460-0408
info@paradox-pr.ca   Paradox Public Relations
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1525000002TS11525000388-04274420150908