Source	Marketwire
Date	09/22/2015
Time	06:08:27 AM

Company	 COLUMBUS GOLD CORPORATION
Title	Columbus Gold Drills 152.4 Meters of 0.71 gpt Gold, Including 28.9 Meters 
of 2.16 gpt Gold at Eastside Gold Discovery in Nevada





    CDNX Symbol: CGT











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Columbus Gold Corporation

TSX VENTURE SYMBOL: CGT
OTCQX SYMBOL: CBGDF

September 22, 2015

Columbus Gold Drills 152.4 Meters of 0.71 gpt Gold, Including 28.9 Meters of 
2.16 gpt Gold at Eastside Gold Discovery in Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 22, 2015) - Columbus Gold 
Corporation (TSX VENTURE:CGT)(OTCQX:CBGDF) announces results of its summer RC 
drilling program at its 100% controlled Eastside gold project in Nevada.

The drill program was successful in achieving the objective of validating that 
oxide gold mineralization encountered in surface sampling grading up to 16 g/t 
gold, extends at depth in the form of zones of lower grade "cloud" gold 
mineralization that overlays zones of better-grade. The current drilling has 
also revealed that the zones of better-grade gold mineralization are unusually 
thick and much larger than previously interpreted and that they are open in all 
directions. In addition, many of the holes drilled into the better-grade zones 
bottomed in significant gold values.

Robert Giustra, Chairman and CEO of Columbus Gold, commented: "These drill 
results indicate that gold mineralization at Eastside is considerably more 
widespread than previously understood. This bodes well for a project that is 
located in an area with outstanding infrastructure and for which preliminary 
metallurgical testing suggests good recoveries."

A total of 12,298 meters (40,347 feet) was drilled in 51 holes, widely spaced 
over a mineralized area of at least 1,050 X 550 meters. Of the 51 holes, 46 
completed or hit the intended target and of those 46 holes, all intersected 
gold mineralization, and 38 of them return significant gold results. In 
addition 17 holes bottomed in gold. Following are significant intercepts:

/T/

ES-80  152.4 m of 0.71 g/t gold, including 28.9 m of 2.16 g/t and 3 m of
10.88 g/t gold

ES-83  109 m of 0.69 g/t gold, including 10.8 m of 2.30 g/t and 18.2 m of
1.32 g/t gold and an additional 10.6 m of 1.49 g/t gold

ES-84  63.6 m of 1.20 g/t gold, including 4.5 m of 2.06 g/t, 1.5 m of
2.43 g/t gold, 7.6 m of 4.25 g/t gold and 1.5 m of 2.65 g/t gold

ES-86  24.4 m of 2.70 g/t gold, including 3 m of 17.3 g/t gold

ES-39  27.4 m of 2.54 g/t gold and 36.5 g/t silver, including 3 m of
19.61 g/t gold

ES-40  32.0 m of 1.248 g/t gold and 3 m of 203 g/t silver

ES-45  59.4 m of 0.92 g/t gold, including 25.9 m of 1.62 g/t gold

ES-46  59.4 m of 0.58 g/t gold, including 16.8 m of 1.03 g/t gold

ES-58  19.8 m of 1.00 g/t gold and 4.6 m of 1.01 g/t gold

ES-61  21.3 m of 0.89 g/t gold, including 3 m of 2.07 g/t gold

ES-67  22.9 m of 1.37 g/t gold, including 7.6 m of 2.95 g/t gold

ES-71  35.1 m of 0.90 g/t gold, including 12.2 m of 2.61 g/t and 7.6 m of
3.53 g/t gold and an additional 19.8 m of 0.96 g/t gold, including
3 m of 4.57 g/t gold

ES-78  7.6 m of 3.19 g/t gold

ES-81  56.4 m of 0.62 g/t gold and 11 g/t silver, including 13.7 m of
1.13 g/t gold

/T/

A more detailed table of significant drill results is available at the 
following link:

www.columbusgold.com/i/nr/2015-09-22-assays-significant.pdf

Columbus is very encouraged by the upside potential at Eastside. Planning for 
the next phase of drilling is in progress and will include deep core drilling 
to further examine gold mineralization at depth. The deeper drilling to date 
indicates that gold mineralization could underlay the entire drilled area and 
the thickness of the gold intercepts in these deeper holes makes Eastside an 
attractive target for large volumes of gold mineralization.

A drill-hole location map is available at the following link:

www.columbusgold.com/i/nr/2015-09-22-map.pdf

East-west cross sections spaced at 40 meter intervals, with a 40 meter clipping 
plane, through the main mineralized area are available at the following link:

www.columbusgold.com/i/nr/2015-09-22-sections.pdf

Cross sections spaced at 120 meter intervals, with a 120 meter clipping plane, 
which include geology, are available at the following link:

www.columbusgold.com/i/nr/2015-09-22-sections-geo.pdf

A table of comprehensive drill results is available at the following link:

www.columbusgold.com/i/nr/2015-09-22-assays-all.pdf

Eastside gold mineralization occurs in a discrete package of overlapping, 
rhyolite flow dome complexes which were emplaced and/or erupted 7.2 million 
years ago. These flow dome complexes are confined to an outcrop belt about two 
miles wide and seven miles long which is completely enclosed in Columbus Gold's 
claim block. Detailed mapping and sampling of the entire claim block by 
Columbus geologists has yielded numerous additional targets outside of the area 
of the current drilling.

The project has outstanding infrastructure for mining and processing; is 32 km 
(20 mi) west of Tonopah, Nevada, and lies 9.7 km (6 mi) north of paved highway 
US 95, the main road route from Las Vegas to Reno. A good gravel road from the 
highway, along with a major power transmission line both pass through the claim 
block. The current drilling area is on the east flank of the Monte Cristo Range 
and a portion of the claim block extends well into the adjacent flats, which 
would provide excellent operating sites. The valley is known to have shallow 
water available in the same aquifer, which provided water for milling the 
Tonopah ores in the early 1900s. The area is high desert with sparse 
vegetation, and year-round drilling is possible.

Gold and silver assays for Phase IV drilling were performed by American Assay 
Labs in Sparks, Nevada. American inserts blinds and standards in the drill-hole 
assay string-generally 7% of all assays performed are of standards or blinds. 
For Phase IV drilling, gold analyses are by fire assay with atomic absorption 
finish. Silver assays are by fire assay with gravimetric finish. In addition, 
Columbus Gold also inserts blank samples and also standard samples of known 
gold and silver assay values in the drill assay string for quality control. 
Additional check sampling is ongoing and, if material differences occur, those 
will be reported. All Phase IV holes were surveyed downhole by IDS.

Andy Wallace is a Certified Professional Geologist (CPG) with the American 
Institute of Professional Geologists and is the Qualified Person under NI 
43-101 who has reviewed and approved the technical content of this press 
release. Mr. Wallace is the principal of Cordilleran Exploration Company 
(Cordex), which is conducting exploration and project generation activities for 
Columbus Gold on an exclusive basis.

ON BEHALF OF THE BOARD,

Robert F. Giustra, Chairman & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This release contains forward-looking information and statements, as defined by 
law including without limitation Canadian securities laws and the "safe harbor" 
provisions of the US Private Securities Litigation Reform Act of 1995 
("forward-looking statements"), respecting the potential for gold 
mineralization underlaying the entire drilled area and the potential volumes of 
gold mineralization; a new FS that the Company intends to commission; the time 
frame in which the Company expects to complete the tendering process for the 
commission of the FS; completion of the FS; and projected funding of 
exploration and development programs by Nord Gold N.V. pursuant to the terms of 
the option agreement and the related completion of the FS . Forward-looking 
statements involve risks, uncertainties and other factors that may cause actual 
results to be materially different from those expressed or implied by the 
forward-looking statements, including without limitation: the ability to 
complete the FS by the proposed target date or at all; risks associated with 
Nord Gold N.V. electing not to exercise its option and make the related option 
payments and the ability to complete the FS by the stated deadline or at all; 
cost increases; availability of qualified workers and drill equipment; access 
to power supply sources and power prices; risks associated with exploration 
projects, mineral reserve and resource estimates (including the risk of 
assumption and methodology errors); dependence on third parties for services; 
non-performance by contractual counterparties; title risks; and general 
business and economic conditions. Forward-looking statements are based on a 
number of assumptions that may prove to be incorrect, including without 
limitation assumptions as to: future drill results; general business and 
economic conditions; the timing and receipt of required approvals; availability 
of financing; power prices; ability to procure equipment and supplies including 
without limitation drill rigs; that political risk will remain on current 
levels; and ongoing relations with employees, partners and joint venturers. 
Although Columbus Gold has attempted to identify important factors that could 
cause actual actions, events or results to differ materially from those 
described in forward-looking statements, there may be other factors that cause 
actions, events or results not to be anticipated, estimated or intended. There 
can be no assurance that forward-looking statements will prove to be accurate, 
as actual results and future events could differ materially from those 
anticipated in such statements. Columbus Gold undertakes no obligation to 
update forward-looking statements if circumstances or management's estimates or 
opinions should change except as required by applicable law. The reader is 
cautioned not to place undue reliance on forward-looking statements.

- 30 -

CONTACT INFO:

Columbus Gold Corporation - Institutional/Analysts:
Peter A. Ball
Senior Vice President
(604) 634-0973
peter@columbusgroup.com

or

Columbus Gold Corporation - Media/Communications:
Jorge Martinez
VP Communications & Technology
(604) 634-0972
jorge@columbusgroup.com
www.columbusgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=543166473