Source	MARKET NEWS
Date	09/22/2015
Time	05:28:33 AM

Company	 Rathdowney Resources Ltd.
Title	Additional Results from Drilling at Rathdowney's





    CDNX Symbol: RTH











Press Release	





Additional Results from Drilling at Rathdowney's Project Olza:Expansion of 
Zone 5; Advancement of other Studies --->@NEWS RELEASE
RATHDOWNEY RESOURCES LTD ("RTH-V;RATHF-0")
- Additional Results from Drilling at Rathdowney's Project Olza:
- Expansion of Zone 5; Advancement of other Studies

Rathdowney Resources Ltd. ("Rathdowney" or the "Company")
announces additional results from new drilling and an update on other
programs at its flagship Olza Zinc-Lead-Silver Project in southwest
Poland.

Current activities at Project Olza are designed to support mine
planning studies and permitting as outlined for projects in Poland.
Programs are also directed toward building on the positive results
announced earlier this year:

//st

In February 2015, the Company announced an increase in mineral resources
to 24.4 million tonnes in the inferred category grading 7.02% Zn+Pb (at a
2% Zn cut-off)1;
In April 2015, Rathdowney announced the robust results of a Preliminary
Economic Assessment ("PEA") indicating strong potential financial returns
for a 6,000 tonnes per day conventional underground mine and mill
operation2; and
In June 2015, initial results from new drilling in the vicinity of Zone
5, one of the zones that comprise the current mineral resources, showed
important extensions to the mineralized zone.
//et

Today's results include silver assays for holes OLZ-230 and OLZ-241 adding
to zinc and lead results announced in the June 2015 release and zinc, lead
and silver assays for 14 new holes (OLZ-242 to OLZ-255).

Significant widths and grades of zinc, lead and/or silver
mineralization were encountered in 11 of the 14 new holes. Full details
are provided in the Table of Assay Results attached to this release.
Highlights include:

//st

4.6 m of 6.6% Zn+Pb and 9.5 g/t Ag, including 2.2 m of 9.9% Zn+Pb and
13.2 g/t Ag in hole OLZ-244
6.7 m of 6.6% Zn+Pb and 9.6 g/t Ag, including 3.9 m of 8.6% Zn+Pb and
11.2 g/t Ag in hole OLZ-247
6.9 m of 3.6% Zn+Pb and 15.9 g/t Ag, including 1.8 m of 10.4% Zn+Pb and
41.4 g/t Ag in hole OLZ-255
//et

This new information complements the excellent results from the 16 holes
reported in the June release. Each of the new holes was drilled outside of
the currently defined mineral resource as shown on the map at
http://www.rathdowneyresources.com/i/pdf/rdr/2015-09-22_NRM_8sBnmq.pdf,
indicating further extensions to Zone 5 and excellent potential to increase
mineral resources with additional drilling.

Key geotechnical data is also being collected from each hole for
engineering studies to assess sites for infrastructure development.
Concurrently, hydrogeological studies and environmental data collection
programs to support permitting are progressing.

"The Olza team has done an outstanding job to advance the drilling
program," said President & CEO Robert Konski.  "Importantly, the assay
results continue to confirm strong intervals of zinc-lead-silver
mineralization as well as providing valuable data for our ongoing
engineering studies. We look forward to receiving the additional
results and updating the mineral resource estimate."

Rathdowney is committed to responsible mineral exploration and
development with respectful, mutually beneficial discussions and
opportunities for local communities. Our Project Olza community
specialists discuss our programs with representatives of local
communities and government during all phases of work.

Konski added, "These programs could not be advanced successfully
without the key support of our stakeholder engagement professionals."




//st
1 Individual grades are 5.53% Zn & 1.49% Pb. For further information see
Rathdowney's new release date Feb 2, 2015. Mineral resources that are not
mineral reserves do not have demonstrated economic viability. 2 For
additional details on the PEA, see Rathdowney's news releases dated Apr 20,
2015 & May 14, 2015.

//et
Table of Assay Results




//st
Drill Hole
Number           From     To        Length  Zn+Pb**   Zn      Pb       Ag
(m)      (m)       (m)     (%)       (%)     (%)     (g/t)

OLZ-230**        108.60   111.50    2.90    2.80      1.78    1.02     42.6
OLZ-241**        103.35   106.60    3.25    16.00     15.91   0.08      2.2
Incl   103.35   104.60    1.25    36.85     36.68   0.16      4.4
OLZ-242          88.70    91.80     3.10    2.99      2.99    0.01     13.2
Incl    89.30   91.00     1.70    4.15      4.15    0.01     18.6
OLZ-243          95.90    98.40     2.50    5.85      4.31    1.54      6.0
Incl    96.50   98.40     1.90    7.34      5.32    2.02      7.2
104.20   107.95    3.75    1.82      1.80    0.03      4.9
Incl   104.20   105.30    1.10    3.20      3.14    0.06     10.9
OLZ-244          97.50    103.50    6.00    5.32      5.04    0.28      7.8
Incl    98.40   103.00    4.60    6.58      6.22    0.36      9.5
&   100.80   103.00    2.20    9.89      9.30    0.59     13.2
OLZ-245          109.00   111.70    2.70    1.41      1.37    0.03      3.9
OLZ-247          98.00    116.80    18.80   4.60      4.04    0.56      7.3
Incl    99.30   106.00    6.70    6.61      6.47    0.14      9.6
&   102.10   106.00    3.90    8.64      8.55    0.09     11.2
OLZ-250          97.20    99.50     2.30    2.89      2.74    0.15      5.6
OLZ-251          91.80    99.35     7.55    2.27      1.97    0.29      3.2
Incl    94.00   95.50     1.50    5.86      5.18    0.67      8.2
Incl    97.70   98.30     0.60    6.00      4.56    1.44      4.5
OLZ-252          88.90    90.60     1.70    4.58      4.38    0.20     17.1
OLZ-253          89.60    94.70     5.10    2.53      2.29    0.24      4.7
OLZ-254          115.00   116.50    1.50    3.38      1.08    2.30     45.1
OLZ-255          113.80   120.65    6.85    3.64      3.45    0.19     15.9
Incl   118.20   120.00    1.80    10.36     9.94    0.42     41.4
All diamond core holes were drilled vertically through the sub-horizontal
mineralized horizons so intersections represent approximate true widths. No
significant results in holes 246, 248 & 249.
*Figures may not add due to rounding.
** Repeated with Ag results not available at time of previous    release.
//et

About Rathdowney and Project Olza

Rathdowney Resources Ltd. is focused on advancing Project Olza
through permitting and into production.

Project Olza is located in the Upper Silesian Mining District of
southwestern Poland, a world-class region of Mississippi Valley-type
deposits with well-developed mining infrastructure. Easily accessible
by road, the Olza project site is a one-hour drive from Krakow, a major
city with full services, including an international airport. The
deposits at Olza are 25 km from the ZGH zinc smelter at Boleslaw. A
railway line runs through the Olza project-area, linking it to the
local facilities and also to other smelters through ports on the Baltic
Sea.

Dr. Keith Roberts, PGeo., is the qualified person, as defined
under NI43-101, for the drilling program at Project Olza and has
reviewed the technical information in this release.

On behalf of the Board of Directors Robert Konski President & CEO



//st
Sample preparation for the current drilling program is performed at the
Bureau Veritas (BV) laboratory in Krakow, Poland. Core samples are weighed,
dried & crushed to )70% passing 10 mesh (2 mm), then 500 g sub-samples are
riffle split & pulverized to )85% passing 200 mesh (75 m). Samples are
shipped by air freight to the Vancouver laboratory of Bureau Veritas
Commodities Canada Ltd., an ISO 9001 accredited laboratory, for analysis.
All samples are assayed for Pb, Zn, Ag & 38 additional elements by 4 acid
(HF-HNO3-HClO4, HCl) digestion of an 0.5 g sample with an ICP-AES/ICP-MS
(inductively coupled atomic emission spectrometry/mass spectrometry) finish
(BV Code: MA270). Samples with Zn values )40% or Pb values )10%, the upper
limits for the MA270 method, are re-analyzed by BV method MA371; 4 acid
digestion of 0.1 g sample with ICP-AES finish. As part of a comprehensive
QAQC program, one standard & one replicate are inserted into the sample
stream in each group of 20 samples, as well as one or more blanks in each
analytical batch.

//et

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This release includes certain statements that may be deemed
"forward-looking statements". All statements in this release, other
than statements of historical facts, that address exploration drilling,
exploitation activities and events or developments that the Company
expects, are forward looking statements. Although the Company believes
the expectations expressed in such forward-looking statements are based
on reasonable assumptions, such statements are not guarantees of future
performance and actual results or developments may differ materially
from those in the forward-looking statements. Assumptions used by the
Company to develop forward-looking statements include the following:
the Olza project will obtain all required environmental and other
permits and all land use and other licenses, studies and development of
the Olza project will continue to be positive, and no geological or
technical problems will occur. Factors that could cause actual results
to differ materially from those in forward-looking statements include
market prices, exploitation and exploration successes, continuity of
mineralization, potential environmental issues and liabilities
associated with exploration, development and mining activities,
uncertainties related to the ability to obtain necessary permits,
licenses and title and delays due to third party opposition, changes in
government policies regarding mining and natural resource exploration
and exploitation, continued availability of capital and financing, and
general economic, market or business conditions. Investors are
cautioned that any such statements are not guarantees of future
performance and actual results or developments may differ materially
from those projected in the forward-looking statements. For more
information on the Company, investors should review the Company's
continuous disclosure filings that are available at www.sedar.com.

Information Concerning Estimates of Inferred Resources

This news release uses the term "inferred mineral resources".
Rathdowney Resources Ltd. advises investors that although these terms
are recognized and required by Canadian regulations (under National
Instrument 43-101 Standards of Disclosure for Mineral Projects), the
U.S. Securities and Exchange Commission does not recognize them.
Investors are cautioned not to assume that any part or all of the
mineral deposits in these categories will ever be converted into
reserves. In addition, "inferred resources" have a great amount of
uncertainty as to their existence, and economic and legal feasibility.
It cannot be assumed that all or any part of an Inferred Mineral
Resource will ever be upgraded to a higher category. Under Canadian
rules, estimates of Inferred Mineral Resources may not form the basis
of feasibility or pre-feasibility studies, or economic studies except
for Preliminary Economic Assessment as defined under 43-101. Investors
are cautioned not to assume that part or all of an inferred resource
exists, or is economically or legally mineable.









































TSX Venture closing price for RTH-V
Date: 2015/09/18
Closing Price: 0.14

TEL:     778-373-6728   Susie Bell, Investor Relations
TF (NA): 1-800-667-2114
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1526400007TS11526400648-05264420150922