Source	Marketwire
Date	09/23/2015
Time	05:02:11 AM

Company	 KAMINAK GOLD CORPORATION
Title	Kaminak Increases Grade, Oxide Ounces and Indicated Resources in Updated 
Mineral Resource Estimate at Coffee Gold Project and Provides Feasibility Study 
Update





    CDNX Symbol: KAM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kaminak Gold Corporation

TSX VENTURE SYMBOL: KAM

September 23, 2015

Kaminak Increases Grade, Oxide Ounces and Indicated Resources in Updated 
Mineral Resource Estimate at Coffee Gold Project and Provides Feasibility Study 
Update


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 23, 2015) - Kaminak Gold 
Corporation (TSX VENTURE:KAM) is pleased to announce an updated Mineral 
Resource Estimate prepared in accordance with Canadian National Instrument 
43-101 ("NI 43-101"), together with a feasibility study progress report, on the 
Company's 100% owned, flagship, development track Coffee Gold Project located 
in Yukon, Canada.

As part of the ongoing feasibility study initiated at Coffee in 2014, Kaminak 
undertook a 70,000 metre infill drilling campaign on the four main Coffee 
deposits: Supremo, Latte, Double Double and Kona, with the aim of upgrading the 
2.1 million ounce, primarily oxide gold resource contained in the conceptual 
pit shells defined in the 2014 Preliminary Economic Assessment ("PEA", see 
press release June 10, 2014) from the Inferred to the Indicated resource 
category. In order to compare with previous mineral resource estimates reported 
at Coffee, the base case estimate is reported at a cut-off grade of 0.5 grams 
per tonne gold ("g/t Au") for Oxide, Upper and Middle Transitional facies 
mineralization and a 1 g/t Au cut-off for Lower Transitional and Sulphide 
material. Using these cut-offs, the updated estimate of mineral resources for 
Coffee is 52.4 million tonnes at an average grade of 1.68 g/t Au for 2,824,000 
oz of contained gold in the Indicated category and 42.7 million tonnes at a 
grade of 1.52 g/t Au for 2,088,000 oz of contained gold in the Inferred 
category.

2015 COFFEE MINERAL RESOURCE ESTIMATE

Highlights:

/T/

--  New estimate represents an 8% increase in the resource grade for
Indicated resources and a 12% increase in resource grade for Inferred
resources.
--  The 2014-15 drilling program at Coffee increased the confidence in the
interpretation of higher-grade zones within the deposits and
successfully upgraded a significant portion of the previous Inferred
resource into the Indicated category, including all of the contained
ounces in the resource pit shell generated for the 2014 PEA.
--  Indicated Resources increased to over 52 million tonnes grading 1.68 g/t
Au for 2,824,000oz of contained gold using the base case cut-off grades.
This represents an almost four-fold increase in tonnage and ounces
compared to the 2014 estimate (see table 1).

/T/

Supporting graphics for this updated mineral resource estimate news release can 
be viewed at the following link: 
http://kaminak.com/_resources/pdf/Coffee_Block_Model.pdf

A comparison of the updated September 2015 resource estimate to the previous 
estimate, released January 2014, is shown in Table 1 below:

/T/


Table 1: Comparison of Estimated Mineral Resources 2015 vs. 2014

----------------------------------------------------------------------------
INDICATED                                      September 2015
Cut-Off
Oxide type                         g/t Au    ktonnes     Au g/t     koz Au
----------------------------------------------------------------------------
Oxide (OX)                              0.5     38,095       1.68      2,055
Upper Transitional (UT)                 0.5      7,649       1.65        406
Middle Transitional (MT)(i)             0.5      4,241       1.55        211
Lower Transitional                      1.0      2,294       1.94        143
Sulphide                                1.0        138       2.09          9
----------------------------------------------------------------------------
OX+UT+MT                                0.5     49,985       1.66      2,671
----------------------------------------------------------------------------
Total Indicated                                 52,417       1.68      2,824
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
INFERRED                                       September 2015
Cut-Off
Oxide type                         g/t Au    ktonnes     Au g/t     koz Au
----------------------------------------------------------------------------
Oxide                                   0.5     18,576       1.30        775
Upper Transitional                      0.5      8,244       1.42        378
Middle Transitional(i)                  0.5      6,030       1.69        328
Lower Transitional                      1.0      6,803       1.94        424
Sulphide                                1.0      3,030       1.87        182
----------------------------------------------------------------------------
OX+UT+MT                                0.5     32,850       1.40      1,481
----------------------------------------------------------------------------
Total Inferred                                  42,683       1.52      2,088
----------------------------------------------------------------------------


Table 1: Comparison of Estimated Mineral Resources 2015 vs. 2014

----------------------------------------------------------------------------
INDICATED                                       January 2014
Cut-Off
Oxide type                         g/t Au    ktonnes     Au g/t     koz Au
----------------------------------------------------------------------------
Oxide (OX)                              0.5      8,555       1.75        480
Upper Transitional (UT)                 0.5      3,619       1.32        153
Middle Transitional (MT)(i)               -          -          -          -
Lower Transitional                      0.5      2,141       1.21         83
Sulphide                                1.0         42       1.52          2
----------------------------------------------------------------------------
OX+UT+MT                                0.5     12,174       1.62        634
----------------------------------------------------------------------------
Total Indicated                                 14,357       1.56        719
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
INFERRED                                        January 2014
Cut-Off
Oxide type                         g/t Au    ktonnes     Au g/t     koz Au
----------------------------------------------------------------------------
Oxide                                   0.5     50,437       1.28      2,078
Upper Transitional                      0.5     15,967       1.39        714
Middle Transitional(i)                    -          -          -          -
Lower Transitional                      0.5      6,662       1.43        306
Sulphide                                1.0      5,525       1.89        336
----------------------------------------------------------------------------
OX+UT+MT                                0.5     66,404       1.31      2,792
----------------------------------------------------------------------------
Total Inferred                                  78,591       1.36      3,434
----------------------------------------------------------------------------
(i)Middle Transitional not estimated in Jan-2014 resource, previously
included within the 2014 Upper Transitional grouping.
Additional Notes: Definition of Upper Trans, Middle Trans & Lower Trans are
provided in the Mineral Resource Estimation Parameters section below. 2015
Base Case cut-off grade of 0.5g/t Au for Oxide, Upper and Middle Transition
mineral resources, and 1.0g/t Au for Lower Transition and Sulphide mineral
resources, are based on reasonable projections of technical and economic
parameters which demonstrate reasonable prospects of economic viability. All
figures are rounded to reflect the relative accuracy of the estimates. Some
categories may not balance due to rounding. Mineral resources are not
mineral reserves and do not have a demonstrated economic viability.

/T/

Revised and preliminary design parameters indicate that the resource cut-off 
grade limits will be reduced to 0.3 g/t Au for Oxide and Upper Transitional, 
0.4 g/t Au for Middle Transitional and 1.0 g/t Au for Lower Transitional and 
Sulphide resources. For comparative purposes, based on these lower cut-off 
grades, the 2015 Indicated resource totals 63.7 million tonnes averaging 1.45 
g/t Au for 2,968,000 ounces of contained gold, and the Inferred resource totals 
52.4 million tonnes at an average grade of 1.31 g/t Au for 2,212,000 ounces of 
contained gold (see Table 2 below).

/T/


Table 2: Coffee Indicated and Inferred Resources 2015 at Projected
Feasibility Study resource cut-off grades (0.3 g/t Au Oxide & Upper
Transition Zones; 0.4 g/t Au Middle Transition Zone, 1 g/t Au Lower
Transition and Sulphide)

----------------------------------------------------------------------------
Cut-Off
Oxide type            Au g/t        Indicated                Inferred

ktonnes  Au g/t  koz Au ktonnes  Au g/t  koz Au
----------------------------------------------------------------------------
Oxide                    0.3  47,127    1.43   2,170  25,020    1.07     857
Upper Transitional       0.3   9,461    1.41     429  10,646    1.19     408
Middle Transitional      0.4   4,647    1.45     217   6,855    1.54     340
Lower Transitional       1.0   2,294    1.94     143   6,803    1.94     424
Sulphide                 1.0     138    2.09       9   3,030    1.87     182
----------------------------------------------------------------------------
OX+UT                    0.3  56,587    1.43   2,598  35,665    1.10   1,265
OX+UT+MT             0.3-0.4  61,235    1.43   2,815  42,520    1.17   1,605
----------------------------------------------------------------------------
All                           63,666    1.45   2,968  52,354    1.31   2,212
----------------------------------------------------------------------------
Additional Notes: Definition of Upper Trans, Middle Trans & Lower Trans are
provided in the Mineral Resource Estimation Parameters section below. 2015
Base Case cut-off grade of 0.5g/t Au for Oxide, Upper and Middle Transition
mineral resources, and 1.0g/t Au for Lower Transition and Sulphide mineral
resources, are based on reasonable projections of technical and economic
parameters which demonstrate reasonable prospects of economic viability. All
figures are rounded to reflect the relative accuracy of the estimates. Some
categories may not balance due to rounding. Mineral resources are not
mineral reserves and do not have a demonstrated economic viability.

/T/

"Drilling in 2014-15 has successfully grown Coffee's gold inventory to an 
indicated resource of approx. 3 million ounces at a grade of 1.45g/t Au plus an 
Inferred resource of approx. 2.2 million ounces at a grade of 1.31g/t Au, using 
projected feasibility resource cut-off grades. The high conversion rate from 
Inferred to Indicated together with the increase in grade and global resources, 
further demonstrates the confidence in the modeling approach taken by SIM 
Geological Inc. and underpins our confidence in the quality and predictability 
of the Coffee resource as we head into the home stretch of the feasibility 
study, which is fully funded and on track for completion in early Q1, 2016" 
stated Eira Thomas, Kaminak President & CEO.

FEASIBILITY STUDY UPDATE

Kaminak initiated a Feasibility Study (FS) at Coffee in July of 2014 after 
receiving results from a preliminary economic assessment (PEA) confirming that 
Coffee represents a robust, high margin, 11-year, open pit, gold mining 
opportunity using a gold price of US$1250 and a Canadian/US exchange rate of 
$0.95, generating a pre-tax NPV of C$522 Million and an IRR of 33%.

The feasibility study contract as awarded to JDS Energy and Mining in March, 
2015, includes oversight from Fred Lightner, P.E., Kaminak's Director of Mining 
and contributions from SRK, The Mines Group, RRD International, TetraTech EBA, 
Lorax Environmental, and a multidisciplinary environmental baseline team of 
independent consultants, the majority of which are Yukon based.

As of September 18, 2015, all field-related FS programs, including infill 
drilling, were complete and engineering work is well underway. Interim results 
from FS work completed to date are summarized as follows:

/T/

--  FS tracking on schedule and budget, estimated completion date remains
Q1, 2016.
--  Capital costs, operating costs and production metrics are tracking in
line with estimates in the PEA and total in-pit ounces are not expected
to be materially impacted by the increase in ounces reported herein.
--  The heap leach facility has been re-designed and re-located as a free
draining ridge-top heap leach pad and is expected to result in cost
savings and reduce construction time from 22 to 18 months.
--  New access road route selected from the north (Dawson City) will
substantially reduce new road construction (see press release of
September 16, 2015).
--  Two stages of crushing to produce 2 inch sized heap leach feed for the
pad has been selected to optimize metallurgical recoveries. Recently
completed geotechnical studies determined that run of mine feed-size was
underestimated in the PEA.
--  Liquefied natural gas (LNG) incorporated as the primary fuel source 
foron-site power generation, which is expected to substantially reduce
overall energy costs estimated in the PEA.

/T/

Eira Thomas, CEO commented: "Resource and conversion drilling has gone very 
well and most of the assumptions used in the PEA remain relevant and 
defensible. Coffee remains a strong project and one of the few development 
track gold projects located in Canada that can deliver sizeable, high margin 
production in excess of 160,000 ounce per annum in the current gold price 
environment."

2014-15 DRILLING PROGRAM OBJECTIVES COMPLETED

The Company announced on August 13, 2015 the completion of 70,000m of infill 
drilling with the objective of upgrading 2014 PEA in-pit Inferred resources to 
the Indicated category. The location and spacing of infill drilling was 
determined in consultation with independent Qualified Person Robert Sim, P.Geo 
of SIM Geological Inc., who completed the 2012, 2014 and 2015 Coffee Gold 
Project mineral resource estimates.

All objectives were achieved with the successful conversion of Inferred to 
Indicated class resources within the 2014 PEA modelled open pit shells. 
Drilling also extended beyond the limits of the PEA pit shells in order to 
accommodate possible future depth expansion, resulting in the expansion of 
resources in some locations. A resource estimate has also been produced for the 
Kona North deposit (discovery announced September 2, 2014). Estimates of 
mineral resources by deposit area are shown in Table 3 below.

The additional drilling has provided much better control on the distribution of 
mineralization in the Coffee deposit and, in some instances, allows for 
increased confidence in the interpretation of narrower domains, thereby 
reducing internal dilution and increasing the overall grade of the resource. 
The closer-spaced drilling also allows for better continuity of grade from 
section to section, further reducing the amount of internal dilution in the 
block model.

/T/


Table 3: 2015 Resources by Deposit at Base Case Cut-Off(i)

----------------------------------------------------------------------------
Deposit                        Indicated                   Inferred

ktonnes   Au g/t   koz Au  ktonnes   Au g/t   koz Au
----------------------------------------------------------------------------
Supremo                  34,453     1.72    1,907   22,927     1.47    1,081
Latte                    14,499     1.46      681   14,408     1.48      686
Double Double             1,838     2.81      166    2,318     1.73      129
Kona                      1,628     1.35       71    1,600     1.58       81
Kona North                    0        0        0    1,430     2.40      110
----------------------------------------------------------------------------
Total All Zones          52,417     1.68    2,824   42,683     1.52    2,088
----------------------------------------------------------------------------
(i)2015 Base Case cut-off grade of 0.5g/t Au for Oxide, Upper and Middle
Transition mineral resources, and 1.0g/t Au for Lower Transition and
Sulphide mineral resources, are based on reasonable projections of technical
and economic parameters which demonstrate reasonable prospects of economic
viability. All figures are rounded to reflect the relative accuracy of the
estimates. Some categories may not balance due to rounding. Mineral
resources are not mineral reserves and do not have a demonstrated economic
viability.

/T/

COFFEE GOLD PROJECT MINERAL RESOURCE ESTIMATION PARAMETERS

The Coffee Gold Project September 2015 Indicated and Inferred Mineral Resource 
Estimate was completed by independent Qualified Person Robert Sim, P.Geo. of 
SIM Geological Inc. and is reported in accordance with the guidelines of the 
Canadian Securities Administrators National Instrument 43-101. The estimate is 
derived from 1478 diamond core and reverse circulation drill holes completed 
from 2010 to 2015 for a total of 261,426 metres. The majority of the resource 
comprises the Latte - Supremo - Double Double deposits, which occur within 
close proximity to one another over an area measuring approximately 2km x 2km. 
The Kona and Kona North deposits lie approximately 2.5 kilometres west of Latte.

Three-dimensional block models were created within mineralization domain 
wireframes based on geostatistical applications using commercial mine planning 
software MineSight(R) (v10.0-2). The block size across all deposit areas is 10 
x 2.5 x 5 metres. The long axis of the blocks is aligned with the strike of the 
mineralized domain, and the shorter dimension is aligned across the strike 
direction.

In contrast to the maiden 2012 Resource Estimate which utilized only 
qualitative visual logging to define the oxidation surfaces, and the 2014 
Resource Estimate which applied a combination of qualitative and quantitative 
data, the updated 2015 resource estimate uses a more refined interpolative 
modelling methodology to apply more rigorous quantifiable cyanide soluble gold 
(AuCN) data resulting in much more detailed resolution of the distribution of 
oxidation facies within the block model. Since 2013, Kaminak has undertaken 
cyanide leach assaying, in conjunction with the traditional fire assaying 
method, to measure the cyanide soluble characteristics of the gold in the 
Coffee Deposit. Samples selected for AuCN analysis were restricted to intervals 
where fire assay gold grades are greater than 0.3 g/t due to the detection 
limit of the cyanide assay analytical method This data is reasonably 
distributed but, because it excludes lower-grade sample intervals, is not 
sufficient to support direct estimation of AuCN estimates in model blocks. As 
an alternative, the ratio of AuCN/AuFireAssay is calculated in samples where 
AuCN data is present and these ratios are interpolated in the block model. 
These estimated ratios are used to define oxide types inside the mineralized 
domains. Oxidation is channeled along the structural corridors that host the 
gold deposits, and it is common to find intense oxidation at depths of over 
200m below surface. Strong oxidation is present over the majority of the 
Supremo and Double Double deposits. Oxidation is less pervasive at Latte, 
extending to about 125m below surface in some areas.

Five oxide types or domains have been interpreted for the Coffee deposit based 
on the AuCN/total Au ratios as described in Table 4 below.

/T/


Table 4: Oxidation Facies designation parameters

----------------------------------------------------------------------------
Cyanide leach ratio
Facies Type                   (cyanide assay/fire assay)
----------------------------------------------------------------------------
Oxide                               0.90-1.0
Upper Transition                          0.70-0.90
Middle Transition                         0.50-0.70
Lower Transition                          0.10-0.50
Sulphide                               0-0.10
----------------------------------------------------------------------------

/T/

The resources are classified according to their proximity to sample locations 
and are reported, as required by NI 43-101, according to the CIM Definition 
Standards for Mineral Resources and Mineral Reserves. The Coffee Mineral 
Resource Estimate comprises relatively continuous, sub-vertical zones of gold 
mineralization, the majority of which occurs at depths less than 150m below 
surface. The resource has been subjected to a series of floating cone shells 
based on reasonable projected technical and economic parameters for a deposit 
of this type, scale and location. The results indicate that the vast majority 
of the resource exhibits reasonable prospects for eventual economic extraction, 
and as a result the mineral resources presented in this release are not 
restricted within a pit shell. There are currently no mineral reserves at the 
Coffee project, however as detailed herein, the Coffee Feasibility Study is 
currently underway and remains on schedule for completion Q1 2016.

Full details of the resource modeling parameters and assumptions will be 
published in the NI 43-101 Coffee Feasibility Study.

On behalf of the Board of Directors of Kaminak

Eira Thomas, President and CEO

Kaminak Gold Corporation

For further information about Kaminak Gold Corporation or this news release, 
please visit our website at www.kaminak.com.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Robert Sim, P.Geo., Consultant to the Company and a Qualified Person as defined 
by National Instrument 43-101 ("NI 43-101") has reviewed and approved the 
contents of this news release related to the mineral resource estimate. All 
samples were collected in accordance with industry standards. Splits from the 
drill core and RC percussion samples were submitted to the ALS sample 
preparation laboratory in Whitehorse, Yukon Territory, Canada, and then 
transferred to ALS' laboratory in Vancouver, British Columbia, Canada for fire 
assay and ICP analysis. Accuracy of results is tested through the systematic 
inclusion of standards, blanks and check assays. The mineral resource estimate 
referenced in this press release was prepared in September 2015 by Robert Sim, 
P.Geo. an independent Qualified Person as defined by NI 43-101. Kaminak's 
additional disclosure of a technical or scientific nature in this press release 
has been reviewed and approved by Mr Tim Smith, MSc, P.Geo., Kaminak's Vice 
President of Exploration, who serves as a Qualified Person under the definition 
of National Instrument 43-101.

Cautionary Note concerning estimates of Inferred and Indicated Resources:

This news release uses the terms "Inferred Resources" and "Indicated 
Resources", which have a great amount of uncertainty as to their existence, and 
great uncertainty as to their economic and legal feasibility. It cannot be 
assumed that all or any part of an Inferred and/or Indicated Mineral Resource 
will ever be upgraded to a higher category. Under Canadian rules, estimates of 
Inferred Resources may not form the basis of feasibility or other economic 
studies. Kaminak advises U.S. investors that while this term is recognized and 
required by Canadian regulations, the U.S. Securities and Exchange Commission 
does not recognize it. U.S. investors are cautioned not to assume that part or 
all of an Inferred and Indicated resource exists, or is economically or legally 
minable.

Caution Concerning Forward-Looking Statements

Certain disclosures in this release, including management's assessment of 
plans, projects and intentions with respect to the further development of the 
Coffee Project and future exploration programs, constitute forward-looking 
statements that are subject to numerous risks, uncertainties and other factors 
relating to Kaminak's operations as a mineral exploration company that may 
cause future results to differ materially from those expressed or implied in 
such forward-looking statements, including risks as to the completion of the 
plans and projects. Readers are cautioned not to place undue reliance on 
forward-looking statements. Except as required by law, Kaminak expressly 
disclaims any intention or obligation to update or revise any forward-looking 
statements, whether as a result of new information, future events, or otherwise.

The mineral resource figures referred to in this press release are estimates 
and therefore insufficient to allow meaningful application of the technical and 
economic parameters to enable an evaluation of technical or economic viability 
and no assurances can be given that mining of the Coffee Project is 
commercially viable or that the indicated levels of gold will be produced. Such 
estimates are expressions of judgment based on knowledge, mining experience, 
analysis of drilling results and industry practices. Valid estimates made at a 
given time may significantly change when new information becomes available. 
While the Company believes that the resource estimates included in this press 
release are well established, by their nature, resource estimates are imprecise 
and depend, to a certain extent, upon statistical inferences which may 
ultimately prove unreliable. If such estimates are inaccurate or are reduced in 
the future, this could have a material adverse impact on the Company.

- 30 -

CONTACT INFO:

Kaminak Gold Corporation
Tony Reda
Vice-President of Corporate Development
604.646.4534 or Toll Free: 1.888.331.2269
info@kaminak.com
www.kaminak.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=543160050


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kaminak Gold Corporation

TSX VENTURE SYMBOL: KAM

September 23, 2015

Kaminak Increases Grade, Oxide Ounces and Indicated Resources in Updated 
Mineral Resource Estimate at Coffee Gold Project and Provides Feasibility Study 
Update


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 23, 2015) - Kaminak Gold 
Corporation (TSX VENTURE:KAM) is pleased to announce an updated Mineral 
Resource Estimate prepared in accordance with Canadian National Instrument 
43-101 ("NI 43-101"), together with a feasibility study progress report, on the 
Company's 100% owned, flagship, development track Coffee Gold Project located 
in Yukon, Canada.

As part of the ongoing feasibility study initiated at Coffee in 2014, Kaminak 
undertook a 70,000 metre infill drilling campaign on the four main Coffee 
deposits: Supremo, Latte, Double Double and Kona, with the aim of upgrading the 
2.1 million ounce, primarily oxide gold resource contained in the conceptual 
pit shells defined in the 2014 Preliminary Economic Assessment ("PEA", see 
press release June 10, 2014) from the Inferred to the Indicated resource 
category. In order to compare with previous mineral resource estimates reported 
at Coffee, the base case estimate is reported at a cut-off grade of 0.5 grams 
per tonne gold ("g/t Au") for Oxide, Upper and Middle Transitional facies 
mineralization and a 1 g/t Au cut-off for Lower Transitional and Sulphide 
material. Using these cut-offs, the updated estimate of mineral resources for 
Coffee is 52.4 million tonnes at an average grade of 1.68 g/t Au for 2,824,000 
oz of contained gold in the Indicated category and 42.7 million tonnes at a 
grade of 1.52 g/t Au for 2,088,000 oz of contained gold in the Inferred 
category.

2015 COFFEE MINERAL RESOURCE ESTIMATE

Highlights:

/T/

--  New estimate represents an 8% increase in the resource grade for
Indicated resources and a 12% increase in resource grade for Inferred
resources.
--  The 2014-15 drilling program at Coffee increased the confidence in the
interpretation of higher-grade zones within the deposits and
successfully upgraded a significant portion of the previous Inferred
resource into the Indicated category, including all of the contained
ounces in the resource pit shell generated for the 2014 PEA.
--  Indicated Resources increased to over 52 million tonnes grading 1.68 g/t
Au for 2,824,000oz of contained gold using the base case cut-off grades.
This represents an almost four-fold increase in tonnage and ounces
compared to the 2014 estimate (see table 1).

/T/

Supporting graphics for this updated mineral resource estimate news release can 
be viewed at the following link: 
http://kaminak.com/_resources/pdf/Coffee_Block_Model.pdf

A comparison of the updated September 2015 resource estimate to the previous 
estimate, released January 2014, is shown in Table 1 below:

/T/


Table 1: Comparison of Estimated Mineral Resources 2015 vs. 2014

----------------------------------------------------------------------------
INDICATED                                      September 2015
Cut-Off
Oxide type                         g/t Au    ktonnes     Au g/t     koz Au
----------------------------------------------------------------------------
Oxide (OX)                              0.5     38,095       1.68      2,055
Upper Transitional (UT)                 0.5      7,649       1.65        406
Middle Transitional (MT)(i)             0.5      4,241       1.55        211
Lower Transitional                      1.0      2,294       1.94        143
Sulphide                                1.0        138       2.09          9
----------------------------------------------------------------------------
OX+UT+MT                                0.5     49,985       1.66      2,671
----------------------------------------------------------------------------
Total Indicated                                 52,417       1.68      2,824
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
INFERRED                                       September 2015
Cut-Off
Oxide type                         g/t Au    ktonnes     Au g/t     koz Au
----------------------------------------------------------------------------
Oxide                                   0.5     18,576       1.30        775
Upper Transitional                      0.5      8,244       1.42        378
Middle Transitional(i)                  0.5      6,030       1.69        328
Lower Transitional                      1.0      6,803       1.94        424
Sulphide                                1.0      3,030       1.87        182
----------------------------------------------------------------------------
OX+UT+MT                                0.5     32,850       1.40      1,481
----------------------------------------------------------------------------
Total Inferred                                  42,683       1.52      2,088
----------------------------------------------------------------------------


Table 1: Comparison of Estimated Mineral Resources 2015 vs. 2014

----------------------------------------------------------------------------
INDICATED                                       January 2014
Cut-Off
Oxide type                         g/t Au    ktonnes     Au g/t     koz Au
----------------------------------------------------------------------------
Oxide (OX)                              0.5      8,555       1.75        480
Upper Transitional (UT)                 0.5      3,619       1.32        153
Middle Transitional (MT)(i)               -          -          -          -
Lower Transitional                      0.5      2,141       1.21         83
Sulphide                                1.0         42       1.52          2
----------------------------------------------------------------------------
OX+UT+MT                                0.5     12,174       1.62        634
----------------------------------------------------------------------------
Total Indicated                                 14,357       1.56        719
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
INFERRED                                        January 2014
Cut-Off
Oxide type                         g/t Au    ktonnes     Au g/t     koz Au
----------------------------------------------------------------------------
Oxide                                   0.5     50,437       1.28      2,078
Upper Transitional                      0.5     15,967       1.39        714
Middle Transitional(i)                    -          -          -          -
Lower Transitional                      0.5      6,662       1.43        306
Sulphide                                1.0      5,525       1.89        336
----------------------------------------------------------------------------
OX+UT+MT                                0.5     66,404       1.31      2,792
----------------------------------------------------------------------------
Total Inferred                                  78,591       1.36      3,434
----------------------------------------------------------------------------
(i)Middle Transitional not estimated in Jan-2014 resource, previously
included within the 2014 Upper Transitional grouping.
Additional Notes: Definition of Upper Trans, Middle Trans & Lower Trans are
provided in the Mineral Resource Estimation Parameters section below. 2015
Base Case cut-off grade of 0.5g/t Au for Oxide, Upper and Middle Transition
mineral resources, and 1.0g/t Au for Lower Transition and Sulphide mineral
resources, are based on reasonable projections of technical and economic
parameters which demonstrate reasonable prospects of economic viability. All
figures are rounded to reflect the relative accuracy of the estimates. Some
categories may not balance due to rounding. Mineral resources are not
mineral reserves and do not have a demonstrated economic viability.

/T/

Revised and preliminary design parameters indicate that the resource cut-off 
grade limits will be reduced to 0.3 g/t Au for Oxide and Upper Transitional, 
0.4 g/t Au for Middle Transitional and 1.0 g/t Au for Lower Transitional and 
Sulphide resources. For comparative purposes, based on these lower cut-off 
grades, the 2015 Indicated resource totals 63.7 million tonnes averaging 1.45 
g/t Au for 2,968,000 ounces of contained gold, and the Inferred resource totals 
52.4 million tonnes at an average grade of 1.31 g/t Au for 2,212,000 ounces of 
contained gold (see Table 2 below).

/T/


Table 2: Coffee Indicated and Inferred Resources 2015 at Projected
Feasibility Study resource cut-off grades (0.3 g/t Au Oxide & Upper
Transition Zones; 0.4 g/t Au Middle Transition Zone, 1 g/t Au Lower
Transition and Sulphide)

----------------------------------------------------------------------------
Cut-Off
Oxide type            Au g/t        Indicated                Inferred

ktonnes  Au g/t  koz Au ktonnes  Au g/t  koz Au
----------------------------------------------------------------------------
Oxide                    0.3  47,127    1.43   2,170  25,020    1.07     857
Upper Transitional       0.3   9,461    1.41     429  10,646    1.19     408
Middle Transitional      0.4   4,647    1.45     217   6,855    1.54     340
Lower Transitional       1.0   2,294    1.94     143   6,803    1.94     424
Sulphide                 1.0     138    2.09       9   3,030    1.87     182
----------------------------------------------------------------------------
OX+UT                    0.3  56,587    1.43   2,598  35,665    1.10   1,265
OX+UT+MT             0.3-0.4  61,235    1.43   2,815  42,520    1.17   1,605
----------------------------------------------------------------------------
All                           63,666    1.45   2,968  52,354    1.31   2,212
----------------------------------------------------------------------------
Additional Notes: Definition of Upper Trans, Middle Trans & Lower Trans are
provided in the Mineral Resource Estimation Parameters section below. 2015
Base Case cut-off grade of 0.5g/t Au for Oxide, Upper and Middle Transition
mineral resources, and 1.0g/t Au for Lower Transition and Sulphide mineral
resources, are based on reasonable projections of technical and economic
parameters which demonstrate reasonable prospects of economic viability. All
figures are rounded to reflect the relative accuracy of the estimates. Some
categories may not balance due to rounding. Mineral resources are not
mineral reserves and do not have a demonstrated economic viability.

/T/

"Drilling in 2014-15 has successfully grown Coffee's gold inventory to an 
indicated resource of approx. 3 million ounces at a grade of 1.45g/t Au plus an 
Inferred resource of approx. 2.2 million ounces at a grade of 1.31g/t Au, using 
projected feasibility resource cut-off grades. The high conversion rate from 
Inferred to Indicated together with the increase in grade and global resources, 
further demonstrates the confidence in the modeling approach taken by SIM 
Geological Inc. and underpins our confidence in the quality and predictability 
of the Coffee resource as we head into the home stretch of the feasibility 
study, which is fully funded and on track for completion in early Q1, 2016" 
stated Eira Thomas, Kaminak President & CEO.

FEASIBILITY STUDY UPDATE

Kaminak initiated a Feasibility Study (FS) at Coffee in July of 2014 after 
receiving results from a preliminary economic assessment (PEA) confirming that 
Coffee represents a robust, high margin, 11-year, open pit, gold mining 
opportunity using a gold price of US$1250 and a Canadian/US exchange rate of 
$0.95, generating a pre-tax NPV of C$522 Million and an IRR of 33%.

The feasibility study contract as awarded to JDS Energy and Mining in March, 
2015, includes oversight from Fred Lightner, P.E., Kaminak's Director of Mining 
and contributions from SRK, The Mines Group, RRD International, TetraTech EBA, 
Lorax Environmental, and a multidisciplinary environmental baseline team of 
independent consultants, the majority of which are Yukon based.

As of September 18, 2015, all field-related FS programs, including infill 
drilling, were complete and engineering work is well underway. Interim results 
from FS work completed to date are summarized as follows:

/T/

--  FS tracking on schedule and budget, estimated completion date remains
Q1, 2016.
--  Capital costs, operating costs and production metrics are tracking in
line with estimates in the PEA and total in-pit ounces are not expected
to be materially impacted by the increase in ounces reported herein.
--  The heap leach facility has been re-designed and re-located as a free
draining ridge-top heap leach pad and is expected to result in cost
savings and reduce construction time from 22 to 18 months.
--  New access road route selected from the north (Dawson City) will
substantially reduce new road construction (see press release of
September 16, 2015).
--  Two stages of crushing to produce 2 inch sized heap leach feed for the
pad has been selected to optimize metallurgical recoveries. Recently
completed geotechnical studies determined that run of mine feed-size was
underestimated in the PEA.
--  Liquefied natural gas (LNG) incorporated as the primary fuel source 
foron-site power generation, which is expected to substantially reduce
overall energy costs estimated in the PEA.

/T/

Eira Thomas, CEO commented: "Resource and conversion drilling has gone very 
well and most of the assumptions used in the PEA remain relevant and 
defensible. Coffee remains a strong project and one of the few development 
track gold projects located in Canada that can deliver sizeable, high margin 
production in excess of 160,000 ounce per annum in the current gold price 
environment."

2014-15 DRILLING PROGRAM OBJECTIVES COMPLETED

The Company announced on August 13, 2015 the completion of 70,000m of infill 
drilling with the objective of upgrading 2014 PEA in-pit Inferred resources to 
the Indicated category. The location and spacing of infill drilling was 
determined in consultation with independent Qualified Person Robert Sim, P.Geo 
of SIM Geological Inc., who completed the 2012, 2014 and 2015 Coffee Gold 
Project mineral resource estimates.

All objectives were achieved with the successful conversion of Inferred to 
Indicated class resources within the 2014 PEA modelled open pit shells. 
Drilling also extended beyond the limits of the PEA pit shells in order to 
accommodate possible future depth expansion, resulting in the expansion of 
resources in some locations. A resource estimate has also been produced for the 
Kona North deposit (discovery announced September 2, 2014). Estimates of 
mineral resources by deposit area are shown in Table 3 below.

The additional drilling has provided much better control on the distribution of 
mineralization in the Coffee deposit and, in some instances, allows for 
increased confidence in the interpretation of narrower domains, thereby 
reducing internal dilution and increasing the overall grade of the resource. 
The closer-spaced drilling also allows for better continuity of grade from 
section to section, further reducing the amount of internal dilution in the 
block model.

/T/


Table 3: 2015 Resources by Deposit at Base Case Cut-Off(i)

----------------------------------------------------------------------------
Deposit                        Indicated                   Inferred

ktonnes   Au g/t   koz Au  ktonnes   Au g/t   koz Au
----------------------------------------------------------------------------
Supremo                  34,453     1.72    1,907   22,927     1.47    1,081
Latte                    14,499     1.46      681   14,408     1.48      686
Double Double             1,838     2.81      166    2,318     1.73      129
Kona                      1,628     1.35       71    1,600     1.58       81
Kona North                    0        0        0    1,430     2.40      110
----------------------------------------------------------------------------
Total All Zones          52,417     1.68    2,824   42,683     1.52    2,088
----------------------------------------------------------------------------
(i)2015 Base Case cut-off grade of 0.5g/t Au for Oxide, Upper and Middle
Transition mineral resources, and 1.0g/t Au for Lower Transition and
Sulphide mineral resources, are based on reasonable projections of technical
and economic parameters which demonstrate reasonable prospects of economic
viability. All figures are rounded to reflect the relative accuracy of the
estimates. Some categories may not balance due to rounding. Mineral
resources are not mineral reserves and do not have a demonstrated economic
viability.

/T/

COFFEE GOLD PROJECT MINERAL RESOURCE ESTIMATION PARAMETERS

The Coffee Gold Project September 2015 Indicated and Inferred Mineral Resource 
Estimate was completed by independent Qualified Person Robert Sim, P.Geo. of 
SIM Geological Inc. and is reported in accordance with the guidelines of the 
Canadian Securities Administrators National Instrument 43-101. The estimate is 
derived from 1478 diamond core and reverse circulation drill holes completed 
from 2010 to 2015 for a total of 261,426 metres. The majority of the resource 
comprises the Latte - Supremo - Double Double deposits, which occur within 
close proximity to one another over an area measuring approximately 2km x 2km. 
The Kona and Kona North deposits lie approximately 2.5 kilometres west of Latte.

Three-dimensional block models were created within mineralization domain 
wireframes based on geostatistical applications using commercial mine planning 
software MineSight(R) (v10.0-2). The block size across all deposit areas is 10 
x 2.5 x 5 metres. The long axis of the blocks is aligned with the strike of the 
mineralized domain, and the shorter dimension is aligned across the strike 
direction.

In contrast to the maiden 2012 Resource Estimate which utilized only 
qualitative visual logging to define the oxidation surfaces, and the 2014 
Resource Estimate which applied a combination of qualitative and quantitative 
data, the updated 2015 resource estimate uses a more refined interpolative 
modelling methodology to apply more rigorous quantifiable cyanide soluble gold 
(AuCN) data resulting in much more detailed resolution of the distribution of 
oxidation facies within the block model. Since 2013, Kaminak has undertaken 
cyanide leach assaying, in conjunction with the traditional fire assaying 
method, to measure the cyanide soluble characteristics of the gold in the 
Coffee Deposit. Samples selected for AuCN analysis were restricted to intervals 
where fire assay gold grades are greater than 0.3 g/t due to the detection 
limit of the cyanide assay analytical method This data is reasonably 
distributed but, because it excludes lower-grade sample intervals, is not 
sufficient to support direct estimation of AuCN estimates in model blocks. As 
an alternative, the ratio of AuCN/AuFireAssay is calculated in samples where 
AuCN data is present and these ratios are interpolated in the block model. 
These estimated ratios are used to define oxide types inside the mineralized 
domains. Oxidation is channeled along the structural corridors that host the 
gold deposits, and it is common to find intense oxidation at depths of over 
200m below surface. Strong oxidation is present over the majority of the 
Supremo and Double Double deposits. Oxidation is less pervasive at Latte, 
extending to about 125m below surface in some areas.

Five oxide types or domains have been interpreted for the Coffee deposit based 
on the AuCN/total Au ratios as described in Table 4 below.

/T/


Table 4: Oxidation Facies designation parameters

----------------------------------------------------------------------------
Cyanide leach ratio
Facies Type                   (cyanide assay/fire assay)
----------------------------------------------------------------------------
Oxide                               0.90-1.0
Upper Transition                          0.70-0.90
Middle Transition                         0.50-0.70
Lower Transition                          0.10-0.50
Sulphide                               0-0.10
----------------------------------------------------------------------------

/T/

The resources are classified according to their proximity to sample locations 
and are reported, as required by NI 43-101, according to the CIM Definition 
Standards for Mineral Resources and Mineral Reserves. The Coffee Mineral 
Resource Estimate comprises relatively continuous, sub-vertical zones of gold 
mineralization, the majority of which occurs at depths less than 150m below 
surface. The resource has been subjected to a series of floating cone shells 
based on reasonable projected technical and economic parameters for a deposit 
of this type, scale and location. The results indicate that the vast majority 
of the resource exhibits reasonable prospects for eventual economic extraction, 
and as a result the mineral resources presented in this release are not 
restricted within a pit shell. There are currently no mineral reserves at the 
Coffee project, however as detailed herein, the Coffee Feasibility Study is 
currently underway and remains on schedule for completion Q1 2016.

Full details of the resource modeling parameters and assumptions will be 
published in the NI 43-101 Coffee Feasibility Study.

On behalf of the Board of Directors of Kaminak

Eira Thomas, President and CEO

Kaminak Gold Corporation

For further information about Kaminak Gold Corporation or this news release, 
please visit our website at www.kaminak.com.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Robert Sim, P.Geo., Consultant to the Company and a Qualified Person as defined 
by National Instrument 43-101 ("NI 43-101") has reviewed and approved the 
contents of this news release related to the mineral resource estimate. All 
samples were collected in accordance with industry standards. Splits from the 
drill core and RC percussion samples were submitted to the ALS sample 
preparation laboratory in Whitehorse, Yukon Territory, Canada, and then 
transferred to ALS' laboratory in Vancouver, British Columbia, Canada for fire 
assay and ICP analysis. Accuracy of results is tested through the systematic 
inclusion of standards, blanks and check assays. The mineral resource estimate 
referenced in this press release was prepared in September 2015 by Robert Sim, 
P.Geo. an independent Qualified Person as defined by NI 43-101. Kaminak's 
additional disclosure of a technical or scientific nature in this press release 
has been reviewed and approved by Mr Tim Smith, MSc, P.Geo., Kaminak's Vice 
President of Exploration, who serves as a Qualified Person under the definition 
of National Instrument 43-101.

Cautionary Note concerning estimates of Inferred and Indicated Resources:

This news release uses the terms "Inferred Resources" and "Indicated 
Resources", which have a great amount of uncertainty as to their existence, and 
great uncertainty as to their economic and legal feasibility. It cannot be 
assumed that all or any part of an Inferred and/or Indicated Mineral Resource 
will ever be upgraded to a higher category. Under Canadian rules, estimates of 
Inferred Resources may not form the basis of feasibility or other economic 
studies. Kaminak advises U.S. investors that while this term is recognized and 
required by Canadian regulations, the U.S. Securities and Exchange Commission 
does not recognize it. U.S. investors are cautioned not to assume that part or 
all of an Inferred and Indicated resource exists, or is economically or legally 
minable.

Caution Concerning Forward-Looking Statements

Certain disclosures in this release, including management's assessment of 
plans, projects and intentions with respect to the further development of the 
Coffee Project and future exploration programs, constitute forward-looking 
statements that are subject to numerous risks, uncertainties and other factors 
relating to Kaminak's operations as a mineral exploration company that may 
cause future results to differ materially from those expressed or implied in 
such forward-looking statements, including risks as to the completion of the 
plans and projects. Readers are cautioned not to place undue reliance on 
forward-looking statements. Except as required by law, Kaminak expressly 
disclaims any intention or obligation to update or revise any forward-looking 
statements, whether as a result of new information, future events, or otherwise.

The mineral resource figures referred to in this press release are estimates 
and therefore insufficient to allow meaningful application of the technical and 
economic parameters to enable an evaluation of technical or economic viability 
and no assurances can be given that mining of the Coffee Project is 
commercially viable or that the indicated levels of gold will be produced. Such 
estimates are expressions of judgment based on knowledge, mining experience, 
analysis of drilling results and industry practices. Valid estimates made at a 
given time may significantly change when new information becomes available. 
While the Company believes that the resource estimates included in this press 
release are well established, by their nature, resource estimates are imprecise 
and depend, to a certain extent, upon statistical inferences which may 
ultimately prove unreliable. If such estimates are inaccurate or are reduced in 
the future, this could have a material adverse impact on the Company.

- 30 -

CONTACT INFO:

Kaminak Gold Corporation
Tony Reda
Vice-President of Corporate Development
604.646.4534 or Toll Free: 1.888.331.2269
info@kaminak.com
www.kaminak.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=543160050