Source	MARKET NEWS
Date	09/25/2015
Time	05:26:37 AM

Company	 Sama Resources Inc./Ressources Sama Inc.
Title	Yacouba 
Layered Complex Almost Triples In Size A





    CDNX Symbol: SME











Press Release	





SAMA RESOURCES INC ("SME-V")
- Yacouba Layered Complex Almost Triples In Size And Withdraws
- Preliminary Short Form Prospectus

Sama Resources Inc./Ressources Sama Inc. ("Sama" or the "Company")
announced that recent exploration results confirm the sub-horizontal
nature of the Yacouba Layered Complex intrusion packages in the Yepleu
sector over a much larger area then initially interpreted, increasing
the size from 25 km2 to more than 70 km2. Sama's single shallow
borehole (YE16- 390480) drilled one kilometer north of the Yepleu area
intercepted a diorite unit of interpreted magmatic origin carrying
finely disseminated sulphide mineralization including pyrrhotite and
chalcopyrite, thereby confirming the presence of the Yacouba Layered
Complex at the location. Sampling for mineralogical and petrological
studies is ongoing.

Drilling at Samapleu

Seven drill holes were drilled as part of an infill-drilling
program aimed at reducing drill spacing and increasing the strike
length of the already known mineralization at the Samapleu Main and
Extension 1 deposits. Results received to date are detailed in Table 1
below. Several assays remain pending.

The massive and semi-massive sulphide mineralization of boreholes
SM44-428267 and SM25-133537 (See press release dated April 20, 2015) is
characterised by large granular aggregates of nickel, copper and iron
sulphides, named pentlandite, chalcopyrite and pyrrhotite,
respectively. Pentlandite occurs together with pyrrhotite, while the
chalcopyrite, being the third mineral of global abundance appears
either mixed with the pentlandite or as late sulfide centimetric veins
crosscutting the pentlandite-pyrrhotite material.

Contacts between the massive sulphide lenses and the mineralized
pyroxenite host are irregular, but sharp with brecciated textures,
indicating that the massive sulphide material has intruded the
pyroxenite host originating from a source that is yet to be discovered.


Table 1: 2015 Drill Results - Mineralized Intercepts(Intercepts
were defined using 0.1% nickel cut-off grades).

//st
HOLE-ID          From     To LENGTH      Ni      Cu   Co   Pt    Pd
m      m       m       %    %    %  gr/t gr/t
SM25-133537     30.00  63.00  33.00    0.38    0.31 0.02 0.12  0.63
including  32.45  36.65    4.20    1.13 1.03 0.05  0.43 1.73
including  44.85   45.7    0.85    1.22 0.35 0.05  0.16 1.80

SM25-133538     44.45  84.80  40.35 Results awaited
84.80 126.25   41.45    0.61 0.47 0.03  0.17 1.06
including  87.95  88.65    0.70    0.85 1.71 0.04  0.45 1.31
including   93.3   97.2    3.90    1.40 1.01 0.08  0.27 2.47
including    107  108.2    1.20    1.76 0.50 0.09  0.18 2.83
including  115.7    116    0.30    2.07 0.68 0.09  0.04 2.59
including  120.6  124.5    3.90    1.37 0.77 0.06  0.29 2.03

SM44-428267     15.00  68.95  53.95    0.96    0.76 0.04 0.09  0.74
including   27.5   28.5    1.00    0.89 0.98 0.04  0.05 0.75
including  57.65  60.55    2.90    4.45 2.20 0.16  0.01 3.08
including   62.9     68    5.10    3.87 2.56 0.14  0.03 2.83
72.85 106.95   34.10     Results
awaited

SM44-473240     22.10 100.00  77.90    0.28    0.29 0.01 0.18  0.28
including   25.1   27.8    2.70    1.34 0.62 0.05  0.10 1.08
including     98   98.6    0.60    0.90 1.46 0.04 11.60 0.89

SM25-111555     36.50  86.00  49.50    0.31    0.28 0.02 0.15  0.59
including  59.75   60.3    0.55    1.88 1.49 0.08  0.03 2.20
including   78.8  79.15    0.35    1.97 0.49 0.10  0.03 3.03

SM44-459220     18.10  90.90  72.80    0.33    0.24 0.02 0.09  0.34
including   20.7   21.6    0.90    1.26 1.21 0.06  0.51 2.11
including   45.2   46.4    1.20    1.03 0.60 0.04  0.06 1.44
including   85.4   89.5    4.10    1.33 0.83 0.05  0.07 0.83

SM44-429266     15.50  78.00  62.50    0.23    0.33 0.01 0.12  0.23
//et

Readers are invited to view an updated geological map showing the
interpreted surface extent of the Yacouba Layered Complex via the
following link.


http://www.samaresources.com/i/projects/samapleu/YacoubaComplex.png

Core logging and sampling was performed at Sama's facility in
Yorodougou village. Sample preparation was conducted at the Bureau
Veritas Mineral Laboratory's facility in Abidjan. Sample pulps were
delivered to Activation Laboratories Ltd., Ancaster, Thunder Bay,
Canada, for assaying. All samples were assayed for Ni, Cu, Co, Pt, Pd,
Au, Fe and S.

Withdrawal of Short Form Prospectus

The Company is withdrawing its preliminary short form prospectus
dated June 8, 2015 and will not be proceeding with the offering
described in its press release of June 9, 2015. This decision was due
to market conditions and the costs involved in addressing comments of
the securities regulators regarding the Company's technical report with
respect to its Samapleu property. The Company intends to file an
updated technical report when its exploration work on the Samapleu
property is sufficiently advanced so as to warrant such an update.

The technical information in this release has been reviewed and
approved by Dr. Marc-Antoine Audet, P.Geo and President and Chief
Executive Officer, Sama Resources Inc., and Qualified Person as defined
by National Instrument 43-101, Standards of Disclosure for Mineral
Projects.

For more information, please visit the Company's website at
www.samaresources.com or click on the following link to access Sama's
most recent corporate presentation.


http://www.samaresources.com/i/pdf/Sama_Corporate_Presentation.pdf

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Forward-Looking Statements

Certain of the statements made and information contained herein
are "forward-looking statements" within the meaning of Canadian
securities legislation or "forward-looking information" within the
meaning of the Ontario Securities Act and the Securities Act (British
Columbia). This includes statements concerning, among other things, the
Company's plans to file an updated technical report and the Company's
plans at its mineral properties, which involve known and unknown risks,
uncertainties and other factors which may cause the actual results,
performance or achievements of the Company, or industry results, to
vary or be materially different from any future results, performance or
achievements expressed or implied by such forward-looking statements or
forward-looking information. Information regarding drilling results may
also be deemed to be forward-looking statements or forward-looking
information in that they reflect a prediction of what may be found to
be present when and if a project is actually developed.

Forward-looking statements and forward-looking information are
subject to a variety of risks and uncertainties which could cause
actual events or results to differ from those reflected in the
forward-looking statements or forward-looking information, including,
without limitation, the availability of financing for activities, risks
and uncertainties relating to the interpretation of drill results and
the estimation of mineral resources and reserves, the geology, grade
and continuity of mineral deposits, the possibility that future
exploration, development or mining results will not be consistent with
the Company's expectations, metal price fluctuations, environmental and
regulatory requirements, availability of permits, escalating costs of
remediation and mitigation, risk of title loss, the effects of
accidents, equipment breakdowns, labour disputes or other unanticipated
difficulties with or interruptions in exploration or development, the
potential for delays in exploration or development activities, the
inherent uncertainty of cost estimates and the potential for unexpected
costs and expenses, commodity price fluctuations, currency
fluctuations, expectations and beliefs of management and other risks
and uncertainties.

In addition, forward-looking statements and forward-looking
information are based on various assumptions. Should one or more of
these risks and uncertainties materialize, or should underlying
assumptions prove incorrect, actual results may vary materially from
those described in forward-looking information or forward-looking
statements. Accordingly, readers are advised not to place undue
reliance on forward-looking statements or forward-looking information.
Except as required under applicable securities legislation, the Company
undertakes no obligation to publicly update or revise forward-looking
statements or forward-looking information, whether as a result of new
information, future events or otherwise.

TSX Venture closing price for SME-V
Date: 2015/09/23
Closing Price: 0.13

TEL:  (514) 726-4158  Dr. Marc-Antoine Audet, President and CEO
SAMA RESOURCES INC./RESSOURCES SAMA INC.
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1526700004TS11526700334-05245020150925