Source	Marketwire
Date	09/28/2015
Time	05:01:13 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Results from 2015 Exploration Drilling at the Wedge, 
Physik and Reed Dolomite Target Areas, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

September 28, 2015

Scorpio Gold Reports Results from 2015 Exploration Drilling at the Wedge, 
Physik and Reed Dolomite Target Areas, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 28, 2015) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports results 
from the 2015 exploration drilling at the Wedge, Physik and Reed Dolomite 
target areas at its 70% owned Mineral Ridge project, located in Nevada.

Exploration drilling in 2015 tested two previously undrilled areas located 
100-200 meters east of the Wedge deposit and 200-600 meters southeast of Wedge 
within the Reed Dolomite target area. Although drilling returned a number of 
significant intersections (Tables 1 and 2), exploration drilling is now focused 
on other target areas that are deemed more prospective and no further drilling 
is currently planned in these areas. Further to the southeast, which parallels 
the common structural trend of mineralization at Mineral Ridge, follow-up 
drilling was undertaken on the Physik target, where drilling in 2014 
intersected 31.79 g/t gold over 4.57 meters in drill hole MR141107 (see 
November 3, 2014 news release). Drilling in 2015 tested within the vicinity of 
MR141107 but did intersect similar high-grade mineralization. As such, no 
further drilling is currently planned in the Physik target area.

Open pit mining at the Wedge deposit occurred during the first half of 2015 and 
ore production totaled 70,681 tonnes grading 1.57 grams per tonne.

Map Links:

Wedge & Reed Dolomite: DH Plan

Physik Target: DH Plan

Table 1. Wedge Deposit Target Area - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole             Azm   Dip From   To Width   From     To  Width   Gold  Gold
No.            (deg) (deg) (ft) (ft)  (ft)    (m)    (m)    (m)  (OPT) (g/t)
----------------------------------------------------------------------------
MR151386           0   -90                            No Significant Results
----------------------------------------------------------------------------
MR151388           0   -90   90   95     5  27.43  28.96   1.52  0.011  0.38
----------------------------------------------------------------------------
MR151598-600       0   -90                            No Significant Results
----------------------------------------------------------------------------
MR151626           0   -90   25   30     5   7.62   9.14   1.52  0.020  0.69
----------------------------------------------------------------------------
MR151638           0   -90                            No Significant Results
----------------------------------------------------------------------------
MR151646-649       0   -90                            No Significant Results
----------------------------------------------------------------------------
MR151650           0   -90   75   85    10  22.86  25.91   3.05  0.104  3.57
----------------------------------------------------------------------------
135  140     5  41.15  42.67   1.52  0.017  0.58
----------------------------------------------------------------------------
150  155     5  45.72  47.24   1.52  0.059  2.02
----------------------------------------------------------------------------
MR151652           0   -90                            No Significant Results
----------------------------------------------------------------------------
MR151653           0   -90   40   45     5  12.19  13.72   1.52  0.011  0.38
----------------------------------------------------------------------------

/T/

Table 2. Reed Dolomite Target - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole             Azm   Dip  From   To Width   From     To Width   Gold  Gold
No.            (deg) (deg)  (ft) (ft)  (ft)    (m)    (m)   (m)  (OPT) (g/t)
----------------------------------------------------------------------------
MR151666           0   -90   135  145    10  41.15  44.20  3.05  0.016  0.55
----------------------------------------------------------------------------
MR151681           0   -90                            No Significant Results
----------------------------------------------------------------------------
MR151682           0   -90   150  155     5  45.72  47.24  1.52  0.019  0.65
----------------------------------------------------------------------------
MR151683           0   -90    65   70     5  19.81  21.34  1.52  0.048  1.65
----------------------------------------------------------------------------
MR151684           0   -90   235  240     5  71.63  73.15  1.52  0.014  0.48
----------------------------------------------------------------------------
MR151685           0   -90                            No Significant Results
----------------------------------------------------------------------------
MR151687-690       0   -90                            No Significant Results
----------------------------------------------------------------------------

/T/

Table 3. Physik Target - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole              Azm   Dip From   To  Width From    To  Width   Gold   Gold
No.             (deg) (deg) (ft) (ft)   (ft)  (m)   (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR151465            0   -90                           No Significant Results
----------------------------------------------------------------------------
MR151481-482      145   -45                           No Significant Results
----------------------------------------------------------------------------
MR151483          250   -60   25   35     10 7.62 10.67   3.05  0.044   1.51
----------------------------------------------------------------------------
MR151697          300   -50                           No Significant Results
----------------------------------------------------------------------------
MR151698          250   -50    0    5      5 0.00  1.52   1.52  0.015   0.51
----------------------------------------------------------------------------

/T/

All holes presented in Tables 1-3 were completed by reverse circulation (RC) 
drilling. True width is estimated at 80-100% of downhole width. Analytical 
results were performed by American Assay Laboratory Inc. in Sparks, Nevada, an 
ISO/IEC 17025:2005 accredited facility. External check assays to verify lab 
accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 certified and 
ISO/IEC 17025:2005 accredited facility. Further details are presented in the 
Company's quality assurance and quality control program for the Mineral Ridge 
project at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Elevon, LLC (30%). Mineral Ridge is a conventional open pit mining and heap 
leach operation. The Mineral Ridge property is host to multiple gold-bearing 
structures, veins and lenses at exploration, development and production stages. 
Scorpio Gold also holds a 100% interest in the advanced exploration-stage 
Goldwedge property in Manhattan, Nevada, with a fully permitted underground 
mine and 400 ton per day mill facility. The Goldwedge mill facility has been 
placed on a care and maintenance basis for the near-term and can be restarted 
immediately when needed.

Scorpio Gold's President & CEO, Peter J. Hawley, PGeo, is a Qualified Person as 
defined by National Instrument 43-101 and has reviewed and approved the content 
of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Peter J. Hawley
President & CEO
(819) 825-7618
phawley@scorpiogold.com
www.scorpiogold.com

or

Investor Relations:
Jim Macdonald
Torrey Hills Capital
(858) 456-7300
jm@sdthc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=543602107