Source	MARKET NEWS
Date	09/30/2015
Time	06:02:57 AM

Company	 Para Resources Inc.
Title	Reports on 
Filing National Instrument 43 101 Tec





    CDNX Symbol: PBR











Press Release	





PARA RESOURCES INC ("PBR-V")
- Reports on Filing National Instrument 43-101 Technical Report
- On El Limon Gold Project

Para Resources Inc. (the "Company" or "Para") is pleased to advise
that it has filed a technical report dated September 15, 2015 authored
by David Bikerman, EM,MS, MAIG of Bikerman Engineering & Technology
Associates, Inc. (or "BETA") (the "El Limon Report") on the El Limon
project, prepared in accordance with National Instrument 43-101 of the
Canadian Securities Administrators. The El Limon Report is available
for review on SEDAR under Para's profile and also has been posted on
our website: www.pararesources.com
Geoff Hampson, CEO of Para, commented:
"Para is pleased that the El Limon Report has been completed as it
provides far more detail about the El Limon project from both a
historical perspective on past mining operations, as well as our go
forward plan on refurbishing the mine works and increasing production
capabilities. As detailed in our news release of September 11, 2015, we
are excited about the improvements being undertaken at El Limon, and we
look forward to the completion of upgrades. Our representatives have
been negotiating contracts among approximately 60 independent mining
operations in the vicinity of the El Limon mine and the upgraded
capacity will give us tremendous toll-milling opportunities. All in
all, we are extremely pleased with progress as we continue to execute
our plan of acquiring and developing advanced assets with strong
development potential."
El Limon Overview
The El Limon Project is a property of merit with a rich history of
mining. The first mill was built on site in 1938. Gold production from
the El Limon mine has progressed with remarkable continuity over the 75
years since. The grade of the gold-bearing vein mined over the years
was quite high, at over 20 grams per tonne. Recent bulk-tonnage grades
of mineralized material mined average between 5-10 grams of gold per
tonne, while recuperation of pillars has yielded mineralized vein
grading greater than 80 grams of gold per tonne. Additional exploration
will be required to delineate future mine resources and reserves.
The crushing plant and mill are currently being upgraded as part
of a $1.75 million mine reconstruction plan of which approximately
$750,000 has been invested to date. BETA reports that the proposed
upgrades are substantial in scope and when completed should bring the
mill to its fullest potential for gold recovery of +90%. Use of
amalgamation is to be terminated.
The El Limon project is located in the north-central part of
Colombia in Zaragoza, Antioquia, Colombia. The mine site is accessible
via both paved highways and local scheduled flights from Medellin to
nearby cities. The local infrastructure is excellent, with power,
water, fuel and manpower readily available.
BETA states that the Colombian National Mining Agency currently
shows a total project area of 277.5 hectares comprised of 86.4 hectares
in Exploitation Concession RPP #12011 and 191.1 hectares in Exploration
Concession #620. Both titles are located in the Municipality of
Zaragoza, in the northern part of the Department of Antioquia.
Mining of gold veins at the El Limon mine is subject to mining and
environmental standards set by the national government through its
laws, decrees, resolutions etc. BETA reports that an Environmental
Management Plan (Plan de Manejo Ambiental) has been approved for the
concession contract, and the mine is in compliance with the water
management and reforestation requirements of the government. The El
Limon mine operates under Environmental License per Resolution
#130PZ-1402-2703 dated February 27, 2014. The mine is operating in
compliance with the requirements of the Environmental License, the most
recent compliance inspection by Mining Agency officials being August
12, 2015.
The El Limon project is situated in the Zaragoza Gold District
along the Zaragoza-Segovia trend which extends from El Bagre in the
north to Remedios in the south. The main structure present is the Otu
Fault that crosses the area from North to South. Principal towns in the
region include El Bagre, Zaragoza, Segovia, Remedios and Santa Isabel;
all of which are aligned with the north/south Otu fault. Mining
activities are present in all areas, with the principal operations
defined below:
Zaragoza: La Ye and El Limon mines
Segovia: Frontino Gold Mines and Marmajito mine
Remedios: San Pablo mine
Santa Isabel: Quintana mine
The known vein systems of the region extend up to 2-3 km in length
with plunging high-grade ore shoots central to the vein and surrounded
by a lower grade halo. Vein dips are typically around 30-40, and
occasionally sub-vertical. The mineralization of El Limon mine is
embedded in quartz-feldespathic gneisses. The gold occurs in a milky
quartz vein, to the west of Otu Fault; its approximate course is
N10E/40W, with average thickness of 0.40 meters. These features are
very consistent in an extension of almost 400m on strike and 350m along
dip.
Typical production grades of the region range 8-12 g/t Au diluted.
Higher-grade mines also exist, exhibiting grades of 15-20 g/t Au
diluted. Vein widths are typically less than 1 meter, although both the
hanging wall and footwall zones can contain appreciable economic
mineralization within the high-grade cores. Structure is continuous,
except for a series of reverse faults, with displacements ranging from
0.2 up to 40 and 60 meters. The main faults are called El Limon and
Leonel. Gold mineralization is related to sulphide contents, mainly
pyrite, with smaller amounts of galena, sphalerite and tetrahedrite.
The El Limon vein has been developed on 8 levels; production over
the past 15 years has been from levels 5, 6, 7 and 8. The mine has been
developed by room and pillar method on the upper levels; the vein dip
has increased with depth, allowing the mining method of stoping to be
employed. Underground workings are accessed via the mine portal (at
level 0). Track extends from the mine mouth to an incline drift
(shaft), located 150 meters south of the portal. The primary incline
drift is 325 meters long measuring 3m x 3m, and extends down at 50 dip
from level 0 to level 6. A second incline shaft, located on level 6
about 300 meters north of the base of the primary incline, is utilized
to access levels 7 and 8.
Three stopes are currently under development for selective mining
utilizing the method of resuing to minimize dilution. A ventilation
raise is being renovated to allow for better air flow at the mining
faces.
The existing mineral process at El Limon consists of two-stage
crushing, milling, gravity separation, flotation, cyanidation,
Merrill-Crowe precipitation and smelting. The final product sold is
gold/silver dor.
The Company has recently initiated an upgrade and renovation of
the crushing plant and mill circuit at El Limon. Para has operation
control over the upgrades and renovation of the mineral processing
facilities. The planned upgrades include installation of equipment
required to increase mill throughput to 200 tpd. The proposed mineral
process has not changed. The mineral processing plant historically
recovered less than 80% of the gold contained. The renovated plant is
expected to allow recoveries greater than 90%.
BETA has assisted in preparation of a 6-month mine development
plan for the mine. Total cost is estimated at approximately $954,000
(of which approximately $300,000 has been expended to date). Some 2,870
tonnes of ore are expected to be extracted in the process of
implementation; as such gold production is expected to pay for all of
the proposed development activities. Three major goals of this plan
are:1. Repair an existing ventilation shaft to provide adequate
ventilation to working areas. 2. Provide secondary egress from working
areas and to replace the winch to increase worker safety. 3. Develop
stopes and haulage levels to prepare for future production needs.
BETA recommends that Company geologists create a 24-month mining
plan in order to assure that exploration and development proceed well
in advance of mining. Mining engineers should update the calculations
of volume and gold grade of the potential resource.
Para has entered into a shareholders agreement dated May 15, 2015
(the "CML Agreement") with Randall Martin and Saef Exploration Inc.
both of of Miami, Florida and Colombia Milling Limited, a Belize
incorporated company ("Colombia Milling"), whereby it has agreed to
subscribe for one third of the common voting shares of Colombia Milling
for an aggregate total sum of US$1.0 million. Mr. Martin built the El
Limon mine and has a very successful history of building and operating
gold mines in South and Central America. Mr. Martin is the managing
partner of Colombia Milling.
Pursuant to an agreement dated April 13, 2015 (the "El Limon
Agreement"), Colombia Milling will acquire from Red Rock Resources plc
(AIM; RRR)(the "Vendor") of all of the shares (the "Acquired Shares")
of American Gold Mines Limited ("AGM"), a Cayman Islands wholly-owned
subsidiary of the Vendor and owner of 50.002% of the outstanding shares
of Four Points Mining SAS ("Four Points"), a Colombian company and the
owner of certain mineral licenses in northern Colombia, which contain
the El Limon project (the "Property"), and all shareholder loans of
$2,588,700 made by the Vendor to Four Points as well as any and all
other loans made by the Vendor to AGM. Further details regarding the
CML Agreement and EL Limon Agreement are contained in our news release
of July 20, 2015. In addition, Colombia Milling has entered into an
agreement dated April 16, 2015 to acquire 100% of GD Resources S.A.
("GDR") from Surgir Holdings S.A., a company wholly owned and
controlled by Sr. Juan Pablo Duque Arbelaez, in consideration of
U.S.$320,000, U.S.$136,000 of which has been paid as of the date
hereof. GDR is a Panamanian company which owns 11.2% of Four Points,
bringing Colombia Milling's aggregate indirect interest in the Property
to 61.202%. Accordingly, Para will acquire an indirect 20.401% interest
in and to the Property pursuant to the CML Agreement upon receipt of
final TSX Venture Exchange ("Exchange") acceptance and closing. Para
has received conditional acceptance to the acquisition from the
Exchange, and expects final acceptance on delivery of a title report on
the Property.
Mr. David Bikerman, a Member of the Australian Institute of
Geoscientists (MAIG #3558), Mining Engineer, a CP/QP under NI-43-101,
has reviewed and approved the scientific and technical information in
this press release.
ABOUT PARA RESOURCES:
Para Resources is an exploration-stage gold mining and toll
milling company. In addition to its existing properties, Para will
continue to take advantage of current market conditions to acquire and
develop additional assets that have strong exploration and development.


ON BEHALF OF THE BOARD OF DIRECTORS

"C. Geoffrey Hampson"

C. Geoffrey Hampson, Chief Executive Officer and Director




Neither TSX Venture Exchange nor its regulation service provider (as that
term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.

All statements, analysis and other information contained in this press
release about anticipated future events or results constitute
forward-looking statements. Forward-looking statements are often, but not
always, identified by the use of words such as "seek," "anticipate,"
"believe," "plan," "estimate," "expect" and "intend" and statements that an
event or result "may," "will," "should," "could" or "might" occur or be
achieved and other similar expressions. Forward-looking statements are
subject to business and economic risks and uncertainties and other factors
that could cause actual results of operations to differ materially from
those contained in the forward-looking statements. Forward-looking
statements are based on estimates and opinions of management at the date
the statements are made. The company does not undertake any obligation to
update forward-looking statements even if circumstances or management?s
estimates or opinions should change except as required by applicable laws.









































































TSX Venture closing price for PBR-V
Date: 2015/09/29
Closing Price: 0.15

TEL:  (604) 398-3227  Andrea Laird
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1527200017TS11527200818-06001520150930