Source	MARKET NEWS
Date	09/21/2016
Time	05:11:53 AM

Company	 Rosita Mining Corporation
Title	Santa Rita 
Project Returns Positive Metallurgica





    CDNX Symbol: RST











Press Release





ROSITA MINING CORP ("RST-V;MDLXF-0")
- Santa Rita Project Returns Positive Metallurgical Results

Rosita Mining Corporation ("Rosita" or the "Company") is
pleased to announce further positive metallurgical tests for the
Company's Santa Rita Project presently underway at SGS Lakefield in
collaboration with D.E.N.M. Engineering Ltd. Conventional cyanidation
testing resulted in a 91% gold recovery from the surface stockpile ore
and a 80% gold recovery from the tailings.

Test Results

The metallurgical tests were conducted on mineralized material
composited from the Company's previous surface sampling at Santa Rita
for the stockpile and tailings material. The as-tested head grade of
the composited stockpile sample was 0.48 g/t Au and 1.01% Cu.

The tailings sample that was tested assayed 0.79 g/t Au and 0.28 %
Cu.

Metallurgical testing was conducted on minus 1/4 inch material
ground to 80% passing 73-78 microns, typical for modern grinding and
leaching facilities, for a leaching period of 48 hours.

In both cases (stockpile and tailings), the high cyanide
consumption of 8.82 kg/t and 4.46 kg/t respectively is due to the
requirement to maximize the dissolution of soluble copper and improve
the kinetics of the resultant gold leaching. In both cases 69 % of the
cyanide consumption was due to copper complexing with the cyanide; it
is expected that the both the cyanide and copper can be recovered using
SART technology developed by SGS, as outlined below. Also, in both
cases, the gold residual values averaged in the 0.1 g/t range.

A single leach test was also carried out on plus 1/4 inch material
to test heap leach amenability. A similar residual value was obtained
with a 75% recovery. Further heap leach simulation tests will be
carried out to confirm this.

John Cook, President and CEO, stated that "It is good to see an
improvement in the earlier gold recovery results thus reinforcing the
preliminary flow sheet that was reported in the May 31st 2016 press
release".

Next Phase Test Work

The results of this continuing metallurgical test work following
earlier results from Rosita and Alder Resources are very positive, and
indicate that the stockpile and tailings mineralization responds well
to conventional cyanidation at readily achievable grind sizes.

The resultant solutions from these tests will be used for further
SART (Sulphidization, Acidification, Recycling, and Thickening) testing
with a goal to recover cyanide that has been complexed with copper, to
recover the copper as a separate product and to recycle the resultant
cyanide solution into ongoing cyanidation leach testing. This work will
be carried out at SGS Lakefield as per the previous positive SART work,
as reported in the March 21st press release. The results from this
phase of the program will be reported as once additional metallurgical
testing results are finalized.

Once this test campaign is complete, the resultant data will be
used as the base for a 43-101 Preliminary Economic Assessment report to
be completed later this year.

About Rosita Mining Corporation

Rosita is a junior mining and exploration resource company focused
on growing shareholder value through the development of near-term
mining projects and advancing accretive exploration opportunities.

Rosita and Calibre hold a 65% and 35% interest respectively in the
Rosita copper-gold-silver supergene/skarn/porphyry project in Nicaragua
located 275 kilometres northeast of Managua.

Qualified Persons

David Salari, P. Eng., and John Cook, MIMMM, Qualified Persons, as
defined by NI 43-101, have read and approved the contents of this press
release.

For additional information, please visit our website at
www.rositaminingcorp.com.

For further information, contact:

John Cook, President and CEO
Telephone: +1 416 200 8073
Email: johncook@kos.net
Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.
About Rosita Mining Corporation

Rosita is a junior mining and exploration resource company focused
on growing shareholder value through the development of near-term
mining projects and advancing accretive exploration opportunities.



__________________________________________________
_______________________________________________
TSX Venture closing price for RST-V
Date: 2016/09/20
Closing Price: 0.09
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1626400002TS11626400562-05103920160921