Source	MARKET NEWS
Date	09/26/2017
Time	05:04:56 AM

Company	 Red Eagle Exploration Limited
Title	New 
High Grade Discoveries at the California Gol





    CDNX Symbol: XR











Press Release





RED EAGLE EXPLORATION LTD ("XR-V;XRELF-0")
- New High-Grade Discoveries at the California Gold Project

Red Eagle Exploration Limited ("XR") is pleased to announce new
high-grade gold and silver discoveries at the Los Andes Zone of the
California Gold Project in Santander, Colombia.

*  Prospecting and sampling has identified three new exploration
targets;
*  Vein samples averaged 25.32 g/t Aueq over 0.39 meters at Mina
Los Andes and 8.37 g/t Au, 1,081 g/t Ag (22.38 g/t Aueq) and 0.88% Cu
over 0.85 meters at the Jesus Garcia tunnel;
*  Mineralization continues into the wallrock;
*  Only tested with a single drill hole historically; and
*  Located 450 metres southeast of Mubadala's Soto Norte Project's
Pie De Gallo Zone and 700 metres southwest of their La Mascota Zone.

//st

Table 1 - Results by Mineralization Style

Area           Style    Samples  Horizontal  Au     Ag    Aueq*   Cu     Zn
Width (m)   (g/t)  (g/t)         (%)    (%)

Mina Los Andes All      33       Unknown     3.30   149   5.24    NSR   0.23

Vein     7        0.39        15.07  791   25.32   NSR   0.82

Wallrock 26       Unknown     1.15   31    1.56    NSR   0.12

Los Andes Sur  All      11       Unknown     6.80   226   9.75    NSR   0.58

Vein     2        0.85        8.37   1,081 22.38   0.88  1.11

Santa          All      3        Unknown     4.41   61    5.21    NSR   NSR
Catalina Sur

*Aueq calculated assuming $17.50 per ounce Ag and $1,300 per ounce Au

//et

At La Mina de Los Andes all underground channel sampling returned
a length-weighted average grade of 5.24 g/t Aueq.  Seven samples from
zones of quartz veining returned an average grade of 25.32 g/t Aueq
over 0.39 meters with the wallrock returning an average grade of 1.56
g/t Aueq.  See Figure 1 for sample locations.  A previous operator,
Galway Resources, may have intercepted the continuation of this zone
along strike in drill hole GWY234 which returned 8.33 g/t Aueq over 5
metres at a depth of 224.5 metres.  The true width of this reported
intercept is unknown.

At Los Andes Sur sample results averaged 9.75 g/t Aueq.  A
composite of two channel samples across a sulphide bearing vuggy
quartz-alunite vein returned average grades of 8.37 g/t Au, 1,081 g/t
Ag (22.38 g/t Aueq) and 0.88% Cu over 0.85 meters.  In addition, a
surface chip sample returned 32.7 g/t Aueq. The gold mineralization is
hosted in typical high-sulphidation epithermal veins.

Santa Catalina Sur was located by prospecting an area with known
artisanal mine workings. Three chip samples averaged 5.21 g/t Aueq.

All three exploration targets are open along strike and at depth.
XR is carrying out trenching and soil sampling to better define the
mineralized zones, prioritizing targets for underground diamond
drilling as soon as possible.  The true thicknesses of the mineralized
zones are unknown as insufficient work has been completed to interpret
their geometry.

Underground and surface rock chip samples were collected in panels
15-20 centimetres wide and of variable vertical extent over areas
determined by styles of mineralization (vein or silicified wall-rock
breccia).  Underground samples were collected from the vein material in
the back of the underground drift with footwall and hangingwall samples
collected on either side of the vein wherever possible.
Sample preparation was performed at the Asomineros sample
preparation laboratory in Vetas, Colomiba. The sample preparation
laboratory has been audited by Actlabs and XR. Analytical work was
performed by ActLabs of Medellin, Colombia a certified commercial
laboratory. During sampling, quality control standards, field
duplicates and blanks were inserted in to the sample batches to monitor
analytical and sample preparation laboratory performance; all
consistent with industry best practice.  Rock chip samples have
undergone sample preparation consisting of crushing to 80% passing 10
mesh, and pulverization to 85% passing 200 mesh. Gold analyses are
conducted via Fire Assay Fusion with AA finish, and gravimetric
analyses are completed for over-limit () 5g/t) samples. Silver assays
are conducted via Agua Regia digest with an ICP finish.

The technical information contained in this news release has been
reviewed and approved by XR's Vice President Exploration, David G.
Thomas, P. Geo., who is a "Qualified Person" as defined under NI
43-101.

About the California Gold Project

The California Gold Project comprises 250 hectares within the
prolific California-Vetas Gold District, Santander, Colombia, which
also contains the multi-million ounce La Mascota, La Bodega and
Angostura gold deposits. The gold-silver-copper mineralization in the
California Gold Project is part of the same large mineralizing system
localized along a regional northeast-trending fault zone.
Mineralization occurs in northeast, northwest and east-west striking,
generally steeply dipping fault structures containing high grade veins
up to two metres in width.  Vein mineralogy includes enargite, pyrite,
chalcopyrite and sphalerite. Elevation ranges from 2,400 to 2,700
metres above sea level, far below the Paramo boundaries.

The Machuca and Los Andes Zones are located approximately 300 to
450 metres south and southeast of the Pie De Gallo Zone which hosts an
Indicated mineral resource of 2.4 Mt grading 5.5 g/t Au containing
425,000 ounces gold and an Inferred mineral resource of 3.85 Mt grading
5.4 g/t Au containing 670,000 ounces gold1 and 700 to 850 metres
southwest of the La Mascota zone which hosts an Inferred mineral
resource of 18.7 Mt grading 4 g/t Au containing 2.4 million ounces of
gold.2  Both the Pie De Gallo and La Mascota Zones are part of
Mubadala's Soto Norte Project which was originally purchased from
Ventana Gold, Calvista Gold and Galway Resources.

XR is advancing the California Gold Project toward economic
feasibility by the delineation of high-grade vein resources exploitable
by modern underground mining methods.  Underground mapping of existing
mine workings and underground channel sampling are currently underway,
prioritizing targets for underground diamond drilling as soon as
possible.

About Red Eagle Exploration

XR is a precious metals exploration and development corporation
majority owned by gold producer Red Eagle Mining Corporation.  XR has
an experienced exploration and mine development team focused on
building shareholder value through acquiring and de-risking high grade
gold and silver projects with low costs and low technical risks in
Colombia, a jurisdiction with prolific historic production but until
recently limited modern exploration.  XR owns 100% of the Vetas Gold,
California Gold and Santa Ana Silver Projects, which consist of
numerous historic and existing mines and where exploration is currently
underway to delineate high-grade vein resources exploitable by modern
underground mining.

For further information, please contact David Thomas, Vice
President Exploration or:

Patrick Balit
Vice President Corporate Development
Suite 2348 - 666 Burrard Street
Vancouver, BC, V6C 2X8
+1 778 372 2558
balit@redeaglemining.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release. Information set forth in this news release includes
forward-looking statements under applicable securities laws.
Forward-looking statements are statements that relate to future, not
past, events. In this context, forward-looking statements often address
expected future business and financial performance, and often contain
words such as "anticipate", "believe", "plan", "estimate", "expect",
and "intend", statements that an action or event "may", "might",
"could", "should", or "will" be taken or occur, or other similar
expressions. All statements, other than statements of historical fact,
included herein including, without limitation; statements about the
terms and completion of the proposed sale transaction are
forward-looking statements. By their nature, forward-looking statements
involve known and unknown risks, uncertainties and other factors which
may cause the actual results, performance or achievements, or other
future events, to be materially different from any future results,
performance or achievements expressed or implied by such
forward-looking statements. Such factors include, among others, the
following risks: failure to satisfy all conditions precedent to the
transaction, including disinterested shareholder approval and stock
exchange regulatory approval, and the additional risks identified in
the management discussion and analysis section of the Company's interim
and most recent annual financial statement or other reports and filings
with Canadian securities regulators. Forward looking statements are
made based on management's beliefs, estimates and opinions on the date
that statements are made and the respective companies undertakes no
obligation to update forward-looking statements if these beliefs,
estimates and opinions or other circumstances should change, except as
required by applicable securities laws. Investors are cautioned against
attributing undue certainty to forward-looking statements.
1 Technical Report "Resources California Gold-Silver Project"
dated October 25, 2012 available under Galway Resources Ltd.'s SEDAR
profile.

2 Technical Report "Preliminary Assessment La Bodega Project"
dated November 8, 2010 available under Ventana Gold Corp.'s SEDAR
profile.

TSX Venture closing price for XR-V
Date: 2017/09/25
Closing Price: 0.10

TEL: 778-372-2553    RED EAGLE EXPLORATION LTD
FAX: 778-372-2553
E-mail: info@redeaglex.com
Website: http://www.redeaglex.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1726800001TS11726800598-05035620170926