Source	MARKET NEWS
Date	09/26/2017
Time	08:19:59 AM

Company	 Nicola Mining Inc.
Title	Results of 
Reverse Circulation Drilling on 3060





    CDNX Symbol: NIM











Press Release





NICOLA MINING INC ("NIM-V")
- Results of Reverse Circulation Drilling on 3060-Craigmont
- Portal Wastepiles

Nicola Mining Inc. (the "Company") is pleased to announce the
results of a Reverse Circulation drill program ("RC Program"). The
program was designed to evaluate the copper grade and volume of
historical material excavated from underground workings of the
Craigmont Mine, located near Merritt, British Columbia. The material is
located adjacent to the 3060-Portal (figure 1). Results of the RC
Program confirm significant copper mineralization in the material
sampled by drilling.

Composite of RC Drill Hole Results

Map of Historic Stockpile and 3060-Portal Location

Reverse circulation drill hole locations and average grade 0-9m or
depth of hole.   A RC drill rig operated by Boart Longyear Ltd. was
mobilized to site on July 24 and drilling continued until August 1,
2017. The program was temporarily suspended due to poor air quality
resulting from forest fire smoke, which affected the BC Interior this
year. The material tested accounted for approximately 65% of the area
occupied by the excavated material.

Assay results from the drill program are summarized in Table 1.
Highlights of the results are:

* An average grade of 2391 ppm Cu (0.24% Cu) for the first 9
metres of the 29 drill holes.

* An average grade of 10,322 ppm Cu (1.03% Cu) in Hole P-34 and an
average grade of 8632 ppm Cu (0.86% Cu) in Hole P-72.

Table 1. Composite of RC Drill Hole Results
http://www.globenewswire.com/NewsRoom/AttachmentNg/514bd617-4712-4353-8510-
2582f49fda9e

On October 3, 2016, the Company announced that it had entered into
an Exploration and Material Purchase Agreement with Teck Highland
Valley Copper Partnership ("HVCP"), a wholly owned subsidiary of Teck
Resources Limited involving approximately 80 - 90 million tonnes of
mine strip material (refer to Oct. 3, 2016 news release) surrounding
the historic Craigmont open pit. As described in the Oct. 3, 2016 news
release, the historic cut off grade of the open pit was 0.7%.

Figure 1. Map of Historic Stockpile and 3060-Portal Location
http://www.globenewswire.com/NewsRoom/AttachmentNg/e8c98aa8-a96d-4177-a752-
077bec74e351
As Figure 1 illustrates, the RC Program tested material outside of the HVCP
agreement.

In addition to 3060 Portal, the Company had planned to conduct RC
drilling at Portal 3500, prior to postponing the RC Program due to air
quality issues caused by forest fires.

Future RC drilling is expected to focus on the approximate 80 - 90
million tonnes of stockpiles surrounding the pit area.

The Company recognizes that the quantity and grade is conceptual
as there is insufficient data to conclude a NI 43-101 resource;
however, the RC Program has provided significant insight into the
potential of the 80 - 90 million tonnes of mine strip material
surrounding the open pit.

The program demonstrated the viability of using RC drilling to
obtain reliable samples of unconsolidated dump material for tonnage and
grade estimation. In addition, underground mining techniques allow for
more controlled excavation and precise grade control than large-scale
open pit mining. Therefore, the material sampled in the RC Program is
considered to be low grade mineralization external to what was deemed
economic mineralization during historical mining. This suggests some of
the strip material placed in the larger dumps from the open pit is
representative of a similar low-grade mineralization halo.

Figure 2: Reverse circulation drill hole locations and average grade 0-9m
or depth of hole.
http://www.globenewswire.com/NewsRoom/AttachmentNg/0084457c-02e9-4997-a1eb-
777e90028375

Peter Espig, Chief Executive Officer of the Company, commented,
"The RC Program proved extremely valuable as it provides us with
insight into the significant potential of the mine strip material
surrounding the historic pit and gives us confidence that we can
successfully evaluate the tonnage and grade of this material with RC
drilling. Given that the largest cost of mining, which includes
engineering, infrastructure, surveying, and blasting have all been
incurred, the value of the stockpiles can be significant. The RC
Program also seems to confirm a mineralized halo effect that we have
seen around higher-grade mineralized zones of the mine."

Prior to suspending the RC Program, a large portion of the
material residing near the 3060-portal was drill tested. All drill
holes are 6 inches in diameter and were cased while drilling to
maximize rock chip sample return. Holes are approximately 15 metres
apart and comprise a total of 364 m in 29 drill holes. Hole depths
varied based on material encountered in the hole, with the site
geologist terminating each hole when overburden material was
encountered.

Quality Control

The Company implemented a quality control program for this program
to ensure best practices are utilized for sample collection and
analysis of RC cuttings. Samples were collected at 1.0 m intervals down
hole with lithology, alteration and mineralization documented for each
interval. Quality control measures include insertion of standards and
duplicates into the sample stream at a frequency of 1 duplicate and 1
standard for every group of 20 samples. Activation Laboratory (ISO
17025 Certified) in Kamloops, British Columbia conducted sample
analysis using ICP Aqua Regia 38-element (IE3) and fire assay gold
(IA2) packages. Any samples returning values greater than 10,000 ppm
copper were retested using over-limit mass spectrometry methods (8-AR
ICP-MS). Certified reference standards and rock blanks were placed in
the sample stream with a ratio of approximately one sample out of 10.

Qualified Person

Kevin Wells, P.Geo, a consulting geologist to the Company is the
independent qualified person as defined by National Instrument 43-101 -
Standards of Disclosure for Mineral Projects for the technical
disclosure contained in this news release. The scientific and technical
content of this press release was reviewed by Mr. Chris LeClair,
G.I.T., and employee of the Company and verified by Mr. Kevin Wells,
P.Geo.

Nicola Mining Inc. is a junior mining company listed on the TSX
Venture Exchange, and has a fully-permitted 200 tonne per day custom
mill that recommenced operations in June 2016. Its 100% owned
state-of-the-art mill and tailing facility, located near Merritt,
British Columbia, is capable of processing both gold and silver mill
feed via gravity and floatation processes. The Company has 100% of the
Thule Copper property covering 10,084 hectares along the southern end
of the Guichon Batholith. In addition, the Company also owns 100% of
Treasure Mountain, its high-grade silver property, and a gravel pit,
which is located adjacent to its milling operations.

On behalf of the Board of Directors
"Peter Espig"
Peter Espig
CEO & Director

For additional information contact:
Peter Espig
Telephone: (778) 385-1213
Email: peter@nicolamining.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.
______________________________________
_______________________________________________
TSX Venture closing price for NIM-V
Date: 2017/09/25
Closing Price: 0.20
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1726800039TS11726801721-08181820170926