Source	MARKET NEWS
Date	09/05/2017
Time	05:03:49 AM

Company	 Coronet Metals Inc.
Title	Coronet 
Provides Update on Hydrometallurgical Re





    CDNX Symbol: CRF











Press Release





CORONET METALS INC ("CRF-V;CORMF-0")
MINEWORX TECHNOLOGIES LTD ("MWX-V;MWXRF-0")
- Coronet Provides Update on Hydrometallurgical Results
- On Tailings and Dumps

Coronet Metals Inc. ("Coronet" or "the Company") is pleased to
announce that Mineworx Technologies  Ltd. ("Mineworx") completed the
second round of hydrometallurgical test results on Coronet's
gold-bearing tailings and dumps at its 100% owned White Caps Gold
Mining Project ("White Caps" or "the Project").

As per the April 19, 2017 new release, Mineworx will be applying
its license to utilize the EnviroLeach Technologies Inc. (CSE: ETI)
("EnviroLeach") patent-pending, non-cyanide leach formula to process
the estimated 250,000 tonnes of gold bearing historic tailings and mine
dumps at the project.

For the second round of hydrometallurgical testing Mineworx and
Coronet focused on the Dumps and Pink Tailings which represents over
95% of the Project. The Bill Placer and Brown Tails were not tested
during the second round. (See February 2, 2017 news release for those
results).

Highlights of the hydrometallurgical test work can be summarized
as follows:

//st

* Average grades of 2.32 g/t Au on the Pink Tails
* Average grades of 1.33 g/t Au on the White Caps Dumps
* Recovery % as high as 72% in 24 hours on the Pink Tails
* Recovery % as high as 80% in 24 hours on the White Caps Dumps

//et

Approximately 57 kg and 39 kg of the Dumps and Pink Tailings
samples were provided to Mineworx for testing.  These samples were sent
to and independent laboratory, Met-Solve Laboratories, Inc, for
preparation (proper crushing, splitting and grinding as required).

The samples were prepared as follows:

1. Pink Tails

The Pink Tails sample was slightly damp so it was dried and then
rotary split to obtain representative subsamples for a head screen
fraction assay for gold and ICP analysis.  Smaller samples were also
split out for the leach test work.  No grinding was done on this sample
as it was already relatively fine.

2. Dumps

The Dump sample, which contained coarse rocks along with fines,
was subject to crushing prior to being split into sub-samples for a
head screen fraction for gold assay and ICP analysis.  A screen
metallics assay was also done to minimize the nugget effect on this
sample as it was thought to contain coarse gold.  Three subsamples,
weighing 2 kg each, were ground down to particle sizes of 56, 105 and
181 um (P80) for comparing the impact on grind size on leach extraction


Head and Screen Fraction Assays

Multiple head assays were carried out on the samples; head screen
fraction assay (SFA), a bulk assay by Enviroleach on both samples and a
screen metallics assay on the Dumps sample to address any potential
nugget effect.

The average assay results for the Pink Tails and the Dumps were
2.32 g/t Au and 1.33 g/t Au respectively.

In general, the grades appear to be higher in the finer fractions
of both samples with the highest grades occurring in the sub 400 mesh
fractions indicating that the gold is likely finely disseminated.

Leach Test Results

Leach tests using variations of Enviroleach's proprietary
technology were carried out on both samples however the Dumps samples
were ground to different particles size prior to leaching.

1. Dumps

The results from leaching over 24 hours which included measuring
incremental recoveries show that there is a significant increase in
recovery by leaching for 24 hours.  The recoveries were as high as 80%

2. Pink Tails

Similar to the Dumps sample, the results from leaching over 24
hours while measuring incremental recoveries show that there is a
significant increase in recovery going to 24 hours.  The recoveries
were as high as 72% .

Coronet and Mineworx are confident in the the X-leach formula and
will continue to adjust the formula as testing continues.  The 2nd
round results continue to be encouraging with increased recoveries from
the first round of testing. The lower grades on the larger sample used
in second round (2.32 g/t Au on the Pink Tails vs.  5.43 g/t Au in
round one and 1.33 g/t Au on the White Caps Dumps vs 15.94 g/t Au in
round one) shows that the grade of the gold-bearing tailings and dumps
is not uniform and therefore further test work, including bulk sampling
and/or drilling, will be conducted as a next step. Coronet and Mineworx
are discussing the next steps of testing before a decision is
anticipated with respect to commencement of work on a pilot plant to
treat the tails and begin recovering gold at the White Caps property.

Furthermore the Company would like to announce that it has applied
to the TSX Venture Exchange  (the "Exchange") to amend the terms of
1,616,000 common share purchase warrants (the "2016 Warrants") as
follows:

//st

* the expiry date be extended by two years to September 19, 2019, and
* the exercise price be lowered from $0.50 to $0.35 per common share.

//et

The 2016 Warrants were originally issued pursuant to a
non-brokered private placement closed in September 2016. Each 2016
Warrant entitles the holder to acquire one common share in the capital
of the Company at an exercise price of S0.50 per common share until
September 19, 2017. No 2016 Warrants issued under the private placement
have been exercised to date, and none of these warrants are held,
directly or indirectly, by any insiders of the Company.

The amendments to the 2016 Warrants are subject to approval of the
Exchange

Mr. Fred Tejada, P.Geo, a Director of the Company, is a Qualified
Person under the meaning of Canadian National Instrument 43-101 and is
responsible for the technical information contained in this news
release.

Cautionary Notes Regarding The White Caps Production

The White Caps Mining Project has no established resource and is
without a known body of commercial ore. The decision to commence
production at the White Caps Mine and Coronet's plans for small scale
mining and milling operations of the historic tailings and mine dumps
were based on economic models prepared by Coronet in conjunction with
management's knowledge of the property and the prior limited recent
operating history of the White Caps Project. The production decision
and operating plan for the processing of the tailings and mine dumps
were not based on any preliminary economic assessment, a
pre-feasibility study or a feasibility study of mineral reserves
demonstrating economic and technical viability. Accordingly, there is
increased uncertainty and economic and technical risks of failure
associated with the production decision and operating plan, in
particular the risk that mineral quantities and/or grades will be lower
than expected, the risk that construction or operations will be more
difficult or more expensive than expected, the risk that the Company
will not be able to transport or sell the metal it produces on the
terms it expects, or at all, the risk that due to the absence of a
detailed economic and technical analysis according to and in accordance
with NI 43-101 the production and economic variables associated with
mineral extractions and sale may vary considerably. Readers are
cautioned that no reliable estimates of future production capability or
the economics of any extraction activity can be made.

* References to tonnages are historical estimates. The estimated
tonnage of 250,000 tonnes was provided by the two different mining
engineering companies in October 2011 that the Company engaged to
provide an estimate. The stockpile measurement is a technique to
measure the volume and weight of commodity stockpiles. It is a
scientific/ instrumental method, using Total Station equipment to
determine the volume of the stockpile quantity. A qualified person has
not done sufficient work to classify the historical estimate as current
mineral resources or mineral reserves nor does Coronet treat the
historical estimate as current mineral resources or mineral reserves.
The Company will have to conduct independent surveying, drilling,
sampling and assaying of the tailings and mine dumps to determine the
NI 43-101 tonnes and grades of the tailings and mine dumps. In
conjunction with that, the Company will have to continue with
independent metallurgical analysis to verify recoveries. This work will
form the basis to upgrade or verify the historical estimates as NI
43-101 mineral resources or mining reserves.

About Coronet Metals

Coronet Metals Inc. is engaged in the business of acquiring,
exploring and developing natural resource properties, with a focus on
precious mineral properties/projects which have the potential for both
near-term cash flow and significant exploration upside potential.
Coronet's White Caps Gold Project is near the town of Manhattan in
Northern Nye County. The Project is well in line with its strategy of
acquiring precious metals mining projects which have the potential for
both near-term cash flow and exploration upside.

The Company continues to pursue other near-term, promising high
value gold and silver projects in the area that will augment its 120
patented and unpatented claims in the Manhattan District in Nevada. The
Company is in discussions with third parties on possible acquisitions
and to date nothing has been consummated

About Mineworx

Mineworx is positioned for growth through partnerships with
advanced mining and E-Waste opportunities utilizing its licensed
cyanide-free precious metals extraction formula and patent-pending
portable extraction technologies. These three innovations will increase
and enhance business opportunities by deploying cost effective,
environmentally friendly extractive metallurgy solutions.

Forward Looking Information

This news release contains forward-looking statements and other
statements that are not historical facts. Forward-looking statements
are often identified by terms such as "will", "may", "should",
"anticipate", "expects" and similar expressions. All statements other
than statements of historical fact included in this release are
forward-looking statements that involve risks and uncertainties. There
can be no assurance that such statements will prove to be accurate and
actual results and future events could differ materially from those
anticipated in such statements. Important factors that could cause
actual results to differ materially from the Company's expectations are
risks detailed from time to time in the filings made by the Company
with securities regulations.

The reader is cautioned that assumptions used in the preparation
of any forward-looking information may prove to be incorrect. Events or
circumstances may cause actual results to differ materially from those
predicted, as a result of numerous known and unknown risks,
uncertainties, and other factors, many of which are beyond the control
of the Company. As a result, the Company cannot guarantee that any
forward-looking statement will materialize and the reader is cautioned
not to place undue reliance on any forward-looking information. Such
information, although considered reasonable by management at the time
of preparation, may prove to be incorrect and actual results may differ
materially from those anticipated. Forward-looking statements contained
in this news release are expressly qualified by this cautionary
statement. The forward-looking statements contained in this news
release are made as of the date of this news release and the Company
will only update or revise publicly any of the included forward-looking
statements as expressly required by Canadian securities law.

Neither the TSX Venture Exchange nor its regulation services
provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Theo van der Linde
President and CEO
Tel: +1 604-336-3193
Email: tvanderlinde@coronetmetals.com
______________________________
_______________________________________________
TSX Venture closing price for CRF-V
Date: 2017/08/30
Closing Price: 0.13
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1724600001TS11724600503-08275320170904