Source	MARKET NEWS
Date	09/06/2017
Time	07:15:56 AM

Company	 Silver Range Resources Ltd.
Title	Defines Drill Targets at Skylight





    CDNX Symbol: SNG











Press Release





Defines Drill Targets at Skylight --->@NEWS RELEASE
SILVER RANGE RESOURCES LTD ("SNG-V")
- Defines Drill Targets at Skylight

Silver Range Resources Ltd. ("Silver Range") is pleased to provide
encouraging results of a geologic mapping, sampling and geophysical
survey program conducted during April and June at the Skylight Property
in Nye County, Nevada. Results from this work have defined good drill
targets.

At Skylight, extensive silica caps overlie a near-completely
preserved epithermal system in mid-Tertiary felsic tuff. Results from a
three-dimensional induced polarization (3DIP) survey conducted in June
defined a network of linear chargeability anomalies in the centre of
this system. Several of the linears extend into the periphery of the
system, following vein and hydrothermal clay alteration zones exposed
in gullies at lower elevations. Dickite and hydrothermal kaolinite were
noted in two clay alteration zones. Elevated gold, silver and arsenic
soil and rock geochemical values are associated with the linear
chargeability anomalies, particularly at lower elevations, while
scattered high mercury geochemical response was noted over the central
silica caps. The southern end of one of the linears was tested by
Rimfire Minerals and Newmont in a 2007 drill hole, intersecting 10.7 m
@ 0.490 g/t gold (Rimfire Mineral Corporation Press Release dated
November 6, 2007). Silver Range cannot independently verify the
information released by Rimfire. The 3DIP survey also identified a
nexus beneath the silica caps in the south-central region of the target
where several linear chargeability anomalies intersect and the linear
density is highest. This area and the linears with associated
geochemical response will be modelled in detail to design a
comprehensive drill plan. A video presentation describing the results
at Skylight can be found at www.silverrangeresources.com.

Technical information in this news release has been approved by
Mike Power, M.Sc., P.Geo., CPG, President and CEO of Silver Range
Resources Ltd. and a Qualified Person for the purposes of National
Instrument 43-101.

Silver Range is a precious metals prospect generator working in
Nevada, Nunavut and the Northwest Territories. The company is actively
seeking joint venture partners to explore the assets in its portfolio.

ON BEHALF OF SILVER RANGE RESOURCES LTD.
"Mike Power"
President, C.E.O. & Director

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release may contain forward looking statements based on
assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of exploration and
other risk factors beyond its control, and actual results may differ
materially from the expected results.

For further information concerning Silver Range or its exploration projects
please contact:

Investor Inquiries
Richard Drechsler
Vice-President, Communications
Tel: (604) 687-2522
NA Toll-Free: (888) 688-2522
rdrechsler@silverrangeresources.com
http://www.silverrangeresources.com
______________________________________
_______________________________________________
TSX Venture closing price for SNG-V
Date: 2017/09/05
Closing Price: 0.20
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1724800040TS11724801601-07135220170906