Source	MARKET NEWS
Date	09/07/2017
Time	06:40:02 AM

Company	 Valterra Resource Corporation
Title	Identifies Two New Gold Zones on Swift Target in





    CDNX Symbol: VQA











Press Release





Identifies Two New Gold Zones on Swift Target in 2017 Drilling --->@NEWS 
RELEASE
VALTERRA RESOURCE CORP ("VQA-V;VRSCF-0")
- Identifies Two New Gold Zones on Swift Target in 2017 Drilling

Valterra Resource Corporation ("Valterra") reported today on
results from the 2017 diamond drill program on the Swift Katie property
which successfully identified two shallow mineralized gold zones along
the target structure in Swift zone.

Highlights from the drill program include:

//st

* a 0.8 metre downhole interval averaging 30.9g/t Au and 17.8g/t Ag
within
a broader 2.5 metre downhole interval averaging 11.5g/t Au and 6.7 g/t
Ag
from hole SK17-015;
* an additional 22.6 metre downhole interval averaging 1.1g/t Au and
0.5g/t
Ag from hole SK17-015; and
* a 1.4 metre interval averaging 9.7g/t Au and 7.6g/t Ag within a broader
8.6 metre interval averaging 3.1g/t Au and 2.0g/t Ag from hole
SK17-019.

//et

Higher grade gold values were returned from quartz veins and
silicified intervals within a strongly foliated and
quartz-carbonate-altered volcanic rock which can form zones several
10's of metres thick in any given drill hole. Alteration appears
largely structurally controlled and forms an anastomosing network of
northeast-striking shear zones that dip moderately to the southeast.

Gold mineralization has been intersected in relatively shallow
drilling ((200 metres depth) with the thickness of some intercepts,
particularly in hole SK17-015 comparable to mineralized intervals at
Prize Mining's Kena Gold Project, located 30 kilometres to the
Northeast, which is currently modelled as a bulk-tonnage porphyry gold
target.

Drilling tested three areas along an approximate 1000 metre strike
length of the target structure which had been previously traced by a
combination of surface rock and soil sampling, historical trenching and
several short diamond drill holes from the 1980's and most recently by
Valterra in 2016.  Only part of the full strike-length of the
structural target has been drill tested; several additional target
areas have been prioritized for testing in future programs.

The current drill program successfully confirmed high-grade gold
mineralization in two locations along the tested strike-length of the
target structure and returned a significant cumulative thickness of
+1g/t Au mineralization in hole SK17-015. Both gold-enriched areas are
open along strike and down dip and require additional drill testing.

Figure 1: 2017 Plan Map of the Swift target area showing drill hole
distribution

To view an enhanced version of Figure 1, please visit:
http://orders.newsfilecorp.com/files/5345/28866_a1504732904328_45.jpg

//st

Hole #        Collar Data        From     To     Interval    Au      Ag
Comments
(m)     (m)      (m)      (g/t)  (g/t)

AZ Deg   DIP   Depth
Deg    (m)

SK17-012    325     -80   118.3   48.7    53.0      4.3       1.0     1.7
32.7%

dilution

inc.                          48.7    50.2      1.5       2.0     3.1

SK17-013    325     -50   139.0   40.0    56.7      16.7      1.1     0.4
23.9%

dilution

inc.                          44.8    50.0      5.3       2.3     0.6

SK17-014    005     -70   154.5   22.5    24.0      1.5       0.3     0.7

SK17-015    356     -70   160.6   23.5    26.0      2.5      11.5     6.7
inc.                          23.5    24.3      0.8      30.9    17.8

SK17-015                          46.0    55.7      9.8       1.4     0.4

SK17-015                          78.5    101.1     22.6      1.1     0.5

SK17-015                          119.7   126.8     7.1       1.1     0.7

inc.                          119.7   121.0     1.4       3.7     1.5

SK17-016    343     -50   154.5   117.1   117.6     0.5       0.4     1.7

SK17-017    335     -50   215.2    NSV     NSV      NSV       NSV     NSV

SK17-018    315     -70   273.2   190.5   191.9     1.4       0.5     2.4

SK17-018                          226.0   227.5     1.5       0.8     2.3

SK17-019    330     -50   189.0   164.0   172.6     8.6       3.1     2.0
23%

dilution

inc.                          164.0   166.0     2.0       5.1     1.9

and inc.                          169.8   171.2     1.4       9.7     7.6

//et

Samples were analyzed by FA/ICP-ES for gold and 48 element ICP-MS
by MS Analytical, Langley, BC. Silver ()100ppm), copper, lead and zinc
()1%) overlimits assayed by ore grade ICP-ES analysis, High silver
overlimits ()1500g/t Ag) and gold overlimits ()10g/t Au) re-assayed
with FA-Grav. Gold composites calculated using a 0.3g/t Au cut-off and
(20% internal dilution, except where noted. Reported intervals are core
lengths, true widths undetermined. Accuracy of results is tested
through the systematic inclusion of QA/QC standards, blanks and
duplicates into the sample stream.

Exploration results to date support the Company's belief of a
widespread gold-enriched, vein system at the Swift target and a large
alkali porphyry system at the Katie target.  Further work will be
designed to continue to expand the known mineral systems and evaluate
several other targets which remain to be tested on the Project.

About The Swift Katie Property

The Swift Katie Project consists of 19 contiguous MTO mineral
claims, covering over 83 square kilometres within a geologically
favourable and highly metallogenic area of B.C. that historically has
hosted several important mining camps.

Historically the property was explored as two separate
mineralizing systems with the northern claims hosting the Katie Cu-Au
porphyry target and southern claims hosting the Swift Au-Ag vein
targets.

Drilling to date on the Katie zone has identified three
accumulations of semi continuous Cu-Au mineralization over a 1,800m
cumulative strike length.  Initial work by Valterra has identified
eight infill holes totaling 2,600m which, when completed, should
significantly enhance both the size and continuity of the
mineralization. Widespread Cu-in-soil anomalies suggest several
additional untested targets.

Gold-silver mineralization at Swift is hosted in highly deformed
and strongly altered volcaniclastic rocks of the prospective Elise
Formation. The rock package may reflect a transitional environment from
a porphyry to an epithermal system and exhibits some similarity to
styles of mineralization identified in the historic Rossland Mining
Camp (past production: 2.7M oz/Au; 3.4M oz/Ag and 120M lbs Cu) located
just 25km to the west of the property.

About Valterra

Valterra is a Manex Resource Group Company.  The group provides
expertise in exploration, administration, and corporate development
services for Valterra's mineral property located in British Columbia.
Valterra is focused on early stage properties with the potential to
host large deposits, in regions with excellent infrastructure.

Robert Macdonald, M.Sc. P.Geo., is the non-independent Qualified
Person for Valterra responsible for reviewing and approving the
technical content presented in this release.

On behalf of the Board of Directors,

"Lawrence Page"

Lawrence Page, Q.C., President, Valterra Resource Corporation

For further information, please visit Valterra's website at
valterraresource.com or contact Valterra at 604.641.2759 or by email at
ir@mnxLtd.com.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This news release may contain forward-looking statements including
but not limited to comments regarding the timing and content of
upcoming work programs, geological interpretations, receipt of property
titles, potential mineral recovery processes, etc. Forward-looking
statements address future events and conditions and therefore involve
inherent risks and uncertainties. Actual results may differ materially
from those currently anticipated in such statements. These statements
are based on a number of assumptions, including, but not limited to,
assumptions regarding general economic conditions, interest rates,
commodity markets, regulatory and governmental approvals for Valterra
Resource Corporation's projects, and the availability of financing for
Valterra Resource Corporation's development projects on reasonable
terms. Factors that could cause actual results to differ materially
from those in forward looking statements include market prices,
exploitation and exploration successes, the timing and receipt of
government and regulatory approvals, and continued availability of
capital and financing and general economic, market or business
conditions. Valterra Resource Corporation does not assume any
obligation to update or revise its forward-looking statements, whether
as a result of new information, future events or otherwise, except to
the extent required by applicable law.

TSX Venture closing price for VQA-V
Date: 2017/09/05
Closing Price: 0.03

TEL: 604-684-9384    VALTERRA RESOURCE CORP
FAX: 604-688-4670
E-mail: info@mnxLtd.com
Website: http://www.valterraresource.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1724900027TS11724901343-06392320170907