Source	MARKET NEWS
Date	09/11/2017
Time	06:16:25 AM

Company	 Mirasol Resources Ltd.
Title	Best 
Results to Date from Yamana Gold Drilling a





    CDNX Symbol: MRZ











Press Release





MIRASOL RESOURCES LTD ("MRZ-V;MRZLF-0")
- Best Results to Date from Yamana Gold Drilling at the Atlas
- Project

Mirasol Resources Ltd. ("Mirasol", "The Company") is pleased to
report results from the second season of drilling by Yamana Gold at the
Atlas Project, Gorbea JV in the Mio-Pliocene Belt of Northern Chile.

Current drill results at Gorbea include the best down-hole
intersection to date from the Atlas project, comprising 1.07 g/t Au
intersected over 114 m, including 2.49 g/t Au over 36 m in oxidized
high sulphidation epithermal (HSE) vuggy silica breccia.  Drilling
to-date at Atlas (Figure 1) has outlined Au mineralization (the "Steam
Heated Zone") in an area of 650 m by 125 m by over a 200 m vertical
interval (Figure 2). The Steam Heated Zone may represent a body of
Au+Ag mineralization that as defined to date is open to depth and
laterally in all directions outside the area of current drilling.  As
currently known, the top of mineralization is located between
approximately 255 to 310 m depth beneath altered cap rocks, which is a
characteristic in-common with other recent, HSE gold discoveries
elsewhere on this same mineral belt in Chile. Further drilling is
required at Atlas to determine the size, continuity and grade of the
Steam Heated Zone and to establish if extensions of this mineralization
occur closer to surface, where it may be accessible via open pit
mining.

Stephen Nano CEO of Mirasol stated "We are very encouraged by
these results that demonstrate the presence of a large, strongly
mineralized and deeply oxidized, HSE gold system at Atlas.  Yamana has
made significant advances in understanding the controls on gold
mineralization at the project and are planning a large drill program
this season to test for extensions of the Steam Heated Zone
mineralization and to test a number of other compelling targets at
Atlas and the other Gorbea JV projects."

During the last drill season (October 2016 to April 2017), Yamana
completed 2,558 m of diamond core drilling in seven holes (Figure 1,
and Table 1 and Table 2; holes CATRAD0014 to 20) at the Atlas project.
Total drilling completed since inception of the Gorbea JV in May 2015
is over 8,704 m, and Yamana's total exploration spend to May 2017 is
approximately US$5.2M, against the US$10 M required to trigger the 51%
earn-in milestone over a maximum of 4 years.  In addition, on May 12,
2017 Yamana made a US$400,000 option payment to Mirasol Resources to
continue the JV into its third year (see news release May 30, 2017).

Yamana also recently advised Mirasol that it has increased its
2017 Gorbea JV exploration budget by an additional US$700,000.  The
additional exploration funds will be directed to drilling at the Atlas
Steam Heated Zone and other new targets at the project. Yamana is
planning to re-commence drilling at Atlas for the southern hemisphere
2017 spring field season in October.

Last season's (October 2016 to April 2017) drill campaign at Atlas
was focused on a series of outcropping breccia bodies that were
highlighted during a pre-drill geological mapping campaign.

Best results from this drill campaign were received from holes 15
and 16 (Figure 2, Table 1) and include:

//st

* 114.1 m at 1.07 g/t Au and 1.78 g/t Ag, including 36 m at 2.49 g/t Au and
3.08 g/t Ag (hole 15)
* 45.8 m at 0.32 g/t Au and 0.81 g/t Ag (hole 16)

//et

The intersection in hole 15 starts from 347 m down hole.  Hole 16
is interpreted to have drilled across the top of this same breccia
body. Drill holes 15 and 16 were drilled toward each other ("scissor
holes") from the NW and SE to cross each other at depth, testing a zone
beneath an area of coincident outcropping breccia, weakly anomalous
soil geochemistry and a geophysical anomaly that lies midway between
drill holes 7 and 10 from last season's drilling.  Holes 7 and 10
returned the best results from the 2015-16 drill campaign including 40
m at 1.38 g/t Au, with 28 m at 1.82 g/t Au.  The mineralization at
Atlas is interpreted to be oxidized to depths of more than 400 m
downhole.  Deep oxidation is considered a positive feature at Atlas as
it may suggest the potential for favourable metallurgical
characteristics of the mineralization at the project.

The geometric relationship of mineralization intersected in drill
holes 7, 10, 15, and 16 (Figure 3) outlines a target zone with
dimensions of 650 m by 125 m by over a 200 m vertical interval,
potentially representing a body of Au+Ag mineralization that is open to
depth and open in all directions surrounding these holes.  The top of
the mineralization in hole 15 lies approximately 255 to 310 m below
surface from the RL of the drill collar or the hill top, respectively.
However, the geometry of the surface soil anomaly, distribution of
un-explained stream sediment gold anomalies and alteration, suggest the
target zone may extent to the south where topography is more
favourable, highlighting the possibility for mineralization to occur
closer to surface in this area.

Gold and silver mineralization in holes 15 and 16 is hosted in a
multiphase breccia body (Figure 3) characterized by intense
quartz-alunite+/- jarosite alteration with vuggy silica breccia clasts
and a phase of late-stage translucent barite hosting visible gold.
This style of mineralization is typical of HSE Au+Ag deposits elsewhere
in the same belt of mineralization in Chile (click here for information
on these deposits).  These deposits including the recent multi-million
ounce gold discoveries by Barrick Gold at Alturas (6.8 M ounce resource
at 1.00 g/t Au1) and Gold Fields at Salares Norte (3.8 M ounce resource
at 3.6 g/t Au and 43.8 M oz Ag at 53.1 g/t Ag2) located 70 km due south
of the Atlas project.  At these projects gold is hosted in breccia
bodies and the vuggy silica altered wall rocks and was discovered by
drilling through thick geochemically barren alteration caps as seen at
the Atlas project.

Anomalous Au-Ag epithermal path finder elements and changes in
alteration mineral chemistry were also detected in a separate breccia
body intercepted in hole 20 at Atlas.  Based on knowledge gained from
modelling of results from the Steam Heated Zone, the results from hole
20 suggest that further drilling is warranted in this area to test for
higher grade Au-Ag mineralization.

Information gathered from this season's exploration indicates that
the mineralization at Atlas is hosted in a cluster of phreatomagmatic
and hydrothermal breccia bodies that when combined outline a larger
breccia complex.  Preliminary geological models show mineralization
identified at Atlas is hosted in both the breccia bodies and in
stratabound zones of vuggy silica developed in the wall rock adjoining
the breccia. This association of mineralization styles is seen at a
number of other large HSE Au+Ag deposits in the Mio-Pliocene age
mineral belt that hosts the Atlas mineralization.

Mirasol invites investors to follow the Gorbea - Yamana JV story
by visiting www.mirasolresources.com and signing up to receive our new
releases.

Stephen Nano, President and CEO of Mirasol, has approved the
technical content of this news release and is a Qualified Person under
NI 43 -101.

Quality Assurance/Quality Control of the Gorbea exploration
program:

Under the terms of the Gorbea Agreement, all exploration is
managed by Yamana. All pre-Joint Venture exploration on the projects
was supervised by Mirasol CEO Stephen C. Nano, who is the Qualified
Person under NI 43-101. All information generated from the Gorbea Joint
Venture program is reviewed and validated by Mirasol prior to release.
The technical interpretations presented here are those of Mirasol
Resources Ltd.

Yamana applies industry standard exploration methodologies and
techniques. All geochemical rock and drill samples are collected under
the supervision of Yamana's geologists in accordance with industry
practice. Geochemical assays are obtained and reported under a quality
assurance and quality control (QA/QC) program. Samples are dispatched
to an ISO 9001:2000-accredited laboratory in Chile for analysis. Assay
results from drill core samples may be higher, lower or similar to
results obtained from surface samples due to surficial oxidation and
enrichment processes or due to natural geological grade variations in
the primary mineralization.

Forward Looking Statements: The information in this news release
contains forward looking statements that are subject to a number of
known and unknown risks, uncertainties and other factors that may cause
actual results to differ materially from those anticipated in our
forward-looking statements. Factors that could cause such differences
include: changes in world commodity markets, equity markets, costs and
supply of materials relevant to the mining industry, change in
government and changes to regulations affecting the mining industry.
Forward-looking statements in this release include statements regarding
future exploration programs, operation plans, geological
interpretations, mineral tenure issues and mineral recovery processes.
Although we believe the expectations reflected in our forward-looking
statements are reasonable, results may vary, and we cannot guarantee
future results, levels of activity, performance or achievements.
Mirasol disclaims any obligations to update or revise any
forward-looking statements whether as a result of new information,
future events or otherwise, except as may be required by applicable
law.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

1 Barrick Gold Corporation. (2016). Annual Report 2016.2 Gold
Fields. (2016). The Gold Fields Mineral Resource and Mineral Reserve
Supplement to the Integrated Annual Report 2016.

For further information:  Stephen Nano, President and CEO or
Jonathan Rosset, Manager of Corporate Development, Tel: +1 (604)
602-9989, Email: contact@mirasolresources.com, Website:
www.mirasolresources.com

______________________________
_______________________________________________
TSX Venture closing price for MRZ-V
Date: 2017/09/08
Closing Price: 1.78
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1725300012TS11725301098-06131820170911