Source	CANADA NEWSWIRE
Date	09/08/2017
Time	06:04:31 PM

Company	 Salazar Resources Limited
Title	Salazar Intersects 22.42 Metres (True) Averaging 7.4 G/T Gold, 82.1 G/T
Silver, 4.43% Copper and 4.41% Zinc in the El Domo Deposit and
Succesfully Ends the Phase V Diamond Drilling Program at its Curipamba
Project





    CDNX Symbol: SRL











Press Release




" BC-Salazar-Curipamba   09-08 2155
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Salazar Intersects 22.42 Metres (True) Averaging 7.4 G/T Gold, 82.1 G/T
Silver, 4.43% Copper and 4.41% Zinc in the El Domo Deposit and
Succesfully Ends the Phase V Diamond Drilling Program at its Curipamba
Project@

VANCOUVER, Sept. 8, 2017 /CNW/ - Salazar Resources Limited (TSX.V: SRL;
FRANKFURT: CCG.F) ("Salazar" or the "Company") is pleased to report results
from the last eight holes (2,430.30 metres) of the phase V diamond drill
program that was completed on the Company's 100-per-cent owned (21,500 ha)
Curipamba volcanogenic massive sulphide ("VMS") project in Ecuador. Five holes
represent new exploratory and development drilling around the El Domo resource
and were not included in the latest El Domo resource estimate which was
released on January 16, 2015. Three holes were drilled in the Barranco
Colorado area, which is within the Curipamba project, to test regional
exploration targets.
HIGHLIGHTS:
<<

--  Hole CURI-236
o 2.30 metres (true) averaging 1.42 g/t gold, 51.7 g/t silver, 2.45% copper
and 5.59 % zinc in massive and semi-massive chalcopyrite and pyrite.
>>
<<

--  Hole CURI-237
o 36.79 metres averaging 5.0 g/t gold, 53.4 g/t silver, 2.93% copper and 2.9 %
zinc; which includes two intervals:
(number sign) 11.10 metres averaging 1.5 g/t gold, 10.77g/t silver, 0.73% 
copper and
0.70% zinc in Grainstone (a marker unit in the immediate hanging wall of
the massive sulphides) with clasts of semi-massive sulphides
(number sign) 22.42 metres averaging 7.4 g/t gold, 82.1 g/t silver, 4.43% 
copper and
4.41% zinc in massive and semi-massive sphalerite, chalcopyrite and
pyrite.
>>
<<

--  Successful finalization of the phase V drilling program
>>
PROGRAM RESULTS:
The latest eight holes (2,430.30 metres) (Table 1) were drilled as part
of the planned 40-hole (10,000 metres) drill program that was completed with
the purpose of expanding the El Domo VMS deposit and exploring its margins, as
well as testing geophysical anomalies and surface showings around the
Curipamba Project (Figure 1). The drilling activities of the program ended on
August 7th, 2017.
A total of 36 holes (10,472.62 metres) were drilled. Thirty-three (33)
holes were drilled in and around the El Domo deposit and three (3) holes were
drilled in the Barranco Colorado area. In addition to the significant
intersections being reported here, five (5) other holes intersected
significant mineralization: CURI-213, CURI-218, CURI-224, CURI-231and CURI-234
( News Releases of March, May and August 2017).
Hole CURI-236 intersected 2.30 metres averaging 1.42 g/t gold, 51.73 g/t
silver, 2.45% copper and 5.59% zinc in massive and semi-massive of
chalcopyrite and pyrite. This intersection is located in the northeastern
sector of the El Domo deposit, approximately 50 metres south from the CURI-231
which cut 3.09 metres (3.08 m true) averaging 0.60 g/t gold, 9.40 g/t silver,
6.43% copper & 0.18% zinc (news release of August 14, 2017 ). This new
intersection extends the previously interpreted mineralization trend
identified by CURI-224, CURI-198 and CURI-231 an additional 50 metres to the
south, making this new trend a total length of approximately 200m. This trend
will most likely be connected to the main resource body given that the
CURI-236 intersection is only 60 metres northeast from the CURI-166, which
previously marked the edge of the latest El Domo resource estimate.
Hole CURI-237 was a deep exploratory hole that was collared approximately
30 meters north east from the CURI-106 which was drilled in April of 2010 and
intersected 36.33 metres 3.74 g/t gold, 35.85 g/t silver, 4.39 % copper and
1.5% zinc in the west-central sector of the El Domo deposit. CURI-237 was
drilled vertically down to 537.80 metres to test the potential for additional
underlying VMS depositional lenses and the potential for strong feeder zones
related to the existing El Domo VMS body. CURI-237 intersected 36.79 metres
averaging 5.0 g/t gold, 53.4 g/t silver, 2.93% copper and 2.9 % zinc; which
includes two intervals:
<<

--  11.10 metres averaging 1.5 g/t gold, 10.77g/t silver, 0.73% copper and
0.70% zinc in grainstone with clasts of semi-massive sulphides. The
Grainstone is a marker unit in the immediate hanging wall of the VMS
mineralization.
--  22.42 metres averaging 7.4 g/t gold, 82.1 g/t silver, 4.43% copper and
4.41% zinc in massive and semi-massive sulphide of sphalerite,
chalcopyrite and pyrite.
>>
This intersection represents an in-fill addition to the known El Domo
resource. Below the El Domo deposit drilling intersected the usual altered and
mineralized dacitic unit, followed by the rhyolitic flow which is the deepest
formation reached in several previous holes. Below the rhyolite another large
dacitic unit with sporadic sedimentary lenses was intersected with yet another
rhyolitic flow at the base. The hole intersected weak sporadic sulphide
mineralization with sphalerite, chalcopyrite and pyrite all the way down to
the end of the hole in the form of veinlets and fracture fillings. In
addition, this hole showed that the basement marine volcanic rocks, Piñon
Formation, which was believed to be at shallower depths was not encountered
suggesting that the mineralization and alteration system extends as deep as
420 metres below the El Domo deposit.
Fredy Salazar, President and CEO, commented: "The culmination of our
Phase V drilling program marks an important landmark in our company and the
development of our Curipamba project. As a result, the El Domo resource has
been better defined and important mineralization extensions have been
intersected that will add significant value to the previously defined
reserves. Also, the Barranco Colorado holes have shown us the additional
exploration potential on the Curipamba project outside of El Domo. Salazar is
very satisfied with the results and looks forward to the future possibilities
that this drilling campaign has opened for us."
OTHER RESULTS:
CURI-235 collared on the same platform as CURI-234 (6.87 metres (6.45 m
true) averaging 1.47 g/t gold, 10.9 g/t silver, 7.42% copper, 1.01% zinc (news
release of August 14, 2017) was drilled southwesterly to test the possible
extension of CURI-234 mineralization towards the east. It intersected a
massive gypsum interval and the underlying dacitic unit. Gypsum frequently
occurs as part of the outer shell stockwork mineralization.
CURI-238 and CURI-239 were drilled to explore the eastern limits of the
El Domo mineralization. CURI-238 was drilled vertically approximately 150
metres from the El Domo resource. CURI-239 was drilled westerly around 200
metres from the El Domo resource. Both holes intersected weak mineralization
in the underlying dacitic unit.
Holes BC-1, BC-2 and BC-3 were drilled on the southeast corner of the
Barranco Colorado area, Curipamba Project, located approximately 10 km west
from El Domo deposit (Figure 2). Previous detailed surface geologic mapping
identified large phyllic altered andesite and hydrothermal breccias boulders
that averaged 0.5- 8.3 g/t Au, 0.05 - 0.75% Cu, 0.05 - 0.69 % Zn. Soil
sampling identified anomalous values of gold, copper and zinc: up to 0.3 ppm
Au, 600 ppm Cu, and 1000 ppm Zn. Also, geophysical anomalies were recognized
in the induced polarization survey completed in April 2017, which defined the
three initial targets. These holes encountered moderately phyllic alterated
volcanic flows with dioritic and microdioritic intrusions and an acid unit at
the base. Holes BC-1 and BC 2 intersected sporadic decimetric and metric
channels of silicified crackle breccias with pyrite and traces of chalcopyrite
and sphalerite. BC-2 had the better accumulation of this mineralization with
an interval of up to 25 metres in thickness which includes a few sporadic
sphalerite and chalcopyrite filled veins of up to 2cm in thickness. In
addition, the lower part of the BC-1 intersected about 30 meters of a
Dacite/Rhyolite unit with a moderate anhydrite stockwork and up to 7%
disseminated pyrite which exhibits similarities to the underlying dacitic unit
of the El Domo deposit. In conclusion, the surface findings, the remaining
geophysical anomalies and these recent drill holes results show the potential
for massive sulphides in this area. More exploration is warranted in Barranco
Colorado.
TABLE 1
HOLE ID EAST           NORTH            ELEV (M)         AZIMUTH     DIP     
DEPTH (M)        ACCUMULATED

DEPTH
---                                                                             
                          -----

CURI-235              695351.79       9855236.17          1052.99         
145     -66           338.60              338.60
--------              ---------       ----------          -------         
---     ---           ------              ------

CURI-236              695437.07       9855437.60           998.38         
270     -90           215.65              554.25
--------              ---------       ----------           ------         
---     ---           ------              ------

CURI-237              695026.00       9855275.00           906.20          
90     -90           537.80             1092.05
--------              ---------       ----------           ------         
---     ---           ------             -------

CURI-238              695600.00       9855400.00          1075.00         
270     -85           330.60             1422.65
--------              ---------       ----------          -------         
---     ---           ------             -------

CURI-239              695762.00       9855310.00          1115.00         
270     -80           300.00             1722.65
--------              ---------       ----------          -------         
---     ---           ------             -------

BC-01                 684950.00       9851921.00           187.00         
270     -75           417.10             2139.75
-----                 ---------       ----------           ------         
---     ---           ------             -------

BC-02                 684780.00       9851902.00           151.00         
315     -75           167.75             2307.50
-----                 ---------       ----------           ------         
---     ---           ------             -------

BC-03                 684725.00       9852050.00           143.00         
270     -75           122.80             2430.30
-----                 ---------       ----------           ------         
---     ---           ------             -------
(x)PSAD_1956_UTM_Zone_17S
Figure 1El Domo Deposit - Pierce Point Map
Figure 2Barranco Colorado Samples and Drill Hole Map
TABLE 2
SIGNIFICANT INTERSECTIONS
HOLE ID   FROM (M)                       TO (M)                   WIDTH 
(M)       AU (G/T)     AG (G/T)     CU (%)  PB (%) ZN (%)
-------   -------                        -----                    
--------        --------     --------     -----    -----   -----

CURI-235  No significant mineralization encountered in this hole.
--------  -------------------------------------------------------

CURI-236                        153.16                    155.46              
2.3          1.42         51.73      2.45     0.11   5.59
--------                        ------                    ------              
---          ----         -----      ----     ----   ----

CURI-237                          56.5                     93.29            
36.79          5.00         53.40      2.93     0.21   2.90
--------                          ----                     -----            
-----          ----         -----      ----     ----   ----

including                         56.5                      67.6             
11.1          1.49         10.77      0.73     0.17   0.70
---------                         ----                      ----             
----          ----         -----      ----     ----   ----

including                        70.87                     93.29            
22.42          7.43         82.08      4.43     0.27   4.41
---------                        -----                     -----            
-----          ----         -----      ----     ----   ----

CURI-238  No significant mineralization encountered in this hole.
--------  -------------------------------------------------------

CURI-239  No significant mineralization encountered in this hole.
--------  -------------------------------------------------------

BC-1      No significant mineralization encountered in this hole.
----      -------------------------------------------------------

BC-2                             53.76                     56.72             
2.96          1.41          1.55      0.11     0.01   0.85
----                             -----                     -----             
----          ----          ----      ----     ----   ----

BC-3      No significant mineralization encountered in this hole.
----      -------------------------------------------------------
Widths presented in Table 2 are downhole core lengths. Where possible,
true width estimates are noted in the text.
A rigorous chain-of-custody and quality assurance/quality control program
that included the insertion of certified standard control samples and blanks,
and re-analysis of samples with high levels (overlimit) of gold, copper and
zinc, was applied to the NQ-diameter, rock-sawn half-core samples. All samples
were analyzed by Inspectorate Services Perú S.A.C. (Bureau Veritas), a
certified ISO 17025 and ISO 9001:2000 laboratory.
As part of the program's sample quality assurance, twin samples were
taken on all holes as described below. The samples were part of a Brecciated
Dacite and gave the following results (Table 3):
TABLE 3

HOLE         SAMPLE        FROM(M)        TO(M)        LENGTH(M)             
AU(PPM)            AG(PPM)         CU(PPM)        PB(PPM)        ZN(PPM)(equal 
sign)(equal sign)(equal sign)(equal sign)         (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)        (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)         (equal 
sign)(equal sign)(equal sign)(equal sign)         (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)              (equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)             (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)          (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)         (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)         (equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)

CURI-235            170842         288.00       289.40                   
1.40               0.085              0.2               3               
7          6
--------

170843        288.00         289.40         1.40                  
0.089                 0.3                4               8               8
------        ------         ------         ----                  
-----                 ---              ---             ---             ---

CURI-236            170961         155.46       157.30                   
1.84               0.037              0.3             200         
<5             62
--------

170962        155.46         157.30         1.84                  
0.023                 0.2               91        <5                   34
------        ------         ------         ----                  
-----                 ---              ---        ---                 ---

CURI-238      

" BC-Salazar-Curipamba   09-08 2155
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Salazar Intersects 22.42 Metres (True) Averaging 7.4 G/T Gold, 82.1 G/T
Silver, 4.43% Copper and 4.41% Zinc in the El Domo Deposit and
Succesfully Ends the Phase V Diamond Drilling Program at its Curipamba
Project@

VANCOUVER, Sept. 8, 2017 /CNW/ - Salazar Resources Limited (TSX.V: SRL;
FRANKFURT: CCG.F) ("Salazar" or the "Company") is pleased to report results
from the last eight holes (2,430.30 metres) of the phase V diamond drill
program that was completed on the Company's 100-per-cent owned (21,500 ha)
Curipamba volcanogenic massive sulphide ("VMS") project in Ecuador. Five holes
represent new exploratory and development drilling around the El Domo resource
and were not included in the latest El Domo resource estimate which was
released on January 16, 2015. Three holes were drilled in the Barranco
Colorado area, which is within the Curipamba project, to test regional
exploration targets.
HIGHLIGHTS:
<<

--  Hole CURI-236
o 2.30 metres (true) averaging 1.42 g/t gold, 51.7 g/t silver, 2.45% copper
and 5.59 % zinc in massive and semi-massive chalcopyrite and pyrite.
>>
<<

--  Hole CURI-237
o 36.79 metres averaging 5.0 g/t gold, 53.4 g/t silver, 2.93% copper and 2.9 %
zinc; which includes two intervals:
(number sign) 11.10 metres averaging 1.5 g/t gold, 10.77g/t silver, 0.73% 
copper and
0.70% zinc in Grainstone (a marker unit in the immediate hanging wall of
the massive sulphides) with clasts of semi-massive sulphides
(number sign) 22.42 metres averaging 7.4 g/t gold, 82.1 g/t silver, 4.43% 
copper and
4.41% zinc in massive and semi-massive sphalerite, chalcopyrite and
pyrite.
>>
<<

--  Successful finalization of the phase V drilling program
>>
PROGRAM RESULTS:
The latest eight holes (2,430.30 metres) (Table 1) were drilled as part
of the planned 40-hole (10,000 metres) drill program that was completed with
the purpose of expanding the El Domo VMS deposit and exploring its margins, as
well as testing geophysical anomalies and surface showings around the
Curipamba Project (Figure 1). The drilling activities of the program ended on
August 7th, 2017.
A total of 36 holes (10,472.62 metres) were drilled. Thirty-three (33)
holes were drilled in and around the El Domo deposit and three (3) holes were
drilled in the Barranco Colorado area. In addition to the significant
intersections being reported here, five (5) other holes intersected
significant mineralization: CURI-213, CURI-218, CURI-224, CURI-231and CURI-234
( News Releases of March, May and August 2017).
Hole CURI-236 intersected 2.30 metres averaging 1.42 g/t gold, 51.73 g/t
silver, 2.45% copper and 5.59% zinc in massive and semi-massive of
chalcopyrite and pyrite. This intersection is located in the northeastern
sector of the El Domo deposit, approximately 50 metres south from the CURI-231
which cut 3.09 metres (3.08 m true) averaging 0.60 g/t gold, 9.40 g/t silver,
6.43% copper & 0.18% zinc (news release of August 14, 2017 ). This new
intersection extends the previously interpreted mineralization trend
identified by CURI-224, CURI-198 and CURI-231 an additional 50 metres to the
south, making this new trend a total length of approximately 200m. This trend
will most likely be connected to the main resource body given that the
CURI-236 intersection is only 60 metres northeast from the CURI-166, which
previously marked the edge of the latest El Domo resource estimate.
Hole CURI-237 was a deep exploratory hole that was collared approximately
30 meters north east from the CURI-106 which was drilled in April of 2010 and
intersected 36.33 metres 3.74 g/t gold, 35.85 g/t silver, 4.39 % copper and
1.5% zinc in the west-central sector of the El Domo deposit. CURI-237 was
drilled vertically down to 537.80 metres to test the potential for additional
underlying VMS depositional lenses and the potential for strong feeder zones
related to the existing El Domo VMS body. CURI-237 intersected 36.79 metres
averaging 5.0 g/t gold, 53.4 g/t silver, 2.93% copper and 2.9 % zinc; which
includes two intervals:
<<

--  11.10 metres averaging 1.5 g/t gold, 10.77g/t silver, 0.73% copper and
0.70% zinc in grainstone with clasts of semi-massive sulphides. The
Grainstone is a marker unit in the immediate hanging wall of the VMS
mineralization.
--  22.42 metres averaging 7.4 g/t gold, 82.1 g/t silver, 4.43% copper and
4.41% zinc in massive and semi-massive sulphide of sphalerite,
chalcopyrite and pyrite.
>>
This intersection represents an in-fill addition to the known El Domo
resource. Below the El Domo deposit drilling intersected the usual altered and
mineralized dacitic unit, followed by the rhyolitic flow which is the deepest
formation reached in several previous holes. Below the rhyolite another large
dacitic unit with sporadic sedimentary lenses was intersected with yet another
rhyolitic flow at the base. The hole intersected weak sporadic sulphide
mineralization with sphalerite, chalcopyrite and pyrite all the way down to
the end of the hole in the form of veinlets and fracture fillings. In
addition, this hole showed that the basement marine volcanic rocks, Piñon
Formation, which was believed to be at shallower depths was not encountered
suggesting that the mineralization and alteration system extends as deep as
420 metres below the El Domo deposit.
Fredy Salazar, President and CEO, commented: "The culmination of our
Phase V drilling program marks an important landmark in our company and the
development of our Curipamba project. As a result, the El Domo resource has
been better defined and important mineralization extensions have been
intersected that will add significant value to the previously defined
reserves. Also, the Barranco Colorado holes have shown us the additional
exploration potential on the Curipamba project outside of El Domo. Salazar is
very satisfied with the results and looks forward to the future possibilities
that this drilling campaign has opened for us."
OTHER RESULTS:
CURI-235 collared on the same platform as CURI-234 (6.87 metres (6.45 m
true) averaging 1.47 g/t gold, 10.9 g/t silver, 7.42% copper, 1.01% zinc (news
release of August 14, 2017) was drilled southwesterly to test the possible
extension of CURI-234 mineralization towards the east. It intersected a
massive gypsum interval and the underlying dacitic unit. Gypsum frequently
occurs as part of the outer shell stockwork mineralization.
CURI-238 and CURI-239 were drilled to explore the eastern limits of the
El Domo mineralization. CURI-238 was drilled vertically approximately 150
metres from the El Domo resource. CURI-239 was drilled westerly around 200
metres from the El Domo resource. Both holes intersected weak mineralization
in the underlying dacitic unit.
Holes BC-1, BC-2 and BC-3 were drilled on the southeast corner of the
Barranco Colorado area, Curipamba Project, located approximately 10 km west
from El Domo deposit (Figure 2). Previous detailed surface geologic mapping
identified large phyllic altered andesite and hydrothermal breccias boulders
that averaged 0.5- 8.3 g/t Au, 0.05 - 0.75% Cu, 0.05 - 0.69 % Zn. Soil
sampling identified anomalous values of gold, copper and zinc: up to 0.3 ppm
Au, 600 ppm Cu, and 1000 ppm Zn. Also, geophysical anomalies were recognized
in the induced polarization survey completed in April 2017, which defined the
three initial targets. These holes encountered moderately phyllic alterated
volcanic flows with dioritic and microdioritic intrusions and an acid unit at
the base. Holes BC-1 and BC 2 intersected sporadic decimetric and metric
channels of silicified crackle breccias with pyrite and traces of chalcopyrite
and sphalerite. BC-2 had the better accumulation of this mineralization with
an interval of up to 25 metres in thickness which includes a few sporadic
sphalerite and chalcopyrite filled veins of up to 2cm in thickness. In
addition, the lower part of the BC-1 intersected about 30 meters of a
Dacite/Rhyolite unit with a moderate anhydrite stockwork and up to 7%
disseminated pyrite which exhibits similarities to the underlying dacitic unit
of the El Domo deposit. In conclusion, the surface findings, the remaining
geophysical anomalies and these recent drill holes results show the potential
for massive sulphides in this area. More exploration is warranted in Barranco
Colorado.
TABLE 1
HOLE ID EAST           NORTH            ELEV (M)         AZIMUTH     DIP     
DEPTH (M)        ACCUMULATED

DEPTH
---                                                                             
                          -----

CURI-235              695351.79       9855236.17          1052.99         
145     -66           338.60              338.60
--------              ---------       ----------          -------         
---     ---           ------              ------

CURI-236              695437.07       9855437.60           998.38         
270     -90           215.65              554.25
--------              ---------       ----------           ------         
---     ---           ------              ------

CURI-237              695026.00       9855275.00           906.20          
90     -90           537.80             1092.05
--------              ---------       ----------           ------         
---     ---           ------             -------

CURI-238              695600.00       9855400.00          1075.00         
270     -85           330.60             1422.65
--------              ---------       ----------          -------         
---     ---           ------             -------

CURI-239              695762.00       9855310.00          1115.00         
270     -80           300.00             1722.65
--------              ---------       ----------          -------         
---     ---           ------             -------

BC-01                 684950.00       9851921.00           187.00         
270     -75           417.10             2139.75
-----                 ---------       ----------           ------         
---     ---           ------             -------

BC-02                 684780.00       9851902.00           151.00         
315     -75           167.75             2307.50
-----                 ---------       ----------           ------         
---     ---           ------             -------

BC-03                 684725.00       9852050.00           143.00         
270     -75           122.80             2430.30
-----                 ---------       ----------           ------         
---     ---           ------             -------
(x)PSAD_1956_UTM_Zone_17S
Figure 1El Domo Deposit - Pierce Point Map
Figure 2Barranco Colorado Samples and Drill Hole Map
TABLE 2
SIGNIFICANT INTERSECTIONS
HOLE ID   FROM (M)                       TO (M)                   WIDTH 
(M)       AU (G/T)     AG (G/T)     CU (%)  PB (%) ZN (%)
-------   -------                        -----                    
--------        --------     --------     -----    -----   -----

CURI-235  No significant mineralization encountered in this hole.
--------  -------------------------------------------------------

CURI-236                        153.16                    155.46              
2.3          1.42         51.73      2.45     0.11   5.59
--------                        ------                    ------              
---          ----         -----      ----     ----   ----

CURI-237                          56.5                     93.29            
36.79          5.00         53.40      2.93     0.21   2.90
--------                          ----                     -----            
-----          ----         -----      ----     ----   ----

including                         56.5                      67.6             
11.1          1.49         10.77      0.73     0.17   0.70
---------                         ----                      ----             
----          ----         -----      ----     ----   ----

including                        70.87                     93.29            
22.42          7.43         82.08      4.43     0.27   4.41
---------                        -----                     -----            
-----          ----         -----      ----     ----   ----

CURI-238  No significant mineralization encountered in this hole.
--------  -------------------------------------------------------

CURI-239  No significant mineralization encountered in this hole.
--------  -------------------------------------------------------

BC-1      No significant mineralization encountered in this hole.
----      -------------------------------------------------------

BC-2                             53.76                     56.72             
2.96          1.41          1.55      0.11     0.01   0.85
----                             -----                     -----             
----          ----          ----      ----     ----   ----

BC-3      No significant mineralization encountered in this hole.
----      -------------------------------------------------------
Widths presented in Table 2 are downhole core lengths. Where possible,
true width estimates are noted in the text.
A rigorous chain-of-custody and quality assurance/quality control program
that included the insertion of certified standard control samples and blanks,
and re-analysis of samples with high levels (overlimit) of gold, copper and
zinc, was applied to the NQ-diameter, rock-sawn half-core samples. All samples
were analyzed by Inspectorate Services Perú S.A.C. (Bureau Veritas), a
certified ISO 17025 and ISO 9001:2000 laboratory.
As part of the program's sample quality assurance, twin samples were
taken on all holes as described below. The samples were part of a Brecciated
Dacite and gave the following results (Table 3):
TABLE 3

HOLE         SAMPLE        FROM(M)        TO(M)        LENGTH(M)             
AU(PPM)            AG(PPM)         CU(PPM)        PB(PPM)        ZN(PPM)(equal 
sign)(equal sign)(equal sign)(equal sign)         (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)        (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)         (equal 
sign)(equal sign)(equal sign)(equal sign)         (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)              (equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)             (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)          (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)         (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)         (equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)

CURI-235            170842         288.00       289.40                   
1.40               0.085              0.2               3               
7          6
--------

170843        288.00         289.40         1.40                  
0.089                 0.3                4               8               8
------        ------         ------         ----                  
-----                 ---              ---             ---             ---

CURI-236            170961         155.46       157.30                   
1.84               0.037              0.3             200         
<5             62
--------

170962        155.46         157.30         1.84                  
0.023                 0.2               91        <5                   34
------        ------         ------         ----                  
-----                 ---              ---        ---                 ---

CURI-238            170978         288.85       290.80                   
1.95               0.064              1.2             173              36       
1073
--------

170979        288.85         290.80         1.95                  
0.075                   1               53              37             381
------        ------         ------         ----                  
-----                 ---              ---             ---             ---

CURI-239            170988         280.86       281.80                   
0.94               0.067              7.8              18             
236        633
--------

170989        280.86         281.80         0.94                  
0.056                11.6               16             216             586
------        ------         ------         ----                  
-----                ----              ---             ---             ---

BC-01               170826         401.80       403.33                   
1.53        <0.005             <0.2                  23         <5           <5
-----

170827        401.80         403.33         1.53           <0.005              
<0.2                     23        <5              <5
------        ------         ------         ----           ------              
----                    ---        ---            ---

BC-02               170945         154.07       156.00                   
1.93               0.054              0.7              75              
39        362
-----

170946        154.07         156.00         1.93                  
0.051                 0.8               81              37             343
------        ------         ------         ----                  
-----                 ---              ---             ---             ---
The scientific and technical information contained in this news release
has been reviewed and approved by Kieran Downes, Ph.D., P.Geo. a Qualified
Person as defined by National Instrument 43-101.
ON BEHALF OF THE BOARD OF SALAZAR RESOURCES LIMITED
"Fredy Salazar"
Fredy Salazar, President & CEO
Salazar Resources Limited
Salazar Resources Ltd. is a publicly-listed (TSXV: SRL) mineral resource
company engaged in the exploration and development of new highly prospective
areas in Ecuador. Led by a senior Ecuadorian management team and most notably
by its namesake Fredy Salazar, this team has been instrumental in other major
discoveries throughout Ecuador, including Aurelian's Fruta Del Norte
discovery, IAMGold's Quimsacocha Deposit, Mozo Deposit, Ex Newmont's Cangrejos
Project and International Minerals Rio Blanco and Gaby Deposit. Being an
Ecuadorian based company gives the Company a strategic advantage enabling the
Company to complete exploration at a rapid pace. With an excellent property
portfolio (4 projects - 36,269 hectares), good geopolitical positioning and a
number of strategic corporate and financial partnerships, Salazar has
positioned itself to be a strategic player in Ecuador.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
This press release contains "forward -looking information" within the
meaning of applicable Canadian securities laws. All statements included
herein, other than statements of historical fact, are forward-looking
information and such information involves various risks and uncertainties.
Forward-looking information herein includes, but is not limited to, statements
that address activities, events or developments that the Company expects or
anticipates will or may occur in the future, including such things as the
execution of the Phase V drilling program. Such forward-looking information is
based on a number of material factors and assumptions. Although the Company
has attempted to identify important factors that could cause actual actions,
events or results to differ materially from those described in forward-looking
information, there may be other factors that cause actions, events or results
not to be as anticipated, estimated or intended. There can be no assurance
that such information will prove to be accurate, and actual results and future
events could differ materially from those anticipated in such information. A
description of assumptions used to develop such forward-looking information
and a description of risk factors that may cause actual results to differ
materially from forward-looking information can be found in the Company's
disclosure documents on the SEDAR website at www.sedar.com. Accordingly,
readers should not place undue reliance on forward-looking information. The
Company does not undertake to update any forward-looking information except in
accordance with applicable securities laws.
SOURCE Salazar Resources Limited



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/September2017/08/c1363.html

-0-                           09/08/2017
/For further information: Salazar Resources Ltd.,
ir(at)salazarresources.com, www.salazarresources.com/
(SRL.)

CO:  Salazar Resources Limited
ST:  British Columbia
IN:  MIN MNG
SU:

-30-