Source	CANADA NEWSWIRE
Date	09/11/2017
Time	06:05:26 AM

Company	 Mirasol Resources Ltd.
Title	Mirasol Resources Reports Best Results to Date from Yamana Gold Drilling
at the Atlas Project, Gorbea JV, Mio - Pliocene Mineral Belt of Northern
Chile





    CDNX Symbol: MRZ











Press Release




" BC-Mirasol-Yamana-result   09-11 1615
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Mirasol Resources Reports Best Results to Date from Yamana Gold Drilling
at the Atlas Project, Gorbea JV, Mio - Pliocene Mineral Belt of Northern
Chile@

1.07 g/t Au over 114 m, including 2.49 g/t Au over 36 m down hole
VANCOUVER, Sept. 11, 2017 /CNW/ - Mirasol Resources Ltd. (TSX-V: MRZ,
OTCPK: MRZLF "Mirasol", "The Company") is pleased to report results from the
second season of drilling by Yamana Gold at the Atlas Project, Gorbea JV in
the Mio-Pliocene Belt of Northern Chile.
Current drill results at Gorbea include the best down-hole intersection
to date from the Atlas project, comprising 1.07 g/t Au intersected over 114 m,
including 2.49 g/t Au over 36 m in oxidized high sulphidation epithermal (HSE)
vuggy silica breccia. Drilling to-date at Atlas (Figure 1) has outlined Au
mineralization (the "Steam Heated Zone") in an area of 650 m by 125 m by over
a 200 m vertical interval (Figure 2). The Steam Heated Zone may represent a
body of Au+Ag mineralization that as defined to date is open to depth and
laterally in all directions outside the area of current drilling. As currently
known, the top of mineralization is located between approximately 255 to 310 m
depth beneath altered cap rocks, which is a characteristic in-common with
other recent, HSE gold discoveries elsewhere on this same mineral belt in
Chile. Further drilling is required at Atlas to determine the size, continuity
and grade of the Steam Heated Zone and to establish if extensions of this
mineralization occur closer to surface, where it may be accessible via open
pit mining.
Stephen Nano CEO of Mirasol stated "We are very encouraged by these
results that demonstrate the presence of a large, strongly mineralized and
deeply oxidized, HSE gold system at Atlas. Yamana has made significant
advances in understanding the controls on gold mineralization at the project
and are planning a large drill program this season to test for extensions of
the Steam Heated Zone mineralization and to test a number of other compelling
targets at Atlas and the other Gorbea JV projects."
During the last drill season (October 2016 to April 2017), Yamana
completed 2,558 m of diamond core drilling in seven holes (Figure 1, and Table
1 and Table 2; holes CATRAD0014 to 20) at the Atlas project. Total drilling
completed since inception of the Gorbea JV in May 2015 is over 8,704 m, and
Yamana's total exploration spend to May 2017 is approximately US$5.2M, against
the US$10 M required to trigger the 51% earn-in milestone over a maximum of 4
years. In addition, on May 12, 2017 Yamana made a US$400,000 option payment to
Mirasol Resources to continue the JV into its third year (see news release May
30, 2017).
Yamana also recently advised Mirasol that it has increased its 2017
Gorbea JV exploration budget by an additional US$700,000. The additional
exploration funds will be directed to drilling at the Atlas Steam Heated Zone
and other new targets at the project. Yamana is planning to re-commence
drilling at Atlas for the southern hemisphere 2017 spring field season in
October.
Last season's (October 2016 to April 2017) drill campaign at Atlas was
focused on a series of outcropping breccia bodies that were highlighted during
a pre-drill geological mapping campaign.
Best results from this drill campaign were received from holes 15 and 16
(Figure 2, Table 1) and include:
<<

--  114.1 m at 1.07 g/t Au and 1.78 g/t Ag, including 36 m at 2.49 g/t Au
and 3.08 g/t Ag (hole 15)
--  45.8 m at 0.32 g/t Au and 0.81 g/t Ag (hole 16)
>>

The intersection in hole 15 starts from 347 m down hole. Hole 16 is
interpreted to have drilled across the top of this same breccia body. Drill
holes 15 and 16 were drilled toward each other ("scissor holes") from the NW
and SE to cross each other at depth, testing a zone beneath an area of
coincident outcropping breccia, weakly anomalous soil geochemistry and a
geophysical anomaly that lies midway between drill holes 7 and 10 from last
season's drilling. Holes 7 and 10 returned the best results from the 2015-16
drill campaign including 40 m at 1.38 g/t Au, with 28 m at 1.82 g/t Au. The
mineralization at Atlas is interpreted to be oxidized to depths of more than
400 m downhole. Deep oxidation is considered a positive feature at Atlas as it
may suggest the potential for favourable metallurgical characteristics of the
mineralization at the project.
The geometric relationship of mineralization intersected in drill holes
7, 10, 15, and 16 (Figure 3) outlines a target zone with dimensions of 650 m
by 125 m by over a 200 m vertical interval, potentially representing a body of
Au+Ag mineralization that is open to depth and open in all directions
surrounding these holes. The top of the mineralization in hole 15 lies
approximately 255 to 310 m below surface from the RL of the drill collar or
the hill top, respectively. However, the geometry of the surface soil anomaly,
distribution of un-explained stream sediment gold anomalies and alteration,
suggest the target zone may extent to the south where topography is more
favourable, highlighting the possibility for mineralization to occur closer to
surface in this area.
Gold and silver mineralization in holes 15 and 16 is hosted in a
multiphase breccia body (Figure 3) characterized by intense quartz-alunite+/-
jarosite alteration with vuggy silica breccia clasts and a phase of late-stage
translucent barite hosting visible gold. This style of mineralization is
typical of HSE Au+Ag deposits elsewhere in the same belt of mineralization in
Chile (click here for information on these deposits). These deposits including
the recent multi-million ounce gold discoveries by Barrick Gold at Alturas
(6.8 M ounce resource at 1.00 g/t Au1) and Gold Fields at Salares Norte (3.8 M
ounce resource at 3.6 g/t Au and 43.8 M oz Ag at 53.1 g/t Ag2) located 70 km
due south of the Atlas project. At these projects gold is hosted in breccia
bodies and the vuggy silica altered wall rocks and was discovered by drilling
through thick geochemically barren alteration caps as seen at the Atlas
project.
Anomalous Au-Ag epithermal path finder elements and changes in alteration
mineral chemistry were also detected in a separate breccia body intercepted in
hole 20 at Atlas. Based on knowledge gained from modelling of results from the
Steam Heated Zone, the results from hole 20 suggest that further drilling is
warranted in this area to test for higher grade Au-Ag mineralization.
Information gathered from this season's exploration indicates that the
mineralization at Atlas is hosted in a cluster of phreatomagmatic and
hydrothermal breccia bodies that when combined outline a larger breccia
complex. Preliminary geological models show mineralization identified at Atlas
is hosted in both the breccia bodies and in stratabound zones of vuggy silica
developed in the wall rock adjoining the breccia. This association of
mineralization styles is seen at a number of other large HSE Au+Ag deposits in
the Mio-Pliocene age mineral belt that hosts the Atlas mineralization.
Mirasol invites investors to follow the Gorbea - Yamana JV story by
visiting www.mirasolresources.com and signing up to receive our new releases.
Stephen Nano, President and CEO of Mirasol, has approved the technical
content of this news release and is a Qualified Person under NI 43 -101.
Quality Assurance/Quality Control of the Gorbea exploration program:
Under the terms of the Gorbea Agreement, all exploration is managed by
Yamana. All pre-Joint Venture exploration on the projects was supervised by
Mirasol CEO Stephen C. Nano, who is the Qualified Person under NI 43-101. All
information generated from the Gorbea Joint Venture program is reviewed and
validated by Mirasol prior to release. The technical interpretations presented
here are those of Mirasol Resources Ltd.
Yamana applies industry standard exploration methodologies and
techniques. All geochemical rock and drill samples are collected under the
supervision of Yamana's geologists in accordance with industry practice.
Geochemical assays are obtained and reported under a quality assurance and
quality control (QA/QC) program. Samples are dispatched to an ISO
9001:2000-accredited laboratory in Chile for analysis. Assay results from
drill core samples may be higher, lower or similar to results obtained from
surface samples due to surficial oxidation and enrichment processes or due to
natural geological grade variations in the primary mineralization.
Forward Looking Statements: The information in this news release contains
forward looking statements that are subject to a number of known and unknown
risks, uncertainties and other factors that may cause actual results to differ
materially from those anticipated in our forward-looking statements. Factors
that could cause such differences include: changes in world commodity markets,
equity markets, costs and supply of materials relevant to the mining industry,
change in government and changes to regulations affecting the mining industry.
Forward-looking statements in this release include statements regarding future
exploration programs, operation plans, geological interpretations, mineral
tenure issues and mineral recovery processes. Although we believe the
expectations reflected in our forward-looking statements are reasonable,
results may vary, and we cannot guarantee future results, levels of activity,
performance or achievements. Mirasol disclaims any obligations to update or
revise any forward-looking statements whether as a result of new information,
future events or otherwise, except as may be required by applicable law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
___________________________1 Barrick Gold Corporation. (2016). Annual
Report 2016.2 Gold Fields. (2016). The Gold Fields Mineral Resource and
Mineral Reserve Supplement to the Integrated Annual Report 2016.
SOURCE Mirasol Resources Ltd.



View original content:
http://www.newswire.ca/en/releases/archive/September2017/11/c1235.html

-0-                           09/11/2017
/For further information: Stephen Nano, President and CEO or Jonathan
Rosset, Manager of Corporate Development, Tel: +1 (604) 602-9989, Email:
contact(at)mirasolresources.com, Website: www.mirasolresources.com/
/Web Site: http://www.mirasolresources.com /
(MRZ. MRZLF)

CO:  Mirasol Resources Ltd.
ST:  British Columbia
IN:  MNG
SU:  JVN

-30-