Source	MARKET NEWS
Date	09/12/2017
Time	05:46:33 AM

Company	 Algold Resources Ltd.
Title	Intercepts 
6.84 g/t Au over 15 Meters at Eleonor





    CDNX Symbol: ALG











Press Release





ALGOLD RESOURCES LTD ("ALG-V;ALGDF-0")
- Intercepts 6.84 g/t Au over 15 Meters at Eleonore

ALGOLD RESOURCES LTD. ("Algold" or the "Corporation") announced
additional assay results from the diamond ("DDH") and
reverse-circulation ("RC") drilling carried out on its Tijirit property
("Tijirit") in Mauritania as part of the Corporation's Phase III
25,000-meter drilling campaign. The results, which include 6.84 g/t Au
over 15 meters, continue to demonstrate the high-grade nature and the
continuity of the mineralization, both near surface and at depth, over
the 3.5-kilometer strike length of the Eleonore zone (Figure 1).

Highlights*

//st

* RC T17RC107 (Eleonore South) - 6.84 g/t Au over 15 m, including 24.00
g/t
Au over 4 m, approximately 40 meters below the surface and 2.16 g/t Au
over 8 m, including 6.04 g/t Au over 2 m, approximately 100 meters
below
the surface (Figure 2).
* RC T17RC122 (Eleonore South - new sub-zone) - 8.16 g/t Au over 5 m,
including 28.00 g/t Au over 1 m, approximately 50 meters below the
surface (Figure 2).
* DDH T17RD139 (Eleonore South) - 21.53 g/t Au over 1.8 m at
approximately
115 meters below the surface (Figure 2).
* DDH T17RD002 (Eleonore South) - 10.24 g/t Au over 3.7 m at
approximately
130 meters below the surface (Figure 2).
* DDH T17DD016 (Eleonore North) - 14.62 g/t Au over 3.3 m at
approximately
85 meters below the surface (Figure 3) (Photo 1).
* RC T17RC109 (Eleonore North) - 5.76 g/t Au over 2 m at approximately 95
meters vertical depth (Figure 3). This hole extends the Eleonore North
zone by 100 meters.
* RC T17RC115 (Eleonore Central) - 2.70 g/t Au over 7 m, including 8.06
g/t
Au over 2 m, at approximately 35 meters below the surface (Figure 4).

//et

*All intersections reported are down-hole lengths.

Eleonore South
Hole T16RC107 (section E8300), located approximately 50 meters
south of T17RC045 (14.1 g/t Au over 10 m, referenced in Algold's press
release dated April 25, 2017) returned two significant near-surface
mineralized intervals. Hole T16RC107 was orientated at a more optimal
bearing than T17RC045 and served to confirm the north to
north-northeast strike direction of the mineralization. With surface
outcrop masked by a transported overburden, the intersection of these
gold-bearing structures confirms the continuity of high-grade
mineralization associated with kilometer-long shear zones at Eleonore
South zone.

Sixty meters south of hole T17RC107, diamond tail hole T17RD002
(section 8200) was drilled to test for potential plunging high-grade
structures. The hole successfully intersected the vertically dipping
mineralized zone identified in hole T17RC003 and although the result
was not significant, it does suggest that higher-grade, wider
mineralized plunges are possible. Mineralization was also confirmed 50
meters north of hole T17RC045 in hole T17RC112, (Section E8400), which
remains open along strike to the north.

Five hundred meters south of hole T17RC045, diamond tail hole
T17RD139 (section E7880) intersected two gold-rich zones, on the same
structure, 116 meters and 140 meters below the surface. Screen fire
assays confirmed the presence of coarse gold ()105m) as shown in Photo
2 below.

Hole T17RC122 represents a new discovery and the most easterly
mineralized area intersected at Eleonore South. The area displays an
assemblage similar to other Eleonore mineralization identified to date
with quartz, biotite and pyrite associated with local shearing.  The
structure is believed to be dipping near vertically. Results of recent
drilling carried out to test the strike and down-dip extensions of the
structure are still pending.

Eleonore North

In DDH T17DD016, (section 9840) a steeply-dipping visible
gold-bearing quartz vein was intersected at 109 meters.  The gold was
finely disseminated along the selvages of a chlorite-biotite-pyrrhotite
alteration zone. The core drill hole confirms the vertical dip of the
structure and is the deepest intersection on this vein to date, at 85
meters below the surface. The vein remains open at depth.

Hole T17RC109 (section 10600) intersected a high-grade quartz vein
on the shallow-dipping northern most vein, currently identified in the
main Eleonore area.  This hole confirms that the mineralization is
still open at depth, with this intercept being 50 meters down dip of
the mineralization intersected in hole T17RC059.

Drilling Program

The Phase III 20,000-meter RC and 5,000-meter DDH drilling program
was initiated on February 1, 2017 with the objective to further
delineate the high-grade gold deposit. The Phase III drilling program
concluded on August 25, 2017 with 182 RC holes, 18 DDH and 30 RC
pre-collar/diamond tails completed for a total of 24,205 meters of RC
and 5,930 meters of diamond drilling.

As of September 1, 2017, Algold had collected 16,188 samples
(excluding QA/QC) as part of the Phase III drilling program, with 9,522
samples having been sent to the SGS Bamako facilities for analysis.
Algold is in receipt of 8,975 assay results, with 7,213 samples still
pending (excluding QA/QC).

In order to reduce future processing time for assay results
analysis, a Mobile Site Preparation Unit (MSPU) managed by SGS has been
installed on the Tijirit property. The MSPU laboratory became
operational in late August and is expected to increase efficiency and
reduce lag time in the preparation and shipment of assay samples,
thereby reducing overall turnaround time for assay results.

//st

Table 1: Assay Results - Phase III Drilling Program

Hole ID  Prospect  East    North   From   To (m)  Vert- Aver- Width Sec-
Comments
UTM     UTM     (m)            ical  age   ***   tion
Depth* Grade (m)   Line
***
(g/t
Au)



T17DD016 Eleonore  9588.53 9845.13 109.00 112.30  84    14.62 3.30  9840
N

T17RC109 Eleonore  979.52  1246.28 123.00 125.00  95    5.76  2.00  10600
N

T17RC110 Eleonore  9761.70 9841.18 113.00 115.00  88    3.37  2.00  9840
N

T17RC113 Eleonore  9766.47 8798.93 135.00 138.00  102   1.94  3.00  8790
C

T17RC115 Eleonore  9751.04 8921.66 45.00  52.00   37    2.70  7.00  8920
C

Including       47.00  49.00         8.06  2.00
T17RC116 Eleonore  9923.85 8998.34 130.00 133.00  102   2.24  3.00  9000
C

T17RC117 Eleonore  9778.86 8995.46 42.00  51.00   35    1.37  9.00  9000
C

T17RD081 Eleonore  9908.74 9160.51 38.00  44.00   32    1.79  6.00  9160
C
Shallow (45 deg.) dipping mineralization, sample with VG

60.50  62.00   47    4.99  1.50



T17RC107 Eleonore  9933.87 8322.60 42.00  57.00   37    6.84  15.00 E8320
S
50 m south of T17RC045 (14 g/t Au of 10 m)

Including                 42.00  46.00        24.00   4.00

117.00 125.00   95    2.16   8.00

Including                118.00 120.00         6.04   2.00

T17RC122 Eleonore  10211.0 7850.56 62.00  67.00   50    8.16   5.00  E7350
S
New vein discovery

Including                 63.00  64.00        28.00   1.00

T17RC126 Eleonore  9935.77 8299.70 38.00  42.00   31    1.88   4.00  8300
S
New vein discovery

T17RD002 Eleonore  9823.55 8201.96 168.00 171.70  131   10.24 3.70  8200
S

Including                 168.5  170.00         9.90 1.50

T17RD044 Eleonore  9797.84 8298.59 155.75 159.75  122   2.81  4.00  8300
S
186.60 189.65  145   5.81  3.05
145 m below surface - 50 m below T17RC107.

Including                 188.00 188.55       28.30  0.55
VG-bearing zone

T17RD139 Eleonore  10004.5 7869.99 148.75 150.55  116  21.53  1.80  E7880
S
Incl. 64 g/t Au over 0.6 m

182.00 184.4   143   5.14  2.40

Including                 183.00 184.4         7.99  1.40

//et

//st

*Vertical depth of intersection below RL collar.

**Weighted average grade, composite based on a minimum grade of 0.3 g/t
Au with an internal dilution of 0.005 g/t Au over 2 m and an edge grade
of 0.25 g/t Au permitted.

***Down-hole length (believed to be close to true width).

No capping of higher values has been applied.

Note: Complete assay results are available on Algold's website
(www.algold.com).

//et

Detailed geological descriptions of all mineralized zones can be
found on Algold's website (www.algold.com) and on SEDAR (www.sedar.com)
in the report entitled "Algold 43-101 Technical Report: Tijirit Maiden
Mineral Resources Estimates for the Tijirit Gold Project in
Mauritania".

Quality Assurance / Quality Control (QA/QC)Analytical work for
drill core and chips, geochemical samples and rock chip samples is
carried out at the independent SGS Laboratories Ltd. in Bamako, Mali.
The 50 g fire assay with ASS finish analytical services are accredited
by SANAS and are carried out with a quality assurance protocol in line
with ISO 17025:2005. Samples are stored at the Corporation's field
camps and put into sealed bags until delivered by a geologist on behalf
of Algold to the laboratory in Bamako, Mali, where samples are prepared
and analyzed. Until the end of 2016, samples were analyzed at ALS's
facility in Loughrea, Ireland. Beginning in 2017, samples are analyzed
at SGS Laboratory, Bamako. Samples are logged in the tracking system,
weighed, dried and finely crushed to better than 70%, passing a 2 mm
(Tyler 9 mesh, US Std. No.10) screen. A split of up to 1,000 g is taken
and pulverized to better than 85%, passing a 75-micron (Tyler 200 mesh)
screen, and a 50-gram split is analyzed by fire assay with an AA
finish.  Anomalous samples greater than 5 g/t Au are re-analyzed by 50
g fire assay with gravimetric finish.  Selected samples may be
re-analyzed using a 1 kg cyanide leach (Bottle Roll) using "LeachWELL"
or the 1 kg screen fire assay method.  Blanks, duplicates and certified
reference material (standards) are inserted to monitor laboratory
performance during the analysis.

This press release has been reviewed for accuracy and compliance
under National Instrument 43-101 by Andre Ciesielski, DSc., PGeo.,
Algold Resources Ltd Lead Consulting Geologist and Qualified Person,
and Alastair Gallaugher, C.Geo. (Chartered Geologist and Fellow of the
Geological Society of London), BSc. Geology, Algold's Exploration
Manager in Mauritania, Qualified Persons as defined by NI 43-101
Standards of Disclosure for Mineral Projects. Andre Ciesielski has
further approved the scientific and technical disclosure in the news
release.

ABOUT ALGOLDAlgold Resources Ltd is focused on the exploration and
development of gold deposits in West Africa. The board of directors and
management team are seasoned resource industry professionals with
extensive experience in the exploration and development of world-class
gold projects in Africa.

FORWARD-LOOKING INFORMATIONThis press release contains and refers
to forward-looking information based on current expectations. All other
statements other than statements of historical fact included in this
release are forward-looking statements (or forward-looking
information). The Corporation's plans involve various estimates and
assumptions and its business is subject to various risks and
uncertainties. For more details on these estimates, assumptions, risks
and uncertainties, see the Corporation's most recent Management
Discussion and Analysis on file with the Canadian provincial securities
regulatory authorities on SEDAR at www.sedar.com. These forward-looking
statements are made as of the date hereof and there can be no assurance
that such statements will prove to be accurate. Forward-looking
statements are subject to significant risks and uncertainties, and
actual results and future events could differ materially from those
anticipated in such statements. Accordingly, readers should not place
undue reliance on forward-looking statements that are included herein,
except in accordance with applicable securities laws.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Algold Resources Ltd.

Website: www.algold.com

Francois Auclair M.Sc., PGeo, President & Chief Executive Officer
E-mail: f.auclair@algold.com
TEL: +1 (514) 889 5089

Alex Ball, Executive VP, Finance and Corporate Development


























TSX Venture closing price for ALG-V
Date: 2017/09/08
Closing Price: 0.19

TEL: +1 (647) 919 2227
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1725400020TS11725400928-05452820170912