Source	MARKET NEWS
Date	09/12/2017
Time	05:37:30 AM

Company	 Enforcer Gold Corp.
Title	104.68 Gpt 
Au Over 2.0 m From Channel Sampling O





    CDNX Symbol: VEIN











Press Release





ENFORCER GOLD CORP ("VEIN-V")
- 104.68 Gpt Au Over 2.0 m From Channel Sampling Of No. 2 Vein At
- The Montalembert Gold Project

Enforcer Gold Corp ("Enforcer" or the "Company") is pleased to
report results from channel sampling on the Galena, No. 2 and No. 3
veins at the Montalembert Gold Project.

The Galena and No. 2 veins are parallel, north-south striking and
steeply east-dipping shear zones separated by ~80 m. The No. 3 Vein is
located ~175 m south and along strike of the No. 2 Vein. The shear
zones vary in width and cut variably chloritized, carbonatized and
silicified basalt. They host quartz veins/stringers and trace to 5%
pyrite, pyrrhotite, trace chalcopyrite and galena and fine to coarse
free gold. Enforcer has been systematically exposing and channel
sampling along the strike extensions of the veins and peripheral to the
veins.

Of a total 116 sawn channels in the Galena-No.2-No.3 vein area, 27
were infill samples along the Galena Vein, 4 were cut over the trace of
the vein in the Galena North extension, 27 were cut over the No. 2
North extension, 8 were cut over the No. 2 South extension and 13 were
cut over multiple veins at the No. 3 Vein exposure. On the Galena North
exposure, the trace of the vein was lost into deep overburden, hence
channel sampling in this area was largely peripheral to the trace of
the structure. Significant results from the sampling are presented in
Table 1. Plan maps showing sample locations and assay highlights are
available on the Montalembert Map Gallery.

Based on Enforcer's preliminary interpretation, gold emplacement
at Montalembert is related to late-stage extensional quartz veining
that is typically at high angles to the main structures. The Company
has engaged a structural expert with SRK Consulting to perform a
structural analysis of the vein systems to better determine the nature
and controls to gold mineralization. The field study commenced on
September 11, 2017. Enforcer anticipates that this study will aid in
the targeting of high-grade gold shoots along the vein systems.

As previously noted, the grade and continuity of veining and
mineralization in shear-hosted gold deposits in the Abitibi can be
highly erratic. The nuggety nature of the gold distribution will remain
a challenge and potentially impact sampling results. Enforcer continues
to focus on the mineralized structures with the realization that
analytical results will be highly variable. The extension of the
structures and the presence of high-grade mineralization is the most
important factor in the Company's early evaluation of the vein systems.


As announced on August 30, 2017, Enforcer resumed diamond drilling
despite a continued backlog of assays at the lab. The situation has yet
to change as the Company awaits complete results for the first 10 holes
drilled.

President & CEO, Steve Roebuck, comments:

"We continue to be encouraged by the continuity of the shear zones
outside of the historical exposure limits and to find high-grade zones
of gold mineralization along the length of both veins. We expect that
the SRK study will greatly enhance our understanding of the vein
systems and focus our exploration moving forward."

Table 1. 2017 Channel Sampling - Significant Results

//st

Channel ID   Vein         UTM E       UTM N        Width (m)   Au Au (g/t)

MCH223505    No. 2        426657.19   5513783.49   2.0         2.46
North

MCH223511    No. 2        426657.27   5513782.05   1.8         3.92
North

MCH223516    No. 2        426658.01   5513779.80   1.0         0.51
North

MCH223523    No. 2        426657.02   5513774.17   2.1         0.77
North

MCH223539    No. 2        426656.21   5513770.19   1.0         13.50
North

MCH223576    No. 2        426655.61   5513778.66   1.0         105.00
North

MCH223606    Galena       426611.42   5513526.91   1.0         0.75

MCH225503    Galena       426613.92   5513566.15   1.0         1.16

MCH225509    Galena       426597.07   5513623.50   1.0         0.69

MCH225511    Galena       426595.32   5513631.35   1.0         2.36

MCH225513    Galena       426596.14   5513641.70   1.0         0.63

MCH225516    Galena       426596.01   5513651.64   2.0         2.41

MCH225522    Galena       426594.00   5513662.22   1.0         0.84
MCH225535    Galena       426591.52   5513681.45   2.0         0.70

MCH225544    Galena       426588.25   5513676.53   1.0         5.09

MCH225702    No. 2        426654.84   5513792.84   1.0         3,310.00
North

MCH225703    No. 2        426651.49   5513806.44   1.0         1.93
North

MCH225773    Galena       426576.68   5513749.10   1.0         2.77
North

MCH225851    No. 2        426696.60   5513615.20   1.1         0.91
South

MCH225867    No. 2        426662.72   5513777.42   0.8         0.67
North

MCH225874    No. 2        426659.50   5513776.13   1.0         0.67
North

MCH225881    No. 2        426655.72   5513770.22   1.0         0.73
North

MCH225889    No. 3        426690.38   5513477.96   1.2         0.98

MCH225904    No. 3        426692.86   5513470.41   1.1         1.87

MCH225909    No. 3        426694.92   5513468.20   0.9         3.45

MCH225935    No. 3        426703.22   5513458.82   1.0         0.54

MCH225996    No. 2        426656.85   5513785.77   2.0         104.68
North

//et

Qualified Person & QAQC

Independent geological engineer, Mr. Donald Theberge, MBA, PEng,
is a qualified person as defined by National Instrument 43-101 and has
reviewed and approved the content of this news release.

Channel samples were collected from bedrock exposures utilizing a
diamond-blade power saw. Channel samples are typically cut 2" wide and
2" deep and are cut perpendicular to the strike of the quartz-bearing
structures. True width is estimated to be 90-100% of cut width. Sample
preparation, fire assays (gravimetric finish) and metallic sieve assays
were performed by Activation Laboratories Ltd. of Ancaster, Ontario, an
ISO/IEC 17025 (CAN-P-1579) accredited testing laboratory. Details of
the analytical procedure and Enforcer's Quality Assurance/Quality
Control ("QAQC") program are available on the Enforcer website at:
Montalembert QAQC.

About Enforcer Gold Corp

Enforcer Gold Corp is earning a 100% interest in the Montalembert
Gold Project from Globex Mining Enterprises Inc. (TSX: GMX, FSE: GIMN,
OTCQX: GLBXF). The 7,300-hectare property is located 125 km west of
Chibougamau in Quebec's prolific Abitibi greenstone belt. The property
lies 5 km from a paved highway and hydro-electric power and has easy
access to skilled labour, fuel, accommodation and other
industry-related services, allowing for relatively low exploration
costs. Enforcer has committed over $2.2M to fund its 2017 exploration
program that is expected to run uninterrupted through late fall 2017.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

This news release contains "forward-looking statements" that are
based on expectations, estimates, projections and interpretations as at
the date of this news release. Forward-looking statements are
frequently characterized by words such as "plan", "expect", "project",
"intend", "believe", "anticipate", "estimate", "suggest", "indicate"
and other similar words or statements that certain events or conditions
"may" or "will" occur, and include, without limitation, statements
regarding the Company's plans with respect to the exploration of its
Montalembert Project, the exploration potential and analogous deposit
potential of the Montalembert Project and the timing of the Company's
exploration programs. Such forward-looking statements involve known and
unknown risks, uncertainties and other factors which may cause the
actual results, performance or achievements of the Company to be
materially different from any future results, performance or
achievements expressed or implied by such forward-looking statements.
Such risks and other factors may include, but are not limited to, the
results of exploration activities; the ability of the Company to
complete further exploration activities; the ability of the Company to
complete transactions on terms announced; timing and availability of
external financing on acceptable terms and those risk factors outlined
in the Company's Management Discussion and Analysis as filed on SEDAR.
Enforcer Gold does not undertake to update any forward-looking
information except in accordance with applicable securities laws.

TSX Venture closing price for VEIN-V
Date: 2017/09/11
Closing Price: 0.16

TEL:  (647) 496-7984  Steve Roebuck, President & CEO
CELL:  (905) 741-5458
EMAIL:  contact@enforcergold.com
INTERNET:  www.enforcergold.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1725400017TS11725400913-05362920170912