Source	Marketwire
Date	09/14/2017
Time	08:54:35 AM

Company	 GLEN EAGLE RESOURCES INC.
Title	Glen Eagle Resources Inc.: First Results From The Ongoing Exploration 
Program at La Cobra





    CDNX Symbol: GER











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Glen Eagle Resources Inc.

TSX VENTURE SYMBOL: GER

September 14, 2017

Glen Eagle Resources Inc.: First Results From The Ongoing Exploration Program 
at La Cobra


MONTREAL, QUEBEC--(Marketwired - Sept. 14, 2017) - Glen Eagle Resources Inc. 
(TSX VENTURE:GER) ("Glen Eagle" or the "Company") is pleased to announce sample 
results from initial sampling at the La Cobra project in Honduras as well as at 
other sites important to Company production performance at the Cobra Oro CIL 
plant in Choluteca, Honduras.

Given the easy access from the western property entrance, samples were taken 
from the area which was the logical choice to start exploration sampling. 
"Historically, this area has produced lower grades compared to other mining 
areas within the 775 ha La Cobra Concession", said CEO Jean Labrecque, "however 
the consistency of values coming from a limited number of samples remains a 
promising indicator for future site exploration".

/T/

----------------------------------------------------------------------------
Sample         Sample Type                        Property     UTM  Northing
No.                                                           Zone         m
----------------------------------------------------------------------------
Surface Grab Sample
E5810406        Unconsolidated Material           La Cobra    16 P    435431
----------------------------------------------------------------------------
1.2 m Vein Channel Sample True
E5810407        Width                             La Cobra    16 P    435419
----------------------------------------------------------------------------
E5810408       Grab Sample Alteration Zone        La Cobra    16 P     Under
----------------------------------------------------------------------------
1.4 m Vein Channel Sample True
E5810409        Width                             La Cobra    16 P     Under
----------------------------------------------------------------------------
E5810410       Dump Grab Sample Broken Rocks      La Cobra    16 P    435457
----------------------------------------------------------------------------
Certified Reference Sample OREAS
E5810411        62e
----------------------------------------------------------------------------
E5810412       Dump Grab Sample Broken Rocks      La Cobra    16 P    435482
----------------------------------------------------------------------------
E5810413       Artisanal Miner Dump Sample     Client Site    16 P    504648
----------------------------------------------------------------------------
E5810414       Artisanal Miner Dump Sample     Client Site    16 P    460771
----------------------------------------------------------------------------
E5810415       Artisanal Miner Dump Sample     Client Site    16 P    460774
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Sample         Sample Type                      Easting Elevation    Au   Ag
No.                                                   m         m   g/t  g/t
----------------------------------------------------------------------------
Surface Grab Sample
E5810406        Unconsolidated Material         1494154        53  0.66  3.5
----------------------------------------------------------------------------
1.2 m Vein Channel Sample True
E5810407        Width                           1494199        58  4.51  3.6
----------------------------------------------------------------------------
E5810408       Grab Sample Alteration Zone       ground        58  0.98  2.2
----------------------------------------------------------------------------
1.4 m Vein Channel Sample True
E5810409        Width                            ground        58  0.30  2.3
----------------------------------------------------------------------------
E5810410       Dump Grab Sample Broken Rocks    1494185        34  8.23  7.6
----------------------------------------------------------------------------
Certified Reference Sample OREAS
E5810411        62e                                                9.17 10.2
----------------------------------------------------------------------------
E5810412       Dump Grab Sample Broken Rocks    1494194        38  2.50  6.3
----------------------------------------------------------------------------
E5810413       Artisanal Miner Dump Sample      1470657       462  0.31  1.8
----------------------------------------------------------------------------
E5810414       Artisanal Miner Dump Sample      1502674        95  4.93 77.4
----------------------------------------------------------------------------
E5810415       Artisanal Miner Dump Sample      1502678        93  3.97 61.9
----------------------------------------------------------------------------

/T/

Each sample was comprised of approximately 5 to 7 kilos of rocks that were 
later pulverized and homogenized to be more representative of each area being 
sampled. The next sampling program will likely be conducted from the east side 
of the property where historical values are known for their better grade. Fully 
mapping and sampling accessible underground vein exposures will also become a 
priority for ongoing exploration.

Of interest are the results of sample E5810410, which returned 8.23 g/t gold 
and 7.6 g/t silver, sample E5810412, which returned 2.50 g/t gold and 6.3 g/t 
silver. These samples were from the mine, site of a historic past producing 
gold and silver mine in southern Honduras. Samples consisted of blocky vein 
material with no visible mineralization but with evidence of hydrothermal 
alteration and textures potentially indicative of a low-sulphidation epithermal 
gold/silver deposit style. Sample E5810409 was taken from surface in a small 
pit and contained some surface-derived soils as well as rock fragments. The 
underground rock samples were taken of vein footwall alteration as well as vein 
material. The paucity of gold in the vein sample underground together with the 
4.51 g/t gold and 3.6 g/t silver in the same vein at the adit portal may 
suggest that a nugget effect exists.

Glen Eagle is planning a detailed exploration, definition, and resource 
quantification program for the mine dump and adjacent adits in the context of 
an NI 43-101 Technical Report, now underway.

Other samples received included E5810414 and E5810415, which returned gold 
values of 4.93 g/t and 3.97 g/t respectively with silver values of 77.4 g/t and 
61.9 g/t respectively. These samples are from a dump site at another southern 
Honduras past-producing gold/silver operation.

Of interest at this client site is that the vein source of the dump material 
was crushed, but was not processed further. As a result, it does not have to 
undergo primary crushing at the Cobra Oro CIL plant and shipments can be 
unloaded straight into the fine ore bin.

One Certified Reference Material sample was inserted into the sample stream - 
OREAS 62e. The certified gold value for OREAS 62e is 9.13 g/t, with a standard 
deviation of 0.41 g/t. The received gold value for sample E5810411 was 9.17 
g/t, well within the 95% confidence interval. The certified silver value for 
OREAS 62e is 9.86 g/t silver, with a standard deviation of 0.37 g/t (4-acid 
digestion). The received silver value for sample E5810411 was 10.2 g/t, within 
one standard deviation, but slightly outside the 95% confidence interval. Thus, 
these analyses from Agat Laboratories of Mississauga, Ontario, are deemed 
accurate in the analyses provided for gold and silver.

None of the samples showed anomalous concentrations of base metals.

Jim Steel, MBA P.Geo is the independent QP working on the La Cobra project. He 
has read and approved the technical content of this News Release.

"Neither TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release." Values in the 
news release are quoted in Canadian dollars.

- 30 -

CONTACT INFO:

Glen Eagle Resources Inc.
Jean Labrecque
President
514-808-9807

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=598432107