Source	CANADA NEWSWIRE
Date	09/18/2017
Time	05:16:44 AM

Company	 Hannan Metals Ltd.
Title	Hannan Drills 4.0 Metres (at) 0.7% Zinc, 8.9% Lead and 31 G/t Silver (8.6%
ZnEq) in First Step-out Hole at Kilbricken, Ireland





    CDNX Symbol: HAN











Press Release




" BC-Hannan-DrillUpdate   09-18 1530
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Hannan Drills 4.0 Metres (at) 0.7% Zinc, 8.9% Lead and 31 G/t Silver (8.6%
ZnEq) in First Step-out Hole at Kilbricken, Ireland@

VANCOUVER, Sept. 18, 2017 /CNW/ - Hannan Metals Limited("Hannan" or the
"Company") (TSX.V: HAN) (OTCPK: HANNF) is pleased to announce drill results
from the second hole completed in its resource expansion program at the
100%-owned Kilbricken zinc-lead-silver-copper deposit in County Clare,
Ireland. Thirteen holes are planned in this 8,500 metre drill program,
scheduled to be completed during the first quarter of 2018.
Key Points:
<<

--  Significant mineralization was intersected in DH 17-3679-218 ("DH218"),
the first diamond drill hole to test outside the Kilbricken resource
(Figure 1). Massive sulphides were discovered within a down-hole
thickness of 55 metres, including:
>>
<<

o 4.0 metres (at) 0.7% Zn, 8.9% Pb and 31 g/t Ag (8.6% ZnEQ) from 526 metres,
including 1.4 metres (at) 1.6% Zn, 15.2% Pb and 53 g/t Ag from 526 metres and
1.0 metres (at) 0.4% Zn, 13.8% Pb and 46 g/t Ag from 529 metres;
o 6.0 metres (at) 2.5% Zn, 1.8% Pb and 13 g/t Ag (4.4% ZnEQ) from 544 metres,
including 2.1 metres (at) 5.0% Zn, 3.7% Pb and 25 g/t Ag from 548 metres;
o 6.4 metres (at) 4.8% Zn, 1.3% Pb and 15 g/t Ag (6.3% ZnEQ) from 558 metres,
including 1.1 metres (at) 13.3% Zn, 3.1% Pb, 34 g/t Ag from 558 metres;
o 10.0 metres (at) 3.4% Zn, 1.0% Pb and 13 g/t Ag (4.7% ZnEQ) from 571 metres;
>>
<<

--  DH218 is a 50 metre up-dip step out from the Fort Zone and showed good
lateral continuity of mineralization from adjacent holes, including
drill hole DH167 which intersected a lower zone of mineralization of 4.5
metres (at) 0.8% Zn, 2.6% Pb, 18.91% Cu, 867.6g/t Ag from 616.5m; and a 70
metre up-dip step out from drill hole DH217 which intersected 8.0 metres
(at) 4.1% Zn, 33.7% Pb and 174 g/t Ag from 528 metres and 26.6 metres (at)
7.5% Zn, 0.9% Pb and 14 g/t Ag from 588 metres (Hannan Press Release, 20
July 2017) (Figure 1);
--  The mineralized position remains open for further testing up-dip from
DH218;
--  Two holes have been completed by Hannan at Kilbricken, and one in
progress for a total of 1,986 metres. A 8,500 metre resource expansion
drill program is ongoing, with two drill rigs now at site to test along
strike and down dip from the mineral resource area (Hannan Press
Release, 10 July, 2017). Drilling will continue through to Q1 2018.
>>
Mr. Michael Hudson, CEO and Chairman, states: "DH218 is the first hole
drilled by Hannan outside the Kilbricken mineral resource, and clearly
demonstrates the potential for resource expansion at Kilbricken. The
higher-grade mineralization shows good lateral continuity within a broader
mineralized zone totaling 55 metres down hole length which remains opens
up-dip with further opportunities to extend. This is a strong start to our
resource expansion drill program."
A plan and cross section view of the drill results is provided in Figure
1. Table 1 shows highlight intersections and Table 2 shows all relevant collar
and assay information. The true thickness of mineralized intervals at
Kilbricken is interpreted to be greater than 95% of the sampled thickness.
The maiden mineral resource for Kilbricken was published on July 10,
2017, and immediately ranked Kilbricken as one of the top ten base metal
deposits discovered in Ireland by tonnes and grade. Total indicated mineral
resources were calculated as 2.7 million tonnes at 8.8% zinc equivalent
("ZnEq"), including 1.4 million tonnes at 10.8% Zneq and total inferred
mineral resources of 1.7 million tonnes at 8.2% ZnEq, including 0.6 million
tonnes at 10.4% ZnEq. Importantly, as DH218 shows, the initial resource is
expandable at all scales, from near-resource to prospect scale.
NI 43-101 Technical Report:On August 22, 2017, Hannan filed an
independent National Instrument 43-101 Technical Report (the "NI 43-101
Technical Report") on The Mineral Resource Estimate for the Kilbricken
Zinc-Silver-Lead-Copper Project Co. Clare, Ireland For Hannan Metals Ltd in
support of the Company's news release dated July 10, 2017. The NI 43-101
Technical Report was authored by Mr. Geoff Reed of Reed Leyton Consultants and
Dr. John Colthurst who are independent "qualified persons" as defined by
National Instrument 43-101. The NI 43-101 Technical Report may be found under
the Company's profile on SEDAR at www.sedar.com and on the Company's website
at www.hannanmetals.com.
Technical BackgroundA diamond drill rig from Priority Drilling Limited
with water recirculation and drill cuttings collection systems was used for
the drill results reported here. Core diameter is NQ2 (50.6 mm). Core
recoveries were excellent and average close to 95-100% in fresh rock. After
photographing and logging, core intervals averaging 1-2 metre for mineralized
samples were cut in half at Hannan's core facilities in Ennis, County Clare,
Ireland. The remaining half core is retained for verification and reference
purposes.
Analytical samples were transported by Hannan personnel from site to the
ALS Loughrea located at Dublin Road, Loughrea, County Galway, Ireland. At the
laboratory samples are dried, crushed to 100% passing 2mm, then 500 grams
pulverized for multi-element analysis by method ME-MS6, a four-acid digest
performed on 0.25 g of sample to quantitatively dissolve most geological
materials. Analysis is via ICP-MS + ICP-AES. Samples assaying over range 1%
zinc, lead, or copper and 100 g/t silver were re-assayed using methods
Ag/Pb/Zn-OG62, a precise ore grade method to determine lead, zinc and silver
by HF-HNO3-HClO4 Digest, HCl leach and ICP-AES. The QA/QC program of Hannan
consists of the systematic insertion of certified reference material of known
base metal content and blanks at the start of each batch and within
interpreted mineralized rock. In addition, ALS inserts blanks and standards
into the analytical process.
About Hannan Metals Limited (TSX.V:HAN) (OTCPK: HANNF)
Hannan Metals Limited has 100% ownership of the County Clare Zn-Pb-Ag-Cu
project in Ireland, which consists of 9 prospecting licences for 32,223
hectares. Zinc remains in tight supply amidst rising demand and stagnant
supply. Ireland is a leading global jurisdiction for zinc mining and
exploration. In 2015, Ireland was the world's 10th largest zinc producing
nation with 230,000 tonnes produced.
Over the last decade, the team behind Hannan has forged a long and
successful record of financing and discovering mineral projects in Europe.
Additionally, the team holds extensive zinc experience, gained from the
world's largest integrated zinc producer of the time, Pasminco Ltd.
Mr. Michael Hudson FAusIMM, Hannan's Chairman and CEO, a Qualified Person
as defined in National Instrument 43-101, has reviewed and approved the
technical disclosure contained in this news release.
On behalf of the Board,
"Michael Hudson"Michael Hudson, Chairman & CEO
Forward Looking Statements
Certain information set forth in this news release contains
"forward-looking statements", and "forward-looking information" under
applicable securities laws. Except for statements of historical fact, certain
information contained herein constitutes forward-looking statements, which
include the Company's expectations regarding future performance based on
current results, expected cash costs based on the Company's current internal
expectations, estimates, projections, assumptions and beliefs, which may prove
to be incorrect. These statements are not guarantees of future performance and
undue reliance should not be placed on them. Such forward-looking statements
necessarily involve known and unknown risks and uncertainties, which may cause
the Company's actual performance and financial results in future periods to
differ materially from any projects of future performance or results expressed
or implied by such forward-looking statement. These risks and uncertainties
include, but are not limited to: The Company's expectations regarding the
current drill program, liabilities inherent in mine development and
production, geological risks, the financial markets generally, and the ability
of the Company to raise additional capital to fund future operations. There
can be no assurance that forward-looking statements will prove to be accurate,
and actual results and future events could differ materially from those
anticipated in such statements. The Company undertakes no obligation to update
forward-looking statements if circumstances or management's estimates or
opinions should change except as required by applicable securities laws. The
reader is cautioned not to place undue reliance on forward-looking statements.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
Table 1: Highlight intersections from DH 217. Lower cut-off 3% ZnEq.
HOLE                From          To     Width (m)          Zn%     Pb%  Ag 
ppm      ZnEq%
----                ----          ---    --------           ---      ---   
------       ----

DH218                       526          530           4.0      0.67      
8.86          30        8.65
-----                       ---          ---           ---      ----      
----         ---        ----

incl           526          527           1.4      1.56      15.2          
53       15.21
----           ---          ---           ---      ----      ----         
---       -----

incl           529          530           1.0      0.44      13.8          
46       12.82
----           ---          ---           ---      ----      ----         
---       -----

544          550           6.0      2.50      1.84          13        4.37
---          ---           ---      ----      ----         ---        ----

incl           548          550           2.1      5.02      3.69          
25        8.75
----           ---          ---           ---      ----      ----         
---        ----

558          564           6.4      4.80      1.26          14        6.33
---          ---           ---      ----      ----         ---        ----

incl           558          559           1.1      13.3      3.13          
34       16.93
----           ---          ---           ---      ----      ----         
---       -----

571          581            10      3.44      1.00          13        4.72
---          ---           ---      ----      ----         ---        ----

Note: The zinc equivalent (ZnEq) value was calculated using the following 
formula: ZnEq% (equal sign) Zn % + (Cu% (x) 2.102) + Pb% (x) 0.815) + (Ag g/t 
(x) 0.023)
with assumed prices of Zn $2587/t; Cu $5437/t; Pb $2108/t and Ag $18.44/oz.

Table 2: Collar Information for Resource Expansion Program at the
Kilbricken Project (Irish National Grid)
HoleID East        North        Azimuth     Dip       RL         Depth (m)
------ ----        -----        -------     ---      ---          --------

DH217      139133       176006         020      -82      22.433              714
-----      ------       ------         ---      ---      ------              ---

DH218      139165       176035         010      -81      22.735              651
-----      ------       ------         ---      ---      ------              ---

DH219      139168       175979                 -90      22.443              621

0                        In progress


---

SOURCE Hannan Metals Ltd.



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/September2017/18/c8197.html

-0-                           09/18/2017
/For further information: www.hannanmetals.com, 1305 - 1090 West Georgia
St., Vancouver, BC, V6E 3V7, Mariana Bermudez, Corporate Secretary, +1 (604)
685 9316, info(at)hannanmetals.com/
(HAN. HANNF)

CO:  Hannan Metals Ltd.
ST:  British Columbia
IN:  MIN
SU:

-30-